## Slide 1: MASQUE for Enhanced Traffic Management
Ericsson

## Slide 2: MASQUE Specifications
IETF MASQUE (Multiplexed Application Substrate over QUIC Encryption) WG was established in June 2020.​
It was Chartered to specify secure proxy protocols and mechanisms based on QUIC.
Main deliverables include so far:​
RFC 9297 - HTTP Datagrams and the Capsule Protocol (ietf.org)​
Defines the concept of datagrams for HTTP. Primarily to be used for HTTP3 over QUIC with support for the datagrams. ​
RFC 9298 - Proxying UDP in HTTP (ietf.org) ​
Extends HTTP with support for UDP proxying. It uses HTTP datagrams​
Work ongoing and soon to become RFCs as well​
draft-ietf-masque-connect-ip-01 - IP Proxying Support for HTTP ​
Extends HTTP with support for IP proxying​
The MASQUE WG has been rechartered to focus on extensions to the base specifications. This allows the WG to work on extensions such as adding sequence numbers to HTTP datagrams (which will be used by ATSSS).

## Slide 3: MASQUE Technology Principles
An HTTP-based tunnel is established between a client and a relay (aka MASQUE server) which receives traffic from the client through the tunnel and forwards it to a target server or another relay. While earlier versions of HTTP are supported it is mostly intended to be used with HTTP3 over QUIC.​
The MASQUE server provides a proxy service that forwards multiple flows inside an HTTP3 connection:​
  HTTP3 settings indicate support for HTTP datagrams. Extended HTTP CONNECT method with new upgrade tokens indicate UDP or IP proxying. ​
  The HTTP-based CAPSULE protocol allows for tunnel configuration messages and stream-based encoding of encapsulated datagrams.​
  Multiple encapsulated connections: End-to-end security is unaltered by proxy​
​
​
​
​Client establishes HTTP3 tunnel connection to MASQUE proxy (yellow)
Client establishes HTTP3 tunnel connection to MASQUE proxy (yellow)​
This technology allows endpoints and in-network relays to exchange information explicitly​
Client
MASQUE
Server
Target
Server
(or second relay)
HTTP3 / QUIC tunnel
End-to-end
connection

## Slide 4: MASQUE Deployment Examples
3GPP Release 18 ATSSS
Support for MP-QUIC and MASQUE introduced to enable packet splitting of UDP flows across 3GPP and non-3GPP access
Could also support general IP flows but this was not part of rel-18 (could be future extension)
Relay Service for Privacy (on the field)
It consists of two QUIC/MASQUE proxies (relays):
  Ingress proxy: assigns the user an anonymous IP address (maps to their region but not their actual location).
  Egress proxy: decrypts the web address they want to visit and forwards them to their destination.
This separation of information protects the user’s privacy. No single entity can identify both who a user is and which sites they visit.
Application
Server
Application
Application
MASQUE
Ingress proxy
Application
MASQUE Egress proxy
Client
Non-3GPP
AN
RAN
UPF
SMF
N3IWF
Multi-access PDU Session
MASQUE / MP-QUIC client
MASQUE / MP-QUIC proxy
W-AGF

## Slide 5: MASQUE enabled 5GS Benefits this proposal brings
5GS may generalize the usage of MASQUE that has been introduced for ATSSS in Release’18.
MNO may be able to satisfy user E2E concern for privacy and the network needs integrating the MASQUE relay in the UPF (i.e. the Mobile network takes part in the relay service ).
  MASQUE can be used for exchange of explicit information between end-points and in-network relays. Integrated in the UPF Policy Control Enforcement Point, it may facilitate Traffic Detection on guaranteed information for:
    Traffic Management (e.g. QoS, charging…)
    Traffic Data Collection (e.g. for Analytics)
  (Compared to using information from passive listeners, suffering from increasing encryption trend and conditioned to traffic changes)
The information exchanged is controlled, correct and useful. It is not subject to changes in communication patterns and in how traffic flows are observed by the network.
It may be an opportunity for new use cases and for MNOs to establish new and well-defined business relationships

## Slide 6: SID Summary
Main objective of this study is to study the potential of MASQUE technology to enhance 5GC Traffic management capabilities.
The Study evaluates whether ATSSS MASQUE proxy in UPF should be generalized in Release’19.
This study determines whether and how MASQUE capabilities in the 5GC user plane:
  Can benefit the 5GS Traffic management by explicit information exchange on fully encrypted traffic. The study identifies the relevant information that would be exposed.
  Can benefit other 5GC functions like reporting of user plane data as input to analytics or to monitor the correct URSP enforcement in the UE.
  Need to be advertised towards the UE, and which information the UE needs to be provisioned with if any.
  Can integrate in the PCC Framework, and which enhancements are required the PCC framework, if any.
Any solutions consider user plane transmission efficiency and are not be limited to work with QUIC traffic only or specific MASQUE deployments (i.e. one or two-proxies).
Proposal is to leave HR roaming scenarios out of scope in this release.