## Slide 1
Views on Integrated Sensing and Communication
3GPP TSG-WG SA2 Meeting #157 S2-2306807
Berlin, May 22– 26, 2023

## Slide 2
Status Quo in SA1
1. Focus on NR Communication-assisted sensing, no impacts on EPC and E-UTRA
2. Sensing is different from and more than UE positioning: Sensing target may be not UE, and the network may not know the target is a UE even it is. Sensing is to get information about characteristics of the environment and/or objects within the environment (e.g. shape, size, speed, location, distances or relative motion between objects
3. The 5GS can utilize non-3GPP data (e.g. Radar, camera)
Smart Transportation
low-altitude UAV
Smart home
Smart city
Smart factory
Security
Categories of use cases (6)
Indoor
Outdoor
UE send & receive
Sensing modes (6)
gNB send & receive
UE send, gNB receive
UE1 send, UE2 receive
gNB send, UE receive
gNB1 send, gNB2 receive
Observation 1: SA1 can provide consolidated requirement in June. SA2 can agree the SID in Q3, and start the technical work in Q4.
Completion ratio: 80%.
SID completion time: June, 2023
WID is expected to be agreed in May

## Slide 3
Overview of the enhancements on sensing architecture
Expected enhancements from SA2 perspective
Possible topics that needs RAN coordination
RAN3: Signaling procedures between involved entities to support sensing control
Sensing service authorization
Sensing service control
Sensing entities registration/discovery
Sensing measurement collection/result calculation
Sensing result exposure
Policy/Charging
Security
Observation 2: SA2 has topics that can be dealt within SA2 (topics #A), and topics that need RAN coordination (topics #B). Topic #B also includes the one (#B1) that is helpful for the down selection in SA2.
SA2 study should start before RAN WGs, and the normative work in SA2 can start independently with RAN PHY study.
Possible topics can dealt within SA2
Topics #B: framework in SA2, protocol details in RAN. Reserve resource in RAN side.
Topics #A: SA2 leads the E2E architecture design and should start the work as earlier as possible to coordinate among different WGs
Rel-19 ISAC needs the involvement both SA2 and RAN WGs.
RAN work that justifies the feasibilities of Sensing operations
RAN1/RAN4: up to RAN WGs.
  NW-based sensing: SA2 is free of dependency of RAN PHY study.
  UE involved sensing: to be determined by RAN WGs.
Topics #B1: RAN input helpful for down selection

## Slide 4
Expectation on the Rel-19 timeline of ISAC
SA2 timeline
Q3
RAN WGs timeline
ASN.1
Q2
study
normative
Study + normative (Maybe start from 2024 Q2)
study
RAN
SA2
TR 100%
SA1
study
normative
TS 100%
SA2 agrees the SID in Q3
Observation 3: SA2 can start the work in Q4.
Observation 4: SA2 coordinates with RAN in study/normative phase for RAN-related aspects, as what we did in many prior Rel-19 studies
2023 | 2024 | 2025
Q2
Q4
Q3
Q3
Q4
Q4
Q1
Q1
Q2
Q1

## Slide 5
Expectation on work scope of Rel-19 ISAC
SA2 is assumed to provide a future-proof architecture for supporting all potential sensing modes and is free of RAN dependency
Have an end-to-end support for ISAC in Rel-19, at least for some use cases identified by SA1.
Work split among the WGs
  SA2: E2E architectural design under full MNO control, use the 5G system architecture as the baseline.
  RAN3: Protocol design in coordination with SA2.
  RAN1/RAN4: TBD (RAN WGs to determine). SA2 can start the work independently.
No restrictions on the future enhancement for sensing

## Slide 6
Proposal
It is proposed to agree the ISAC SID in 2023Q3 and start the technical work in 2023 Q4.
It is proposed to complete the basic yet future-proved ISAC feature in Rel-19 SA2, including the SID and WID.