## Slide 1
Motivation for study on R19 enhancement for Proximity based Services in 5GS
  3GPP TSG-SA2 Meeting #157
  Berlin, Germany, 22–26 May, 2023
  China Telecom
  S2-2306999

## Slide 2
  SA2 – 5G ProSe background
The 5G System has been enhanced to support Proximity Services in Release 17 as specified in TS 23.304, including:
    ProSe Direct Discovery;
    ProSe Direct Communication including unicast, broadcast and group communication;
    One Hop UE-to-Network Relay (U2N Relay);
    PC5 or Uu Path Selection policy provisioning.
    Further architecture enhancements of 5G System to support Proximity Services have been specified in Release 18, including:
    One hop UE-to-UE Relay (U2U Relay);
    Path switching between two indirect communication path for U2N Relay;
    Direct path switching between PC5 and Uu;
    Multi-path transmission using one indirect path via U2N Relay and Uu path;
    Emergency Services for Remote UE over U2N Relay.;
    Public Warning Notification Relaying by U2N Relay.
Notes: WG – SA1/SA2/SA5/CT1/CT3/CT4
Key driver 立项来源/类别: 1. New capability for consumer （ToC）
2. New capability for B2B （ToB）
3. Extend for R18 (R18或之前版本项目延续）
4. Requirement from other WG/org. (其他WG或者组织需求）
Background Information：与立项技术相关的背景/需求介绍（最好有图、表、use case等展现方式）
Key Objectives：立项的主要研究内容

## Slide 3
  Motivation for ProSe_Ph3 in R19 (1/4)
    Rel-18 5G ProSe leftovers worth to be further investigated in the Rel-19:
    Enhancement of UE-to-Network Relay for support of multiple NR PC5 hops;
    Whether and how to support of non-3GPP RAT (e.g. Wi-Fi or Bluetooth) over PC5 reference point for Layer-3 UE-to-Network Relay.

## Slide 4
Spec | Requirements
TS22.261 | Multi-path U2N Relay should be supported: Connection between remote UE and relay UE can be 3GPP RAT or non-3GPP RAT；. VN service, IMS service for Remote UEs should be supported: A 5G system shall be able to support all types of traffic e.g. voice, data, loT small data, multimedia, MCX for indirect network connection mode. L3 U2N Relay over non-3GPP access should be supported: The 5G system shall support use of a relay UE that supports multiple access types (e.g. 5G RAT,WLAN access, fixed broadband access).
TS22.125 | Identification of access via ProSe U2N Relay should be supported: To identify the relayed traffic of an UE-to-network Relay, e.g. to be able to apply different rating.
  Motivation for ProSe_Ph3 in R19 (2/4)

## Slide 5
  Multi-hop U2N support capability: Multi-hop is supposed to better solve the coverage problem, especially at high frequencies.
  Multi-path U2N support capability: Multi-path is proposed to achieve better data rate and reliability.
  IMS service for ProSe-enabled Remote UEs.
    Voice call should be supported and maintained when a Remote UE moves out of coverage.
  5G VN service for ProSe-enabled Remote UEs.
    There are many working interactions between A and B (document transfer, signature, approval, meeting, etc.)
    VN members hope that they can communicate normally and without interruption no matter where they are.
  Motivation for ProSe_Ph3 in R19 (3/4)

## Slide 6
  UE-to-Network Relay networking where the Relay UE connects with non-3GPP access.
    This is a fixed mobile convergence scenario in the factory floor to achieve better resource utilization. Due to the wiring problem and the possibility of signal interference in the unauthorized frequency band, setting too many Wifi AP points should be avoided. Coverage extension is required.
    The scenario expands the access type where Remote UEs can access a WiFi AP without WiFi authorization.
  Motivation for ProSe_Ph3 in R19 (4/4)
  Service control of non-3GPP RAT (e.g. Wi-Fi or Bluetooth) over PC5 for Layer-3 UE-to-Network Relay.
    Support of non-3GPP link over PC5 that was left out from the initial Rel-18 proposal.
  Identification of the access via ProSe U2N Relay.
    For monitoring and charging purposes.
  NWDAF assisted ProSe.
    Study on whether and how the Proximity Services can benefit from NWDAF reporting.

## Slide 7
  Enhancement of UE-to-Network Relay for support of multiple NR PC5 hops.
Whether and how to support of non-3GPP RAT (e.g. Wi-Fi or Bluetooth) over PC5 reference point for Layer-3 UE-to-Network Relay.
Support of multi-path transmission using different UE-to-Network Relay.
Support of Layer-3 UE-to-Network Relay over non-3GPP access.
Support of IMS service for Remote UEs via UE-to-Network Relay.
Support of VN service for Remote UEs via UE-to-Network Relay.
Support of identifying the access via Layer-3 ProSe UE-to-Network Relay with N3IWF.
Whether and how the Proximity Services can benefit from NWDAF reporting.
  Summary - Proposed Objectives for ProSe_Ph3
Notes: WG – SA1/SA2/SA5/CT1/CT3/CT4
Key driver 立项来源/类别: 1. New capability for consumer （ToC）
2. New capability for B2B （ToB）
3. Extend for R18 (R18或之前版本项目延续）
4. Requirement from other WG/org. (其他WG或者组织需求）
Background Information：与立项技术相关的背景/需求介绍（最好有图、表、use case等展现方式）
Key Objectives：立项的主要研究内容

## Slide 8
THANKS