## Slide 1: Discussion on Advanced Industrial Internet of Things
Huawei, HiSilicon

## Slide 2: Use Cases and Requirements
The industries, e.g. motor vehicle factory, requires hundreds of terminals in a serving area (e.g. as described in TS 22.104). But currently the network can only support limited terminals (due to URLLC devices requiring more recourse for overprovisioning) . It is noticed 5GS has transferred many unnecessary bits:
  For example, Ethernet has a minimum frame size of 64 Bytes, comprising an 18-Byte header and a payload of 46 Bytes. The application-layer packet payload of industrial applications is usually small, e.g. 20 Bytes. (Please see TS 22.104 [1]).
  there are lots of duplicated packets in the industry scenario, the content (except the sequence number) in the payload of the packets does not change (unless there is a status update, such as an alarm).
UE-UE communication is widely used in industry scenario. However some features, e.g. BAT adjustment, Survival Time, cannot be used in UE-UE communication.
  For BAT adjustment in the UE2UE scenario, if the RANs provides the feedback (e.g. BAT offset) independently, the gap between the two RANs may not be synchronized, and the adjustment cannot be performed correctly.
  For Survival Time in the UE2UE scenario, it is unclear how the RAN nodes coordinate the packet loss, especially the packet is lost in the second air interface.

## Slide 3: Use Cases and Requirements
The reliability with a single UE suffers due to the radio channel quality, this becomes worse in the circumstance that has a lot of steels, e.g. warehouse, harbor, workshop, where the work equipment the location varies a lot thus result in poor connection stability.
  Even though URLLC feature supports redundant user plane paths based on multiple UEs per device, but the upper layer protocols are assumed to make use of the multiple user plane paths for high reliability, this assumption places a restriction on a flexible deployment and needs to be lifted.
  The current high reliability using redundant transmission with dual connectivity or redundant user plane paths requires resource overprovisioning.
The connections between different sites and private/public clouds can be controlled via e.g. SD-WAN or E/IP-VPN technologies in campus network deployment, there is a need to support 5G VN integration with legacy LAN network in scenarios like bank branches, chain stores, factory areas, enterprise campuses, and electric grids etc..
  This corresponds to the leftover SA1 requirement in TS22.261, clause 6.24: The Ethernet transport service shall support the transport of Ethernet frames between a UE that an Ethernet device is connected to and an Ethernet network in DN (Data Network). .
  there is a need to further address Identified Gaps and Limitation for Exposure of 5G Capabilities in 5G-ACIA-LS-2022-005

## Slide 4: Use Cases and Requirements
Cooperation between multiple mobile robots/AGVs is commonly needed in industry environment. Usually, one of the mobile robots/AGVs in this ad-hoc cooperative group takes on the role of the controller and becomes the ground master clock of this group. And the other collaborating members should be synchronized to the clock and follow its order in a synchronized way, to make the cooperative movement smoothly.
  In order to support the time synchronization service for one or more multiple ad-hoc cooperative groups, the 5GS needs to support the management of the establishment/update of the ad-hoc cooperative groups and its grand master clock.
  The robots/AGVs may join and leave dynamically during the cooperative working. For a newly joined robot/AGV, it should be synchronized with the group immediately. For the leave case, especially when the controller robot/AGV is left, a new ground master clock should be selected and synchronized to other group members as soon as possible.
For time sensitive sectors, precise time information is a key enabler for communication and orchestration of technologies for accurate and optimal wide area monitoring, protection and control. In previous release, it is assumed that the deployments ensure that the targeted UEs and the NG-RAN nodes serving those UEs support Rel-17 propagation delay compensation as defined in TS 38.300. The mechanism of Rel-17 propagation delay compensation is up to the measurement accuracy of UE and NG-RAN node Rx-Tx time difference as described in TS 38.133. The measurement accuracy varies among different channel conditions. .
  For high accuracy time service consumers (E2E accuracy < 250 ns), the Uu measurement accuracy provided to NG-RAN node is demanding high. Hence, the NG-RAN nodes shall be upgraded to support high accuracy time service. Considering the network deployments, the upgrade may be only for some NG-RAN nodes. It is essential to ensure the service assurance under the non-uniformity distribution especially due to UE mobility.
Industrial co-movement
Indoor Mobility of AGV
Time Synchronization service enhancement
Case#1: Time synchronization service for ad-hoc cooperative group
Case#2: Service assurance for high accuracy Time Synchronization service
use case in TS 22.832

## Slide 5: Proposed objectives
It is proposed to have a Rel-19 study item to continue resolving the existing challenges for industrial IoT:
  How to improve efficiency of transmission capacity and the URLLC performance (lower latency and higher reliability) in the industry scenario
    Avoid transferring unnecessary bits (e.g. paddings) in 5GS to improve the efficiency of transmission capacity and the latency performance;
    Support BAT adjustment and survival time in UE-to-UE scenario;
    Improve the support of redundant user plane paths based on multiple UEs without relying on application layer duplication redundancy protocols;
    Improve the support of redundant user plane paths with adaptive mechanism for optimal usage of 5GS resources and to avoid the duplicated reliability.
  How to support integration of 5G VN and legacy LAN
    Integration architecture, e.g. cross-site tunnel establishment and release, QoS provisioning and monitoring for cross-site tunnel, intelligent traffic steering on cross-site tunnel, exposure for reporting and configuration mapping;
    Management of the DN side devices and the UE side device as 5G VN group members;
    Support loop-free Ethernet topology in the case of Ethernet PDU Sessions;
    Support NEF exposure of 5G capabilities to fulfill industrial applications’ requests: e.g. Acknowledging a AF service request within indicated time, VLAN tag assignment without AAA-Server, UE-to-UE QoS with one NEF API, Per QoS characteristic monitoring, IP address assignment via NEF exposure;
  How to support time synchronization service for ad-hoc cooperative group and service assurance for high accuracy time synchronization service