## Slide 1: Motivation for Architecture Enhancements for Advanced Air Mobility in Cellular Enviroment
Qualcomm Incorporated
S2-2307270

## Slide 2: UAV and UAM standard status – SA2
Rel-17
  Introduced mechanisms for UAV identification and authentication/authorization, authorization of C2 traffic, flight authorization.
Rel-18
  Enhancements were introduced for UAVs for the use of PC5 for Direct C2, Broadcast Remote ID, and Detect and Avoid

## Slide 3: SA1 Release 19 Work
SA1 has introduced new requirements for Release 19
  (SA1 Objective 1) Provide additional information to the UAV operator/USS to execute pre-flight preparations and inflight operation (e.g, flight mission application, flight path recommendation, flight monitoring and control)
  (SA1 Objective 2) Use 5G system to support enhancing the UAV flight/route management based on network capacity and QoS information along the planned route
  (SA1 Objective 3) Use 5G system to further enhance the safety and security of drone operations, e.g. supporting UTM in UAV detection and DAA (Detect and Avoid) with network-based solutions
  (SA1 Objective 4) Identify potential new requirements related to redundancy and reliability of command and control (C2) traffic for UAV.

## Slide 4: Advanced Air Mobility
With the rapid growth in aerial vehicles (UAVs, urban transport, EVTOLs, etc.), a large number of activities (ICAO, RTCA, EASA, EUROCAE, FAA, and many other Civil Aviation Agencies) is focusing on ensuring a complete framework for Advanced Air Mobility is being defined
AAM includes UAM (aimed at congested urban areas) and beyond, including rural areas
  Focus is on small UAVs, medium/large goods transport, and people carriers (“aerotaxis”) flying at low and medium altitude
  High altitude aircraft and traditional crewed aircraft are not part of this

## Slide 5: Proposed Objectives for Release 19 Work in SA2
Enhance NEF services to support MNO-UTM data services for intelligent flight planning, flight monitoring, interfacing with UTM infrastructure (e.g. multiple USS), and QoE estimation and planning​
  This corresponds to (SA1 objective 1) and (SA2 objective 2)
  In addition, several recommendation from aviation industry have been introduced (e.g. GSMA and ACJA) for such enhancements to service exposure
  Ensuring a complete set of service exposure by an MNO to entities in the aviation industry (UAS operators, UTM, C2CSPs, etc.) enables a valuable service proposition by MNOs to the aviation industry, and enable cellular networks to be the safe and reliable communication backbone for the aviation vertical

## Slide 6: Proposed Objectives for Release 19 Work in SA2
Enable network-assisted/ground-based DAA solutions leveraging input from sensing and other "sensors" in RAN and UEs, and leverage NEF and edge computing to provide the ground component of a complete DAA solution​
  This corresponds to (SA1 objective 3)
  There is a clear need in the aviation industry for a network-assisted/ground-based solution to enhance current aircraft-to-aircraft solutions to create a comprehensive safety solution for AAM​.
    Work in various aviation groups (RTCA, EUROCAE, EASA, ACJA, etc.) has identified the need for such network-based solutions
    Network-based solutions enable MNOs to provide valuable value-added services to the aviation vertical

## Slide 7: Proposed Objectives for Release 19 Work in SA2
Enhance multi-PLMN connectivity for redundancy ​
  SA1 has been studying requirements for multi-PLMN connectivity for aerial vehicles to provide improved reliability
    The simultaneous connectivity to multiple PLMN, where one is actively used and the other is standby, gives the unique benefit of maximizing reliability in areas where the coverage of a PLMN may not be optimal
    Architectural enhancements need to be studied and gaps identified to enable such scenarios, building on the features already defined by 3GPP
  This relates to some objectives of DualSteer SI, but focuses on some different aspects such as multi-subscription and different PLMNs

## Slide 8: Proposed Objectives for Release 19 Work in SA2
Study support of C2CSP model, potentially via extensions of IMS DC solution and IMS framework.​
  ICAO and RTCA are defining the model for C2 Connectivity Service Providers to leverage cellular networks
  3GPP has defined several tools that enable the C2CSP framework, including the introduction of the IMS Data Channel which is perfect fit for C2 traffic
  The aim is at identifying the building blocks and architectural enhancements to enable the support of the C2CSP model(s) being defined by the aviation industry (ICAO, RTCA, ACJA, GUTMA)