## Slide 1: Discussion on the support of Network Timing Synchronization Status Reporting
Ericsson

## Slide 2: The Way Forward: Alternative#1
As the way forward Alternative#1 has been chosen. The main aspects shall be as follows:
The TSCTSF invokes Namf_Communication_NonUeN2InfoSubscribe service operation towards the AMF to receive notifications related to N2 information class defined for Time Synchronization Status (TSS) without including a list of NG-RAN IDs/TAs for which subscription applies;
The TSCTSF invokes Namf_Communication_NonUeN2MessageTransfer service operation containing an N2 Container encapsulating Timing Synchronization Status Request message to request the NG-RAN(s) to start reporting the Time Synchronization Status. The NGAP message Time Synchronization Status Request contains a Routing ID encoded with the TSCTSF NF ID. The NG-RAN needs to know when there are multiple TSCTSF instances that have requested the TSS reporting so that the NG-RAN could keep reporting until the last TSCTSF instance requests to stop the reporting.
Upon receiving the responses from the NG-RAN node(s), the AMF includes a list of N2 Containers together with the corresponding NG-RAN IDs where each N2 Container encapsulates the NGAP message Timing Synchronisation Status Response or the Timing Synchronisation Status Failure received from that NG-RAN, in the Namf_Communication_NonUeN2MessageTransfer response or Namf_Communication_N2InfoNotify request messages to the TSCTSF. The AMF adds the corresponding NG-RAN ID to enable the TSCTSF to know which NG-RAN has failed to initiate the TSS reporting (when receiving a Timing Synchronization Status Failure). The Timing Synchronization Status Response may indicate a protocol error.
The NG-RAN includes the Routing ID in the Time Synchronization Status Report message. Upon receiving the NGAP message Time Synchronization Status Report message, the AMF forwards the Time Synchronization Status Report message as an N2 Container in the Namf_Communication_N2InfoNotify Request message to that specific TSCTSF.

## Slide 3: Additional comments received
Regarding the S2-2400200 last week, […] there are two different models in the specs how this could work […]:
1) AMF maintains subscription: Clause 9A.2.3.1 in TS 23.041 (CBCF) uses this model.
- AMF stores the NF instance ID that is subscribing for event notifications.
2) AMF as a relay: Clause 6.14.1 in 23.273 (LMF) uses this model.
- NF Instance ID is sent to the RAN, and RAN uses it to send notifications to NF. AMF acts as a relay in between.
[…] the CR submitted last week was a mix between these two and therefore difficult to follow. I revised your CR to follow the model in 1). Also the second option is possible, if that one is more preferable.
Response to these comments and the proposed changes are summarized in next slides.

## Slide 4: Response to the comments/changes (1/2)
The principle being followed in procedures related to PWS (clause 9A.2 of TS 23.041) and to Broadcast of assistance data (clause 6.14 of TS 23.273) is that AMF only offers communication service:
  NF service consumer of Namf_Communication service shall use the Namf_Communication_NonUeN2MessageTransfer to transfer the non-UE related N2 information, e.g. a NGAP message or a NGAP IE, so that the AMF uses the NGAP Message type or NGAP IE type together with the content of the NGAP message or the NGAP IE included in the request message by the NF service consumer, the CBCF or the LMF, to forward the NGAP message or generate the corresponding NGAP message.
  The NF Service consumer may invoke the Namf_Communication_NonUeN2InfoSubscribe service to request AMF to forward certain types of NGAP messages, e.g. N2 Information class “NRPPa” is to receive “NRPPa-PDU” in NGAP for Broadcast of assistance data, and N2 information class “PWS”, “PWS-BCAL” and “PWS-RF” are the PWS related. This is independent of the first bullet -- AMF just “blindly” forwards the NGAP message or IE as specified for the interested N2 Information class (see clauses 6.1.6.4.3.2 and 6.1.6.4.3.3)
There are some differences between PWS and Broadcast of assistance data:
  Besides N2 Information class is different, the AMF uses NGAP message type to trigger sending of the PWS-related NGAP messages, e.g. Write-Replace Warning Message, while the AMF uses NGAP IE type, e.g. NRPPa-PDU IE, to generate NGAP DOWNLINK NON UE ASSOCIATED NRPPA TRANSPORT message (see clause 6.1.6.2.27 for Type: N2InfoContent)
  In case of CBCF, it will create an explicit subscription by invoking Namf_Communication_NonUeN2InfoSubscribe to receive N2 information class “PWS” “PWS-BCAL” and “PWS-RF”, while it is not the case for LMF. It would be an implicit subscription, where the AMF needs to retrieve the default notification URI for receiving N2 information from the LMF NF Profile via the NF service discovery procedure, see e.g. clause 5.2.2.4.1 for NonUeN2MessageTransfer and clause 5.2.2.4.2 for NonUeN2InfoSubscribe, TS 29.518.

## Slide 5: Response to the comments/changes (2/2)
In details about “not-accepted” changes:
In Step 2: “The AMF uses the TSCTSF Instance ID to associate the request with the subscription initiated in Step 1. ”
  [Ericsson]: The AMF has no need to make any association between the NonUeN2MessageTransfer and NonUeN2InfoSubscribe
  Additionally, in this step we would like to clarify that:
  There is no NGAP signalling interaction between NG-RAN and AMF when the AMF receives Namf_communication_NonUeN2InfoSubscribe
  There is no need to include TAs/NG-RAN IDs in the Subscribe request, since which TAs or NG-RAN nodes need to start TSS reporting can be specified by the TSCTSF when invoking a Namf_NonUeN2MessageTransfer request in step 2.
In Step 6-7: “The AMF uses the source RAN Node ID to associate the update with the NG-RAN timing synchronization status update subscription(s) created in Step 1. The AMF notifies the corresponding TSCTSF(s) using the Notification Target(s) as stored in Step 1. The notification contains the latest received NG-RAN timing synchronization status update as received from the NG-RAN. The AMF may aggregate updates from several NG-RAN nodes into a notification.”
  [Ericsson]: we have not included that part as it is incorrect. A specific TSCTSF instance needs to be notified (therefore a TSCTSF Instance ID is used), and the AMF just forwards the notification in an Namf_Communication_N2InfoNotify.
In Step 10-12: there have been the changes proposed when the TSCTSF first sends a “NonUeN2MessageTransfer” and only then “NonUeN2InfoUnSubscribe” to unsubscribe from the TSS info:
  [Ericsson]: TSCTSF sends Namf_Communication_NonUeN2MessageTransfer with “stop” indication and TSCTSF Instance ID after it sends “NonUeN2InfoUnSubscribe”, however, NG-RAN stops reporting the TSS attributes to the AMF once all TSCTSF instances have unsubscribed from NG-RAN timing synchronization status updates.

## Slide 6
Background information
From SA2#160-AdHoc-e

## Slide 7: Background (1/2)
Requirements: Upon the reception of the clock quality detail level and clock quality acceptance criteria (if applicable) in the AF request, the TSCTSF needs to be subscribed to NG-RAN timing synchronization status updates at the NG-RAN nodes that may provision access stratum time distribution information to the target UE, see clause 4.15.9.5 of TS 23.502, v 18.4.0:
#---excerpt from clause 4.15.9.5 of TS 23.502---
0. The AF requests creation or modification of ASTI or PTP based time synchronization service as described in clauses 4.15.9.4 and 4.15.9.3 including clock quality detail level and clock quality acceptance criteria (if applicable) in the request.
If the request is received at the NEF, it checks whether the AF is authorized to send the request and forwards the request to the TSCTSF.
If network timing synchronization status reports are provisioned using node-level signalling via control plane, the TSCTSF determines the serving AMF(s) and the UPF/NW-TT nodes (if applicable) for the UE(s) that needs to initiate network timing synchronization status monitoring.
Otherwise, if network timing synchronizations status reports are provisioned via OAM, steps 1-3 and 5-7 are skipped.
1-2. (When the procedure is triggered by the AF request to influence the 5G access stratum time distribution or by PTP instance activation, modification):
Upon the reception of the clock quality detail level and clock quality acceptance criteria (if applicable) in the AF request in step 0, the TSCTSF needs to be subscribed to NG-RAN timing synchronization status updates at the NG-RAN nodes that may provision access stratum time distribution information to the target UE. NG-RAN timing synchronization status updates provisioning may be configured via AMF (with node level signalling as illustrated in steps 1-2).
The TSCTSF sends Namf_Communication_NonUeN2InfoSubscribe to initiate the subscription for the NG-RAN timing synchronization status updates from the AMF. As part of this subscription, the TSCTSF may specify TA(s) and/or NG-RAN node(s) in the subscription for the timing synchronization status reporting. Based on local configuration and/or TA or NG-RAN node information as received from the TSCTSF, the AMF may subscribe to some or all NG-RAN nodes in the TA(s) for the timing synchronizations status reporting.
…

## Slide 8: Background (2/2)
#---excerpt from clause 4.15.9.5 of TS 23.502 (continue)---
3. (When the procedure is triggered by the AF request for PTP instance activation, modification and if the UPF/NW-TT is involved in providing time information to DS-TT):
Upon the reception of the clock quality acceptance criteria in the AF request in step 0, the TSCTSF needs to be subscribed to UPF/NW-TT timing synchronization status updates at the UPF/NW-TT that may provision time information via PTP to the target UE. UPF/NW-TT timing synchronization status updates provisioning may be configured via OAM or via UMIC.
4. The RAN node is pre-configured for the thresholds for each timing synchronization status attribute as described in clause 5.27.1.12 of TS 23.501 [2]. When the network timing synchronization status exceeds or meets again any of the pre-configured thresholds, the NG-RAN node detects a change on its timing synchronization status (e.g., degradation, failure, improvement).
5-6. If the NG-RAN node detects a change on its timing synchronization status as described in clause 5.27.1.12 of TS 23.501 [2] and the timing synchronization status reporting is configured via the AMF in step 1, the NG-RAN node notifies the AMF providing a NG-RAN timing synchronization status update. The update can contain the information elements listed in Table 5.27.1.12-1 of TS 23.501 [2], and the scope of the timing synchronization status (as described in clause 5.27.1.12 of TS 23.501 [2]). The AMF forwards the update to the subscribed TSCTSF.
7. …
8. …
#---end of the excerpt---
TSCTSF uses an Namf_Communication_NonUeN2InfoSubscribe to send N2 message to an NG-RAN node(s), previously an Namf_Communication_NonUeN2MessageTransfer had been used for this purpose before it was removed by S2-2309819.

## Slide 9: Alternatives triggering NG-RAN to report TSS attributes (1/2)
In this solution, when doing activation, the Namf_Communication_NonUeN2MessageTransfer Request message would include an N2 Container encapsulating the NGAP message "TIMING SYNCHRONISATION STATUS REQUEST”:
  AMF will TRANSPARENTLY forward the message to the concerning NG-RANs based on the TAI List or NG-RAN node identifiers;
  AMF will transparently forward the response message from NG-RANs, either accept or failure result, via the Namf_Communication_NonUeN2MessageTransfer response message, e.g. upon the first acceptance result and a Namf_Communication_NonUeN2InfoNotify request if there are a large list of NG-RANs involved and some of NG-RANs may respond a little late (since it is not possible for the AMF to wait for outcome from all NG-RANs).
  The similar for deactivation.
Alternative#1 for triggering NG-RAN to start reporting the TSS attributes; it exploits an Namf_Communication_NonUeN2MessageTransfer (updated based on the changes prior SA2#161).
The proposed solution that requires changes in the current specifications.

## Slide 10: Alternatives triggering NG-RAN to report TSS attributes (2/2)
In this solution, upon receiving Namf_Communication_NonUeN2InfoSubscribe request from the TSCTSF with a subscription for Time synchronisation Status:
  AMF shall trigger to send the NGAP "TIMING SYNCHRONISATION STATUS REQUEST" message with START to all concerning NG-RANs
  AMF needs to keep the state if the NG-RAN(s) has been activated for Time synchronisation Status report, so that, the AMF can avoid sending the same message again if there is another TSCTSF request the same.
  AMF shall consider the Time synchronization status report deactivated by the TSCTSF if the AMF receives the Namf_Communication_NonUeN2InfoUnSubscribe request to delete the subscription.
  However, the AMF shall deactivate towards the NG-RAN only when no TSCTSF requests Time synchronisation Status Report.
Alternative#2 for triggering NG-RAN to start reporting the TSS attributes; it exploits an Namf_Communication_NonUeN2InfoSubscribe.
The current solution in the specifications.

## Slide 11: Corresponding Requirements in RAN3 (1/3)
According to baseline RAN3 CR (R3-238135), RAN3 has introduced the following Class 1 NGAP Elementary Procedure and related NGAP Messages to activate timing synchronization status report
TIMING SYNCHRONIZATION STATUS REQUEST:
  This message is sent by the AMF to request the NG-RAN node to start or stop reporting of RAN timing synchronization status information.
  Direction: AMF to NG-RAN node

## Slide 12: Corresponding Requirements in RAN3 (2/3)
9.2.yy.4 TIMING SYNCHRONIZATION STATUS REPORT:
  This message is sent by the NG-RAN node to report previously requested RAN timing synchronisation status information.
  Direction: NG-RAN node to AMF
9.3.1.x3 RAN Timing Synchronization status Information
  This IE indicates the RAN timing synchronisation status information provided towards the AMF as defined in TS 23.501 [9]

## Slide 13: Corresponding Requirements in RAN3 (3/3)
9.3.1.x6 RAN TSS Scope
  This IE indicates the scope of the RAN timing synchronisation status as defined in TS 23.501 [9].

## Slide 14: Consideration for AMF implementation (1/3)
Namf_Communication_NonUeN2MessageTransfer service operation is used by a NF Service Consumer to transfer N2 information to the 5G-AN through the AMF in the following procedures:
  Obtaining non-UE associated network assistance data (See clause 4.13.5.6 in 3GPP TS 23.502 [3]); Warning Request Transfer procedures (See clause 9A in 3GPP TS 23.041 [20]);
  Configuration Transfer procedure (see clause 5.26 of 3GPP TS 23.501 [2])
  RIM Information Transfer procedures (see clause 8.16 of 3GPP TS 38.413 [12]).
  Broadcast of Assistance Data by an LMF (see clause 6.14.1 of 3GPP TS 23.273 [42]).
  Management of network timing synchronization status monitoring procedures (see clause 4.15.9.5.1 of TS 23.502 [3]) * This was added in CT4# August meeting, Nokia's CT4 is attempting to remove it.
Hence, TSCTSF shall use Namf_Communication_NonUeN2MessageTransfer service operation to request the AMF to transport the NGAP TIMING SYNCHRONISATION STATUS REQUEST message which is included in an N2 container. The AMF sends the corresponding N2 message, i.e. the Timing Synchronisation Status Request message, based on the N2 Container, to all applicable NG-RAN node(s). Upon receiving the responses from the NG-RAN node(s), the AMF includes a list of N2 Containers together with the NG-RAN Ids where each N2 Container encapsulates the NGAP message Timing Synchronisation Status Response or the Timing Synchronisation Status Failure received from that NG-RAN, in the Namf_Communication_NonUeN2MessageTransfer response or Namf_Communication_N2InfoNotify request to the TSCTSF.

## Slide 15: Consideration for AMF implementation (2/3)
Namf_Communication_NonUeN2InfoSubscribe service operation can used by a NF Service Consumer (e.g. CBCF, PWS-IWF, TSCTSF) to subscribe to the AMF to get notifications about non-UE-specific-N2 information of a specific type (e.g. PWS Indications, TSS).
An NF Service Consumer (e.g. CBCF, PWS-IWF, TSCTSF) may subscribe to notifications of specific N2 information type (e,g PWS Indications, TSS) that are not associated with any UE. In this case, the NF Service Consumer shall subscribe by using the HTTP POST method with the URI of the "Non-UE-N2-Messages Subscriptions Collection" resource (see clause 6.1.3.9.3.1 and Figure 5.2.2.4.2.1-1 of TS XXXXX)
Note that there is no Update of Namf_Communication_NonUeN2InfoSubscribe request. Hence, if the TSCTSF wants, for example, to MODIFY the range of concerning NG-RAN nodes, it needs to create a new subscription
Basically, the existing AMF implementation for Namf_Communication_NonUeN2InfoSubscribe is quite simple, the AMF simply forwards the received NGAP IE or NGAP message applicable to a specific type (as requested in the subscription request) to the consumer NF who has made the subscription
NonUeN2MessageTransfer | Request/Response | Peer AMF, LMF, CBCF, PWS-IWF, TSCTSF
NonUeN2InfoSubscribe | Subscribe/Notify | CBCF, PWS-IWF, TSCTSF
NonUeN2InfoUnSubscribe |  | CBCF, PWS-IWF, TSCTSF
NonUeN2InfoNotify |  | LMF, CBCF, PWS-IWF, TSCTSF

## Slide 16: Consideration for AMF implementation (3/3)
Other aspects: N2InformationTransferReqDataTransfer and NonUeN2InfoSubscriptionCreateData

## Slide 17: Comparison and Conclusion (1/2)
Alternative#2 imposes extra complexity to AMF, e.g.:
  generating non-MM NGAP messages on its own, i.e., generating a TIMING SYNCHRONISATION STATUS REQUEST for a start based on the Namf_Communication_NonUeN2InfoSubscribe Request, and a TIMING SYNCHRONISATION STATUS REQUEST for stop based on the Namf_Communication_NonUeN2InfoUnSubscribe Request;
  keeping track of the timing synchronisation status of each NG-RAN, i.e. the AMF needs to store which TSCTSFs have requested to start "timing synchronization status reporting" and which TSCTSFs have requested to stop "timing synchronisation status reporting" in a NG-RAN node;
  At the moment, the TIMING SYNCHRONISATION STATUS REQUEST message is very simple, it has only one enumeration type IE (start/stop), and thus Alternative#2 works. However, what if new IEs to be added as part of time synchronization status report activation, e.g. to describe the conditions, e.g. different S-NSSAIs, different thresholds to trigger a report, to activate? Different TSCTSFs from different network slices corresponding to different time-sensitive communication domains likely have different parameters to be reported in the future. Alternative#2 is NOT future-proof.
When comes to handling failure scenarios when, for example, one or more NG-RANs fail to activate timing synchronization status reporting, this should be reported to the TSCTSF, e.g. to retry the same after some time. For Alternative#2, AMFs would need:
  to generate an N2 container encapsulating TIMING SYNCHRONISATION STATUS FAILURE or Response message in the Namf_Communication_NonUeN2InfoNotify request message towards the TSCTSF, while be noted that the TIMING SYNCHRONISATION STATUS Request message was not included by the TSCTSF.
  Or alternatively Namf_Communication_NonUeN2InfoNotify request message would need to be enhanced to carry an NGAP cause per NG-RAN Id (which is then needs to be included in the TIMING SYNCHRONISATION STATUS FAILURE or Response message)

## Slide 18: Comparison and Conclusion (2/2)
Alternative#1 matches the current design of the AMF communication service for Non-Ue-related N2 message transfer. However, comparing the existing services, e.g., for the support of the PWS and NRPP where these procedures are also not intended for an individual UE, NGAP has designed a mechanism using, for example, Message Identifier/Serial Number or Routing ID, to determine if the message is from a different sender or with a different content.
To support the scenario where multiple TSCTSFs are deployed, TIMING SYNCHRONISATION STATUS REQUEST shall contain at least a TSCTSF NF ID (e.g. Routing ID) of the TSCTSF sending the request for START or STOP, so that the NG-RAN could store this information and determine if multiple TSCTSFs have requested activation of TIMING SYNCHRONISATION STATUS reporting; therefore, when doing deactivation, the NG-RAN shall keep the TIMING SYNCHRONISATION STATUS active as long as there is at least ONE TSCTSF left.
Furthermore, to be future-proof, different TSCTSFs configured for different network slices may want to set/have different TSS attribute thresholds for the NG-RAN to trigger TSS reporting or a time condition where the NG-RAN performs TSS reporting only in a specific time.
At the message level of the NGAP message "TIMING SYNCHRONISATION STATUS REPORT”, the Routing ID shall be included to contain a TSCTSF NF ID as the intended receiver, so that the AMF will forward the report only to that specific TSCTSF, similarly as shown below:

## Slide 19: Concluding Remarks
The Timing Synchronisation Status Reporting procedure and its related NGAP messages are not for Mobility Management. In principle, these messages should be made transparent to AMFs. AMFs offer the Namf_communication service to transport these messages between TSCTSF and NG-RAN, similarly as for SMF (for a PDU session), MB-SMF (for a Broadcast MBS session), CBCF (for Public Warning messages), LMF, etc. Since AMF is just offering the communication service, it should not be required to build non-MM related messages on its own instead of just building these NGAP messages based on an N2 container (encapsulating an NGAP IE or an NGAP message). Alternative#1 matches the current design of the AMF communication service for transferring Non-Ue-related N2 messages. This alternative is also future-proof since the NGAP message can be evolved independently of the Namf_Communication service, which is the exact merit of the AMF communication service.
One of the possible motivations for Alternative#2 to consider is that RAN3 has designed the Time Synchronization Status Elementary procedure as a NODE-level procedure between NG-RAN and AMF. However, functional-wise NG-RAN and TSCTSF are peer entities. Consequently, Alternative#1 should ALSO be designed as a node-level procedure (between NG-RAN and TSCTSF) by adding a Routing ID encapsulating a TSCTSF NF ID.
Alternative#2 works only if the TIMING SYNCHRONISATION STATUS REQUEST contains ONLY one ACTION with two enumeration values, START and STOP, i.e. an AMF will be triggered to send a TIMING SYNCHRONISATION STATUS REQUEST with “start” when receiving a Namf_Communication_NonUeN2InfoSubscribe request, and a TIMING SYNCHRONISATION STATUS REQUEST with “stop” when receiving a Namf_Communication_NonUeN2InfoUnSubscribe request. The TSCTSF has no possibility to modify the subscription either. Even when e.g. the TSCTSF would like to extend the TSS reporting scope, covering more NG-RANs, it has to create a new subscription. In case of this alternative, it is also tricky to handle failure scenarios, for example, when one or more NG-RAN nodes fail to activate timing synchronization status reporting; it needs to be reported to the TSCTSF so that it could retry to make the request after some time.
Alternative#1 shall be the way forward (see slide 9 for the procedure)
NOTE that restoration considerations are done by CT4 and thus not included here

## Slide 20
Thank you