## Slide 1: Way Forward for Rel-19 EnergySys
China Mobile, NEC, SK Telecom, Rakuten, vivo, Interdigital
2024 August

## Slide 2: Summary of current status of SA2 discussion
In SA2, for EnergySaving, TR23.700-66 includes 11 solutions for KI#1, 18 solutions for KI#2, and 17 solutions for KI#3. KI#1 is about the architecture of Energy Consumption information calculation, and the basis for KI#2&KI#3.
SA2 mainly discuss one issue, i.e., how to monitor and calculate the energy consumption information for a specific UE(some other granularities, e. g. per UE, per AF, are also investigated, but the per specific UE granularity is the basic requirement).
In TR23.700-66 Clause 8.1, the conclusion includes the information for calculation of the Energy Consumption (EC). Based the information, EC for a specific UE can be calculated, e.g, as the following:
  Specific UE energy consumption within certain period=∑ECupf +ECRAN ;
  ECupf=(UE traffic volume at UPF) /(Total traffic volume at UPF)*(UPF Node level EC);
  ECRAN=(UE traffic volume at RAN node) /(Total traffic volume at RAN node)*(RAN Node level EC);
  NOTE: the above traffic volume, Energy Consumption is calculated for certain period.
The above calculation formula can reflect the energy consumption status of a specific UE in 5GS to some extent.
  However, the UEs in the same UPF/RAN node may have the same energy consumption per bit. So this is also an average of UEs’ energy consumption at the specific Nodes.
  Most companies in SA2 think the above formula can still reflect the UE energy consumption information/status in the 5GS, and it is beneficial to use this information to adjust the network policies e.g. UE policy, BDT policy etc.,

## Slide 3: Summary of current status of SA2 discussion
Observation：
Some companies suggest if the RAN can report the specific UE level energy consumption information to 5GC, then 5GC may get a better idea of this E2E per specific UE level energy consumption. However, this kind of reporting should not be so frequent to avoid the additional energy consumption.
In the discussion on how the operators can utilize the per specific UE level energy consumption information.
  1) )Operators expressed concern that this information should not be related with charging system, if the information is imprecise (e.g., average);
  2) Operators wanted functionalities to adjust the network configuration based on the UE level energy consumption.
  3) Frequent QoS adjustment is not preferred, but some policy control for UE level is supported, e.g. Slice, BDT time.
  4) Renewable information is expected to be included, but needs further coordination between SA2 and SA5.

## Slide 4: Some principles of the EnergySys in 5GS
Some principles we would like to propose when do the EnergySaving in 5GS.
1) Energy consumption information is different than traffic volume. And the EC information cannot be so precise since it is kind of a statistics information for a period but can reflect the energy consumption status actually. Therefore the calculation and reporting of energy consumption info per specific UE can be defined in minutes, to avoid the additional energy consumption in 5GS.
2) This information should not be integrated into charging system.
3) In order to make the energy consumption information closer to the actual network status which supports this UE, it is suggested the RAN can report the RAN side EC information based on the traffic volume, PRBs, signal strength, or other parameters if needed[see Annex].
4) EC information exposure can reflect the UE energy status in the network, and the information is valuable for network configuration optimization, or exposure to 3rd party or NPN owner to reflect the UE’s carbon emission.

## Slide 5: Way forward for the Rel-19 EnergySys
In this release, the per UE level energy consumption information calculation is supported.
In SA2, It is suggested to agree the EnergySys WID that establishes an architecture for EC information calculation for per UE level. And a new network functionality is introduced to support E2E UE level EC information calculation.
  For core network side, it is based on the data volume and the node level EC information;
  For RAN side, it is suggested RAN can report per UE level EC information.
  If RAN conclude not to support b finally, the 5GC new functionality calculate the UE level EC information based on 1) gNB node level data volume from OAM, 2) gNB node level EC information from OAM, and 3) UE level data volume from 5GC.
SA2 send an LS to RAN WGs to inform the SA2 discussion, and check with RAN WGs to see whether the b can be fulfilled or not.

## Slide 6: Annex
Initial analysis for RAN side reporting per UE level EC information
RAN may consider the following information to calculate the per UE level RAN EC information
  Collected by NG-RAN
  PRB usage for UL and DL, which can reflect the radio resource for the UE, may need enhancement in RAN WGs.
  UE report to NG-RAN, already support
  RSRP (Reference Signal Received Power), which can reflect the strength of desired signal; and the distance between UE and RAN node.
  SINR (Signal-to-Interference-plus-Noise Ratio), which can reflect the quality of desired signal;
  CQI (Channel Quality Indicator), PHY channel quality