## Slide 1: Discussion on TEI19 Support for Enhancement of TSC&URLLC_FRER
China Mobile

## Slide 2: Background
To guarantee high reliability, the standard IEEE 802.1CB-2017 Frame Replication and Elimination for Reliability (FRER) enables redundant communication over disjoint paths.
FRER provides five of the functions (not all functions are required in every protocol):
Sequencing function
Sequence encode/decode function
Stream identification
Individual recovery function
Stream splitting function
1
2
4
5
I/O stream
Frame Replication
stream2
stream1
Frame Elimination
Destination MAC address | 0 | 6
Source MAC address | 6 | 6
C-TAG EtherType | 12 | 2
Priority,DE,VLAN ID | 14 | 2
R-TAG EtherType | 16 | 2
Reserved | 18 | 2
Sequence number | 20 | 2
Payload Length/EtherType | 22 | 2
Data | 24 | 26+n
Frame Check Sequence | 24+n | 4
Field
Offset
Length

## Slide 3: One demo with utilizing FRER
    Problems
    There are one master PLC and 200 slave PLCs in one factory. The communication between PLCs previously is based on cable.
    While because of the bending and movement of the cables, the cabling failuers are almost 4-5 times per month, which leads to averaging 20 hours of production line-level downtime per month.
    Testing: Using 5G communication to replace the drag chain cables between master PLC and slave PLCs;
    Conclusion 1: By using FRER and URLLC, the latency(signal from Master PLC to Slave PLC) can be significantly reduced from 48ms to 16ms at 99.99%, matching the reliability requirements of low-latency PLC communication scenarios.
    Conclusion 2: The 5G transformation plan can effectively ensure long-term stable operation of industrial manufacturing businesses in the event of a single module failure.
    Conclusion 3: Through stability testing (72 hours), it has been verified the business can operate stably for a long time.
Slave PLC
5G CPE
RAN
UPF
5GC
master PLC
FRER
FRER
5G CPE
FRER
DS-TT
5G UE
UPF
RAN
FRER
FRER

## Slide 4: Proposal
by using PMIC/UMIC to enable the FRER capability：
For single UE case, support of redundant PDU Sessions for FRER include:
-A UE initiates two redundant PDU Sessions, respectively based on Dual Connectivity based end to end Redundant User Plane Paths as described in clause 5.33.2.1 of TS 23.501 [x] but select the same UPF or a UE initiates two redundant PDU Sessions, respectively via a single RAN and select the same UPF.
-The SMF should select the same UPF to ensure FRER based redundancy transmission, based on local configuration or the specific DNN.
-DS-TT provides a PMIC(which includes the FRER indication) and the DS-TT port MAC address to the UE, which includes the PMIC as an optional Information Element of an N1 SM container and triggers the UE requested PDU Session Establishment procedure or PDU Session Modification procedure to forward the PMIC to the SMF. SMF forwards the PMIC and the port number of the related DS-TT port to TSN AF or TSCTSF as described in clauses 4.3.2.2 and 4.3.3.2 of TS 23.502 [3]
-During the PDU session establishment, the UPF/NW-TT provides the PMIC/UMIC to SMF. The SMF provide the PMIC and UMIC of DS-TT/NW-TT transparently to TSCTSF, as described in Clause 5.28.3.1.
-The TSN AF or TSCTSF provides the FRER configurations in PMIC to the UE/DS-TT for UL replication and DL elimination.
-The TSN AF or TSCTSF provides the FRER configurations in PMIC/UMIC to the UPF/NW-TT for DL replication and UL elimination.