## Slide 1
Nokia
Ambient IoT open issues
(Topology 2 focused)

## Slide 2: Discussion points
Architecture harmonization
Protocol stack
UL Data forwarding
UL Data aggregation
UE selection
UE binding with AIoT device
UE Configuration

## Slide 3: Architecture harmonization
Shall topology#1 and #2 be supported by the same architecture?
AIoT Dev
Reader
(BS or UE)
AMF
(AIoT capable)
AIoT Dev
Reader
(BS or UE)
AIoTF
AIoT Dev
Reader
(BS or UE)
AIoT controller
AMF
ARC-A)
ARC-B)
ARC-C)
Option A) | It is possible to have the harmonized architecture for Topology 1 and 2. The AMF is significantly impacted (To support the new features that will be developed for AIoT in later releases, the legacy AMFs need to be continually updated).
Option B) | It is possible to have the harmonized architecture for Topology 1 and 2 without a significant impact on the legacy entities (This will be easier to manage).
Option C) | Harmonized architecture for both Topology 1 and 2 is not possible because the involvement of the AMF, as well as other 5G NFs, is mandatory to have a UE as the reader in topology 2.
5GC
5GC
Insider or Outside 5GC

## Slide 4: Protocol stack
Which protocol stack should be supported for topology 2?
Should the same protocol stack be used for both AIoT messaging and UP data forwarding?
NAS based
RRC based
UP based
For many use cases where AIoT requests are infrequent, always keeping the UE connected to the CN or maintaining an active PDU session would be inefficient.
When requesting AIoT services to the UE (i.e., so called AIoT signaling), it would be preferrable to use CP based approach (either NAS or RRC)
For UL data forwarding, all the mechanisms may be needed depending on the requirements of the use cases
See Annex for bigger size

## Slide 5: UL Data forwarding
How can a UE reader forward the data read from the AIoT devices to the network?
Option C)
User plane: the UE delivers the data over PDU session targeting the destination entity, which can be one inside 5GC (e.g., AIoTF) or a DN directly  suitable for relatively large data volume, low latency, high QoS
Considering the diversity of AIoT deployment scenarios, it is envisaged that all three mechanisms shown above would need to be supported and selectively used, depending on several factors including the application requirements and/or the network conditions
Can be supported by ARC-A), B) and C); but it’d not be a correct approach to have a PDU session targeting an AMF
Option A)
Option B)
Control plane (UL NAS): the UE establishes RRC connection and forwards the AIoT data as the payload of UL NAS message  suitable for moderate data volumes, less time-sensitive data
Control plane (STD with CIoT optimization): the UE delivers the AIoT data over RRC resume message without establishing the RRC connection  suitable for battery-operated UE with small data
Can be supported by only ARC-A) and B)
Can be supported by only ARC-A) and B)

## Slide 6: UL Data aggregation
Should aggregating AIoT data be supported? If so, how?
  Because there are many AIoT use cases where numerous AIoT devices are involved simultaneously for a service, aggregating AIoT data will be necessary to increase efficiency.
  Then which entity (e.g., UE, gNB and/or CN) will be responsible for the aggregation?
    This may vary depending on the data forwarding mechanism
    With UP, the UE should aggregate the data before sending them to the consumer
    With NAS, the UE may partially aggregate the data and reports it to the AIoT (via AMF) until the AIoT session is over. Then the AIoTF will do the final aggregation.
    With SDT (CIoT optimization), the UE should forward what it receives to the AIoTF (via AMF) as soon as it receives it. The AIoTF will then aggregate the data before providing the result to the AF

## Slide 7: UE selection (1/2)
How to select the UE reader?
  Proximity based selection
    The network can leverage the location information to select the UE.
  Pre-configured binding
    The network can maintain a database of device-reader bindings, where each AIoT device is associated with a specific UE. This approach is suitable only for scenarios where the AIoT devices are static or have predictable movement patterns.
  Dynamic binding
    Based on network request, AIoT devices can periodically update their location and availability information to the network. This allows the network to maintain an up-to-date list of AIoT devices and their associated UEs.
  Multiple UEs talking to the same target AIoT devices at the same time
    Every AIoT-capable UE in the requested area is used simultaneously for AIoT communication.
  Posture information
    The emitter antenna should be omni directional and we don’t see the need to know the posture.
  What other information can be considered for the selection?
    Analytics, authorization info, UE expected behaviours.

## Slide 8: UE selection (2/2)
Nokia view
  To apply pre-configured binding for UE selection when appropriate
    Even in this case, 5GC can offer additional features, such as validating the pre-configured UEs to ensure they are reachable and/or authorized or controlling the UEs.
  To select the UE readers based on location info and other information including analytics, etc.
    If the location info is provided by the AF, the 5GC initially requests all the UEs connected to the cell to communicate with the AIoT devices. The request includes an AIoT indication.
    Based on the indication, only AIoT capable/interested UEs in the cell will communicate with the AIoT devices and respond.
    Based on their responses, 5GC creates and maintains binding information between the responding AIoT devices and their reader UEs.
    If there are overlaps, 5GC can use other info like analytics to decide the reader UEs.
    With this binding information, 5GC can avoid re-identifying the responsible UEs in subsequent requests for the same target AIoT devices.
    5GC can perform the binding discovery procedure again when the stored info is no longer valid.

## Slide 9: UE binding with AIoT device
Is static or dynamic binding between AIoT devices and UEs necessary? If so, what would be the mechanisms?
  Binding could be necessary to avoid re-selecting the UE reader(s) in subsequent communications with the same AIoT devices.
  Static binding
    AIoTF possibly with help of UDR creates and maintains the binding table.
    Detailed procedures are FFS.
  Dynamic binding
    The same questions as the static binding case.
    When the UE reader(s) is selected, the binding table is updated.
    When the stored info is found to be no longer valid, the UE selection procedure is performed again and the binding table is updated.

## Slide 10: UE Configuration
What should be configured in a UE to make it work as a UE reader, and how should it be done?
  The selected UE reader needs to be configured with the necessary information for communicating with the AIoT devices and the CN
    AIoT role: UE reader
    Forwarding method
    AIoT policy (reporting policy, aggregation policy)
    Target reporting destination per AIoT device ID (as one UE can serve multiple Applications at the same time)
    Configuration validity/expiry time
  How and when to configure the UE?
    UE configuration update procedure with AIoT extensions, during UE policy establishment.

## Slide 11: Thank You !

## Slide 12: Annex. Protocol stack
Control plane-based protocol stack
AMF or
AIoTF behind AMF

## Slide 13: Annex. Protocol stack
RRC-based protocol stack
AMF or
AIoTF behind AMF

## Slide 14: Annex. Protocol stack
User plane-based protocol stack
Inside or Outside 5GC