## Slide 1: Discussion on data collection for AI positioning
vivo

## Slide 2: Current conclusion in the TR 23.700-84
Observation：
  MTLF can train ML model for AI/ML based positioning, MTLF needs to collect training data from the LMF, which will trigger the LMF collects data from UE/RAN/PRU. But the detailed E2E procedure for data collection still needs discussion.
  LMF can train ML model for AI/ML based positioning, LMF needs to collect training data itself from UE/RAN/PRU. . But the detailed E2E procedure for data collection still needs discussion.

## Slide 3: Scenario 1: LMF Data collection triggered by NWDAF-1/2
Option 1: NWDAF collects training data via GMLC and AMF to the LMF, then the LMF re-uses LPP/NRPPa protocols for data collection from UE/RAN
Evaluation:
  The AMF can help to select UE list, by checking user consent info on data collection, UE AI positioning capability (i.e. whether UE supports new measurements for AI positioning, ) and other UE LCS privacy info;
  The AMF can allocate LCS correlation ID for each UE . with the LCS correlation ID, the LMF will trigger the Location service. i.e. using LPP or NRPPa to collect data :
    Comply with the existing LCS service logic, the LMF will not initiate UE positioning without AMF triggering,
    UE and LMF are fenced from each other, the LMF will not know the UE ID, but only LCS correlation ID from the AMF.
Issue to be resolved: whether NWDAF collects training data from LMF directly or via GMLC/AMF?

## Slide 4: Scenario 1: LMF Data collection triggered by NWDAF-2/2
Option 2: NWDAF collects training data from LMF directly, then the LMF re-uses LPP/NRPPa protocols for data collection from UE/RAN
Evaluation:
  NWDAF may need to select UEs based on user consent info on data collection, UE AI positioning capability and other UE LCS privacy info, these info are usually from AMF;
  LMF will not get LCS correlation ID but only UE ID(e.g. SUPI) from NWDAF.
  With UE ID, the LMF collects data from UE/RAN using LPP or NRPPa, which breaks the existing LCS service logic:
    impacts on AMF (to transfer LPP/NRPPa, together with UE ID not LCS correlation ID)
    Impacts on UE (to get LPP/NRPPa, together with UE ID not LCS correlation ID)
    Impacts on LMF (to initiate LPP/NRPPa message even without LCS correlation ID)
Proposal 1: For Scenario 1, option 1 is higher priority.

## Slide 5: Scenario 2: LMF data collection based on internal trigger
Issue to be resolved: without UE ID or LCS correlation ID, how the LMF triggers data collection
Solution and Evaluation: (this solution keeps consistence with Option 1 for scenario 1 )
  The AMF can help to select UE list, by checking user consent info on data collection, UE AI positioning capability (i.e. whether UE supports new measurements for AI positioning, ) and other UE LCS privacy info;
  The AMF can allocate LCS correlation ID for each UE . with the LCS correlation ID, the LMF will trigger the Location service. i.e. using LPP or NRPPa to collect data :
    Comply with the existing LCS service logic, the LMF will not initiate UE positioning without AMF triggering,
    UE and LMF are fenced from each other, the LMF will not know the UE ID, but only LCS correlation ID from the AMF.
Proposal 2: For Scenario 2, the above solution is proposed to be adopted.