## Slide 1: Discussion on the multiple NWDAF case if AF is VFL server
KDDI

## Slide 2: Current conclusion in the TR 23.700-84
This material aims to raise a discussion on Note 11 in Conclusion #2 in the TR23.700-84.
NOTE 11: How multiple NWDAFs are involved in VFL when AF is acting as VFL server is defined in normative phase.
Proposal: In August meeting, normative work focus on one NWDAF case when AF is VFL Server. But high-level way forward for this perspective should be determined.

## Slide 3: Summary of current status
Option 1 : AF integrates data from multiple NWDAFs
  5GC exposes multiple NWDAFs to AF. (i.e., an AF has multiple subscriptions for each NWDAF.)
  NEF’s role:
    translation of external and internal IDs, (e.g., UE IDs).
    forward intermediate results from NWDAF to AF and from AF to NWDAF.
    anonymize NWDAF IDs
Evaluation :
  High risks to expose network deployment.
  Lower specification workload. Similar procedure to the case where NWDAF is VFL Server.

## Slide 4: Summary of current status
Option 2: NEF integrates data from multiple NWDAFs
  5GC exposes as only one NWDAF is involved.
  NEF’s role:
    translation of external and internal IDs (e.g., UE IDs).
    Integrate and forward intermediate results from NWDAF to AF, and that from AF to NWDAF.
Evaluation :
  Lower risk than Option 1.
  Additional AIML capability is needed to NEF, including integrating the intermediate results from multiple NWDAFs, splitting the intermediate result from AF into multiple NWDAFs.

## Slide 5: Summary of current status
Option 3: NWDAF integrates data from multiple NWDAFs
  5GC exposes as only one NWDAF is involved in the VFL process.
  Only one NWDAF is involved in the VFL process initiated by AF. The NWDAF collects data from other NWDAFs, where the NWDAF can use another VFL process.
  NEF’s role:
    translation of external and internal IDs, (e.g., UE IDs).
    forward intermediate results from NWDAF to AF and from AF to NWDAF.
Evaluation :
  Lower risk than Option 1.
  Large part is up to implementation.

## Slide 6: Way forward
TBD