## Slide 1: R19 EnergySys Proposal
vivo
2024 August

## Slide 2: How to calculate per UE Energy Consumption？
In TR 23.700-66, UE Energy Consumption is calculated by the ratio of UE granularity data traffic to the total traffic, cannot reflect the difference in energy consumption of UE in different locations and environments, etc.
  For example, the energy consumption of the UE of the same service at the edge of the cell is the same as that in the center of the cell
Observation: The energy consumption is not basically related to data volume, it is important to involve RAN when talking about network energy saving and energy efficiency considering the majority of network energy is consumed in the RAN. Especially, when UE locates in different areas with different radio conditions, the energy consumption will be different.

## Slide 3: How to use the UE energy consumption？
Possible scenarios:
  RAT camping adjustment, e.g. for the UE is located in 5G/4G border area and network enforce the UE to camp on 5G in priority and data transmission over 5G consume more energy with bad user experience compared to the UE camp on 4G
  work with IoT enterprise customers who use high amounts of network energy to improve how they position/mount their devices/antenna.
  work with office-enterprise customers to adapt their indoor coverage solutions.
  knowledge of which customers (enterprise or consumer) are profitable and which ones are not. knowledge of a consumer-customer’s CO2 emissions. Many customers are interested in this.
  knowledge of an enterprise-customer’s CO2 emissions. Many enterprises are now mandated to include accurate information on their CO2 emissions in their financial reports.
  identification of network areas where network power consumption per UE is high. This can be used to trigger network investigations leading to coverage optimization and/or interference reduction (e.g., downtilt).
  identification of UEs using high levels of RAN energy that are probably indoors. For these, operators could more actively work on moving them onto WiFi.
  identification of UE types that use unusually low or high amounts of network energy, leading to a better understanding of the actual impact to the network from watches or glasses.
Observation:
  Feasibility of energy based charging needs to be further identified
  UE energy consumption may be used for different purposes

## Slide 4: EC Calculation: CN NF or CHF?
Observation:
  In R19, if UE energy consumption is generated only based on the data volume, CHF enhancement is more simple and has less system impact
  If RAN level UE energy consumption can be calculated and provided, maybe CN based solution has more flexibility, because UE energy consumption can be used for other network operation (as stated in the previous slide) other than billing
RAN
CN NF
OAM
EECF/SMF/NWDAF
EE Info input
Calculation
EC expose
AF
5G internal
CN based
CN NF
OAM
CHF
EE Info input
Calculation
EC expose
AF
5G internal
CHF based
RAN

## Slide 5: Way forward for R19:Suggested work for different WGs
RAN side energy related information, for example:
  UE energy consumption at RAN side
  Other RAN parameters can indirectly reflect UE’s energy usage in different radio environment and locations, etc.
SA2
SA5 (OAM)
SA5 (charging)
Calculate and Aggregate energy related information
per-UE, per service, per PDU, per QoS flow…
Policy decision （e.g., AM policy, RAT adjustment）, analytics and prediction, NW optimization (e.g. NF discovery/selection and UP path selection),
Exposure to AF and internal NFs
Spending Limit control (energy related)
UE charging and credit (spending) control
Receive energy related record, e.g., from SMF
- Trigger spending limit (interact with PCF)
Collect energy related information per NF, per Network Slice
(EC & EE in R18, Carbon Emission and Renewable Energy in R19)
Monitor & Calculate
Differentiate UE energy consumption in different wireless conditions, e.g., locations, frequency
Observation: Per UE RAN information is a key factor to justify why CN to be involved for e.g. RAT camping adjustment.
LS to RAN WG is needed
RAN

## Slide 6: RAN report information(refer to CMCC’s discussion)
Option1：
  RAN report UE RSRP/SINR/CQI or generate UE EC levels (i.e., level1, level2,level3) and then report to CN
  Network impact low, all reuse existing parameters
  Depending on the signal quality of UE (RSRP/SINR/CQI), different UE energy consumption levels are determined, for example, strong signal quality with low energy consumption level
  CN generate UE Energy Consumption by considering different UE EC levels
Option2:
  RAN report PRB usage of UE
  Need FFS,RAN enhancement to support UE level PRB usage generation
mean value of Qi coefficient corresponds to different RSRP, different RSRPS correspond to different coefficients

## Slide 7: vivo’s observations
Evaluate and identify more scenarios other than Charging
User experience needs to be maintained when achieving network energy efficiency
It is essential to involve RAN impact to provide UE level energy related information in Rel-19
  The energy consumption is not basically related to data volume, it is important to involve RAN when talking about network energy saving and energy efficiency considering the majority of network energy is consumed in the RAN
  FINER granularity methods (e.g., RSRP based UE EC level reporting from RAN) compared to data volume is needed