## Slide 1: Options for NWDAF Assistance to PCF for QoS Profile Determination
NTT DOCOMO
S2-2409969

## Slide 2: Recap: Concluded Principles in the TR
The PCF may send a analytics request or subscription to NWDAF for QoS and policy assistance information analytics. The PCF may include an analytics ID, Filter Information, one or multiple sets of QoS parameters, the candidate value list(s) for each QoS parameter, requesting expected service experience (e.g. QoE), etc.
Based on the PCF request, the QoS and policy assistance information analytics provided by NWDAF may include: expected QoE can be achieved by the candidate QoS parameters (the values of the QoS parameters are within the candidate value list provided by the PCF).
The PCF may request one or more analytics from the NWDAF that are used within the same analytics target period, i.e. Observed service experience, QoS sustainability, Network Performance analytics, analytics of the duration and usage of the established QoS Flows.
NOTE 7: To provide the assistance for policy control and QoS, NWDAF shall not be aware of PCF internal logic.

## Slide 3: Current Situation
Different views/interpretations of concluded principles  No CR was agreed for KI#3
The purpose of this DP is seeking a possible way forward via classifying the proposals/views

## Slide 4: Current Situation
Different views/interpretations of concluded principles  No CR was agreed for KI#3
The purpose of this DP is seeking a possible way forward via classifying the proposals/views
Capabilities of PCF could be a criterion for solutions classification since the basic assumption of KI#3 is the incapability of PCF to learn from its past decisions
  If PCF is fully intelligent, i.e., it could learn from its own experiences (e.g., if PCF could train a ML model based on QoE and other observations such as QoS sustainability, etc. of the past QoS profiles) then no assistance from NWDAF would be needed
  However, since currently it is not the case, NWDAF may provide some assistance (derived by its learning capability, i.e., training ML models) which the objective of KI#3
The question: How much (in)capability should be assumed for PCF?
  The question is clarified in the following slides by investigating different options.
  These are NOT the comprehensive list of options, other suggestions are welcome

## Slide 5: Option 1
PCF can/does not know/determine the relation between the QoS profiles (determined by the PCF itself) and the real observations (e.g., the observed QoE, sustainability of QoS, …)
NWDAF is responsible to provide candidate QoS profiles for the given UE in a specific time, location, etc. by ML models which are trained using the observation/monitoring of the impacts/consequences of the previous QoS profiles provided by the PCF
  E.g., NWDAF attempts for determine QoS profiles that maximize the QoE
NWDAF
PCF
QoS flow information
QoE information
Network Resource info
Other inputs
Candidate QoS Profiles
PCC Rules
SMF
UE ID, Time, Location, …

## Slide 6: Option 2
PCF can/does not fully know/determine the relation between the QoS profiles (determined by the PCF itself) and the real network observations (e.g., the observed QoE, sustainability of QoS, …) but based on its internal logic can derive candidate QoS profiles (which would be suitable for the UE)
NWDAF is responsible to evaluate the candidate QoS profiles for the given UE in a specific time, location, etc. by ML models which are trained using the observation/monitoring of the impacts/consequences of the previous QoS profiles provided by the PCF
  E.g., NWDAF provides evaluation (e.g. QoE) of given candidate QoS profiles
  The evaluation can be combination of multiple analytics (e.g., QoE, QoS Sustainability, …)
NWDAF
PCF
QoS flow information
QoE information
Network Resource info
Other inputs
Evaluation of
Candidate QoS Profiles
PCC Rules
SMF
UE ID, Time, Location, …,
Candidate QoS Profiles

## Slide 7: Option 3
PCF can/does not derive analytics but it can take the analytics by provided NWADF into account in determining the QoS profiles. It is the internal logic of PCF whether and how to consider the relationship of analytics outputs and QoS profiles
NWDAF is responsible to generate existing/extended/new analytics
  E.g., NWDAF provides extended analytics (such as OSE) corresponding to the a given QoS profiles
  E.g., NWDAF provides new analytics for the established QoS flow
NWDAF
PCF
QoS flow information
QoE information
Network Resource info
Other inputs
Analytics Responses subject to the given QoS profiles
PCC Rules
SMF
Analytics request with
QoS Profiles as filters

## Slide 8: Comparison
 | Option 1 | Option 2 | Option 3
Level of NWDAF assistance to PCF | Maximum | Medium | Minimum
How are QoS profiles determined | - NWDAF derives candidate QoS profiles based on the observation of the pat decision by PCF. - PCF modifies/selects/… final QoS profiles based on the candidates proposed by NWDAF | - PCF based on its internal logic, derives a set of candidate QoS profiles - NWDAF evaluates the candidate QoS profiles based on the metric provided by the PCF - PCF derive the final QoS profiles based on the evaluation by NWDAF | - PCF subscribes to the NWDAF for analytics and consider them based on its internal logic to derive the QoS profiles; i.e., the PCF knows how to relate the analytics to the QoS parameters The key point is that all the analytics are targeted to the same time window and the ML models are trained the same data
Similarity to the proposed solutions* | Huawei’s (original) proposal/idea that NWDAF provides recommendation | Samsung’s proposal | Nokia’s proposal DCM’s proposal
Comments | If it is going to be a generic service, it is not clear how NWDAF can provide recommended action (here QoS profile) without knowing the internal logic of the consumer NF (here the PCF) | Whether the existing service operations are suitable for requesting and getting evaluation of actions by another NF or not needs further investigation | Whereas it is the minimum assistance by NWDAF to PCF, it is the existing mechanism. PCF is already a consumer of NWDAF analytics such as “Network Performance” or “DN Performance”
* The purpose of the mapping is just to show some similarities, details of the proposal solution may be different.

## Slide 9: Way forward?!
A question needs to be answered to find a way forward:
Whether is it acceptable to have multiple options or not?
Note: The options depend on PCF capabilities which are determined by PCF internal logic implementation
  DCM’s view: Yes
  Other companies view: ?
If yes  Which options can be selected?
  DCM’s view: In this release, Option 2 and Option 3 are technically feasible
  Other views ?
If no  which one should be selected?
  DCM’s view: Option 2
  Other views ?

## Slide 10
Thank you.