## Slide 1: Discussion on AI based positioning
SA2#165
vivo
S2-2409673

## Slide 2: Background
The following editor’s note is captured in TS 23.288(CR#1164) for LMF-based AI/ML positioning:
Editor’s Note: How to indicate supporting model training for the LMF-based AI/ML positioning as defined in TS 23.273[39] by the MTLF to NRF, e.g., using a specific analytics ID or a new indication is FFS.
Here discusses two options for MTLF to indicate supporting model training to NRF :
    Option 1: New analytics ID (e.g LMF side AI based positioning)
    Option 2: New indication to indicate supporting model training to NRF

## Slide 3: Option 1: new analytics ID
Observation:
  Same as other existing analytics IDs (e.g. OSE, NF load information…), if an MTLF supports ML model training for AI positioning, it will register to NRF in its NF profile still using analytics ID but with a new value (e.g. analytics ID=LMF side AI based positioning ).
  the LMF uses analytics ID= LMF side AI based positioning to discover MTLF supporting ML model training for AI positioning, and to retrieve ML model from the MTLF.
  however, this new analytics ID=“LMF side AI based positioning “ has different meaning as the other ones, the related model retrieved from MTLF is not analytics generating in AnLF, but only for UE location calculation in LMF.
Evaluation:
  Since AI based positioning is different from the existing analytics which only comprise statistics and predictions, if using an analytics ID as the index to retrieve the ML model for AI positioning case, there may be logical confusion and misunderstanding.
  Main Spec impacts:
  define a new value for analytics ID for AI positioning case, e.g. analytics ID=LMF side AI based positioning;
  Introduce a new subclause in clause 6 to describe this analytics ID=LMF side AI based positioning, with clear clarification it is just for LMF to calculate UE location which is different from other analytics IDs. e.g. OSE, NF load information, etc.

## Slide 4: Option 2: New indication
Observation:
  Apart from other analytics ID(s) if available, in case an MTLF supports ML model training for AI positioning, it will register to NRF in its NF profile with a new indication per service(Nnwdaf_MLModelProvision service).
  The analytics ID IE will become from mandatory to conditional (if for analytics generation), during MTLF registration, MTLF discovery and ML model retrieval procedures.
  Open issue to be discussed: in S2-2408610, Nokia ‘s paper pointed out there will be backward compatibility if introducing new indication to retrieve ML model by the LMF from the MTLF. But after some analysis, we find there may be no such issue because:
    Rather than deleting existing functionality related to analytics IDs, R19 MTLF is just extended to support ML model training for AI positioning using this new indication.
    Only R19 LMF uses the new indication to discover MTLF from NRF, and then use new indication to obtain ML model for AI positioning calculation.
    However, backward AnLFs (R18, R17 and R16) still can use analytics ID to discover MTLF from NRF, and then use analytics ID to obtain ML model for analytics, which are not related to AI positioning case.
Evaluation:
  Decouple with existing analytics ID, it can avoid confusion with analytics since MTLF support AI positioning model training has nothing to do with statistics/prediction. A new indication can accurately reflect the MTLF new capability.
  Main Spec impacts: For AI positioning case, enhance MTLF registration and discovery from NRF, and ML model retrieval between LMF and MTLG, using new indication rather than analytics ID.

## Slide 5: Way forward
Proposal: Rather than analytics ID, use a new semantic (new indication or new IE, e.g. service ID) to indicate supporting model training and to retrieve model for the LMF-based AI/ML positioning .
 | New analytics ID | New semantic（indication or service ID）
OPPO |  | Support
MTK |  | Support
Ericsson |  | Support
Lenovo |  | Support
Huawei |  | Support
Samsung |  | Support
vivo |  | Support
DCM |  | Support
CATT | Support | 
QC | Support | 
… |  |