## Slide 1: Discussion on data collection from UE
SA2#165
vivo
S2-2409735

## Slide 2
Background
RAN2 has discussed the topic of UE side data collection for UE-side model training and agreed on a TP for TR 38.843 as shown below:
  1a. UE collects and directly transfers training data to the data collection entity outside the MNO (e.g. Over-The-Top (OTT) server) for UE-side model training. No 3GPP specification impact is expected.
  1b. UE collects training data and transfers it to the server for data collection for UE-side model training (inside the MNO) and then optionally from the server for data collection for UE-side model training to the OTT server (outside the MNO).
  2 .UE collects training data and transfers it to Core Network. Core Network transfers the training data to the server for data collection for UE-side model training/OTT server.
  3. UE collects training data and transfers it to OAM. OAM transfers the training data to the server for data collection for UE-side model training/OTT server.
RAN sends SA2 LS S2-2409600/RP-242389 and asks TSG SA to initiate the work and at least for SA WG2 to provide inputs on solutions 1b, 2, and 3 by RAN#106.
This paper is to
  Discuss and analyze the high level call flows and feasibility for alternative solutions for solution 1b, 2 and leave solution 3 to SA5 at the moment.
  Provide draft analysis in terms of MNO controllability, visibility and User data privacy & user consent

## Slide 3
OTT UP solution for data collection from UE (RAN option 1b)
Solution description：
A DCAF (data collection AF) is deployed by MNO or 3rd party o collect data from UE client；
Before data collection, a connection between UE and DCAF in application layer is set up，which is over the 3GPP UP path (e.g. PDU session)；
Over the applicable layer connection, the DCAF requests UE client for specific standardized data content
After data collection and data processing, UE client reports the data to the DCAF via the applicable layer connection, which is over the 3GPP UP path（e.g. PDU session）
The DCAF interact with data consumer for data reporting/collection/exposure
Solution Feasibility | MNO Controllability | MNO Visibility | Data integrity and confidentiality | Privacy, anonymity and user consent
Feasible. This solution has been defined for the case that NWDAF collects UE data in SA2 since R18 (TS 23.288) SA4 has also defined a general framework for UE data collection in TS 26.531(stage 2) and TS 26.532(stage 3). | Depends on DCAF deployment Full MNO Controllability if DCAF is deployed by MNO Partial MNO Controllability if DCAF is deployed by 3rd party | Depends on DCAF deployment Full MNO Visibility if DCAF is deployed by MNO . Partial MNO Visibility if DCAF is deployed by 3rd party . | Out of 3GPP and rely on application layer security | Related to MNO controllability and MNO visibility (whether MNO is data controller, and whether user consents reported data) The MNO will handle user consent, and requirements in Annex V of TS 33.501 is applied if DCAF is deployed by MNO (trusted mode). Out of 3GPP if DCAF is deployed by 3rd party (untrusted mode).

## Slide 4
MNO CP solution for data collection from UE (RAN option 2 - CP solution)
Solution description：
Alt 1：CP solution without DCCF
  Data consumer interacts with AMF for UE data collection request/response via SBI directly;
  AMF transfer the data collection request to UE via DL NAS;
  Then the AMF transfers the data reporting from UE to data consumer via SBI.
Alt 2：CP solution with DCCF
  Add a DCCF as a B2B data collection agent between AMF and data consumer.
Note:
this refers to the data collection framework in CN defined for AI cases in TS 23.288.
The DCCF as a B2B agent is used to isolate data consumers and data producers, which helps to realize multiple reuse for one data collection from UE.
This may be more efficient and extensible for feature usages
Solution Feasibility | MNO Controllability | MNO Visibility | Data integrity and confidentiality | Privacy, anonymity and user consent
Technically Feasible. Both alternatives are technically workable, which could be easily extended per previous features supported e.g. Data collection via DCCF in SA2 R18/R17 eNA | Supported as CN NFs(AMF and DCCF) can control the data collection procedure, e.g. Authentication and authorization per UE, or per UE per data type Determine the data reporting path (CP or UP) Initiate, update and terminating data collection | Supported The data content reported by UE is 3GPP standardized, which is visible for MNO. | UE->AMF: reuse NAS security AMF->consumer: reuse SBA security | As MNO has controllability and visibility (MNO is data controller and user consents reported data), the requirements in Annex V of TS 33.501 is applied. The CN NFs can be user consent enforcement point.

## Slide 5
MNO UP solution for data collection from UE (RAN option 2- UP solution)
Solution description：
Alt 1: UP solution without DCCF
  Data consumer interacts with AMF for UE data collection request/response via SBI directly, in the request the data consumer indicates its UP info for data reporting
  AMF transfer the data collection request (including the UP info for data reporting ) to UE via DL NAS
  The UE reports the collected data to the UP info pointing to the data consumer via PDU session
Note 1: different from option 1b, this UP solution is similar as LCS over user plane, in which the MNO CN NF can participate.
Alt 2: UP solution with DCCF
  Add a DCCF as a B2B data collection agent, the DCCF can also provide an UP info pointing to DCCF or MFAF
  Via user plane, the data from UE will be reported the DCCF or MFAF pointed by the UP info.
Note 2: this also refers to the data collection framework in CN defined for AI cases in TS 23.288. The DCCF and MFAF can help to realize multiple reuse for one data collection from UE.
Solution Feasibility | MNO Controllability | MNO Visibility | Data integrity and confidentiality | Privacy, anonymity and user consent
Same with RAN Option 2-CP solution in slide4 | Same with RAN Option 2-CP solution in slide4 | Same with RAN Option 2-CP solution in slide4 | Same with RAN option 1b in slide3 | Same with RAN Option 2-CP solution in slide4

## Slide 6: Summary
 | Option 1b | Option 2 - CP solution | Option 2 - UP solution
Solution Feasibility | Y | Y (Technically Feasible) | Y (Technically Feasible)
MNO Controllability | Depends on DCAF deployment. Full MNO Controllability for MNO deployed DCAF and partial MNO Controllability for 3rd party deployed DCAF | Y | Y
MNO Visibility | Depends on DCAF deployment. Full MNO Visibility for MNO deployed DCAF and partial MNO Visibility for 3rd party deployed DCAF | Y | Y
Data integrity and confidentiality | Out of 3GPP and rely on application layer security | Reuse NAS and SBA security | The same with option 1b
privacy, anonymity and user consent | Related to MNO controllability and MNO visibility (whether MNO is data controller, and whether user consents reported data) The MNO will handle user consent, and requirements in Annex V of TS 33.501 is applied if DCAF is deployed by MNO Out of 3GPP if DCAF is deployed by 3rd party. | As MNO has controllability and visibility (MNO is data controller and user consents reported data), the requirements in Annex V of TS 33.501 is applied. The CN NFs can be user consent enforcement point | The same with option 2-CP solution
Efficiency and extensibility | TBD | Better efficiency and extensibility if DCCF/MFAF is used | Better efficiency and extensibility if DCCF/MFAF is used
Proposal
Provide the above draft analysis as SA2 inputs on solutions for option 1b, 2 to RAN working groups
The data content for UE side model should be 3GPP standardized to support the full MNO visibility
Having MNO controllability and MNO visibility of UE data are essential for user consent as
  user can only consent the data reporting if only the data content is fully visible to the user
  the data controller has responsibility to protect user privacy