## Slide 1: Discussion on IP routing between BH PLMN and MWAB broadcasted PLMN
Huawei
SA WG2 Meeting #165 S2-2409752
14th Oct – 18th Oct, Hyderabad, IN

## Slide 2: Background
Considering different possible deployment scenarios as described in the Annex S of TS 23.501, it is necessary to clarify the IP routing between BH PLMN and MWAB broadcasted PLMN.
For example, it is possible that the NAT on N6 is used when the N3 message which carries the data traffic of normal UE is transferred via BH PDU session (see figure on the right).
MWAB-UE
BH
UPF
BH PDU session
NR
NR
N3
BH SMF
UE
Access
BH
MWAB node
gNB
N6
(from BH UPF point of view)
N3
UPF
NAT
AMF
NATed IP
SMF
MWAB-gNB

## Slide 3: Discussion
The N3 UPF receives the AN Tunnel information of MWAB-gNB (including IP address of MWAB-UE )during PDU Session Establishment of UE.
The AN Tunnel information is included in the N2 SM container, which is transparent to the BH PLMN .
Problem:
If MWAB-UE IP is a private IP address and NAT functionality in the UPF of BH PDU Session is used, when N3 message which carries the data traffic of UE is routed by BH UPF via N6, the source IP address of N3 GTP-U payload will be NATed, which is different from the AN tunnel information of MWAB-gNB provided to UE SMF during BH PDU Session establishment.
And that may cause the UE UPF fail to identify the traffic from MWAB-gNB.
Uplink N3 GTP-U message via BH PDU session
Source：(Private)MWAB-UE IP
Destination：N3 UPF IP
Uplink N3 GTP-U message via BH PDU session
Source：NATed IP
Destination：N3 UPF IP

## Slide 4: Proposal
N2 message routing which includes N2 SM container
N3 message routing which includes GTP-U header
The BH SMF/UPF allocates IP address to MWAB-UE based on the dedicated S-NSSAI/DNN during BH PDU Session Establishment, to make sure BH PLMN can reach MWAB broadcasted PLMN via IP-routing (and vice versa).
This IP address is sent to MWAB-gNB by MWAB-UE via internal interface and used for the communication of backhaul links.
The entities of the network (e.g. AMF, UPF, other gNBs and OAM server) belonging to the MWAB broadcasted PLMN can identify the MWAB when receiving this IP address from backhaul links.
Reachable via IP-routing