## Slide 1: InterPLMN Handover to a CSG Cell
2011.4.6
Samsung
S2-111520

## Slide 2: Contents
Current Specification Status
Problems
Possible Solutions
S2-111520

## Slide 3: Current specification Status (1)
Allowed CSG list in UE (24.268) and HSS
  a list of allowed CSG lists of the PLMN
Measurement Report (36.311)
  UE reports the CSG cell of the PLMN, which exist in its allowed CSG list
   no limitation to the registered PLMN
S2-111520

## Slide 4: Current specification Status (2)
MME’s authorization for accessing a CSG cell
(23.401, 23.060, 29.002)
  HSS sends the allowed CSG list of the registered PLMN
  MME authorizes the CSG access of the UE based on allowed CSG list from the HSS
   MME does not know the allowed CSG list of other PLMNs including the equivalent PLMNs
S2-111520

## Slide 5: Problem Scenario 1 TAU failure after HO completion (1)
Condition
  The allowed CSG lists at UE and HSS
  are Identical
  = {{PLMNA,(CSG1, CSG2)}
  { PLMNB,(CSG1,CSG3)}}
  Equivalent PLMNs for the UE
  = {PLMNA, PLMNB}
Procedures
1~3.The UE is registered to the PLMN A via cell 1 using Attach or TAU
  MME: CSG list of the PLMN A = (CSG1,CSG2)
  eNB : equivalent PLMN list = {PLMN A,B}
UE
Cell 1
Cell2 (CSG1)
MME1 in PLMN A
MME2 in PLMN B
1. Attach/TAU
3-1.
Attach accept/ Initial Context Setup (ePLMNs={A,B})
UE context:
ePLMNs = {A,B}
3-2.
Attach accept
HSS
The allowed CSG list for UE = {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG1,CSG3))}
The allowed CSG list in UE
= {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG1,CSG3))}
2. Location Update/
UE context including CSG list (CSG1, CSG2)
UE context:
ePLMNs = {A,B}
CSG list =(CSG1,CSG2)
S2-111520

## Slide 6: Problem Scenario 1 TAU failure after HO completion (2)
4. CSG list is updated
  HSS deletes CSG1 is from the allowed CSG list of PLMN B
    {{PLMNA,(CSG1, CSG2)}
    { PLMNB,(CSG3)}}
  UE is not updated yet
    {{PLMNA,(CSG1, CSG2)}{ PLMNB,(CSG1,CSG3)}}
6. The UE reports cell2 to cell 1
  because CSG1 exists at the allowed CSG list of PLMN B
7. eNB decides to HO to Cell1
  because PLMN B is ePLMN of PLMN A and
  The UE reports the CSG membership
UE
Cell1
Cell2 (CSG1)
MME1 in PLMN A
MME2 in PLMN B
HSS
The allowed CSG list for UE = {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG1,CSG3))}
The allowed CSG list in UE
= {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG1,CSG3))}
6. Measurement report
on Cell2
(CSG1, PLMN B, membership)
UE
UE context:
ePLMNs = {A,B}
UE context:
ePLMNs = {A,B}
CSG list =(CSG1,CSG2)
7.
HO Required to cell 2
5. move
4. allowed CSG list is updated
S2-111520

## Slide 7: Problem Scenario 1 TAU failure after HO completion (3)
  HO preparation is performed
    MME1 proceeds interPLMN HO based on allowed CSG list in MME 1
    MME2 proceeds interPLMN HO based on equivalent PLMN list
  9 . HO execution is performed
  10~11. UE performs TAU
    MME 2 : CSG list of PLMN B
    = {CSG3}
  12. MME rejects TAU based
    Because CSG3 does not exist in the allowed CSG list
Cell1
Cell2 (CSG1)
MME1 in PLMN A
MME2 in PLMN B
HSS
The allowed CSG list for UE = {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG1,CSG3))}
The allowed CSG list in UE
= {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG1,CSG3))}
UE
UE context:
ePLMNs = {A,B}
UE context:
ePLMNs = {A,B}
CSG list =(CSG1,CSG2)
8. Handover Preparation :
9. HO Execution
12. reject
TAU
11. Location update/
UE context including CSG list (CSG3)
10. Try TAU After HO
UE context:
ePLMNs = {A,B}
CSG list =(CSG3)
S2-111520

## Slide 8: Problem Scenario 2 interPLMN HO prohibition to authorized CSG cell (1)
Condition
  The allowed CSG lists at UE and HSS are Identical
  = {{PLMNA,(CSG1, CSG2)}
  { PLMNB,(CSG2,CSG3)}}
  Equivalent PLMNs for the UE
  = {PLMNA, PLMNB}
  UE is registered to PLMN A via Cell1
Procedure
The UE is registered to the PLMN A via cell 1
2~3. UE reports cell2 to cell 1
  - CSG3 exists in allowed CSG list of PLMN B in the UE
UE
Cell1
Cell2 (CSG3)
MME1 in PLMN A
MME2 in PLMN B
HSS
The allowed CSG list for UE = {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG2,CSG3))}
The allowed CSG list in UE
= {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG2,CSG3))}
3. Measurement report
on Cell2
(CSG3, PLMN B, membership)
UE
UE context:
ePLMNs = {A,B}
UE context:
ePLMNs = {A,B}
CSG list =(CSG1,CSG2)
2. move
1. Attach/TAU
S2-111520

## Slide 9: Problem Scenario 2 interPLMN HO prohibition to authorized CSG cell (2)
4. eNB decides HO to cell2
  PLMN B is ePLMN of PLMN A
  The UE reports the CSG membership
5. MME1 rejects HO
  CSG3 does not exist in the allowed CSG list in MME1
Cell1
Cell2 (CSG3)
MME1 in PLMN A
MME2 in PLMN B
HSS
The allowed CSG list for UE = {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG2,CSG3))}
The allowed CSG list in UE
= {(PLMNA,(CSG1,CSG2))
(PLMNB,(CSG2,CSG3))}
UE
UE context:
ePLMNs = {A,B}
UE context:
ePLMNs = {A,B}
CSG list =(CSG1,CSG2)
4. HO required
5. REJECT
S2-111520

## Slide 10: Summary of Problems
Problem scenario 1
  UE reporting the wrong CSG cell is handovered and its TAU is rejected, because MME does not know the allowed CSG list of the target PLMN.
Problem scenario 2
  UE reporting the right CSG cell is not handovered and cannot use the better link quality, because MME does not know the allowed CSG list of the target PLMN.
S2-111520

## Slide 11: Possible Solutions (1) Configuration on (H)(e)NB or SGSN/MME
Solution 1: interPLMN Handover to a CSG cell is not supported
  a) HeNB/eNB Configuration
  : (H)(e)NB does not trigger a handover to a CSG in the other PLMN including equivalent PLMNs
  + No signal to SGSN/MME at all
  - Configuration should be changed if SGSN/MME is up-graded to rel-10/11
  b) MME/SGSN Configuration
  : MME/SGSN rejects a handover to a CSG cell in the other PLMN including equivalent PLMNs
  + Same philosophy with existing CSG authorization
  : source MME performs CSG authorization
  + No configuration change if SGSN/MME is up-graded to rel-10/11
  - Signal to SGSN/MME
S2-111520

## Slide 12: Possible Solutions (2) Configuration on HSS and rejection by SGSN/MME
Solution 2 : interPLMN Handover is supported only if the allowed CSG list of ePLMNs are identical
  Identical CSG list flag for equivalent PLMNs
  : indicate whether all equivalent PLMNs have the identical CSG lists
  MME
    Flag is false: reject the interPLMN HO to a CSG cell
    Flag is true : accept the interPLMN HO based on the CSG list of the registered PLMN.
MME
HSS
Equivalent PLMNs = {A,B,C}
Update Location Request (Equivalent PLMNs, MME id, ….)
Update Location Ack
(IMSI, subscription data (allowed CSG list for the registered PLMN, identical CSG list flag for equivalent PLMNs))
S2-111520

## Slide 13: Possible Solutions (3) Configuration on HSS and rejection by SGSN/MME
Solution 3
: HSS provide all CSG lists of all equivalent PLMNs and MME authorize interPLMN handover based on the CSG list of the target PLMN
  MME
    Has no the allowed CSG list of the target PLMN
     MME/SGSN rejects interPLMN handover
    Has the allowed CSG list of the target PLMN and the CSG id exist in the allowed CSG list
     MME/SGSN authorizes interPLMN handover
MME
HSS
Equivalent PLMNs = {A,B,C}
Update Location Request (Equivalent PLMNs, MME id, ….)
Update Location Ack
(IMSI, subscription data (
allowed CSG lists for all equivalent PLMNs))
S2-111520

## Slide 14: Suggestion
For Rel-9
  Solution 1-b)
For rel-10/Rel-11
  Solution 3
Related CRs
  23.401: S2-111521, S2-111522, S2-111523
  23.060: S2-111524, S2-111525, S2-111526
S2-111520