## Slide 1: S2-122051 breakout session discussion. Chris Pudney: Vodafone
Situation: - LTE capable device roaming in 3G & LTE network; - No LTE subscription
In subsequent slides:
  black text is from S2-122051
  Red text is meant to reflect the drafting session discussion
  Green text are additional post-session thoughts
Summary: discuss at next SA2 meeting and then potentially liaise to August CT x and/or RAN y meetings
3GPP SA2 Kyoto, May 2012
S2-122617

## Slide 2: 1: Inter RAT handover from UTRAN to E-UTRAN
(1) For the UE, the source RNC initiates an Inter-RAT handover to E-UTRAN and sends a Relocation Required message to the source SGSN. (2) The source SGSN recognizes it’s an Inter-RAT handover to E-UTRAN from the Target eNB-ID IE. The source SGSN, knowing the roaming agreement, aborts the procedure. (3) The steps (1) and (2) repeat.
The above problematic scenario causes unnecessary signalling traffic for RNC and SGSN of VPLMN.
If the SGSN sees the RNC-ID as that of an LTE target, the SGSN can return a ‘permanent failure’ cause.
‘service handover’ information in the Iu Assignment Request can be used to stop the UMTS RNC initiating a handover to LTE.  BUT does the SGSN know that the UE does not have an LTE subscription? -> ‘Access Restriction Data’ (see clause 2.4.18 in 23.008) might not be supported by a legacy HSS.
   the SGSN could use IMSI analysis to ‘know’ that the HPLMN does not use LTE
    -  this gets more complex if the HPLMN has some HLRs that support LTE and some HLRs that do not support LTE

## Slide 3: 2: Inter RAT handover from UTRAN to E-UTRAN, 23.401 Annex D type
(1) For the UE, the source RNC initiates an Inter-RAT handover to E-UTRAN. The source RNC may be configured to use RNC IDs instead of eNodeB IDs to identify a target eNodeB. The source RNC sends a Relocation Required message to the old Gn/Gp SGSN of pre-Rel-8. (Note: For the old Gn/Gp SGSN of Rel-8 onwards, the same discussion with the above scenario 1 applies.) (2) The old Gn/Gp SGSN sends a Forward Relocation Request message to the new MME. (3) The new MME sends a Create Session Request message, with P-GW related IEs being replaced by GGSN equivalents, to the S-GW. (4) The Inter-RAT handover continues. The UE sends a HO to E-UTRAN Complete message to the target eNodeB. (5) The Inter-RAT handover further continues. The S-GW sends a Modify Bearer Request message to the GGSN. That request fails. (6) The steps from (1) to (5) repeat.
The above problematic scenario causes frequent service disruptions for an inbound roamer and unnecessary signalling traffic for RNC, SGSN, MME, and S-GW of VPLMN.
Target MME does not access HSS until after the handover completes -> this causes a problem
 need to upgrade the logic in the source SGSN so the handover is stopped in the source SGSN -> but still need knowledge in source SGSN that the UE does not have an LTE subscription

## Slide 4: 3: Inter RAT release with redirection from UTRAN to E-UTRAN
(1) The source RNC sends an RRC Connection Release message with a Redirection info IE to the UE. The Redirection info IE contains an Inter-RAT info IE being set as E-UTRA. (2) The UE comes to Idle Mode, camping on E-UTRAN. (3) The UE sends a TAU Request message though eNodeB to MME. (4) The MME finds that the authentication procedure fails and returns a TAU Reject message. (5) The UE sets the EPS update status to EU3 ROAMING NOT ALLOWED. The UE considers the USIM as invalid for both EPS services and GPRS services.
The above problematic scenario causes denial of service for an inbound roamer.
Send EMM#15 “no suitable cells in TA” -> but does the mobile move to LTE before finding that the cell is not suitable? (and hence do this cyclicly). Battery impact? Check RAN specs or 23.122 for any “5 minute ban on the frequency on which cause 15 was received” that might solve this cyclic behaviour.
Or use RFSP? (but the legacy HSS will probably not be supporting this and hence the SGSN has to generate it locally)
Service Handover IE can also help (but would also be a little bit “non-standard” in the RNC)
  Last 2 need SGSN to be aware of no-LTE subscription.
At least need to ensure that MME does not send ‘PLMN not allowed’ (Need to check CT 4/1 spec such as TS 29.010 that might specify the mapping between MAP/Diameter cause values and EMM cause values).

## Slide 5: 4: Fast redirection from UTRAN to E-UTRAN
(1) Prior to sending a Service Request message, the UE sends an RRC Connection Request message with a Pre-Redirection info IE being set as Support of E-UTRA FDD(or Support of E-UTRA TDD) to an RNC. (2) The RNC sends an RRC Connection Reject message with a Redirection info IE to the UE. The Redirection info IE contains an Inter-RAT info IE being set as E-UTRA. (3) The UE camps on E-UTRAN. (4) The UE sends a TAU Request message though eNodeB to MME. (5) The MME finds that the authentication procedure fails and returns a TAU Reject message. (6) The UE sets the EPS update status to EU3 ROAMING NOT ALLOWED. The UE considers the USIM as invalid for both EPS services and GPRS services.
The above problematic scenario causes denial of service for an inbound roamer.
Service handover IE does not help as this happens before Service Request
UE might avoid sending the request unless it has successfully TAUed to LTE in that PLMN/ePLMN (* but this might not be permitted by 25.331 *).

## Slide 6
End of document