## Slide 1
DISCUSSION
Gemalto
UE Configuration used in
WLAN Network Selection

## Slide 2: WLAN Network Selection: A multiple steps process
Generate Ordered list of WSIDs
Generate Ordered list of PLMNs
Authenticate to “Network”
Find Active ANDSF Rule and Apply
Scan of SSIDs
Lists of WSIDs in USIM / ME
Acquire list of available and allowed PLMN
Lists of PLMNs in USIM / ME
Acquire ANDSF rules from HPLMN/VPLMN
Lists of ANDSF rules in ME
Credentials in USIM / ME
Authentication process
WLAN UE Switch on
WLAN selected
Mandatory steps
Optional
step
Notes: In grey separate specific Security Presentation

## Slide 3: WLAN Network Selection: WSID Ordering
Generate Ordered list of WSIDs
Generate Ordered list of PLMNs
Authenticate to “Network”
Find Active ANDSF Rule and Apply
Scan of SSIDs
Lists of WSIDs in USIM / ME
Acquire list of available and allowed PLMN
Lists of PLMNs in USIM / ME
Acquire ANDSF rules from HPLMN/VPLMN
Lists of ANDSF rules in ME
Credentials in USIM/ME
Authentication process
WLAN UE Switch on
WLAN selected
Notes: In grey separate specific Security Presentation

## Slide 4: Ordering of available WSIDs for PLMN Discovery
WLAN UE scanning procedure
To find available WSIDs
Ordering WSIDs
Priority Order data file in USIM (DF WLAN in 31.102):
Home I-WLAN Specific Identifier list
User Controlled WLAN Specific Identifier list
Operator Controlled WLAN Specific Identifier list
Priority Order data file in ME (I-WLAN MO in 24.235):
Home I-WLAN Specific Identifier list
User Controlled WLAN Specific Identifier list
Operator Controlled WLAN Specific Identifier list
Other WSIDs supporting 3GPP-WLAN interworking
Acquire PLMN for each WSID in priority order
Notes: 24.234

## Slide 5: Parameters for WLAN Network Selection in USIM (24.234)
HPLMN Direct Access Indicator (WLAN UE may attempt to select HPLMN via WLANs that support non IEEE 802.1x authentication mechanism)
Home I-WLAN Specific Identifier List (WSIDs related to I-WLANs that have direct relationship with the HPLMN)
User Controlled WLAN Specific Identifier list (WSIDs)
Operator Controlled WLAN Specific Identifier list (WSIDs)
Pseudonym (format specified in 33.234)
Re-authentication identity
I-WLAN Equivalent HPLMN Presentation Indication (presentation of highest priority EHPLMN or all EHPLMNs to user)
I-WLAN HPLMN Priority Indication (HPLMN preferred over “I-WLAN Last Registered PLMN”)
I-WLAN Last registered PLMN (last successfully registered PLMN via I-WLQAN)
User Controlled PLMN Selector for I-WLAN access
Operator Controlled PLMN Selector for I-WLAN access

## Slide 6: Contents of files at the DF WLAN level (31.102)
EFPseudo (Pseudonym)
EFUPLMNWLAN (User controlled PLMN selector for I-WLAN Access)
EFOPLMNWLAN (Operator controlled PLMN selector for I-WLAN Access)
EFUWSIDL (User controlled WLAN Specific Identifier List)
EFOWSIDL (Operator controlled WLAN Specific Identifier List)
EFWRI (WLAN Re-authentication Identity)
EFHWSIDL (Home I-WLAN Specific Identifier List)
EFWEHPLMNPI (I-WLAN Equivalent HPLMN Presentation Indication)
EFWHPI (I-WLAN HPLMN Priority Indication)
EFWLRPLMN (I-WLAN Last Registered PLMN)
EFHPLMNDAI (HPLMN Direct Access Indicator)

## Slide 7: WLAN related procedures (31.102)
WLAN Selection related Procedures
  The ME shall read the User, Home and Operator controlled WSIDs, the I-WLAN Equivalent HPLMN Presentation Indication, I-WLAN HPLMN Priority Indication, the I-WLAN Last Registered PLMN and the HPLMN Direct Access Indication from the corresponding list files (i.e. EFUWSIDL, EFHWSIDL, EFOWSIDL, EFWEHPLMNPI , EFWLRPLMN, EFWHPI and EFHPLMDAI)to perform WLAN selection procedures as described in TS 24.234.
  The user may change the User controlled WSIDs.
WLAN PLMN Selection related procedures
  The ME shall read the User controlled PLMN selector and/or Operator controlled PLMN selector in EFPLMNWLAN and EFOPLMNWLAN respectively for WLAN PLMN Selection procedures as described in TS 24.234.
  The user may change the User controlled PLMN selector for WLAN.
WLAN access authentication related procedures
  When the ME tries a full authentication, it shall inspect if a valid Pseudonym is available in EFPseudo.and use it as the user name portion of the NAI for WLAN access authentication following the procedures described in TS 24.234.
  The ME shall manage pseudonyms as defined in TS 24.234.
WLAN access re-authentication related procedures
  When the ME tries a fast re-authentication, it shall inspect if a valid reauthentication identity is available in EFWRI and use it as the user name portion of the NAI for WLAN access re-authentication following the procedures described in TS 24.234.
  The ME shall manage re-authentiction identities, Master Key and counter values as described in TS 24.234.

## Slide 8: WLAN Network Selection: PLMN ordering
Generate Ordered list of WSIDs
Generate Ordered list of PLMNs
Authenticate to “Network”
Find Active ANDSF Rule and Apply
Scan of SSIDs
Lists of WSIDs in USIM / ME
Acquire list of available and allowed PLMN
Lists of PLMNs in USIM / ME
Acquire ANDSF rules from HPLMN/VPLMN
Lists of ANDSF rules in ME
Credentials in USIM/ME
Authentication process
WLAN UE Switch on
WLAN selected

## Slide 9: WLAN UE Acquires available and allowable PLMN list for each WSID
For each WSID in order of priority
IEEE 802.1x auth?
N
Y
WLAN UE issues an EAP-Response/Identity to WLAN (“alternative NAI”). RFC 4284 (Identity Selection Hints for EAP)
N
Perform association
Perform tunnel management , clause 8
IEEE 802.11u?
UE requests PLMN list via ANQP procedure
WLAN sends to UE list of supported PLMNs
Y
HPLMN Direct Access?
Y
N
More WSID?
Failed
N
Y
WLAN UE got the list of supported PLMNs
Notes: Automatic Network Selection as in 5.2.4 of 24.234
1) together with the WLAN UE support IEEE Std 802.11u™-2011 [23], the WLAN UE shall send an ANQP request to each WSID. If the WSID supports advertisement of PLMNS, it shall send back an ANQP response to the WLAN UE including the Supported PLMNs list for WLAN access. See Annex A. If the WLAN UE receives a ANQP response where the "Info ID" is not "3GPP Cellular Network information" the behaviour of the WLAN UE is outside the scope of this specification.
2) do not support IEEE 802.1x authentication, if the "HPLMN Direct Access Indicator" as specified in subclause 7.11 allows direct access and if the WLAN UE chooses to perform direct access to HPLMN, then the WLAN UE shall sequentially perform association and perform tunnel management procedures as specified in the clause 8 with each broadcast WSID that does not support IEEE 802.1x authentication.
3) support IEEE 802.1x authentication, the WLAN UE shall request for a list of supported PLMNs by issuing an EAP-Response/Identity message to the WLAN including as identity the alternative NAI. See subclause 4.2.5.
4.2.5 Username
The generation of, and the rules for the use of the username part of an NAI in the WLAN UE are defined in subclause 6.1. The format of the username part of an NAI is defined in 3GPP TS 23.003 [1A].
Clause 8:
The purpose of tunnel management procedures is to define the procedures for establishment or disconnection of an end-to-end tunnel between the WLAN UE and the PDG. Tunnel establishment procedure is always initiated by a WLAN UE, whereas Tunnel Disconnection procedure can be initiated by the WLAN UE or network.

## Slide 10: PLMN Priority after I-WLAN network selection
List of available and allowable PLMN acquired
N
I-WLAN HPLMN priority?
Y
PLMN Priority list:
Highest EHPLMN available
HPLMN
I-WLAN Last registered PLMN in USIM
I-WLAN Last registered PLMN in ME
PLMN Priority list:
I-WLAN Last registered PLMN in USIM
I-WLAN Last registered PLMN in ME
Highest EHPLMN available
HPLMN
PLMN Priority list:
“User Controlled PLMN selector for I-WLAN access” file in USIM
“Operator Controlled PLMN selector for I-WLAN access” file in USIM
“User Controlled PLMN selector for I-WLAN access” file in ME
“Operator Controlled PLMN selector for I-WLAN access” file in ME
PLMN Priority list:
“User Controlled PLMN selector with access technology” file in USIM
“Operator Controlled PLMN selector with access technology” file in USIM
Notes: Section 5.2.4 of 24.234
…the WLAN UE shall choose an available and allowable PLMN in the following order:
a) If the "I-WLAN HPLMN Priority Indication" as specified in subclause 7.10 is available and set to prioritise HPLMN, then:
i) HPLMN (if the EHPLMN list is not present, or is empty);
ii) if the EHPLMN list is present and contains at least one entry the highest EHPLMN that is available; and
iii) if the "I-WLAN Last Registered PLMN" data file is available in the USIM, the PLMN in the "I-WLAN Last Registered PLMN" in the USIM;
else if the "I-WLAN Last Registered PLMN" data file is not available in the USIM and the ME supports the "I-WLAN Last Registered PLMN", the PLMN in the "I-WLAN Last Registered PLMN" in the ME;
b) If "I-WLAN HPLMN Priority Indication" as specified in subclause 7.10 is available and is not set or is not present on the USIM:
i) if the "I-WLAN Last Registered PLMN" data file is available in the USIM, the PLMN in the "I-WLAN last Registered PLMN" in the USIM;
else if the "I-WLAN Last Registered PLMN" data file is not available in the USIM and the ME supports the "I-WLAN Last Registered PLMN" and the last registered PLMN for I-WLAN is available and set to prefer the last registered PLMN, then the PLMN in the "I-WLAN Last Registered PLMN" in the ME;
ii) HPLMN (if the EHPLMN list is not present, or exists but is empty); or
iii) if the EHPLMN list is present and contains at least one entry the highest EHPLMN that is available.
c) If the "User Controlled PLMN Selector for I-WLAN access" data file is available in the USIM, each PLMN in the "User Controlled PLMN Selector for I-WLAN access" data file in the USIM (in priority order) ;
d) If the "Operator Controlled PLMN Selector for I-WLAN access" data file is available in the USIM, each PLMN in the "Operator Controlled PLMN Selector for I-WLAN access" data file in the USIM (in priority order);
NOTE: Requirements for the presence of the "User Controlled PLMN Selector for I-WLAN access" data file and the "Operator Controlled PLMN Selector for I-WLAN access" data file are defined in 3GPP TS 31.102 [13].
e) If neither "User Controlled PLMN Selector for I-WLAN access" nor "Operator Controlled PLMN Selector for I‑WLAN access" data file is available in the USIM or in case when SIM is inserted:
i) each PLMN in the "User Controlled PLMN Selector with Access Technology" data file, if available in the USIM/SIM (in priority order);
ii) each PLMN in the "Operator Controlled PLMN Selector with Access Technology" data file, if available in the USIM/SIM (in priority order).
f) If none of the PLMN selector lists in steps b, c and d is available and the ME supports at least one of the optional "User Controlled PLMN Selector for I-WLAN access" or "Operator Controlled PLMN Selector for I-WLAN access" lists in the ME:
i) each PLMN in the "User Controlled PLMN Selector for I-WLAN access" data file in the ME (in priority order);
ii) each PLMN in the "Operator Controlled PLMN Selector for I-WLAN access" data file in the ME (in priority order).
g) Any other PLMN in random order.

## Slide 11: WLAN Network Selection: Optional ANDSF step
Generate Ordered list of WSIDs
Generate Ordered list of PLMNs
Authenticate to “Network”
Find Active ANDSF Rule and Apply
Scan of SSIDs
Lists of WSIDs in USIM / ME
Acquire list of available and allowed PLMN
Lists of PLMNs in USIM / ME
Acquire ANDSF rules from HPLMN/VPLMN
Lists of ANDSF rules in ME
Credentials in USIM/ME
Authentication process
WLAN UE Switch on
WLAN selected

## Slide 12: I-WLAN & 3GPP Core Network Architecture (23.402) Which Algorithm for Authentication?
3GPP CN
Trusted I-WLAN
Un-trusted I-WLAN
UE
ePDG
AAA/HSS
AAA
proxy
AAA
proxy
UE
AP
AP

## Slide 13: Authentication and key agreement
For trusted non-3GPP access networks
  EAP-AKA’, as defined in RFC 5448, shall be used for mutual authentication and key agreement between the UE and the 3GPP AAA Server.
    E.g. EAP-AKA’ is used for TWAN : Trusted WLAN Access Network (TWAN)
For un-trusted access networks
  The UE and the ePDG shall perform mutual authentication during the IPsec tunnel establishment.
  The UE and the ePDG shall use IKEv2, as specified in RFC 5996, to establish IPsec security association.
  Public key signature-based authentication with certificates to authenticate the ePDG
  EAP-AKA (RFC 4187), within IKEv2, to authenticate the UEs.
Notes:     For untrusted access networks:
    Remark : In addition, before the IPsec tunnel establishment between the UE and the ePDG can be performed, the UE needs to obtain IP connectivity across the access network, which may require an access authentication, which is independent of the EAP-AKA authentication run in conjunction with the IPsec tunnel establishment. This additional access authentication and key agreement is not required for the security of the EPC. It may be required for the security of the untrusted non-3GPP access network.
    TWAN
    Trusted WLAN Access is interfaced with the EPC as a trusted non-3GPP access via the STa interface to the 3GPP AAA Server/Proxy and the S2a interface tot the PDN GW as defined in TS 33.234.
Authentication and key agreement with S2b for Private network access from untrusted non-3GPP access
  Two procedures for authentication and authorization for the Private network access are possible with S2b.
    One procedure when External AAA Server supports the PAP procedure
    One procedure when External AAA Server supports the CHAP procedure. CHAP provides stronger security than PAP
  Remark: EAP is not supported for S2b (between ePDG & PDN interface)

## Slide 14: WLAN Network Selection: Optional ANDSF step
Generate Ordered list of WSIDs
Generate Ordered list of PLMNs
Authenticate to “Network”
Find Active ANDSF Rule and Apply
Scan of SSIDs
Lists of WSIDs in USIM / ME
Acquire list of available and allowed PLMN
Lists of PLMNs in USIM / ME
Acquire ANDSF rules from HPLMN/VPLMN
Lists of ANDSF rules in ME
Credentials in USIM/ME
Authentication process
WLAN UE Switch on
WLAN selected

## Slide 15: Conclusion
There are many configuration information available in the UE to order known WSIDs
Main principles of WLAN NS are:
  The operator has the choice to use whether a UICC or ME based configuration to prioritize the WLAN Network Selection
  The operator may choose not to configure the UICC with WLAN Network Selection information thus give priority to the ME/ANDSF based information
It is a natural process to improve WLAN NS to take into account new contextual information from the AP
  But this can be done also via UICC/ME configuration
  Shall allow the operator to choose whether to use a UICC or ME based configuration