3GPP TSG-SA3 Meeting #49bis 	(S3a071042

Sophia Antipolis, 11 - 13 Dec 2007

| CR-Form-v9.3 |
| --- |
| CHANGE REQUEST |
| ( | 33.203 | CR | 0120 | ( rev | 1 | ( Current version: | 8.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Co-existence of authentication schemes |
| --- | --- |
| Source to WG: ( | BT, CableLabs, Ericsson, Nokia, Nokia Siemens Networks, Orange, Telecom Italia |
| Source to TSG: ( | SA3 |
| Work item code: ( | IMS-Sec |  | Date: ( | 12/12/2007 |
| Category: ( | B |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) |
| Reason for change: ( | 3GPP specifications define several authentication schemes for Common IMS in Release 8. IMS core network entities may have to handle registration messages differently depending on which authentication scheme is used. As the UE does not explicitly indicate the authentication scheme, elaborate rules are needed for the IMS core network entities to distinguish among authentication schemes. These rules are therefore important to ensure that a single IMS core network can be used to support different access networks using different authentication schemes. |
| Summary of change: ( | TR 33.803 v7.0.0 on “Coexistence between TISPAN and 3GPP authentication schemes” was suitably adapted. |
| Consequences if ( not approved: | The idea of a single core network for Common IMS may not be realisable in full. Interoperability problems may arise. |
| Clauses affected: ( | Annex P |
|  | Y | N |  |  |
| Other specs ( | X |  | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*********************************FIRST CHANGE************************

Annex P (normative):
Co-existence of authentication schemes IMS AKA, Early IMS security, NASS-IMS-bundled authentication and SIP Digest

Editor’s note: the correct references to other Common IMS specifications have to be added once they are available. Acronyms have to be added to section 3.

### Editor’s note: a terminology clean up may be needed, e.g. the term “TISPAN NASS” may need to be checked once the corresponding TISPAN specifications are available in 3GPP documents; stage 3 terminology is used when stage 2 terminology may have been more appropriate.

# P.1 Scope of this Annex

This Annex is meant to ensure that the same IMS core network entities can be used to support various authentication schemes defined for Common IMS. In this context, rules are developed how an x-CSCF can decide from a registration request which authentication scheme to apply. If these rules are not adhered to compatibility problems may arise.

The following authentication schemes are taken into account in this Annex:

-	IMS AKA without and with NAT traversal;

-	Early IMS security mechanisms (EIS);

-	NASS-IMS-bundled authentication (NBA);

-	SIP Digest.

These authentication schemes are specified in the following places:

- IMS AKA without NAT traversal is specified in the main body of this specification;

- IMS AKA with NAT traversal is specified in Annex M of this specification;

- SIP Digest without TLS is specified in Annex N of this specification;

- SIP Digest with TLS is specified in Annexes N and O of this specification;

- NASS-IMS-bundled authentication is specified in Annex XXX of this specification;

- Early IMS security is specified in TS 33.jkl [xx].

P.2 Requirements on co-existence of authentication schemes

-	It shall be possible to deploy one IMS in a fixed mobile convergence situation.

-	As a minimum it shall be possible to serve both fixed and mobile subscribers at the same S-CSCF.

-	Incompatibilities between the authentication schemes considered here shall be avoided.

P.3 P-CSCF procedure selection

When the P-CSCF receives a registration request it shall proceed as follows:

The P-CSCF shall first check whether the Security-Client header exists in the received REGISTER message:

- If the REGISTER request contains a Security-Client header then, for an initial registration, the P-CSCF shall select the sec-mechanism and mode (cf. Annex H) from the corresponding parameters offered in the Security-Client header according to its priorities.

    - If the P-CSCF selects the sec-mechanism "ipsec-3GPP" and the mode "trans" it shall perform the steps required for IMS AKA without NAT traversal.

    - If the P-CSCF selects the sec-mechanism "ipsec-3GPP" and the mode "UDP-enc-tun" it shall perform the steps required for IMS AKA with NAT traversal.

    - If the P-CSCF selects the sec-mechanism "tls" it shall perform the steps required for SIP Digest with TLS.

- If the REGISTER request does not contain a Security-Client header, or the P-CSCF does not select any sec-mechanism from the Security-Client header, then the P-CSCF shall behave as follows:

    - If the REGISTER request does not contain an Authorization header and was received over an access networks defined in 3GPP specifications then the P-CSCF shall perform the steps required for Early IMS security.

    - If the REGISTER request does not contain an Authorization header and was received over a TISPAN NASS then the P-CSCF shall perform the steps required for NASS-IMS-bundled authentication.

    - If the REGISTER request contains an Authorization header and was not received over a TISPAN NASS then the P-CSCF shall perform the steps required for SIP Digest without TLS.

Editor’s note: An editor’s note in Annex N states that SIP Digest over mobile is not allowed. It is ffs whether a reference to this editor’s note is sufficient in Annex P, or whether more detailed provisions are needed in Annex P.

    - If the REGISTER request contains an Authorization header and was received over a TISPAN NASS, and the P-CSCF supports both SIP Digest and NBA, then the P-CSCF shall perform the steps required for NBA as well as the steps required for SIP Digest, unless it is configured to behave differently.

Editor’s note: It is ffs whether all access networks need to be addressed explicitly in the above list, as in S3-a071009, or whether the above text is sufficient.

  - For a subsequent registration, the P-CSCF shall continue to use the selected mechanism.

NOTE_p2: Note that Annex N states that SIP Digest authentication shall not apply to access networks defined in 3GPP specifications.

NOTE_p3: The use of Authorization headers in IMS REGISTER requests is defined in TS 24.229 [8].

NOTE_p4: The inclusion of an Authorization header in a REGISTER request is optional for NBA and mandatory for SIP Digest. Therefore, when a REGISTER request received over a TISPAN NASS contains an Authorization header the P-CSCF cannot know whether the request relates to SIP Digest or NBA unless it is configured to select one of the schemes according to certain criteria, e.g. IP address range. The steps required for SIP Digest and for NBA are not in contradiction. Rather, for NBA the P-CSCF needs to perform additional steps, namely an exchange with the TISPAN NASS and an inclusion of NASS location information in the REGISTER request, on top of the steps required for SIP Digest.

A P-CSCF is said to be “TISPAN-enabled” if it handles P-Access-Network-Info headers as follows:

- A “TISPAN-enabled” P-CSCF shall insert a P-Access-Network-Info header containing the "network-provided" parameter and remove any such header containing the "network-provided" parameter sent by the UE if the REGISTER request was received over a TISPAN NASS.

- A “TISPAN-enabled” P-CSCF may insert a P-Access-Network-Info header containing the "network-provided" parameter and shall remove any such header containing the "network-provided" parameter sent by the UE if the REGISTER request was not received over a TISPAN NASS.

NOTE_p5: For the purposes of NBA, the P-CSCF includes NASS location information in the P-Access-Network-Info header. But, according to TS 24.229 [8], the P-CSCF handles any P-Access-Network-Info header included by the UE transparently, and, hence, an S-CSCF could receive a P-Access-Network-Info header with false NASS location information inserted by the UE even when the access network is not a TISPAN NASS. This would negatively impact the security of NASS-IMS-bundled authentication. Therefore, the removal of a P-Access-Network-Info header with the "network-provided" parameter is mandated for TISPAN-enabled P-CSCFs even when the access network is not a TISPAN NASS.

Editor’s note: the term “TISPAN-enabled” P-CSCF may have to be reconsidered.

Editor’s note: it is ffs whether the property “TISPAN-enabled” is mandatory or optional for implementation. SA3 agrees that leaving it optional is sufficient for security purposes, but non-security considerations, e.g. charging, as discussed in SA2 and CT1 may necessitate making this property mandatory.

How the P-CSCF knows the access network type of a specific network interface is implementation-dependent (e.g. it can know the access network type from different UE IP address ranges or by using different network interfaces for different access network types).

## P.4	Determination of requested authentication scheme in S-CSCF

### P.4.1	Stepwise approach

When receiving a REGISTER request the S-CSCF distinguishes among authentication methods using the following three steps. How these steps are performed is described in clause P.4.2.

-	Step 1: the S-CSCF first checks whether the IMS REGISTER request relates to IMS AKA or not. In the case of IMS AKA, the S-CSCF shall behave according to this specification. Otherwise, the S-CSCF proceeds to step 2.

-	Step 2: for a non-IMS-AKA REGISTER request, the S-CSCF next checks whether the request relates to Early IMS security. In the case of Early IMS security, the S-CSCF shall behave according to TS 33.jkl [xx]. Otherwise, the S-CSCF proceeds to step 3.

-	Step 3: In step 3, the S-CSCF requests the HSS to perform the distinction among SIP Digest and NBA.

NOTE_p6:	The distinctions in steps 1 and 2 are required because the records of an IMS AKA or Early IMS user may reside on an HSS of an earlier release. Such an HSS requires the authentication scheme to be determined by the S-CSCF according to the specification for IMS AKA and Early IMS security.

For subsequent REGISTER requests, the authentication scheme shall not change.

### P.4.2	Mechanisms for performing steps 1 to 3 in P.4.1

Step 1:

The S-CSCF checks for the presence of an Authorization header in the REGISTER request, and, if present, checks further for the presence of an "integrity-protected" flag within this header. If the flag is present and has either the value “yes” or the value “no” the S-CSCF concludes that the REGISTER request relates to IMS AKA.

NOTE_p7: the "integrity-protected" flag and its values are defined in TS 24.229 [8].

Step 2:

This step rests on two conditions:

1)	The S-CSCF shall know, e.g. using the mechanism in clause P.5, which P-CSCFs are TISPAN-enabled in the sense of clause P.3.

2)	It shall be ensured that P-CSCFs, which are not TISPAN-enabled, do not connect to TISPAN NASS.

The S-CSCF then shall proceed as follows:

If there is no Authorization header in the REGISTER request, and

-	there is no P-Access-Network-Info header containing the "network-provided" parameter, in which the access-type parameter indicates TISPAN NASS, or

-	the REGISTER request is received from a P-CSCF, which is not “TISPAN-enabled”,

then Early IMS security is used.

Editor’s note: the above text needs to be double checked as it was claimed at SA3#49bis that a subcase was missing.

Otherwise, the S-CSCF proceeds to step 3.

NOTE_p8: instead of specifying “Otherwise, the S-CSCF proceeds to step 3.” it would have been logically equivalent to specify: 
“Otherwise, if either

- there is an Authorization header, which does not contain an "integrity-protected" flag with one of the values “yes” or “no”, or

- there is no Authorization header, and the access-type parameter in the P-Access-Network-Info header containing the "network-provided" parameter indicates TISPAN access, and the request is received from a TISPAN-enabled P-CSCF,

then the S-CSCF proceeds to step 3. ”

Step 3:

The S-CSCF shall send an authentication request to the HSS indicating that the authentication scheme is unknown. The S-CSCF shall infer the authentication scheme used by the subscriber from authentication request response by the HSS. When SIP Digest is used the S-CSCF will learn from the "integrity-protected" flag in the subsequently received REGISTER request containing the challenge response whether SIP Digest with or without TLS is used.

NOTE_p9: the procedure in step 3 is based on the assumption that a user always uses either NBA or SIP Digest, but not sometimes NBA and sometimes SIP Digest.

Editor’s note: it is ffs whether the distinction in step 3 should be finer grained. The need for such a more detailed distinction should be demonstrated by appropriate use cases.

P.5 	Co-existence of TISPAN-enabled and other P-CSCFs

This section introduces a configuration-based solution, which enables an S-CSCF to serve both TISPAN-enabled P-CSCFs and P-CSCFs that are not TISPAN-enabled.

Configuration-based solution:

The S-CSCF shall be configured in such a way that it knows which P-CSCFs are TISPAN-enabled, according to section P.3. The S-CSCF knows the P-CSCF which forwarded the registration request from the Via header.

NOTE_p10:	Both EIS and NBA require the P-CSCF to be in the home network. This may help in realising the configuration-based solution.

Editor’s note: It is ffs whether a protocol- based solution should be added. In such a solution, a TISPAN-enabled P-CSCF could include an indication about its capability to handle the "P-Access-Network-Info" header correctly, according to section P.3, in an appropriate header field.

P.6 	Considerations on the Cx interface

The specification of certain Cx commands in TS 29.228 [xx] requires the inclusion of a private user identity (IMPI). When a registration request is sent without an Authorization header then such a private identity is not available.

For EIS, an Authorization header is never included in a registration request. However, it is specified for EIS in TS 33.jkl [xx] how to derive a private identity from a public identity. This derived private identity is then used in Cx commands.

For NBA the inclusion of an Authorization header in a registration request is optional. The handling of private user identities in Cx commands relating to registration requests without Authorization header remains left open in NBA specifications.

NOTE_p11: Proprietary solutions may be required in networks where NBA clients may send registration requests without Authorization header. Some of these proprietary solutions may require the I-CSCF to handle Cx commands in a way specific to NBA clients. In such a case the I-CSCF may use the P-Access-Network Info header to determine whether the request was sent over a TISPAN NASS network. In contrast to the procedures for the S-CSCF in clause P.5, the correctness of the information in the P-Access-Network Info header is not security-critical in the context of the I-CSCF discussed in this note. Note also that such proprietary solutions may lead to interoperability problems between an HSS and an x-CSCF from different vendors.

Editor’s note: the agreed new WID on NBA stage 3 in CT1 may lead to a standardized solution for the problem. Then NOTE_p11 would need to be revisited.

******************************END FIRST CHANGE***********************

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.