Third Generation Partnership Project (3GPP™)

FINAL Meeting Report
for
TSG SA WG3
meeting: March 09 ad hoc

Sophia-Antipolis, France, 23/03/2009 to 26/03/2009

1	Opening of the meeting	3

2	Agreement of the agenda	3

3	Assignment of input documents	3

4	Report of relevant issues from SA#43	3

5	Incoming LS’s sent to SA3 relevant for the ad hoc	3

6	Technical contributions in SAE/LTE	4

6.1	Security architecture	4

6.2	Authentication and key agreement	7

6.3	Key derivation	7

6.4	Integrity and ciphering mechanisms	12

6.5	Security mode establishment and mobility aspects	12

6.6	Mobility with GSM, UMTS networks	15

6.7	Mobility with non-3GPP networks	18

6.8	Network domain security	22

6.9	eNodeB security	23

6.10	Emergency call	23

6.11	Other areas	24

7	Joint meeting with TISPAN WG7	25

7.1	Prevention of Unsolicited Communication	26

7.2	Media security	29

7.3	Customer premises network security [H(e)NB in 3GPP and CNG in TISPAN]	30

7.4	IPTV security issues	30

7.5	Connection of NGCN to IMS	30

8	Technical contributions in other ad hoc work items	30

8.1	Home (e)NB security	31

8.2	IMS media plane security	40

8.3	Protection against Unsolicited Communication for IMS	42

9	Close	42

Annex A: List of contribution documents	43

Annex B: List of change requests	53

Annex C: Lists of liaisons	60

C1: Incoming liaison statements	60

C2: Outgoing liaison statements	62

Annex F: List of action items	63

Annex G: List of participants	64

## 1	Opening of the meeting

The Chairman opened the meeting welcoming the Delegates to ETSI premises.

A minute of silence in the memory of Nigel Barnes, who sadly passed away, was kept.

## 2	Agreement of the agenda

S3-090400	Agenda for SA WG3 ad hoc meeting
					Source: SA WG3 Chairman

Discussion:

The Chairman presented the agenda. New Rapporteurs for 33.401 and 33.402 were assigned as Marc Blommaert is not participating to the SA3 meetings anymore. Dajiang Zhang volunteered to take 33.401 and Guenther Horn volunteered to take 33.402; this was confirmed. The SAE/LTE document order will be provided by the new Rapporteurs from now on.

The new Rapporteur for 33.102 will be Guenther Horn. A Rapporteur for 33.310 has to be assigned; this will be done in the May meeting.

Decision: 		The document was agreed.

## 3	Assignment of input documents

## 4	Report of relevant issues from SA#43

S3-090402	Report from SA#43 Plenary
					Source: SA WG3 Chairman

Discussion:

The Chairman presented the report.

Decision: 		The document was noted.

S3-090401	Report from SA3#54
					Source: SA WG3 Secretary

Discussion:

For information. Not presented.

Decision: 		The document was noted.

## 5	Incoming LS’s sent to SA3 relevant for the ad hoc

S3-090410	Reply LS on Receive of ETWS outside home-PLMN
					Source: S1-090199

Decision: 		The document was not addressed.

S3-090407	New Q.16/13 study item on Mobility Security. Response to the 3GPP liaison statement S3-081567
					Source: COM13-LS032

Discussion:

ZTE presented the contribution.

Decision: 		The document was noted.

S3-090552	Mobility Security Framework in NGN in ITU-T
					Source: ZTE Corporation

Discussion:

ZTE presented the contribution. Comments to the document were invited.

Decision: 		The document was noted.

## 6	Technical contributions in SAE/LTE

S3-090631	Reply LS to S3-090596 = R2-092666 on Concurrent Running of Security Procedures
					Source: R2-092676

Decision: 		The document was noted.

### 6.1	Security architecture

S3-090417	33.401 CR: Correction of UE EPS security capability default set
					Source: Ericsson

Discussion:

Ericsson presented the CR.

Decision: 		The document was agreed.

S3-090420	33.401 CR: Storage of EPS NAS security context
					Source: Ericsson, Gemalto

Discussion:

Ericsson presented the CR. It was decided to come back to 420 after 574 has been discussed.

Decision: 		The document was revised to S3-090640.

S3-090640	33.401 CR: Storage of EPS NAS security context
					Source: Ericsson, Gemalto

(Replaces S3-090420)

Decision: 		The document was agreed.

S3-090422	33.401 CR: Correction of eKSI usage in AS
					Source: Ericsson, Nokia Siemens Networks, NEC Corporation

Discussion:

Ericsson presented the CR. Huawei suggested that this CR has to be merged with 513.

Decision: 		The document was merged in S3-090583.

S3-090513	Corrections of 33.401
					Source: Huawei,ZTE

Discussion:

Huawei presented the CR. It was agreed to merge the two documents. Qualcomm suggested that 570 is also related but is not contradicting and can be taken later.

Decision: 		The document was merged in S3-090583.

S3-090583	Corrections of eKSI and AS in 33.401
					Source: Huawei,ZTE, Ericsson,

(Replaces S3-090513)

Decision: 		The document was agreed.

S3-090423	Editorial corrections to security context establishment clause
					Source: Ericsson

Discussion:

Ericsson presented the CR.

Decision: 		The document was agreed.

S3-090437	LS on the removal of KNASint and KNASenc from EFEPSNSC
					Source: C6-090055

Discussion:

NEC presented the LS. Huawei suggested replying to this LS asking whether the effects of such a decision have been considered on the ME. Alcatel-Lucent suggested that Rel-99 UICC will have to run the necessary computation in any case, so the effect is small; Gemalto suggested that the most efficient way should be selected and supported the idea of a reply LS.

The subjects to be asked in the LS were agreed to be the cost evaluation, and the impact on ME. Also, the removal of NH will be asked as it is not needed.

Decision: 		The document was replied to.

S3-090584	Reply to: LS on the removal of KNASint and KNASenc from EFEPSNSC
					Source: current meeting

Decision: 		The document was agreed.

S3-090546	CR to 33.401 Removal of NAS keys storage
					Source: NEC Corporation, Nokia Corporation, Nokia Siemens Networks, NTT DOCOMO

Discussion:

NEC presented the CR. The reply LS S3-090584 will be used to decide if the CR is agreed, but the content is agreed in principle.

Decision: 		The document was conditionally agreed.

S3-090524	Correction of EPS AS/NAS Security Context definition
					Source: China Mobile,ZTE

Decision: 		The document was revised to S3-090557.

S3-090516	corrections for Attach procedure
					Source: Huawei

Discussion:

Huawei presented the CR. A check with 24.301 should be done to make sure that there are no such cases. Also, 33.401 clause 7.2.5.1 in the last sentence should be checked and decide whether to remove the sentence or not. Agreed in principle.

Decision: 		The document was revised to S3-090585.

S3-090585	corrections for Attach procedure
					Source: Huawei

(Replaces S3-090516)

Decision: 		The document was agreed.

S3-090557	Correction of EPS AS/NAS Security Context definition
					Source: China Mobile,Nokia Corporation, Nokia Siemens Networks

Discussion:

China Mobile presented the CR. The sentence where the UE shall delete the AS security context was decided to be kept. The two bullets could also be combined together.

Decision: 		The document was revised to S3-090586.

S3-090586	Correction of EPS AS/NAS Security Context definition
					Source: China Mobile,Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090557)

Decision: 		The document was agreed.

S3-090566	Clarification of LTE USIM requirement
					Source: NTT DOCOMO

Decision: 		The document was [not addressed].

S3-090574	Completing the handling of security contexts in TS 33.401
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the contribution.

Decision: 		The document was noted.

S3-090571	Correcting the handling of EPS security context
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the CR. Some offline checks must be done to ensure the most secure solution. The state diagram must also be checked. It was decided to have a revision of this to be discussed over email.

Decision: 		The document was revised to S3-090639.

S3-090639	Correcting the handling of EPS security context
					Source: Qualcomm Europe

(Replaces S3-090571)

Decision: 		The document was sent for email discussion.

### 6.2	Authentication and key agreement

S3-090547	AKA procedure in case of NAS security actived
					Source: ZTE Corporation, HUAWEI

Discussion:

ZTE presented the CR. This is already covered by stage 3 specifications so it is not needed.

Decision: 		The document was noted.

### 6.3	Key derivation

S3-090440	LS response to R2-087408 (Reply LS on PCI Clarification)
					Source: R3-090544

Discussion:

Ericsson presented the LS.

Decision: 		The document was noted.

S3-090418	33.401 CR: Resolving ed note on PLMN ID encoding
					Source: Ericsson

Discussion:

Ericsson presented the CR.

Decision: 		The document was agreed.

S3-090531	Removal of the paragraph mentioning IMSI from the Annex A2
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

Discussion:

Obsoleted by agreeing 418.

Decision: 		The document was withdrawn.

S3-090427	33.401 CR: Introduction to forward security
					Source: Ericsson

Discussion:

Ericsson presented the CR. The Chairman pointed out that the terminology had been developed in the specification using backward security for what in the CR is meant by forward security, so there should be done several substitutions in the specification. Nokia Siemens Networks suggested transferring the introduction in the definition clause.

Decision: 		The document was revised to S3-090587.

S3-090587	33.401 CR: Introduction to forward security
					Source: Ericsson

(Replaces S3-090427)

Decision: 		The document was agreed.

S3-090507	Clarification on Multiple KeNB*s Preparation in Section 7.4.3
					Source: Huawei

Discussion:

Huawei presented the CR.

Decision: 		The document was revised to S3-090588.

S3-090588	Clarification on Multiple KeNB*s Preparation in Section 7.4.3
					Source: Huawei

(Replaces S3-090507)

Decision: 		The document was agreed.

S3-090510	Add the frequency EARFCN-DL
					Source: Huawei,ZTE

Discussion:

Some minor editorials to be applied.

Decision: 		The document was merged in S3-090588.

S3-090589	Add the frequency EARFCN-DL
					Source: Huawei,ZTE

(Replaces S3-090510)

Decision: 		The document was withdrawn.

S3-090522	Correction of KeNB derivations
					Source: China Mobile,ZTE

Decision: 		The document was revised to S3-090555.

S3-090529	The definition of eKSI format
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile

Discussion:

Alcatel-Lucent presented the CR. Some changes have to be applied.

Decision: 		The document was revised to S3-090590.

S3-090590	The definition of eKSI format
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile

(Replaces S3-090529)

Decision: 		The document was agreed.

S3-090530	Additional condition of KeNB refresh
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile

Discussion:

Alcatel-Lucent presented the CR. Some clarification is needed, but the intention was agreed that it is not to impact the stage 3.

Decision: 		The document was withdrawn.

S3-090591	Correction on KeNB refresh
					Source: Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090561)

Decision: 		The document was agreed.

S3-090548	Key-Change-On the Fly Clarification
					Source: ZTE Corporation

Discussion:

ZTE presented the CR. The first sentence is pending the discussion of 564; the rest of the CR is pending a check that the stage 3 specification does not already address that.

Subsequently to the agreement of 564, the first change was agreed to be removed.

Decision: 		The document was noted.

S3-090592	Key-Change-On the Fly Clarification
					Source: ZTE Corporation

(Replaces S3-090549)

Decision: 		The document was agreed.

S3-090555	Correction of KeNB derivations
					Source: China Mobile,ZTE,Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090522)

Discussion:

The summary of change must be clarified.

Decision: 		The document was revised to S3-090593.

S3-090593	Correction of KeNB derivations
					Source: China Mobile,ZTE,Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090555)

Decision: 		The document was agreed.

S3-090562	Correction on Key Identification
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the CR. Qualcomm suggested that the CR should be rephrased to be more abstract; this was agreed and has to be discussed offline.

Decision: 		The document was revised to S3-090594.

S3-090594	Correction on Key Identification
					Source: Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090562)

Decision: 		The document was agreed.

S3-090564	NH derivation rules for re-keying
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution. Huawei suggested revising 'derived' to 'handled' for the NH; this was agreed. ZTE suggested that 548 in the first change does the same thing; it was agreed to remove this first change from 548. A rewording must be done on the CR.

Decision: 		The document was revised to S3-090595.

S3-090595	NH derivation rules for re-keying
					Source: Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090564)

Decision: 		The document was agreed.

S3-090561	Correction on KeNB refresh
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the CR.

Decision: 		The document was revised to S3-090591.

S3-090560	Discussion on potential problems with concurrent key handling procedures
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution.

Decision: 		The document was noted.

S3-090570	Clarifications to calculating the initial K_eNB and K_eNB after key change on the fly
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the CR. It was agreed to send an LS attaching this CR to inform RAN2 and RAN3 and possibly receive a reply within the same week, but start the work immediately.

Timeline:

- comments by: April 3;

- new version by: April 6;

- final remarks by: April 8;

- final version by: April 9.

Decision: 		The document was sent for email approval.

S3-090596	LS on concurrent running of security procedures
					Source: current meeting

Discussion:

Nokia Siemens Networks presented the LS.

Decision: 		The document was agreed.

S3-090549	Clarification for Forward Security
					Source: ZTE Corporation

Discussion:

Note 1 can be removed as this case does not occur.

Decision: 		The document was revised to S3-090592.

### 6.4	Integrity and ciphering mechanisms

S3-090434	LS on exception lists for integrity protection of NAS messages
					Source: C1-091369

Discussion:

Nokia Siemens Networks presented the contribution on behalf of Motorola.

Decision: 		The document was noted.

S3-090511	The correction on input key of Null ciphering algorithm
					Source: Huawei,ZTE

Discussion:

Huawei presented the CR.

Decision: 		The document was agreed.

### 6.5	Security mode establishment and mobility aspects

S3-090442	LS on Security for TAU Request
					Source: S2-091788

Discussion:

Huawei presented the LS.

Decision: 		The document was replied to.

S3-090515	idle mode procedure in EUTRAN
					Source: Huawei

Discussion:

Huawei presented the CR. Subsequently to the discussion below, the decision on the CR is postponed until the reply from SA2.

Decision: 		The document was postponed.

S3-090573	Proposed response to S3-090442 (=S2-091788)
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the contribution. Huawei suggested that the case discussed is very infrequent and should not be addressed here again. The level of frequency was discussed; it was decided that an LS to SA2 should be sent to understand this level.

Decision: 		The document was noted.

S3-090599	Reply to: LS on Security for TAU Request
					Source: current meeting

Decision: 		The document was agreed.

S3-090441	LS on transfer of UE Security Capabilities to target eNBs
					Source: R3-090664

Discussion:

Ericsson presented the LS. It was decided to put 421, 512 and 559 in offline discussion as all three are addressing the action from RAN3, and merge them. A simple reply to notify this will be done.

Decision: 		The document was replied to.

S3-090600	Reply to: LS on transfer of UE Security Capabilities to target eNBs
					Source: current meeting

Decision: 		The document was agreed.

S3-090421	33.401 CR: UE security capability handling at S1 HO
					Source: Ericsson

Decision: 		The document was merged in S3-090601.

S3-090512	Clarification of NAS algorithm selection during S1 HO
					Source: Huawei,ZTE

Decision: 		The document was merged in S3-090601.

S3-090559	Correction on Transfer of Capabilities in S1-handover
					Source: Nokia Corporation, Nokia Siemens Networks

Decision: 		The document was merged in S3-090601.

S3-090601	33.401 CR: UE security capability handling at S1 HO
					Source: Ericsson

(Replaces S3-090421)

Decision: 		The document was agreed.

S3-090518	Corrections for the EPS security context fetching between MMEs
					Source: Huawei

Discussion:

Huawei presented the CR. No comments.

Decision: 		The document was agreed.

S3-090523	Correction of EPS AS Security Mode Command Procedure
					Source: China Mobile

Decision: 		The document was revised to S3-090556.

S3-090556	Correction of EPS AS Security Mode Command Procedure
					Source: China Mobile,Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090523)

Discussion:

China Mobile presented the contribution. NTT DOCOMO suggested some rewording, supporting the overall purpose of the CR. Some offline discussion was necessary.

Decision: 		The document was revised to S3-090602.

S3-090602	Correction of EPS AS Security Mode Command Procedure
					Source: China Mobile,Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090556)

Decision: 		The document was agreed.

S3-090565	RRC Connection Re-establishment – security corrections
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution. Some offline checking with the RAN specification is necessary.

Decision: 		The document was revised to S3-090603.

S3-090603	RRC Connection Re-establishment – security corrections
					Source: Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090565)

Decision: 		The document was agreed.

S3-090572	Correcting MME behaviour at S1-handover
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the CR. Huawei suggested that there could be some concerns on the NCC wrap around; Qualcomm agreed that there is a limit to the NCC number but there should not be a reason to prepare 7 S1-handovers without executing them. It was agreed to mention this issue in the LS to RAN2, without asking the group to solve this for SA3. It was agreed to mention that SA3 has agreed on this CR but needs RAN groups to check what impact or concern this CR could raise.

Decision: 		The document was conditionally agreed.

S3-090604	LS to RAN2 and RAN3 on Correcting MME behaviour at S1-handover
					Source: current meeting

Decision: 		The document was agreed.

### 6.6	Mobility with GSM, UMTS networks

S3-090405	LS on Security parameter handling
					Source: C1-090756

Discussion:

Nokia Siemens Networks presented the LS.

Decision: 		The document was noted.

S3-090409	LS on handling of dynamic UE UTRAN capability during Handover
					Source: R2-091922

Discussion:

Ericsson presented the LS. No issues were identified.

Decision: 		The document was noted.

S3-090435	Reply LS on preventing inter-RAT HO for UE with SIM access
					Source: C4-090512

Discussion:

Vodafone presented the LS.

Decision: 		The document was noted.

S3-090438	LS on preventing inter-RAT HO for UE with SIM access
					Source: GP-090351

Discussion:

Nokia Siemens Networks presented the LS.

Decision: 		The document was noted.

S3-090508	START/NAS COUNT relay on Inter-RAT mobility
					Source: Huawei

Discussion:

Huawei presented the contribution. The backward compatibility issue needs some more study; the possibility for a policy for AKA re-runs should also be studied; further contributions are possible and in the SA3#55 this should be decided to be on time for Release 9.

Decision: 		The document was noted.

S3-090416	33.401 CR: Activation of native EPS NAS security context after IRAT HO
					Source: Ericsson, NEC Corporation

Discussion:

Ericsson presented the CR. Nokia Siemens Networks suggested that some improvement of step 5 would be needed, but did not have an issue with the general concept of aligning the TAU procedures.

Decision: 		The document was revised to S3-090606.

S3-090606	33.401 CR: Activation of native EPS NAS security context after IRAT HO
					Source: Ericsson, NEC Corporation

(Replaces S3-090416)

Decision: 		The document was agreed.

S3-090414	33.401 CR: Removal of KSI_ASME from TAU Accept
					Source: Ericsson, NEC Corporation

Discussion:

Ericsson presented the CR. Agreed in principle but has to be merged with S3-090606.

Decision: 		The document was merged in S3-090606.

S3-090415	33.401 CR: Correction of UE security capability handling in the TAU procedure
					Source: Ericsson, NEC Corporation

Discussion:

Ericsson presented the CR. Agreed in principle but has to be merged with S3-090606.

Qualcomm suggested that a sentence on security negotiations (bidding down protection) could be missing; this has to be checked.

Decision: 		The document was merged in S3-090606.

S3-090419	33.401 CR: Correction of MM context transfer
					Source: Ericsson

Discussion:

Ericsson presented the CR. Agreed in principle but has to be merged with S3-090606.

Decision: 		The document was merged in S3-090606.

S3-090519	corrections for idle mode procedure in EUTRAN
					Source: Huawei

Discussion:

Huawei presented the CR. 'with' should be deleted in the second change.

Decision: 		The document was revised to S3-090607.

S3-090607	correctinos for idle mode procedure in EUTRAN
					Source: Huawei

(Replaces S3-090519)

Decision: 		The document was agreed.

S3-090558	Keys to be used in HO from E-UTRAN to UTRAN and GERAN
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the CR.

Decision: 		The document was agreed.

S3-090563	Keys to be used in HO from UTRAN and GERAN to E-UTRAN
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the CR. It was agreed that if an issue is identified something until the May meeting this CR can be corrected.

Decision: 		The document was agreed.

### 6.7	Mobility with non-3GPP networks

S3-090436	LS on Prefix for EAP-AKA'
					Source: C4-090799

Discussion:

Qualcomm presented the LS.

Decision: 		The document was replied to.

S3-090544	Hint digits in EAP-AKA’
					Source: Ericsson, Nokia Siemens Networks, Nokia Corporation

Discussion:

Nokia Siemens Networks presented the contribution.

Decision: 		The document was revised to S3-090615.

S3-090580	comments to S3-090544(Hint digits in EAP-AKA’)
					Source: Huawei

Discussion:

Huawei presented the commenting contribution. Nokia Siemens Networks suggested that the first comment is untrue as the statement that NAIs with EPC label in the realm exists in subclause 19.2 of 23.003. Huawei suggested that the comment aims to point out that this is not the only option; Nokia Siemens Networks pointed out this is a ‘shall’ in the specification. Huawei suggested that the argumentation of Nokia Siemens Networks is based on the proposed CT4 CR; Nokia Siemens Networks suggested that the argumentation references the CR to point out that the addition of hint digits is not useful under any scenario.

Alcatel-Lucent suggested that the CR is proposing to address issues with legacy AAA servers that could not handle this without hint digits; also, Alcatel-Lucent asked whether the addition of hint digits could bring problems; Nokia Siemens Networks suggested that IETF is concerned with the addition of these hint digits.

Nokia Siemens Networks proposed to send an LS to CT4 to ask them to revise the CR removing EAP-AKA'-specific hint digits.

Qualcomm and Alcatel-Lucent referenced the RFC 4187 where the AAA asks for the EAP-AKA-specific identity if it cannot parse the IMSI.

Nokia Siemens Networks suggested that the main issue is that there is no reason for 3GPP to specify these hint digits. Huawei suggested that the purpose of SA3 is to evaluate security issues with these solutions.

It was agreed that the hints would not create security issues but would not bring any security benefits for EPC.

Huawei expressed the preference for a protocol-based solution. Alcatel-Lucent suggested that in case 2 of table 1 the last statement is incorrect (the AAA server can actually fail back to EAP-AKA). It was agreed to put in the LS that SA3 did not decide yet about this part and it is under dispute.

It was also agreed to attach the papers discussed in the LS. It was also agreed that the changes to 33.402 should be minimal.

Decision: 		The document was noted.

S3-090615	Hint digits in EAP-AKA’
					Source: Ericsson, Nokia Siemens Networks, Nokia Corporation

(Replaces S3-090544)

Discussion:

Counter comments to 580.

Decision: 		The document was noted.

S3-090614	Reply to: LS on Prefix for EAP-AKA'
					Source: current meeting

Discussion:

Nokia Siemens Networks presented the proposed LS.

Decision: 		The document was agreed.

S3-090545	Use of NAI prefix for EAP-AKA’
					Source: Ericsson, Nokia Siemens Networks, Nokia Corporation

Discussion:

Postponed to the May meeting as there is currently no agreement on the issue of hint digits above.

Decision: 		The document was postponed.

S3-090517	clarification for EAP-AKA'
					Source: Huawei

Discussion:

Huawei presented the CR. Alcatel-Lucent suggested removing the 'based on' part. It was agreed to not agree this at the moment as the CT4 response to 614 is expected.

Decision: 		The document was postponed.

S3-090425	33.402 CR: Clarification of order for identity request and AVs fetching
					Source: Ericsson

Discussion:

Ericsson presented the CR. Some step and Note renumbering is necessary.

Decision: 		The document was revised to S3-090616.

S3-090616	33.402 CR: Clarification of order for identity request and AVs fetching
					Source: Ericsson

(Replaces S3-090425)

Decision: 		The document was agreed.

S3-090443	LS on Enhanced Security for S2c
					Source: S2-091795

Discussion:

Qualcomm presented the LS.

Decision: 		The document was replied to.

S3-090575	Proposed response to LS on Enhanced Security for S2c
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the contribution. Telecom Italia supported the contribution. France Telecom suggested that sometimes links cannot be clearly defined as trusted and supported the Qualcomm proposal; Nokia Siemens Networks suggested that this is addessed by the S2b interface.

The second question adds a new option.

The third question in the LS remains unsolved within SA3 as Qualcomm, Telecom Italia and France Telecom support it while Nokia Siemens Networks and Ericsson consider that the disadvantages outweight the advantages.

Nokia Siemens Networks suggested that moreover there are no advantages as there is no confidentiality in S2b either (IPSec tunnel).

Decision: 		The document was revised to S3-090617.

S3-090617	Reply to: LS on Enhanced Security for S2c
					Source: current meeting

(Replaces S3-090575)

Decision: 		The document was agreed.

S3-090488	Authorization for ANDSF
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia presented the contribution. Qualcomm proposed some rewording which was agreed.

Decision: 		The document was revised to S3-090618.

S3-090618	Authorization for ANDSF
					Source: Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090488)

Decision: 		The document was agreed.

S3-090551	Update UE-ANDSF Communication Security Solution
					Source: ZTE Corporation

Discussion:

ZTE presented the contribution. The Chairman suggested that no FFS can be put for Release 8. ZTE agreed to remove the FFS.

It was agreed to clarify if there is a security hole for the May meeting and add this for Release 9.

Decision: 		The document was noted.

S3-090424	33.402 CR: Clarification on use of USIM/UICC in non-3GPP accesses
					Source: Ericsson

Discussion:

Ericsson presented the CR.

Decision: 		The document was agreed.

S3-090550	Clarification for DSMIPv6 Bootstrap
					Source: ZTE Corporation

Discussion:

ZTE presented the contribution. Qualcomm suggested the change in step 7 should actually be in step 14. It was to leave this open until the May meeting.

Decision: 		The document was postponed.

S3-090532	Change in the Clause 6.2. Removal of explicit CK’/IK’ function
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

Discussion:

Alcatel-Lucent presented the CR. The reason for change is missing to say that there is a mismatch. Huawei suggested that there is no mismatch. There was some discussion on this and it was suggested to have formulas only in one place; it was agreed.

It was decided to study the matter until the May meeting and if there is a mismatch, a reference to be put. Alcatel-Lucent suggested that this might be an issue for 3GPP2.

Decision: 		The document was revised to S3-090630.

S3-090630	Change in the Clause 6.2. Removal of explicit CK’/IK’ function
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

(Replaces S3-090532)

Decision: 		The document was agreed.

S3-090487	CR Remove Duplicate Section Number in 7.6.1.3.4
					Source: Huawei

Decision: 		The document was revised to S3-090608.

S3-090608	CR Remove Duplicate Section Number in 7.6.1.3.4
					Source: Huawei

(Replaces S3-090487)

Decision: 		The document was agreed.

### 6.8	Network domain security

S3-090456	Update of referenced RFCs and hash algorithm
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the CR. Category should be C. Some offline checking of the reference titles must be done; references [3] and [13] should be Void. It was agreed to make SHA-1 and SHA-256 mandatory to be supported.

Decision: 		The document was revised to S3-090609.

S3-090609	Update of referenced RFCs and hash algorithm
					Source: Qualcomm Europe

(Replaces S3-090456)

Discussion:

Agreed in principle, but it is out of scope for the ad hoc so a second check has to be done in SA3#55.

ACTION:	Agreed in principle, but it is out of scope for the ad hoc so a second check has to be done in SA3#55.
	(action on: Brian Rosenberg)

Decision: 		The document was conditionally agreed.

S3-090473	Corrections for TS 33.310
					Source: Huawei

Discussion:

Agreed in principle, but it is out of scope for the ad hoc so a second check has to be done in SA3#55.

ACTION:	Agreed in principle, but it is out of scope for the ad hoc so a second check has to be done in SA3#55.
	(action on: Dony He)

Decision: 		The document was conditionally agreed.

S3-090483	Draft WID: NDS enhancements to support backhaul security
					Source: Nokia Siemens Networks, T-Mobile, TeliaSonera, Vodafone

Discussion:

Vodafone presented the WID.

No objection in principle, but it is out of scope for the ad hoc so a second check has to be done in SA3#55. Vodafone suggested that this could also be an opportunity to invite the first technical contributions. Huawei suggested some timing issues could occur.

Decision: 		The document was conditionally agreed.

### 6.9	eNodeB security

S3-090521	Addition of security requirements on eNB
					Source: China Mobile, Alcatel-lucent, Vodafone, ZTE

Decision: 		The document was revised to S3-090554.

S3-090554	Addition of security requirements on eNB
					Source: China Mobile, Alcatel-lucent, Vodafone, ZTE

(Replaces S3-090521)

Discussion:

China Mobile rpesented the CR. Category should be changed, along with some other cover page corrections. The title and the text must be in line with each other. This has to be revised for the May meeting.

Decision: 		The document was noted.

S3-090605	Analysis about eNB Security
					Source: ZTE

Decision: 		The document was noted.

### 6.10	Emergency call

S3-090534	Addition of the NULL algorithm for Integrity Protection to the Clause 5.1.4
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

Decision: 		The document was revised to S3-090582.

S3-090535	Addition of EC Clause
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

Decision: 		The document was revised to S3-090579.

S3-090536	Addition of the Emergency Calling Clause
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

Discussion:

Alcatel-Lucent presented the CR. It was agreed that this CR can be agreed and then could be changed in the May meeting.

Decision: 		The document was agreed.

S3-090582	Addition of the NULL algorithm for Integrity Protection to the Clause 5.1.4
					Source: Alcatel-Lucent, Alcatel Shanghai Bell Co. Ltd., Verizon Wireless, Ericsson

Discussion:

Alcatel-Lucent presented the CR. Some changes are necessary.

Decision: 		The document was revised to S3-090619.

S3-090619	Addition of the NULL algorithm for Integrity Protection to the Clause 5.1.4
					Source: Alcatel-Lucent, Alcatel Shanghai Bell Co. Ltd., Verizon Wireless, Ericsson

(Replaces S3-090582)

Decision: 		The document was agreed.

S3-090579	Addition of EC Clauses to the Rel-9 TS 33.401
					Source: Alcatel-Lucent, Alcatel Shanghai Bell Co. Ltd., Rogers Wireless, Verizon Wireless

Discussion:

Alcatel-Lucent presented the CR.

Decision: 		The document was agreed.

### 6.11	Other areas

S3-090426	33.401 CR: Update of abbreviations list
					Source: Ericsson

Discussion:

Ericsson presented the contribution. 528 does the same and has to be merged. Also, the Huawei contribution on EARFCN has to remove the addition of the abbreviation and put it.

Decision: 		The document was merged in S3-090620.

S3-090528	Addition of missing Abbreviations
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile

Decision: 		The document was merged in S3-090620.

S3-090620	33.401 CR: Update of abbreviations list
					Source: Ericsson

(Replaces S3-090426)

Decision: 		The document was agreed.

S3-090533	Clarifications for Annex A and References
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

Discussion:

Alcatel-Lucent presented the contribuiton.

Decision: 		The document was revised to S3-090621.

S3-090621	Clarifications for Annex A and References
					Source: Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent

(Replaces S3-090533)

Decision: 		The document was agreed.

S3-090553	Changing SGSN to the enhanced MSC server in SRVCC
					Source: Nokia Corporation, Nokia Siemens Networks, China Mobile

Discussion:

Nokia presented the contribution.

Decision: 		The document was agreed.

## 7	Joint meeting with TISPAN WG7

The SA3 Chairman welcomed TISPAN WG7 for the joint session. Item 7 of the agenda in S3-090400 was reviewd.

S3-090411	Reply LS on “Key management for 3GP SRTP recording profile”
					Source: S4-090169

Decision: 		The document was not addressed (out of scope for ad hoc).

S3-090412	[IMS] Correction of wrong message name in annex N (Rel-9)
					Source: Nokia Corporation, Nokia Siemens Networks

Decision: 		The document was postponed.

S3-090429	[IMS] Correction of wrong message name in annex N (Rel-8)
					Source: Nokia Corporation, Nokia Siemens Networks

Decision: 		The document was postponed.

S3-090598	H(e)NB security presentation
					Source: Rapporteur

Discussion:

The Rapporteur presented the contribution.  It was noted that the "Huawei proprietary" on the deck of slides is a typo, as the content is 3GPP content. Hosting Party was clarified and it was mentioned that the term owner is not used as the scenario is not clear anymore; Telecom Italia suggested that the detail of ownership should be clarified.

The Chairman suggested that this is not up to SA3 to decide and SA1 should be consulted via an LS on this.

Decision: 		The document was noted.

### 7.1	Prevention of Unsolicited Communication

S3-090466	3GPP SA3 & TISPAN WG7 JM
					Source: Rapporteur

Discussion:

NEC presented the contribution. It was asked what exactly are the protocols being extended in slide 8; it was clarified that could be protocols other than SIP that might have to be defined. The TISPAN WG7 Chairperson suggested that it would be useful to have a common solution for PUC/I aspects.

Decision: 		The document was noted.

S3-090439	Recommendation ITU-T X.1244, Overall aspects of countering spam in IP-based multimedia applications
					Source: LS033

Discussion:

The SA3 Chairman presented the LS.

Decision: 		The document was noted.

S3-090428	PUCI - Inter-domain specific threats
					Source: Orange

Discussion:

Orange presented the contribution. Ericsson suggested that shall should be replaced by should as this is a TR. A hanging paragraph is present. Nokia Siemens Networks suggested that there might be an overlap between this and other section; this will be addressed by an Editor's Note.

Decision: 		The document was agreed with modifications.

S3-090493	pCR on PUCI TR section 6.2
					Source: InterDigital

Discussion:

InterDigital presented the contribution. It was agreed for this requirement to be converted to a Note. This was agreed. Also the should has to become a may and the 'and', an 'or', as there cannot be requirements in a Note.

Decision: 		The document was agreed with modifications.

S3-090525	Architectural Issues with PUCI
					Source: China Mobile, Ericsson, Nokia Corporation, Nokia Siemens Networks, Rogers Wireless

Discussion:

Nokia Siemens Networks presented the contribution. BT supported the proposal, though the scoring issue could be improved with further contributions in the next meeting.

Decision: 		The document was agreed.

S3-090526	Interdependencies between Technical and Legal Aspects of UC Prevention
					Source: China Mobile, Ericsson, Nokia Corporation , Nokia Siemens Networks, Rogers Wireless

Discussion:

Nokia Siemens Networks presented the contribution. BT suggested that the scoring is done individually by the receiver. There was support to create a pCR on this issue for the next meeting.

Decision: 		The document was noted.

S3-090527	SPIT/UC Protection with Supplementary Services
					Source: China Mobile, Ericsson, Nokia Corporation, Nokia Siemens Networks, Rogers Wireless

Discussion:

Nokia Siemens Networks presented the contribution. BT suggested that the reputation system shoud be avoided as it is difficult to create an effective solution. Qualcomm suggested that this is a TR and this can stay for the time being. Qualcomm asked to remove DTMF; Nokia Siemens Networks suggested that SIP does DTMF emulation; Qualcomm suggested that there are other variants that have different names; it was agreed to change DTMF to something more general (key-press-based signaling).

Decision: 		The document was agreed with modifications.

S3-090465	pCR PUCI IMR Solution
					Source: NEC Corporation

Discussion:

NEC presented the contribution. It was agreed to add an editor's note on the fact that the contents of the table need some rationale. Some further study has to be conducted on whether the text is included.

Decision: 		The document was agreed with modifications.

S3-090454	PUCI pCR TR 33.cde: Criteria for evaluation of Solutions
					Source: InterDigital Communications

Discussion:

InterDigital presented the contribution.

Decision: 		The document was merged with 462 into 611.

S3-090462	pCR PUCI Evaluation Criteria
					Source: NEC Corporation

Discussion:

NEC presented the contribution, discussed in conjunction with 454. Qualcomm suggested that some of the requirements in both contributions are subjective. Orange suggested that the requirements should derive from the threats; NEC suggested that the requirements presented do come from the the threats but not enlisted for the sake of briefness.

It was agreed to combine the two contributions and insert the merger into clause 8 of the PUCI TR (S3-090611).

Decision: 		The document was merged with 454 into 611.

S3-090404	Reply liaison statement on PUC(I) work
					Source: 19tTD283_LS_to_3GPP_SA3_-_PUCI

Discussion:

NEC presented the contribution. The MMS/SMS work is going to be officially stopped; Orange will provide some information next time.

Decision: 		The document was noted.

S3-090408	Response to 3GPP on the PUCI Work Item
					Source: OMA-LS_787-REQ_to_3GPP_Protection_against_Unsolicited_Communication_for_IMS-20090128-A

Discussion:

NEC presented the LS.

Decision: 		The document was replied to.

S3-090431	Draft Reply LS to OMA-LS_787-REQ
					Source: Ericsson

Discussion:

Ericsson presented the draft LS. The first question must be simplified. Also, the LS will be modified as a further answer will not be provided by SA3 after this one.

Decision: 		The document was revised to S3-090612.

S3-090612	Reply to: Response to 3GPP on the PUCI Work Item
					Source: current meeting

Decision: 		The document was agreed.

S3-090467	pCR PUCI Adding of references, definitions and abbreviations
					Source: NEC Corporation

Discussion:

NEC presented the contribution. Reference [3] should be removed. An LS will be sent to SA1 on this.

Decision: 		The document was agreed with modifications.

S3-090433	Integration of S3-090139 and S3-090181 for PUCI Threats Text in TR
					Source: Ericsson, Nokia Corporation, Nokia Siemens Networks

Discussion:

Ericsson presented the pCR. BT pointed out that these are not exclusive approaches. Some reworking of the structure should be done as per numbering and hanging paragraphs.

Decision: 		The document was agreed with modifications.

S3-090611	New version of TR 33.837 on PUCI
					Source: Rapporteur

Decision: 		The document was agreed.

S3-090613	LS on Unsolicited Communication to SA1
					Source: current meeting

Decision: 		The document was agreed.

### 7.2	Media security

S3-090403	TR 33.828 v1.0.0
					Source: MCC

Decision: 		The document was revised to S3-090637.

S3-090597	IMS media security presentation
					Source: Rapporteur

Discussion:

The Rapporteur presented the contribution. It was clarified that IPTV is not explictly addressed in the proposed WID from SA3.

Decision: 		The document was noted.

### 7.3	Customer premises network security [H(e)NB in 3GPP and CNG in TISPAN]

S3-090495	Clarification of UICC requirement for IMS AKA
					Source: Telenor, BT

Decision: 		The document was revised to S3-090610.

S3-090610	Clarification of UICC requirement for IMS AKA
					Source: Telenor, BT

(Replaces S3-090495)

Discussion:

Telenor presented the contribution. It was stated that the IMC credential can be cloned as the credentials are not safely stored as e.g. on the UICC.

Concerning IMS AKA, it was asked if the objective is to have a higher level of security than http digest or NBA then why UICC should not be used. It was pointed out that it is TISPAN discussion to determine whether IMC or UICC is used with the IMS AKA.

Whether a TISPAN CNG can be considered a "non-3GPP terminal" needs to be clarified for the TISPAN specific annex of 33 203 annex L. This needs to be handled during Release 9.

It was suggested that this proposed change could be handled in section 9 of 33.203. The next TISPAN meeting in June should produce some input to be handled in the September Plenary.

ACTION:	Address the concerns/issues raised in SA3-090610 in contributions to the SA3 meeting in May. Then 3GPP SA3 will send an LS to WG7 with the proposed solution.
	(action on: TISPAN WG7)

Decision: 		The document was noted.

S3-090581	Comparing TISPAN CNG and 3GPP H(e)NB
					Source: BT, Telenor

Discussion:

BT presented the contribution.

ACTION:	Provide comments on draft TS on H(e)NB
	(action on: TISPAN WG7 )

Decision: 		The document was noted.

### 7.4	IPTV security issues

No input.

### 7.5	Connection of NGCN to IMS

The TISPAN WG7 and SA3 Chairpersons thanked the Delegates for their useful contributions and work; some good progress was done during the Joint Meeting.

## 8	Technical contributions in other ad hoc work items

S3-090444	LS on security aspects of new work item RTTI support in IMS charging
					Source: S5-091559

Decision: 		The document was postponed.

S3-090455	LS on local breakout and optimal media routing
					Source: S2-091755

Decision: 		The document was postponed.

S3-090484	Draft WID: 128 bit encryption for GSM and GPRS
					Source: Ericsson, Orange, T-Mobile, Telenor, TeliaSonera, Vodafone

Discussion:

Vodafone presented the contribution. Nokia Siemens Networks suggested that if stage 3 groups and GERAN are agreeing to this, it would be OK for SA3. Vodafone pointed out that this has already been discussed in GERAN.

The WID is out of scope for the ad hoc so it has to be resubmitted for SA3#55 for formal agreement.

Decision: 		The document was noted.

### 8.1	Home (e)NB security

Two conference calls will be done on H(e)NB issues.

S3-090406	Reply LS on paging optimisation via allowed CSG list in paging message for LTE and UMTS
					Source: C1-090811

Decision: 		The document was noted.

S3-090482	TR 33.820 on Security of H(e)NB (Relase 8)
					Source: MCC

Decision: 		The document was noted.

S3-090475	Update to H(e)NB system architecture
					Source: Samsung

Discussion:

Samsung presented the CR. Airvana suggested that it is under the competence of RAN3 to NDS/IP issues. Telecom Italia suggested that the notes are now conflicting; it was specified that Home GW is different than HNB GW. The OAM part has to be corrected in the first figure as it is optional.

Decision: 		The document was revised to S3-090622.

S3-090622	Update to H(e)NB system architecture
					Source: Samsung

(Replaces S3-090475)

Decision: 		The document was agreed.

S3-090469	Pseudo-CR on TS 33.xyz: Security Architecture of H(e)NB
					Source: Huawei

Discussion:

Huawei presented the contribution. Qualcomm and Nokia Siemens Networks did not support the addition of 4.2 as during the insertion in the TR there was discussion and this is not fully supported for normative work. The picture should be aligned. The Note was agreed to be removed. 'Proposed' was agreed to be removed.

Decision: 		The document was agreed with modifications.

S3-090504	pCR on text for section 4 (architecture) of TS 33.xyz
					Source: Airvana, Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution. 'by permission of' was agreed to be removed. The 'operator CA' was agreed to be changed to 'a CA trusted by the operator'. The Editor's Note could be removed.

Telecom Italia suggested that the solution-related requirements should be addressed somewhere else in the TS; this will be addressed by an Editor's Note.

Decision: 		The document was agreed with modifications.

S3-090540	Commenting pCR on S3-090504 Security Architecture
					Source: InterDigital

Discussion:

InterDigital presented the contribution. Orange, Nokia Siemens Networks  and Telecom Italia suggested that no discussions on validation have taken place and did not support the contribution.

Decision: 		The document was noted.

S3-090452	H(e)NB TS: TrE functionality
					Source: InterDigital Communications, Infineon

Discussion:

InterDigital presented the contribution. Orange asked all the references to HPM and PVE to be removed. Qualcomm suggested to the secure start up normal boot requirement; also the root of trust requirement was asked to be removed. Also, 5.1.2.2.2 was asked to be removed. Nokia Siemens Networks also made several remarks on the text. Orange suggested that the 'irremovable' is missing.

A revision with all the comments should be submitted for the next meeting to be inserted in the TS.

Decision: 		The document was noted.

S3-090453	H(e)NB TS 6.1 device integrity check
					Source: InterDigital Communications

Decision: 		The document was not presented.

S3-090470	Pseudo-CR on TS 33.xyz on Measures for Clock Protection
					Source: Huawei,ZTE

Discussion:

Huawei presented the pCR.

Decision: 		The document was agreed.

S3-090496	comments on S3-090470
					Source: InterDigital Communications

Discussion:

InterDigital presented the commenting contribution.

Decision: 		The document was noted.

S3-090578	Comment on S3-090470 “Pseudo-CR on TS 33.xyz on Measures for Clock Protection” by Huawei, ZTE
					Source: Airvana, Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the commenting contribution. Qualcomm supported the contirbution. Vodafone suggested that some messages could go out of the IPSec tunnel; Airvana suggested that SA3 should not be deciding these issues. It was agreed to keep the first sentence from 5.3.

Decision: 		The document was noted.

S3-090471	Pseudo-CR on TS 33.xyz: Access Control Mechanisms for H(e)NB
					Source: Huawei,ZTE

Discussion:

Huawei presented the contribution.

Decision: 		The document was noted.

S3-090539	Commenting pCR on S3-090471 on Access Control mechanisms
					Source: InterDigital

Discussion:

InterDigital presented the commenting contribution.

Decision: 		The document was noted.

S3-090576	Comments on S3-090471 “Pseudo-CR on TS 33.xyz: Access Control Mechanisms for H(e)NB” by Huawei, ZTE
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the commenting contribution.

Decision: 		The document was noted.

S3-090489	PCR: Update of Access Control Mechanisms for H(e)NB
					Source: Samsung

Discussion:

Samsung presented the contribution. The titles were revised to CSG and non-CSG methods. The reference issues and all the three documents above could not be agreed so more discussion is necessary until the May meeting.

Decision: 		The document was agreed with modifications.

S3-090477	pCR on rearranging the ToC of TS 33.xyz with respect to management features
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution. Some modifications were agreed online.

Decision: 		The document was agreed with modifications.

S3-090472	Pseudo-CR on TS 33.xyz: add authentication description to Section 5
					Source: Huawei

Discussion:

Huawei presented the contribution.

Decision: 		The document was noted.

S3-090577	Comments on:  Pseudo-CR on TS 33.xyz: add authentication description to Section 5
					Source: Airvana

Discussion:

Airvana presented the commenting contribution. Huawei suggested that some operator input would be useful on this issue. Orange supported the Airvana contribution. Note 3 should be an Editor's Note. Qualcomm made some further editorial comments that have to be applied.

Decision: 		The document was agreed with modifications.

S3-090497	Clarification of Section 7.4 Authentication Method Selection
					Source: Airvana, Huawei, InterDigital, NEC Corporation, T-Mobile

Discussion:

Airvana presented the CR.

Decision: 		The document was agreed.

S3-090568	Recommendation for Hosting Party Authentication
					Source: Gemalto, Orange, TeliaSonera, Telecom Italia, Sagem Orga, Giesecke&Devrient

Discussion:

Gemalto presented the contribution.

Decision: 		The document was noted.

S3-090569	CR to 33.820: Recommendation for Hosting Party authentication
					Source: Gemalto, Orange, TeliaSonera, Telecom Italia, Sagem Orga, Giesecke&Devrient

Discussion:

Gemalto presented the CR. Alcatel-Lucent did not support the contribution; Huawei supported the contirbution. Vodafone suggested that the cost of the upgrade could be high. Some more discussion is needed and the CR will be reconsidered in the next meeting.

Decision: 		The document was noted.

S3-090479	A new security framework for HNB authentication,IPSEC key negotiation and integrity protection
					Source: ZTE Corporation

Discussion:

ZTE presented the contribution.

Decision: 		The document was noted.

S3-090478	A method to protect hardware integrity
					Source: ZTE Corporation

Discussion:

ZTE presented the contribution.

Decision: 		The document was noted.

S3-090480	About authentication identity of HNB
					Source: ZTE Corporation

Discussion:

ZTE presented the contribution. Not enough support.

Decision: 		The document was noted.

S3-090485	33.820 CR 7.2.2.3 H(e)NB Authentication
					Source: Huawei

Discussion:

Huawei presented the contribution. Some removals were agreed. The only thing agreed is the changes to a and d. Some further editorials are necessary

Decision: 		The document was revised to S3-090626.

S3-090626	33.820 CR 7.2.2.3 H(e)NB Authentication
					Source: Huawei

(Replaces S3-090485)

Decision: 		The document was agreed.

S3-090541	Comments on S3-090485 from Huawei
					Source: InterDigital

Decision: 		The document was noted.

S3-090457	Clarification of Certificate Profile
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the CR. Category should be F.

Decision: 		The document was revised to S3-090627.

S3-090627	Clarification of Certificate Profile
					Source: Qualcomm Europe

(Replaces S3-090457)

Decision: 		The document was agreed.

S3-090445	33.820CR: Clarification of Access Control Mechanisms
					Source: Qualcomm Europe

Decision: 		The document was revised to S3-090625.

S3-090476	CR to 33.820 Update of Access Control Mechanisms for H(e)NB
					Source: Samsung

Decision: 		The document was merged in S3-090625.

S3-090625	CR to 33.820 Update of Access Control Mechanisms for H(e)NB
					Source: Qualcomm Europe, Samsung

(Replaces S3-090445)

Discussion:

Qualcomm presented the CR. The Editor's Note must be improved.

Decision: 		The document was agreed.

S3-090446	CR33.820: Conclusions on Location Security
					Source: Qualcomm Europe

Discussion:

Qualcomm presented the CR.

Decision: 		The document was revised to S3-090628.

S3-090567	Comments on S3-090446_CR_LocationSecurityConclusions
					Source: Airvana

Discussion:

Airvana presented the commenting contribution.

Decision: 		The document was noted.

S3-090628	CR33.820: Conclusions on Location Security
					Source: Qualcomm Europe

(Replaces S3-090446)

Decision: 		The document was agreed.

S3-090447	CR TR33.820 7.5.2.1 introduction to validation
					Source: InterDigital Communications

Discussion:

InterDigital presented the CR. The deleted in the end should be restored.

Decision: 		The document was revised to S3-090632.

S3-090632	CR TR33.820 7.5.2.1 introduction to validation
					Source: InterDigital Communications

(Replaces S3-090447)

Decision: 		The document was agreed.

S3-090448	CR TR33.820 7.5.2.4 semi-autonomous validation
					Source: InterDigital Communications

Discussion:

InterDigital presented the CR. Nokia Siemens Networks made some remarks that were taken into account, on step 3 and 4.d; also the last sentence of the first paragraph was removed. Airvana suggested changing the TrE ID to HNB ID in step 3; this was agreed. Orange asked not to remove the Editor's Note.

Decision: 		The document was revised to S3-090633.

S3-090633	CR TR33.820 7.5.2.4 semi-autonomous validation
					Source: InterDigital Communications

(Replaces S3-090448)

Decision: 		The document was agreed.

S3-090506	corrected version of S3-090449
					Source: InterDigital Communications

Discussion:

Postponed for SA3#55.

Decision: 		The document was postponed.

S3-090451	CR TR33.820 8.2 conclusions re validation
					Source: InterDigital Communications

Discussion:

Postponed for SA3#55.

Decision: 		The document was postponed.

S3-090450	CR TR33.820 75., 7.6 binding of authentication & validation
					Source: InterDigital Communications

Discussion:

InterDigital presented the CR. Telecom Italia, Gemalto and Airvana suggested that introducing proposals that have not the full consensus in the TR is not useful. This was agreed and the objective of the further work on the TR will be to remove Editor's Notes and fill in or remove empty clauses.

7.6.1.3.4 and 7.6.3.2.2 were agreed to be added.

Decision: 		The document was revised to S3-090634.

S3-090634	CR TR33.820 75., 7.6 binding of authentication & validation
					Source: InterDigital Communications

(Replaces S3-090450)

Decision: 		The document was revised to S3-090641.

S3-090641	CR TR33.820 75., 7.6 binding of authentication & validation
					Source: InterDigital Communications

(Replaces S3-090634)

Decision: 		The document was [not addressed].

S3-090474	33.820: Correction of text on autonomous validation
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the CR.

Decision: 		The document was revised to S3-090635.

S3-090635	33.820: Correction of text on autonomous validation
					Source: Nokia Corporation, Nokia Siemens Networks

(Replaces S3-090474)

Decision: 		The document was agreed.

S3-090542	Comments on S3-090474 on Analysis of Autonomous Validation
					Source: InterDigital

Discussion:

InterDigital presented the commenting contribution. As the contribution adds numerous Editor's Notes it was decided to keep the Editor's Note being removed in 474. It was agreed to insert the Editor's Note in 7.5.2.2 as Note. InterDigital suggested to convert the Editor's Notes in 7.5.3 to text.

Decision: 		The document was noted.

S3-090481	Some comments about software integrity verify
					Source: ZTE Corporation

Discussion:

ZTE presented the contribution. Some offline discussion must take place and a CR must be drafted on this.

Decision: 		The document was revised to S3-090629.

S3-090629	Some comments about software integrity verify
					Source: ZTE Corporation

(Replaces S3-090481)

Decision: 		The document was withdrawn.

S3-090486	33.820 CR on H(e)NB Validation
					Source: Huawei

Discussion:

Nokia Siemens Networks presented the CR.

Decision: 		The document was revised to S3-090636.

S3-090636	33.820 CR on H(e)NB Validation
					Source: Huawei

(Replaces S3-090486)

Decision: 		The document was agreed.

S3-090543	Comments on S3-090486 from Huawei on Validation
					Source: InterDigital

Discussion:

InterDigital presented the commenting contribution. Qualcomm suggested that trusted and secure boot should be explained more thoroughly; this will be handled by an Editor's Note. The stage 3 changes were not accepted.

Decision: 		The document was noted.

S3-090623	New version of TS.xyz on HeNB security
					Source: Rapporteur

Decision: 		The document was agreed.

S3-090624	LS to SA1 on HeNB
					Source: current meeting

Discussion:

Timeline:

- comments by: April 3;

- new version by: April 6;

- final remarks by: April 8;

- final version by: April 9.

Decision: 		The document was sent for email approval.

### 8.2	IMS media plane security

S3-090637	TR 33.828 v1.1.0
					Source: Rapporteur

Discussion:

Agreed as the new baseline.

Decision: 		The document was agreed.

S3-090638	TR 33.828 v1.2.0
					Source: Rapporteur

Discussion:

Timeline:

- Rapporteur version: April 3

- Comments by: April 17;

Decision: 		The document was sent for email approval.

S3-090498	Clarification of Definitions
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution.

Decision: 		The document was agreed.

S3-090460	pseudo-CR to 33.828: Replace the term
					Source: Gemalto

Discussion:

Gemalto presented the contribution. Ericsson asked where the conclusion that the UICC must be there was taken from. Gemalto suggested to agree two possibilities (present or not present). It was agreed that the term UE is too restrictive. Some offline re-working is needed.

Decision: 		The document was noted.

S3-090499	Clarification of Use Cases
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution. Some modifications agreed.

Decision: 		The document was agreed with modifications.

S3-090500	Correction of Requirements
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution. Ericsson asked to add another reference in the last change (6.1.4.4.5); this was agreed.

Decision: 		The document was agreed with modifications.

S3-090494	TBS: Assurance of terminating side identity
					Source: Ericsson

Discussion:

Ericsson presented the contribution.

Decision: 		The document was agreed.

S3-090490	IMS e2m media plane security: endpoints and coexistence
					Source: Ericsson

Discussion:

Ericsson presented the contribution. It was decided that the section where to place this clause should be defined. Some comments from Nokia Siemens Networks were accepted.

Decision: 		The document was agreed with modifications.

S3-090491	IMS e2m media plane security: control interface
					Source: Ericsson

Discussion:

Ericsson presented the contribution.

Decision: 		The document was noted.

S3-090492	IMS e2m media plane security: key mixing
					Source: Ericsson

Discussion:

Ericsson presented the contribution.

Decision: 		The document was agreed with modifications.

S3-090501	Clarifications on SDES solution
					Source: Nokia Corporation, Nokia Siemens Networks

Discussion:

Nokia Siemens Networks presented the contribution. Some rewording was applied to improve readability.

Decision: 		The document was agreed with modifications.

### 8.3	Protection against Unsolicited Communication for IMS

## 9	Close

Any other business:

China Mobile specified that the July meeting would be difficult to be attended by Chinese delegates. NAF have already made contractual commitments with the facilities. It was decided that as the invitiation is already out then it is difficult to change the venue. Huawei suggested that even 18 months would be difficult and so 26 weeks should be provided before a meeting in the USA.

An attempt will be made to change the location to a nearby Canadian location within the next 2 weeks.

The Chairman thanked the Delegates for their hard work.

The meeting was closed.

## Annex A: List of contribution documents

| Document | Title | Source | Decision | Replaces | Replaced by |
| --- | --- | --- | --- | --- | --- |
| S3-090400 | Agenda for SA WG3 ad hoc meeting | SA WG3 Chairman | agreed | - | - |
| S3-090401 | Report from SA3#54 | SA WG3 Secretary | noted | - | - |
| S3-090402 | Report from SA#43 Plenary | SA WG3 Chairman | noted | - | - |
| S3-090403 | TR 33.828 v1.0.0 | MCC | revised | - | S3-090637 |
| S3-090404 | Reply liaison statement on PUC(I) work | 19tTD283_LS_to_3GPP_SA3_-_PUCI | noted | - | - |
| S3-090405 | LS on Security parameter handling | C1-090756 | noted | - | - |
| S3-090406 | Reply LS on paging optimisation via allowed CSG list in paging message for LTE and UMTS | C1-090811 | noted | - | - |
| S3-090407 | New Q.16/13 study item on Mobility Security. Response to the 3GPP liaison statement S3-081567 | COM13-LS032 | noted | - | - |
| S3-090408 | Response to 3GPP on the PUCI Work Item | OMA-LS_787-REQ_to_3GPP_Protection_against_Unsolicited_Communication_for_IMS-20090128-A | replied to | - | - |
| S3-090409 | LS on handling of dynamic UE UTRAN capability during Handover | R2-091922 | noted | - | - |
| S3-090410 | Reply LS on Receive of ETWS outside home-PLMN | S1-090199 | not addressed | - | - |
| S3-090411 | Reply LS on “Key management for 3GP SRTP recording profile” | S4-090169 | not addressed (out of scope for ad hoc) | - | - |
| S3-090412 | [IMS] Correction of wrong message name in annex N (Rel-9) | Nokia Corporation, Nokia Siemens Networks | postponed | - | - |
| S3-090414 | 33.401 CR: Removal of KSI_ASME from TAU Accept | Ericsson, NEC Corporation | merged in S3-090606 | - | - |
| S3-090415 | 33.401 CR: Correction of UE security capability handling in the TAU procedure | Ericsson, NEC Corporation | merged in S3-090606 | - | - |
| S3-090416 | 33.401 CR: Activation of native EPS NAS security context after IRAT HO | Ericsson, NEC Corporation | revised | - | S3-090606 |
| S3-090417 | 33.401 CR: Correction of UE EPS security capability default set | Ericsson | agreed | - | - |
| S3-090418 | 33.401 CR: Resolving ed note on PLMN ID encoding | Ericsson | agreed | - | - |
| S3-090419 | 33.401 CR: Correction of MM context transfer | Ericsson | merged in S3-090606 | - | - |
| S3-090420 | 33.401 CR: Storage of EPS NAS security context | Ericsson, Gemalto | revised | - | S3-090640 |
| S3-090421 | 33.401 CR: UE security capability handling at S1 HO | Ericsson | merged in S3-090601 | - | - |
| S3-090422 | 33.401 CR: Correction of eKSI usage in AS | Ericsson, Nokia Siemens Networks, NEC Corporation | merged in S3-090583 | - | - |
| S3-090423 | Editorial corrections to security context establishment clause | Ericsson | agreed | - | - |
| S3-090424 | 33.402 CR: Clarification on use of USIM/UICC in non-3GPP accesses | Ericsson | agreed | - | - |
| S3-090425 | 33.402 CR: Clarification of order for identity request and AVs fetching | Ericsson | revised | - | S3-090616 |
| S3-090426 | 33.401 CR: Update of abbreviations list | Ericsson | merged in S3-090620 | - | S3-090620 |
| S3-090427 | 33.401 CR: Introduction to forward security | Ericsson | revised | - | S3-090587 |
| S3-090428 | PUCI - Inter-domain specific threats | Orange | agreed with modifications | - | - |
| S3-090429 | [IMS] Correction of wrong message name in annex N (Rel-8) | Nokia Corporation, Nokia Siemens Networks | postponed | - | - |
| S3-090431 | Draft Reply LS to OMA-LS_787-REQ | Ericsson | revised | - | S3-090612 |
| S3-090433 | Integration of S3-090139 and S3-090181 for PUCI Threats Text in TR | Ericsson, Nokia Corporation, Nokia Siemens Networks | agreed with modifications | - | - |
| S3-090434 | LS on exception lists for integrity protection of NAS messages | C1-091369 | noted | - | - |
| S3-090435 | Reply LS on preventing inter-RAT HO for UE with SIM access | C4-090512 | noted | - | - |
| S3-090436 | LS on Prefix for EAP-AKA' | C4-090799 | replied to | - | - |
| S3-090437 | LS on the removal of KNASint and KNASenc from EFEPSNSC | C6-090055 | replied to | - | - |
| S3-090438 | LS on preventing inter-RAT HO for UE with SIM access | GP-090351 | noted | - | - |
| S3-090439 | Recommendation ITU-T X.1244, Overall aspects of countering spam in IP-based multimedia applications | LS033 | noted | - | - |
| S3-090440 | LS response to R2-087408 (Reply LS on PCI Clarification) | R3-090544 | noted | - | - |
| S3-090441 | LS on transfer of UE Security Capabilities to target eNBs | R3-090664 | replied to | - | - |
| S3-090442 | LS on Security for TAU Request | S2-091788 | replied to | - | - |
| S3-090443 | LS on Enhanced Security for S2c | S2-091795 | replied to | - | - |
| S3-090444 | LS on security aspects of new work item RTTI support in IMS charging | S5-091559 | postponed | - | - |
| S3-090445 | 33.820CR: Clarification of Access Control Mechanisms | Qualcomm Europe | revised | - | S3-090625 |
| S3-090446 | CR33.820: Conclusions on Location Security | Qualcomm Europe | revised | - | S3-090628 |
| S3-090447 | CR TR33.820 7.5.2.1 introduction to validation | InterDigital Communications | revised | - | S3-090632 |
| S3-090448 | CR TR33.820 7.5.2.4 semi-autonomous validation | InterDigital Communications | revised | - | S3-090633 |
| S3-090450 | CR TR33.820 75., 7.6 binding of authentication & validation | InterDigital Communications | revised | - | S3-090634 |
| S3-090451 | CR TR33.820 8.2 conclusions re validation | InterDigital Communications | postponed | - | - |
| S3-090452 | H(e)NB TS: TrE functionality | InterDigital Communications, Infineon | noted | - | - |
| S3-090453 | H(e)NB TS 6.1 device integrity check | InterDigital Communications | not presented | - | - |
| S3-090454 | PUCI pCR TR 33.cde: Criteria for evaluation of Solutions | InterDigital Communications | merged with 462 into 611 | - | - |
| S3-090455 | LS on local breakout and optimal media routing | S2-091755 | postponed | - | - |
| S3-090456 | Update of referenced RFCs and hash algorithm | Qualcomm Europe | revised | - | S3-090609 |
| S3-090457 | Clarification of Certificate Profile | Qualcomm Europe | revised | - | S3-090627 |
| S3-090460 | pseudo-CR to 33.828: Replace the term | Gemalto | noted | - | - |
| S3-090462 | pCR PUCI Evaluation Criteria | NEC Corporation | merged with 454 into 611 | - | - |
| S3-090465 | pCR PUCI IMR Solution | NEC Corporation | agreed with modifications | - | - |
| S3-090466 | 3GPP SA3 & TISPAN WG7 JM | Rapporteur | noted | - | - |
| S3-090467 | pCR PUCI Adding of references, definitions and abbreviations | NEC Corporation | agreed with modifications | - | - |
| S3-090469 | Pseudo-CR on TS 33.xyz: Security Architecture of H(e)NB | Huawei | agreed with modifications | - | - |
| S3-090470 | Pseudo-CR on TS 33.xyz on Measures for Clock Protection | Huawei,ZTE | agreed | - | - |
| S3-090471 | Pseudo-CR on TS 33.xyz: Access Control Mechanisms for H(e)NB | Huawei,ZTE | noted | - | - |
| S3-090472 | Pseudo-CR on TS 33.xyz: add authentication description to Section 5 | Huawei | noted | - | - |
| S3-090473 | Corrections for TS 33.310 | Huawei | conditionally agreed | - | - |
| S3-090474 | 33.820: Correction of text on autonomous validation | Nokia Corporation, Nokia Siemens Networks | revised | - | S3-090635 |
| S3-090475 | Update to H(e)NB system architecture | Samsung | revised | - | S3-090622 |
| S3-090476 | CR to 33.820 Update of Access Control Mechanisms for H(e)NB | Samsung | merged in S3-090625 | - | - |
| S3-090477 | pCR on rearranging the ToC of TS 33.xyz with respect to management features | Nokia Corporation, Nokia Siemens Networks | agreed with modifications | - | - |
| S3-090478 | A method to protect hardware integrity | ZTE Corporation | noted | - | - |
| S3-090479 | A new security framework for HNB authentication,IPSEC key negotiation and integrity protection | ZTE Corporation | noted | - | - |
| S3-090480 | About authentication identity of HNB | ZTE Corporation | noted | - | - |
| S3-090481 | Some comments about software integrity verify | ZTE Corporation | revised | - | S3-090629 |
| S3-090482 | TR 33.820 on Security of H(e)NB (Relase 8) | MCC | noted | - | - |
| S3-090483 | Draft WID: NDS enhancements to support backhaul security | Nokia Siemens Networks, T-Mobile, TeliaSonera, Vodafone | conditionally agreed | - | - |
| S3-090484 | Draft WID: 128 bit encryption for GSM and GPRS | Ericsson, Orange, T-Mobile, Telenor, TeliaSonera, Vodafone | noted | - | - |
| S3-090485 | 33.820 CR 7.2.2.3 H(e)NB Authentication | Huawei | revised | - | S3-090626 |
| S3-090486 | 33.820 CR on H(e)NB Validation | Huawei | revised | - | S3-090636 |
| S3-090487 | CR Remove Duplicate Section Number in 7.6.1.3.4 | Huawei | revised | - | S3-090608 |
| S3-090488 | Authorization for ANDSF | Nokia Corporation, Nokia Siemens Networks | revised | - | S3-090618 |
| S3-090489 | PCR: Update of Access Control Mechanisms for H(e)NB | Samsung | agreed with modifications | - | - |
| S3-090490 | IMS e2m media plane security: endpoints and coexistence | Ericsson | agreed with modifications | - | - |
| S3-090491 | IMS e2m media plane security: control interface | Ericsson | noted | - | - |
| S3-090492 | IMS e2m media plane security: key mixing | Ericsson | agreed with modifications | - | - |
| S3-090493 | pCR on PUCI TR section 6.2 | InterDigital | agreed with modifications | - | - |
| S3-090494 | TBS: Assurance of terminating side identity | Ericsson | agreed | - | - |
| S3-090495 | Clarification of UICC requirement for IMS AKA | Telenor, BT | revised | - | S3-090610 |
| S3-090496 | comments on S3-090470 | InterDigital Communications | noted | - | - |
| S3-090497 | Clarification of Section 7.4 Authentication Method Selection | Airvana, Huawei, InterDigital, NEC Corporation, T-Mobile | agreed | - | - |
| S3-090498 | Clarification of Definitions | Nokia Corporation, Nokia Siemens Networks | agreed | - | - |
| S3-090499 | Clarification of Use Cases | Nokia Corporation, Nokia Siemens Networks | agreed with modifications | - | - |
| S3-090500 | Correction of Requirements | Nokia Corporation, Nokia Siemens Networks | agreed with modifications | - | - |
| S3-090501 | Clarifications on SDES solution | Nokia Corporation, Nokia Siemens Networks | agreed with modifications | - | - |
| S3-090504 | pCR on text for section 4 (architecture) of TS 33.xyz | Airvana, Nokia Corporation, Nokia Siemens Networks | agreed with modifications | - | - |
| S3-090506 | corrected version of S3-090449 | InterDigital Communications | postponed | - | - |
| S3-090507 | Clarification on Multiple KeNB*s Preparation in Section 7.4.3 | Huawei | revised | - | S3-090588 |
| S3-090508 | START/NAS COUNT relay on Inter-RAT mobility | Huawei | noted | - | - |
| S3-090510 | Add the frequency EARFCN-DL | Huawei,ZTE | merged in S3-090588 | - | - |
| S3-090511 | The correction on input key of Null ciphering algorithm | Huawei,ZTE | agreed | - | - |
| S3-090512 | Clarification of NAS algorithm selection during S1 HO | Huawei,ZTE | merged in S3-090601 | - | - |
| S3-090513 | Corrections of 33.401 | Huawei,ZTE | merged in S3-090583 | - | S3-090583 |
| S3-090515 | idle mode procedure in EUTRAN | Huawei | postponed | - | - |
| S3-090516 | corrections for Attach procedure | Huawei | revised | - | S3-090585 |
| S3-090517 | clarification for EAP-AKA' | Huawei | postponed | - | - |
| S3-090518 | Corrections for the EPS security context fetching between MMEs | Huawei | agreed | - | - |
| S3-090519 | correctinos for idle mode procedure in EUTRAN | Huawei | revised | - | S3-090607 |
| S3-090521 | Addition of security requirements on eNB | China Mobile, Alcatel-lucent, Vodafone, ZTE | revised | - | S3-090554 |
| S3-090522 | Correction of KeNB derivations | China Mobile,ZTE | revised | - | S3-090555 |
| S3-090523 | Correction of EPS AS Security Mode Command Procedure | China Mobile | revised | - | S3-090556 |
| S3-090524 | Correction of EPS AS/NAS Security Context definition | China Mobile,ZTE | revised | - | S3-090557 |
| S3-090525 | Architectural Issues with PUCI | China Mobile, Ericsson, Nokia Corporation, Nokia Siemens Networks, Rogers Wireless | agreed | - | - |
| S3-090526 | Interdependencies between Technical and Legal Aspects of UC Prevention | China Mobile, Ericsson, Nokia Corporation , Nokia Siemens Networks, Rogers Wireless | noted | - | - |
| S3-090527 | SPIT/UC Protection with Supplementary Services | China Mobile, Ericsson, Nokia Corporation, Nokia Siemens Networks, Rogers Wireless | agreed with modifications | - | - |
| S3-090528 | Addition of missing Abbreviations | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | merged in S3-090620 | - | - |
| S3-090529 | The definition of eKSI format | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | revised | - | S3-090590 |
| S3-090530 | Additional condition of KeNB refresh | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | withdrawn | - | - |
| S3-090531 | Removal of the paragraph mentioning IMSI from the Annex A2 | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | withdrawn | - | - |
| S3-090532 | Change in the Clause 6.2. Removal of explicit CK’/IK’ function | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | S3-090630 |
| S3-090533 | Clarifications for Annex A and References | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | S3-090621 |
| S3-090534 | Addition of the NULL algorithm for Integrity Protection to the Clause 5.1.4 | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | S3-090582 |
| S3-090535 | Addition of EC Clause | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | S3-090579 |
| S3-090536 | Addition of the Emergency Calling Clause | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | agreed | - | - |
| S3-090539 | Commenting pCR on S3-090471 on Access Control mechanisms | InterDigital | noted | - | - |
| S3-090540 | Commenting pCR on S3-090504 Security Architecture | InterDigital | noted | - | - |
| S3-090541 | Comments on S3-090485 from Huawei | InterDigital | noted | - | - |
| S3-090542 | Comments on S3-090474 on Analysis of Autonomous Validation | InterDigital | noted | - | - |
| S3-090543 | Comments on S3-090486 from Huawei on Validation | InterDigital | noted | - | - |
| S3-090544 | Hint digits in EAP-AKA’ | Ericsson, Nokia Siemens Networks, Nokia Corporation | revised | - | S3-090615 |
| S3-090545 | Use of NAI prefix for EAP-AKA’ | Ericsson, Nokia Siemens Networks, Nokia Corporation | postponed | - | - |
| S3-090546 | CR to 33.401 Removal of NAS keys storage | NEC Corporation, Nokia Corporation, Nokia Siemens Networks, NTT DOCOMO | conditionally agreed | - | - |
| S3-090547 | AKA procedure in case of NAS security actived | ZTE Corporation, HUAWEI | noted | - | - |
| S3-090548 | Key-Change-On the Fly Clarification | ZTE Corporation | noted | - | - |
| S3-090549 | Clarification for Forward Security | ZTE Corporation | revised | - | S3-090592 |
| S3-090550 | Clarification for DSMIPv6 Bootstrap | ZTE Corporation | postponed | - | - |
| S3-090551 | Update UE-ANDSF Communication Security Solution | ZTE Corporation | noted | - | - |
| S3-090552 | Mobility Security Framework in NGN in ITU-T | ZTE Corporation | noted | - | - |
| S3-090553 | Changing SGSN to the enhanced MSC server in SRVCC | Nokia Corporation, Nokia Siemens Networks, China Mobile | agreed | - | - |
| S3-090554 | Addition of security requirements on eNB | China Mobile, Alcatel-lucent, Vodafone, ZTE | noted | S3-090521 | - |
| S3-090555 | Correction of KeNB derivations | China Mobile,ZTE,Nokia Corporation, Nokia Siemens Networks | revised | S3-090522 | S3-090593 |
| S3-090556 | Correction of EPS AS Security Mode Command Procedure | China Mobile,Nokia Corporation, Nokia Siemens Networks | revised | S3-090523 | S3-090602 |
| S3-090557 | Correction of EPS AS/NAS Security Context definition | China Mobile,Nokia Corporation, Nokia Siemens Networks | revised | - | S3-090586 |
| S3-090558 | Keys to be used in HO from E-UTRAN to UTRAN and GERAN | Nokia Corporation, Nokia Siemens Networks | agreed | - | - |
| S3-090559 | Correction on Transfer of Capabilities in S1-handover | Nokia Corporation, Nokia Siemens Networks | merged in S3-090601 | - | - |
| S3-090560 | Discussion on potential problems with concurrent key handling procedures | Nokia Corporation, Nokia Siemens Networks | noted | - | - |
| S3-090561 | Correction on KeNB refresh | Nokia Corporation, Nokia Siemens Networks | revised | - | S3-090591 |
| S3-090562 | Correction on Key Identification | Nokia Corporation, Nokia Siemens Networks | revised | - | S3-090594 |
| S3-090563 | Keys to be used in HO from UTRAN and GERAN to E-UTRAN | Nokia Corporation, Nokia Siemens Networks | agreed | - | - |
| S3-090564 | NH derivation rules for re-keying | Nokia Corporation, Nokia Siemens Networks | revised | - | S3-090595 |
| S3-090565 | RRC Connection Re-establishment – security corrections | Nokia Corporation, Nokia Siemens Networks | revised | - | S3-090603 |
| S3-090566 | Clarification of LTE USIM requirement | NTT DOCOMO | [not addressed] | - | - |
| S3-090567 | Comments on S3-090446_CR_LocationSecurityConclusions | Airvana | noted | - | - |
| S3-090568 | Recommendation for Hosting Party Authentication | Gemalto, Orange, TeliaSonera, Telecom Italia, Sagem Orga, Giesecke&Devrient | noted | - | - |
| S3-090569 | CR to 33.820: Recommendation for Hosting Party authentication | Gemalto, Orange, TeliaSonera, Telecom Italia, Sagem Orga, Giesecke&Devrient | noted | - | - |
| S3-090570 | Clarifications to calculating the initial K_eNB and K_eNB after key change on the fly | Qualcomm Europe | sent for email approval | - | - |
| S3-090571 | Correcting the handling of EPS security context | Qualcomm Europe | revised | - | S3-090639 |
| S3-090572 | Correcting MME behaviour at S1-handover | Qualcomm Europe | conditionally agreed | - | - |
| S3-090573 | Proposed response to S3-090442 (=S2-091788) | Qualcomm Europe | noted | - | - |
| S3-090574 | Completing the handling of security contexts in TS 33.401 | Qualcomm Europe | noted | - | - |
| S3-090575 | Proposed response to LS on Enhanced Security for S2c | Qualcomm Europe | revised | - | S3-090617 |
| S3-090576 | Comments on S3-090471 “Pseudo-CR on TS 33.xyz: Access Control Mechanisms for H(e)NB” by Huawei, ZTE | Nokia Corporation, Nokia Siemens Networks | noted | - | - |
| S3-090577 | Comments on: Pseudo-CR on TS 33.xyz: add authentication description to Section 5 | Airvana | agreed with modifications | - | - |
| S3-090578 | Comment on S3-090470 “Pseudo-CR on TS 33.xyz on Measures for Clock Protection” by Huawei, ZTE | Airvana, Nokia Corporation, Nokia Siemens Networks | noted | - | - |
| S3-090579 | Addition of EC Clauses to the Rel-9 TS 33.401 | Alcatel-Lucent, Alcatel Shanghai Bell Co. Ltd., Rogers Wireless, Verizon Wireless | agreed | - | - |
| S3-090580 | comments to S3-090544(Hint digits in EAP-AKA’) | Huawei | noted | - | - |
| S3-090581 | Comparing TISPAN CNG and 3GPP H(e)NB | BT, Telenor | noted | - | - |
| S3-090582 | Addition of the NULL algorithm for Integrity Protection to the Clause 5.1.4 | Alcatel-Lucent, Alcatel Shanghai Bell Co. Ltd., Verizon Wireless, Ericsson | revised | - | S3-090619 |
| S3-090583 | Corrections of eKSI and AS in 33.401 | Huawei,ZTE, Ericsson, | agreed | S3-090513 | - |
| S3-090584 | Reply to: LS on the removal of KNASint and KNASenc from EFEPSNSC | current meeting | agreed | - | - |
| S3-090585 | corrections for Attach procedure | Huawei | agreed | S3-090516 | - |
| S3-090586 | Correction of EPS AS/NAS Security Context definition | China Mobile,Nokia Corporation, Nokia Siemens Networks | agreed | S3-090557 | - |
| S3-090587 | 33.401 CR: Introduction to forward security | Ericsson | agreed | S3-090427 | - |
| S3-090588 | Clarification on Multiple KeNB*s Preparation in Section 7.4.3 | Huawei | agreed | S3-090507 | - |
| S3-090589 | Add the frequency EARFCN-DL | Huawei,ZTE | withdrawn | S3-090510 | - |
| S3-090590 | The definition of eKSI format | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | agreed | S3-090529 | - |
| S3-090591 | Correction on KeNB refresh | Nokia Corporation, Nokia Siemens Networks | agreed | S3-090561 | - |
| S3-090592 | Key-Change-On the Fly Clarification | ZTE Corporation | agreed | S3-090549 | - |
| S3-090593 | Correction of KeNB derivations | China Mobile,ZTE,Nokia Corporation, Nokia Siemens Networks | agreed | S3-090555 | - |
| S3-090594 | Correction on Key Identification | Nokia Corporation, Nokia Siemens Networks | agreed | S3-090562 | - |
| S3-090595 | NH derivation rules for re-keying | Nokia Corporation, Nokia Siemens Networks | agreed | S3-090564 | - |
| S3-090596 | LS on concurrent running of security procedures | current meeting | agreed | - | - |
| S3-090597 | IMS media security presentation | Rapporteur | noted | - | - |
| S3-090598 | H(e)NB security presentation | Rapporteur | noted | - | - |
| S3-090599 | Reply to: LS on Security for TAU Request | current meeting | agreed | - | - |
| S3-090600 | Reply to: LS on transfer of UE Security Capabilities to target eNBs | current meeting | agreed | - | - |
| S3-090601 | 33.401 CR: UE security capability handling at S1 HO | Ericsson | agreed | S3-090421 | - |
| S3-090602 | Correction of EPS AS Security Mode Command Procedure | China Mobile,Nokia Corporation, Nokia Siemens Networks | agreed | S3-090556 | - |
| S3-090603 | RRC Connection Re-establishment – security corrections | Nokia Corporation, Nokia Siemens Networks | agreed | S3-090565 | - |
| S3-090604 | LS to RAN2 and RAN3 on Correcting MME behaviour at S1-handover | current meeting | agreed | - | - |
| S3-090605 | Analysis about eNB Security | ZTE | noted | - | - |
| S3-090606 | 33.401 CR: Activation of native EPS NAS security context after IRAT HO | Ericsson, NEC Corporation | agreed | S3-090416 | - |
| S3-090607 | correctinos for idle mode procedure in EUTRAN | Huawei | agreed | S3-090519 | - |
| S3-090608 | CR Remove Duplicate Section Number in 7.6.1.3.4 | Huawei | agreed | S3-090487 | - |
| S3-090609 | Update of referenced RFCs and hash algorithm | Qualcomm Europe | conditionally agreed | S3-090456 | - |
| S3-090610 | Clarification of UICC requirement for IMS AKA | Telenor, BT | noted | S3-090495 | - |
| S3-090611 | New version of TR 33.837 on PUCI | Rapporteur | agreed | - | - |
| S3-090612 | Reply to: Response to 3GPP on the PUCI Work Item | current meeting | agreed | - | - |
| S3-090613 | LS on Unsolicited Communication to SA1 | current meeting | agreed | - | - |
| S3-090614 | Reply to: LS on Prefix for EAP-AKA' | current meeting | agreed | - | - |
| S3-090615 | Hint digits in EAP-AKA’ | Ericsson, Nokia Siemens Networks, Nokia Corporation | noted | S3-090544 | - |
| S3-090616 | 33.402 CR: Clarification of order for identity request and AVs fetching | Ericsson | agreed | S3-090425 | - |
| S3-090617 | Reply to: LS on Enhanced Security for S2c | current meeting | agreed | S3-090575 | - |
| S3-090618 | Authorization for ANDSF | Nokia Corporation, Nokia Siemens Networks | agreed | S3-090488 | - |
| S3-090619 | Addition of the NULL algorithm for Integrity Protection to the Clause 5.1.4 | Alcatel-Lucent, Alcatel Shanghai Bell Co. Ltd., Verizon Wireless, Ericsson | agreed | S3-090582 | - |
| S3-090620 | 33.401 CR: Update of abbreviations list | Ericsson | agreed | S3-090426 | - |
| S3-090621 | Clarifications for Annex A and References | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | agreed | S3-090533 | - |
| S3-090622 | Update to H(e)NB system architecture | Samsung | agreed | S3-090475 | - |
| S3-090623 | New version of TS.xyz on HeNB security | Rapporteur | agreed | - | - |
| S3-090624 | LS to SA1 on HeNB | current meeting | sent for email approval | - | - |
| S3-090625 | CR to 33.820 Update of Access Control Mechanisms for H(e)NB | Qualcomm Europe, Samsung | agreed | S3-090445 | - |
| S3-090626 | 33.820 CR 7.2.2.3 H(e)NB Authentication | Huawei | agreed | S3-090485 | - |
| S3-090627 | Clarification of Certificate Profile | Qualcomm Europe | agreed | S3-090457 | - |
| S3-090628 | CR33.820: Conclusions on Location Security | Qualcomm Europe | agreed | S3-090446 | - |
| S3-090629 | Some comments about software integrity verify | ZTE Corporation | withdrawn | S3-090481 | - |
| S3-090630 | Change in the Clause 6.2. Removal of explicit CK’/IK’ function | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | agreed | S3-090532 | - |
| S3-090631 | Reply LS to S3-090596 = R2-092666 on Concurrent Running of Security Procedures | R2-092676 | noted | - | - |
| S3-090632 | CR TR33.820 7.5.2.1 introduction to validation | InterDigital Communications | agreed | S3-090447 | - |
| S3-090633 | CR TR33.820 7.5.2.4 semi-autonomous validation | InterDigital Communications | agreed | S3-090448 | - |
| S3-090634 | CR TR33.820 75., 7.6 binding of authentication & validation | InterDigital Communications | revised | S3-090450 | S3-090641 |
| S3-090635 | 33.820: Correction of text on autonomous validation | Nokia Corporation, Nokia Siemens Networks | agreed | S3-090474 | - |
| S3-090636 | 33.820 CR on H(e)NB Validation | Huawei | agreed | S3-090486 | - |
| S3-090637 | TR 33.828 v1.1.0 | Rapporteur | agreed | - | - |
| S3-090638 | TR 33.828 v1.2.0 | Rapporteur | sent for email approval | - | - |
| S3-090639 | Correcting the handling of EPS security context | Qualcomm Europe | sent for email discussion | S3-090571 | - |
| S3-090640 | 33.401 CR: Storage of EPS NAS security context | Ericsson, Gemalto | agreed | S3-090420 | - |
| S3-090641 | CR TR33.820 75., 7.6 binding of authentication & validation | InterDigital Communications | [not addressed] | S3-090634 | - |

## Annex B: List of change requests

| Document | Title | Source | Decision | Spec | CR | Rev | Rel | Cat | WI |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| S3-090412 | [IMS] Correction of wrong message name in annex N (Rel-9) | Nokia Corporation, Nokia Siemens Networks | postponed | - | - | - | - | - | - |
| S3-090414 | 33.401 CR: Removal of KSI_ASME from TAU Accept | Ericsson, NEC Corporation | merged in S3-090606 | - | - | - | - | - | - |
| S3-090415 | 33.401 CR: Correction of UE security capability handling in the TAU procedure | Ericsson, NEC Corporation | merged in S3-090606 | - | - | - | - | - | - |
| S3-090416 | 33.401 CR: Activation of native EPS NAS security context after IRAT HO | Ericsson, NEC Corporation | revised | - | - | - | - | - | - |
| S3-090417 | 33.401 CR: Correction of UE EPS security capability default set | Ericsson | agreed | - | - | - | - | - | - |
| S3-090418 | 33.401 CR: Resolving ed note on PLMN ID encoding | Ericsson | agreed | - | - | - | - | - | - |
| S3-090419 | 33.401 CR: Correction of MM context transfer | Ericsson | merged in S3-090606 | - | - | - | - | - | - |
| S3-090420 | 33.401 CR: Storage of EPS NAS security context | Ericsson, Gemalto | revised | - | - | - | - | - | - |
| S3-090421 | 33.401 CR: UE security capability handling at S1 HO | Ericsson | merged in S3-090601 | - | - | - | - | - | - |
| S3-090422 | 33.401 CR: Correction of eKSI usage in AS | Ericsson, Nokia Siemens Networks, NEC Corporation | merged in S3-090583 | - | - | - | - | - | - |
| S3-090423 | Editorial corrections to security context establishment clause | Ericsson | agreed | - | - | - | - | - | - |
| S3-090424 | 33.402 CR: Clarification on use of USIM/UICC in non-3GPP accesses | Ericsson | agreed | - | - | - | - | - | - |
| S3-090425 | 33.402 CR: Clarification of order for identity request and AVs fetching | Ericsson | revised | - | - | - | - | - | - |
| S3-090426 | 33.401 CR: Update of abbreviations list | Ericsson | merged in S3-090620 | - | - | - | - | - | - |
| S3-090427 | 33.401 CR: Introduction to forward security | Ericsson | revised | - | - | - | - | - | - |
| S3-090429 | [IMS] Correction of wrong message name in annex N (Rel-8) | Nokia Corporation, Nokia Siemens Networks | postponed | - | - | - | - | - | - |
| S3-090445 | 33.820CR: Clarification of Access Control Mechanisms | Qualcomm Europe | revised | - | - | - | - | - | - |
| S3-090446 | CR33.820: Conclusions on Location Security | Qualcomm Europe | revised | - | - | - | - | - | - |
| S3-090447 | CR TR33.820 7.5.2.1 introduction to validation | InterDigital Communications | revised | - | - | - | - | - | - |
| S3-090448 | CR TR33.820 7.5.2.4 semi-autonomous validation | InterDigital Communications | revised | - | - | - | - | - | - |
| S3-090450 | CR TR33.820 75., 7.6 binding of authentication & validation | InterDigital Communications | revised | - | - | - | - | - | - |
| S3-090451 | CR TR33.820 8.2 conclusions re validation | InterDigital Communications | postponed | - | - | - | - | - | - |
| S3-090456 | Update of referenced RFCs and hash algorithm | Qualcomm Europe | revised | - | - | - | - | - | - |
| S3-090457 | Clarification of Certificate Profile | Qualcomm Europe | revised | - | - | - | - | - | - |
| S3-090473 | Corrections for TS 33.310 | Huawei | conditionally agreed | - | - | - | - | - | - |
| S3-090474 | 33.820: Correction of text on autonomous validation | Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090475 | Update to H(e)NB system architecture | Samsung | revised | - | - | - | - | - | - |
| S3-090476 | CR to 33.820 Update of Access Control Mechanisms for H(e)NB | Samsung | merged in S3-090625 | - | - | - | - | - | - |
| S3-090485 | 33.820 CR 7.2.2.3 H(e)NB Authentication | Huawei | revised | - | - | - | - | - | - |
| S3-090486 | 33.820 CR on H(e)NB Validation | Huawei | revised | - | - | - | - | - | - |
| S3-090487 | CR Remove Duplicate Section Number in 7.6.1.3.4 | Huawei | revised | - | - | - | - | - | - |
| S3-090488 | Authorization for ANDSF | Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090497 | Clarification of Section 7.4 Authentication Method Selection | Airvana, Huawei, InterDigital, NEC Corporation, T-Mobile | agreed | - | - | - | - | - | - |
| S3-090506 | corrected version of S3-090449 | InterDigital Communications | postponed | - | - | - | - | - | - |
| S3-090507 | Clarification on Multiple KeNB*s Preparation in Section 7.4.3 | Huawei | revised | - | - | - | - | - | - |
| S3-090510 | Add the frequency EARFCN-DL | Huawei,ZTE | merged in S3-090588 | - | - | - | - | - | - |
| S3-090511 | The correction on input key of Null ciphering algorithm | Huawei,ZTE | agreed | - | - | - | - | - | - |
| S3-090512 | Clarification of NAS algorithm selection during S1 HO | Huawei,ZTE | merged in S3-090601 | - | - | - | - | - | - |
| S3-090513 | Corrections of 33.401 | Huawei,ZTE | merged in S3-090583 | - | - | - | - | - | - |
| S3-090515 | idle mode procedure in EUTRAN | Huawei | postponed | - | - | - | - | - | - |
| S3-090516 | corrections for Attach procedure | Huawei | revised | - | - | - | - | - | - |
| S3-090517 | clarification for EAP-AKA' | Huawei | postponed | - | - | - | - | - | - |
| S3-090518 | Corrections for the EPS security context fetching between MMEs | Huawei | agreed | - | - | - | - | - | - |
| S3-090519 | correctinos for idle mode procedure in EUTRAN | Huawei | revised | - | - | - | - | - | - |
| S3-090521 | Addition of security requirements on eNB | China Mobile, Alcatel-lucent, Vodafone, ZTE | revised | - | - | - | - | - | - |
| S3-090522 | Correction of KeNB derivations | China Mobile,ZTE | revised | - | - | - | - | - | - |
| S3-090528 | Addition of missing Abbreviations | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | merged in S3-090620 | - | - | - | - | - | - |
| S3-090529 | The definition of eKSI format | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | revised | - | - | - | - | - | - |
| S3-090530 | Additional condition of KeNB refresh | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | withdrawn | - | - | - | - | - | - |
| S3-090532 | Change in the Clause 6.2. Removal of explicit CK’/IK’ function | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | - | - | - | - | - |
| S3-090533 | Clarifications for Annex A and References | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | - | - | - | - | - |
| S3-090534 | Addition of the NULL algorithm for Integrity Protection to the Clause 5.1.4 | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | - | - | - | - | - |
| S3-090535 | Addition of EC Clause | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | revised | - | - | - | - | - | - |
| S3-090536 | Addition of the Emergency Calling Clause | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | agreed | - | - | - | - | - | - |
| S3-090545 | Use of NAI prefix for EAP-AKA’ | Ericsson, Nokia Siemens Networks, Nokia Corporation | postponed | - | - | - | - | - | - |
| S3-090546 | CR to 33.401 Removal of NAS keys storage | NEC Corporation, Nokia Corporation, Nokia Siemens Networks, NTT DOCOMO | conditionally agreed | - | - | - | - | - | - |
| S3-090547 | AKA procedure in case of NAS security actived | ZTE Corporation, HUAWEI | noted | - | - | - | - | - | - |
| S3-090548 | Key-Change-On the Fly Clarification | ZTE Corporation | noted | - | - | - | - | - | - |
| S3-090549 | Clarification for Forward Security | ZTE Corporation | revised | - | - | - | - | - | - |
| S3-090550 | Clarification for DSMIPv6 Bootstrap | ZTE Corporation | postponed | - | - | - | - | - | - |
| S3-090551 | Update UE-ANDSF Communication Security Solution | ZTE Corporation | noted | - | - | - | - | - | - |
| S3-090553 | Changing SGSN to the enhanced MSC server in SRVCC | Nokia Corporation, Nokia Siemens Networks, China Mobile | agreed | - | - | - | - | - | - |
| S3-090554 | Addition of security requirements on eNB | China Mobile, Alcatel-lucent, Vodafone, ZTE | noted | - | - | - | - | - | - |
| S3-090555 | Correction of KeNB derivations | China Mobile,ZTE,Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090556 | Correction of EPS AS Security Mode Command Procedure | China Mobile,Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090557 | Correction of EPS AS/NAS Security Context definition | China Mobile,Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090558 | Keys to be used in HO from E-UTRAN to UTRAN and GERAN | Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090559 | Correction on Transfer of Capabilities in S1-handover | Nokia Corporation, Nokia Siemens Networks | merged in S3-090601 | - | - | - | - | - | - |
| S3-090561 | Correction on KeNB refresh | Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090562 | Correction on Key Identification | Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090563 | Keys to be used in HO from UTRAN and GERAN to E-UTRAN | Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090565 | RRC Connection Re-establishment – security corrections | Nokia Corporation, Nokia Siemens Networks | revised | - | - | - | - | - | - |
| S3-090566 | Clarification of LTE USIM requirement | NTT DOCOMO | [not addressed] | - | - | - | - | - | - |
| S3-090567 | Comments on S3-090446_CR_LocationSecurityConclusions | Airvana | noted | - | - | - | - | - | - |
| S3-090569 | CR to 33.820: Recommendation for Hosting Party authentication | Gemalto, Orange, TeliaSonera, Telecom Italia, Sagem Orga, Giesecke&Devrient | noted | - | - | - | - | - | - |
| S3-090570 | Clarifications to calculating the initial K_eNB and K_eNB after key change on the fly | Qualcomm Europe | sent for email approval | - | - | - | - | - | - |
| S3-090571 | Correcting the handling of EPS security context | Qualcomm Europe | revised | - | - | - | - | - | - |
| S3-090572 | Correcting MME behaviour at S1-handover | Qualcomm Europe | conditionally agreed | - | - | - | - | - | - |
| S3-090579 | Addition of EC Clauses to the Rel-9 TS 33.401 | Alcatel-Lucent, Alcatel Shanghai Bell Co. Ltd., Rogers Wireless, Verizon Wireless | agreed | - | - | - | - | - | - |
| S3-090583 | Corrections of eKSI and AS in 33.401 | Huawei,ZTE, Ericsson, | agreed | - | - | - | - | - | - |
| S3-090585 | corrections for Attach procedure | Huawei | agreed | - | - | - | - | - | - |
| S3-090586 | Correction of EPS AS/NAS Security Context definition | China Mobile,Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090587 | 33.401 CR: Introduction to forward security | Ericsson | agreed | - | - | - | - | - | - |
| S3-090588 | Clarification on Multiple KeNB*s Preparation in Section 7.4.3 | Huawei | agreed | - | - | - | - | - | - |
| S3-090589 | Add the frequency EARFCN-DL | Huawei,ZTE | withdrawn | - | - | - | - | - | - |
| S3-090590 | The definition of eKSI format | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent, China Mobile | agreed | - | - | - | - | - | - |
| S3-090591 | Correction on KeNB refresh | Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090592 | Key-Change-On the Fly Clarification | ZTE Corporation | agreed | - | - | - | - | - | - |
| S3-090593 | Correction of KeNB derivations | China Mobile,ZTE,Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090594 | Correction on Key Identification | Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090601 | 33.401 CR: UE security capability handling at S1 HO | Ericsson | agreed | - | - | - | - | - | - |
| S3-090602 | Correction of EPS AS Security Mode Command Procedure | China Mobile,Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090603 | RRC Connection Re-establishment – security corrections | Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090606 | 33.401 CR: Activation of native EPS NAS security context after IRAT HO | Ericsson, NEC Corporation | agreed | - | - | - | - | - | - |
| S3-090607 | correctinos for idle mode procedure in EUTRAN | Huawei | agreed | - | - | - | - | - | - |
| S3-090608 | CR Remove Duplicate Section Number in 7.6.1.3.4 | Huawei | agreed | - | - | - | - | - | - |
| S3-090609 | Update of referenced RFCs and hash algorithm | Qualcomm Europe | conditionally agreed | - | - | - | - | - | - |
| S3-090616 | 33.402 CR: Clarification of order for identity request and AVs fetching | Ericsson | agreed | - | - | - | - | - | - |
| S3-090618 | Authorization for ANDSF | Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090620 | 33.401 CR: Update of abbreviations list | Ericsson | agreed | - | - | - | - | - | - |
| S3-090621 | Clarifications for Annex A and References | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | agreed | - | - | - | - | - | - |
| S3-090622 | Update to H(e)NB system architecture | Samsung | agreed | - | - | - | - | - | - |
| S3-090625 | CR to 33.820 Update of Access Control Mechanisms for H(e)NB | Qualcomm Europe, Samsung | agreed | - | - | - | - | - | - |
| S3-090626 | 33.820 CR 7.2.2.3 H(e)NB Authentication | Huawei | agreed | - | - | - | - | - | - |
| S3-090627 | Clarification of Certificate Profile | Qualcomm Europe | agreed | - | - | - | - | - | - |
| S3-090628 | CR33.820: Conclusions on Location Security | Qualcomm Europe | agreed | - | - | - | - | - | - |
| S3-090629 | Some comments about software integrity verify | ZTE Corporation | withdrawn | - | - | - | - | - | - |
| S3-090630 | Change in the Clause 6.2. Removal of explicit CK’/IK’ function | Alcatel Shanghai Bell Co. Ltd., Alcatel-Lucent | agreed | - | - | - | - | - | - |
| S3-090632 | CR TR33.820 7.5.2.1 introduction to validation | InterDigital Communications | agreed | - | - | - | - | - | - |
| S3-090633 | CR TR33.820 7.5.2.4 semi-autonomous validation | InterDigital Communications | agreed | - | - | - | - | - | - |
| S3-090634 | CR TR33.820 75., 7.6 binding of authentication & validation | InterDigital Communications | revised | - | - | - | - | - | - |
| S3-090635 | 33.820: Correction of text on autonomous validation | Nokia Corporation, Nokia Siemens Networks | agreed | - | - | - | - | - | - |
| S3-090636 | 33.820 CR on H(e)NB Validation | Huawei | agreed | - | - | - | - | - | - |
| S3-090639 | Correcting the handling of EPS security context | Qualcomm Europe | sent for email discussion | - | - | - | - | - | - |
| S3-090640 | 33.401 CR: Storage of EPS NAS security context | Ericsson, Gemalto | agreed | - | - | - | - | - | - |
| S3-090641 | CR TR33.820 75., 7.6 binding of authentication & validation | InterDigital Communications | [not addressed] | - | - | - | - | - | - |

## Annex C: Lists of liaisons

### C1: Incoming liaison statements

| Document | Title | From | Decision | Reply in |
| --- | --- | --- | --- | --- |
| S3-090404 | Reply liaison statement on PUC(I) work | 19tTD283_LS_to_3GPP_SA3_-_PUCI | noted |  |
| S3-090405 | LS on Security parameter handling | C1-090756 | noted |  |
| S3-090406 | Reply LS on paging optimisation via allowed CSG list in paging message for LTE and UMTS | C1-090811 | noted |  |
| S3-090407 | New Q.16/13 study item on Mobility Security. Response to the 3GPP liaison statement S3-081567 | COM13-LS032 | noted |  |
| S3-090408 | Response to 3GPP on the PUCI Work Item | OMA-LS_787-REQ_to_3GPP_Protection_against_Unsolicited_Communication_for_IMS-20090128-A | replied to | S3-090612 |
| S3-090409 | LS on handling of dynamic UE UTRAN capability during Handover | R2-091922 | noted |  |
| S3-090410 | Reply LS on Receive of ETWS outside home-PLMN | S1-090199 | not addressed |  |
| S3-090411 | Reply LS on “Key management for 3GP SRTP recording profile” | S4-090169 | not addressed (out of scope for ad hoc) |  |
| S3-090434 | LS on exception lists for integrity protection of NAS messages | C1-091369 | noted |  |
| S3-090435 | Reply LS on preventing inter-RAT HO for UE with SIM access | C4-090512 | noted |  |
| S3-090436 | LS on Prefix for EAP-AKA' | C4-090799 | replied to | S3-090614 |
| S3-090437 | LS on the removal of KNASint and KNASenc from EFEPSNSC | C6-090055 | replied to | S3-090584 |
| S3-090438 | LS on preventing inter-RAT HO for UE with SIM access | GP-090351 | noted |  |
| S3-090439 | Recommendation ITU-T X.1244, Overall aspects of countering spam in IP-based multimedia applications | LS033 | noted |  |
| S3-090440 | LS response to R2-087408 (Reply LS on PCI Clarification) | R3-090544 | noted |  |
| S3-090441 | LS on transfer of UE Security Capabilities to target eNBs | R3-090664 | replied to | S3-090600 |
| S3-090442 | LS on Security for TAU Request | S2-091788 | replied to | S3-090599 |
| S3-090443 | LS on Enhanced Security for S2c | S2-091795 | replied to | S3-090617 |
| S3-090596 | LS on concurrent running of security procedures | current meeting | agreed |  |
| S3-090631 | Reply LS to S3-090596 = R2-092666 on Concurrent Running of Security Procedures | R2-092676 | noted |  |

### C2: Outgoing liaison statements

| Document | Title | To | Cc | reply to i/c LS |
| --- | --- | --- | --- | --- |
| S3-090584 | Reply to: LS on the removal of KNASint and KNASenc from EFEPSNSC | C6-090055 | - | S3-090437 |
| S3-090599 | Reply to: LS on Security for TAU Request | S2-091788 | - | S3-090442 |
| S3-090600 | Reply to: LS on transfer of UE Security Capabilities to target eNBs | R3-090664 | - | S3-090441 |
| S3-090604 | LS to RAN2 and RAN3 on Correcting MME behaviour at S1-handover | - | - |  |
| S3-090612 | Reply to: Response to 3GPP on the PUCI Work Item | OMA-LS_787-REQ_to_3GPP_Protection_against_Unsolicited_Communication_for_IMS-20090128-A | - | S3-090408 |
| S3-090614 | Reply to: LS on Prefix for EAP-AKA' | C4-090799 | - | S3-090436 |
| S3-090617 | Reply to: LS on Enhanced Security for S2c | S2-091795 | - | S3-090443 |

## Annex F: List of action items

| Meeting/Number | Agenda item | Document | Details | Responsible |
| --- | --- | --- | --- | --- |
| March 09 ad hoc/1 | 6.8 | S3-090609 | Second check has to be done in SA3#55. | Brian Rosenberg |
| March 09 ad hoc/2 | 6.8 | S3-090473 | Second check has to be done in SA3#55. | Dony He |
| March 09 ad hoc/3 | 7 | S3-090581 | Provide comments on draft TS on H(e)NB | TISPAN WG7 |
| March 09 ad hoc/4 | 7.2 | S3-090610 | Address the concerns/issues raised in SA3-090610 in contributions to the SA3 meeting in May. Then 3GPP SA3 will send an LS to WG7 with the proposed solution. | TISPAN WG7 |

## Annex G: List of participants