## Slide 1: MITRE R19 Priorities
Presentation to SA3#113 Chicago
S3-234567
3GPP TSG-SA3 Meeting #113 Chicago, USA, 6 - 10 November 2023
S3-234567

## Slide 2
Topic (applicable SIDs/WIDs) | Objectives
Continuous security monitoring and dynamic access control [1, 2] ZTS; [3] Security of PLMN hosting a NPN; [4] AI/ML enhancements | Integrate continuous security monitoring and dynamic access control into 5GS authentication and authorization: Determine standard security related data collected to evaluate the NF for detection of abnormal behavior; Determine how to mitigate threat of a compromised NF via dynamic authorization, including revocation, segmentation, and enforcement of dynamic access decisions; Consider collaborative behavior in roaming and NPN scenarios Leveraging AI/ML to predict, detect, prevent, and mitigate anomalous network behavior.
Resource Isolation [5] | Compromised or misconfigured resources (e.g., VNFs/CNFs) may jeopardize privacy, confidentiality, or availability of another NF sharing the same resources Ensure isolation between network slices; Reduce effect of a compromised or misconfigured NF resource on another NF.
SA3 Prime (SIDs/WIDs) (POC: David Gabay)
S3-234567

## Slide 3: Feature Security Dependent on Other WGs (POC: David Gabay)
Topic (applicable SIDs/WIDs) | Objectives
[6, 7] 256-bit WID/SID | Begin the transition to 256-bit Integrity and encryption algorithms Interoperability is assured whenever possible; Define the 256-bit integrity and encryption algorithms
SA3 Prime (SIDs/WIDs) (POC: David Gabay)
Topic (applicable SIDs/WIDs) | Objectives
[8] ProSe phase 3 | Support for multi-hop U2U/U2N relay Consideration for secure routing protocols and key management; Privacy from intermediate relay nodes; Support for Non-3GPP RAT over PC5 U2N/U2U relay;
S3-234567

## Slide 4
Topic (applicable SIDs/WIDs) | Objectives
Alternative Authentication without 5GC [9] | Support alternative authentication for UE in out of coverage scenarios Enhance existing security architecture to support alternative authentication method without use of the 5GC
SA3 Prime (SIDs/WIDs)(POC: Dr. DJ Shyy)
S3-234567

## Slide 5
Thank you!
David Gabay (dgabay@mitre.org)
Dr. DJ Shyy (djshyy@mitre.org)
S3-234567
3GPP TSG-SA3 Meeting #113 Chicago, USA, 6 - 10 November 2023