## Slide 1: Discussion on security for LTM (L1/L2 Triggered Mobility)
OPPO
3GPP TSG-SA3 Meeting #113
Chicago, US, 06-10 November 2023

## Slide 2: R18 intra-CU LTM
Rel-18 introduces LTM (L1/L2-Triggered Mobility) to reduce handover latency, signaling overhead and interruption time.
LTM is a procedure in which a gNB receives L1 measurement report(s) from a UE, and on their basis the gNB changes UE’s serving cell by a cell switch command signaled via a MAC CE. The cell switch command indicates an LTM candidate cell configuration that the gNB previously prepared and provided to the UE through RRC signalling. Then the UE switches to the target cell according to the cell switch command.

## Slide 3: R19 Inter-CU LTM
R18 LTM
R18 mobility limits to intra-CU LTM
R19 may extend the scenario to inter-CU
R19 potential scenario
R18 LTM only support intra-CU to simplified design, however, limitation of use cases.
In RAN#101, many companies has proposed to further study inter-CU LTM for R19 mobility enhancement, which has not been approved yet.
To further extend and inherit the benefits brought by LTM, RAN has high possibility to further consider the inter-CU LTM in R19.

## Slide 4: Motivation and Proposal
Motivation:
  For R18 intra-CU LTM [1], no security requirement and procedure required. However, in R19, once the inter-CU case is introduced, there comes the security gap for key update.
  In the L3 based handover [2], the HO Command message is transmitted from gNB to UE carried in the RRC signalling, which is protected using AS security. For the LTM, the Cell switch command is transmitted from gNB to UE carried in the L1/L2 signalling (i.e., MAC CE).
  Due to lack of security protection for the L1/L2 signalling, if the security parameter (e.g., NCC) is included in the Cell switch command carried in MAC CE, it can be modified, or replayed by an attacker. Consequently, the security key mismatch occurs and further causing the handover failure.
Proposal:
  It is proposed to further analyse the gap and potential security requirement for the inter-CU LTM as long as it is agreed.

## Slide 5: References and Abbreviations
References
  [1] R2-2311610 “38.300 running CR for introduction of NR further mobility enhancements”
  [2] 3GPP TS 33.501
Abbreviations
  LTM L1/L2 Triggered Mobility

## Slide 6
Thank You!