## Slide 1: RCS File Transfer Vulnerabilities - XCAP Exploitation (1) CVD-2023-0074
1. RCS File Upload Resume Attack
Manipulation of victim's supplementary service settings in XCAP Server, e.g. set barring-of-all-incoming-calls
Exploits absence of file upload resume URL validation by UE and unprotected HTTP between UE and XCAP Server
Victim UE starts RCS file upload (sends picture in chat) to compromised RCS Content Server, which interrupts it
Victim UE requests file upload resume URL, which instead of RCS Content Server points to MNO's XCAP Server
Attacker's rogue Wi-Fi AP redirects XCAP IP traffic to attacker's XCAP Proxy, which injects malicious XCAP settings into HTTP PUT
Outcome: GSMA to mandate TLS with proper certificate validation between UE and RCS Content & XCAP Servers
HTTP PUT
Notes: There are two issues as we have mentioned.
The first issue is the lack of certificate validation of file server. It is specific by phone manufacturer. In China, we have found three manufacturers have this issue.
But this issue isn't the key issue.
The key issue is that UE accept the forward url, even thought forward server name is different from HBP Server.
For example: If an attacker has controlled the true HBP Server(RCS FileServer, true certificate server), he can use the key issue to reply fake forward url and enlarge the attack(Calling barring) by MITM.
Many manufacturers have the key issue. we think the standard of RCS about Upload File process should make some security improvements about the key issue.
How did you come to solution of using the file upload resume procedure to redirect the UE? We see many other ways of redirecting a UE to the XCAP server URL, but we assume you had a good reason to do it this way. If we are correct, the follow up question is: have you found any other scenarios that would yield the same result (i.e. redirect the UE using the correct method making the authentication successful).
Answer:
Yes, These are two scenarios.
The first scenario is sending a malicious RCS message to victim(0 click).
UE sends request to XCAP server by the HTTP GET method.
Attacker can steal security infomation of victim.
We will send the poc to GSMA and request another CVD id soon.
The second scenario is RCS File upload resume.
UE send request to XCAP server by HTTP PUT method.
As we know, HTTP PUT method is more dangerous than GET method, So we submit it to GSMA as the first.
Do we understand it correctly: the XCAP server of the operator is available on the internet, so for your upstream (to reach the XCAP server) you don’t need to be on the mobile network and open e.g. a dedicated radio bearer?
Answer:
Yes, In china, Many service (5G RCS、MMS、VOLTE and so on) is both on the internet and mobile network.
We can access some servers of MNO from the internet.
UE has the UI for Supplementary service (calling forward, calling barring).
It is easy to setup test environment and reproduce the poc on the internet.
Compared to internet network, it is hard to set up MITM on a real mobile network.
But we still have success in first scenario(Q2) with femtocells on a real mobile network.
Moreover, It is illegal to setup pseudo base-station in china.
To summarize, we choose XCAP server and the internet network for POC.
In this paper, we introduce UMA+, an unauthorized multiangulation
attack that resolves such untouched yet critical
challenges of the prior attacks (§4). UMA+ shares general
key concepts of the unauthorized localization attack. UMA+
utilizes multiangulation as a localization method, which is
based on Angle of Arrival (AoA) measurement.
UMA+ tackles the challenges by taking advantage of the
following contributions:
(1) We present a bearer-knocking attack, which is to obtain
the victim’s temporary identifier regardless of the UE’s
status (§5). In this attack, we monitor the dedicated control
channel for the voice call and SMS signaling, instead of relying
on the silent calls and monitoring the paging channel.
(2) We propose a power-boosting attack, which enforces
UE to increase transmission power (§6). This attack mainly
exploits the transmit power control (TPC) command which
is delivered without any security protection. Therefore, with
the help of signal overshadowing attack [39], we inject the
manipulated TPC command into the victim UE. By doing
this, the attacker can detect the victim’s uplink signal, which
is undetectable without the power-boosting attack.
(3) Lastly, we analyze the impact of a cellular repeater to the
unauthorized localization attack (§7). Based on the analysis,
we establish a proper strategy for differentiating the signal
between the victim and the repeater. This strategy examines
the variations in signal strength of the UE and repeater after
the power-boosting attack to identify the UE’s signal.
Background: Transmit Power Control in LTE
In LTE radio network, eNB (base station) controls the uplink transmission power of UE (User Equipment) to handle network capacity and signal interference. To control uplink transmission power, eNB sends TPC (Transmit Power Control) command through DCI (Downlink Control Indicator) messages after random access procedure (i.e., PRACH). After receiving TPC command, UE adjusts its uplink transmission power with a closed-loop power control algorithm. With TPC command, eNB controls both control and data channels on the uplink (i.e., PUCCH and PUSCH).
Generally, the closed-loop power control algorithm adopts the accumulated power control that follows gradually changed as defined below table up to 23 dBm. The table shows uplink power control in PUSCH (i.e., ∆_𝑷𝑼𝑺𝑪𝑯 according to TPC command in DCI message).
TPC command in DCI msg.
0
1
2
3
Accumulated ∆_𝑷𝑼𝑺𝑪𝑯 (dB)
-1
0
+1
+3
Please refer to 3GPP TS 26.213.
Background: Uplink Scheduling in LTE
For radio communication in LTE, eNB allocates uplink resources for each UE through DCI messages. Over the downlink channel, eNB broadcasts DCI format 0 message that consists of the target RNTI, resource allocation for uplink data (i.e., PUSCH scheduling), and TPC command for PUSCH, etc. Each UE receives DCI 0 message corresponding to its RNTI and transmits its uplink data after 4 milliseconds over the allocated frequency area in the uplink channel. Uplink scheduling is required to guarantee radio channel quality and fair access to network resources.
Please refer to 3GPP TS 26.212.
Vulnerability
We found the vulnerability of transmission power control and uplink scheduling in the LTE radio network. DCI messages used for uplink transmission power control and scheduling are delivered to UE by eNB over the air. At this time, eNB transmits DCI messages without any security protection (i.e., encryption or integrity check). In other words, any authentication process is not performed to control UE’s transmission power and allocate radio resources. Therefore, anyone can eavesdrop and forge the transmission power control and uplink scheduling.
Implementation
We implemented an attack manipulating transmission power control and uplink scheduling. Since there is no security protection for transmission power control, we could compromise the radio control mechanism by exploiting the signal overshadowing attack*. The key idea is to inject manipulated subframes that contain DCI format 0 message to the target UE. In manipulated DCI 0 message, TPC is set to increase or decrease the target’s transmission power and uplink resource is arbitrarily allocated without eNB’s intention.
First, we identify the radio configuration of legitimate eNB to mimic its downlink subframe. The configuration includes target PCI (Physical Cell Identification), channel bandwidth, PHICH (Physical channel HybridARQ Indicator Channe) configuration, cyclic prefix and transmission mode of eNB. This configuration can be obtained by decoding MIB (Master Information Block), PSS (Primary Synchronization Signal), and SSS (Secondary Synchronization Signal) that are broadcasted by eNB.
Then, we generate a downlink subframe based on the radio configuration of eNB to manipulate the radio control mechanism. The downlink subframe includes a malicious DCI 0 message and it consists of the target RNTI, arbitrary scheduled uplink transmission information, and the TPC command having a value of 3 or 0 to increase/decrease the uplink transmission power.
Finally, the manipulated subframe is injected into the appropriate subframe number (i.e., signal overshadowing) on the downlink channel. In our work, we inject the manipulated subframe to subframe number 9 to minimize the impact on the target UE’s LTE service, but an attacker can exploit any subframe number to inject malicious DCI message. In addition, we repeatedly conduct signal overshadowing into every subframe number 9 to continuously allocate uplink resources and overcome the transmission power control from eNB.
Evaluation
We examined our attack in the industry-grade LTE network, AMARI Callbox Classic, and commercial LTE network to demonstrate the attack feasibility. As the target UE and signal generator (i.e., subframe injector), Samsung Galaxy S10 5G and USRP X310 are used, respectively.
First, we injected manipulated DCI 0 having a value of TPC command 3 and arbitrary resource allocation. In the result, we found that the transmission power of PUSCH increases up to 23dBm (i.e., maximum uplink transmission power) and UE continuously transmits the uplink signal over arbitrarily allocated resources. We figured out that BLER (Block Error Rate) of uplink decoding in eNB on AMARI Callbox Classic significantly increases to over 90% due to unexpected uplink transmission.
In addition, when we injected a value of TPC command 0, the uplink transmission power of UE continuously decreases. Then, UE is disconnected from the radio network and tries to reconnect to the radio network.
Location tracking
Many researchers have studied about location tracking attacks without any privileges in LTE networks*. In their works, an unprivileged attacker first identifies the target’s uplink signal and measures the ToA (Time of Arrival) or AoA (Angle of Arrival) of the uplink signal. Then, based on the measurement, the attacker estimates the location of the target (i.e., uplink signal source).
However, unfortunately, they overlooked the case that the uplink signal is undetectable (i.e., real-world challenges). When the attacker traces the location of UE in the real-world environment, the target’s uplink signal might be undetectable. For example, when UE is located close to eNB, UE transmits its uplink data with low signal power due to high channel quality with eNB**. If the target’s uplink signal is undetectable due to low transmission power, the attacker cannot estimate the target’s location.
To solve such problems during location tracking, the attacker should boost the uplink transmission power of the target UE. By exploiting this vulnerability, the attacker can boost UE’s transmission power without the target’s recognition and fully perform a stealthy location tracking attack.
Denial of Service (DoS)
By exploiting this vulnerability, an attacker can perform DoS attacks on LTE radio networks in two ways: 1) Network-bursting, and 2) Cancelling-out.
Network-bursting is an attack that compromises radio network capability by forcing all UEs connected to the same eNB to increase their uplink transmission power or transmit the uplink signal over unadmitted resources. If the attacker performs network-bursting on an eNB with many connected UEs, the hardware capability of the eNB, such as the antenna and signal processor, can be destroyed. In addition, when the eNB receives unexpected uplink data that a number of UEs transmit according to arbitrarily allocated resources by the attacker, the BLER is significantly increased. This scheduling corruption by multiple UEs might cause Distributed DoS and affect the network's capability. We confirmed that VoLTE service of two UEs connected to eNB on AMARI Callbox is terminated by force due to high BLER when we manipulate transmission power and resource allocation for both UEs.
Cancelling-out exploits this vulnerability to make the UE unable to communicate with the eNB. By repeatedly injecting manipulated DCI 0, including a value of TPC command 0, to the target UE, the attacker can cause radio communication failure for the target. Although the radio connection would be re-established and the target's RNTI would change after one attack, the attacker can trace the target’s RNTI based on previous identity tracking attacks* and retry the cancelling-out attack with the target’s RNTI value.
*S. Kumar et al. “LTE radio analytics mad easy and accessible”, ACM SIGCOMM 2014.
*M. Kotuliak et al. “LTRACK: Stealthy Tracking of Mobile Phones in LTE”, USENIX Security 2022.
**Y. Michalevsky et al. “PowerSpy: Location tracking using mobile device power analysis”, USENIX Security 2015.

## Slide 2: RCS File Transfer Vulnerabilities - XCAP Exploitation (2) CVD-2023-0074
2. RCS File Transfer URL Tampering Attack
Leakage of victim's supplementary service settings in XCAP Server
Exploits absence of thumbnail URL validation in SIP MESSAGE XML body and unprotected HTTP between UE and XCAP Server
Attacker UE sends to victim XML body with manipulated thumbnail URL pointing to MNO's XCAP Server instead of RCS Content Server
Victim UE automatically (no user action) accesses thumbnail URL, sending HTTP GET to XCAP Server
Attacker's rogue Wi-Fi AP redirects XCAP IP traffic to attacker's XCAP Proxy, which sniffs XCAP settings from HTTP
Outcome: GSMA to mandate TLS with proper certificate validation between UE and XCAP Server
HTTP GET
Notes: How did you come to solution of using the file upload resume procedure to redirect the UE? We see many other ways of redirecting a UE to the XCAP server URL, but we assume you had a good reason to do it this way. If we are correct, the follow up question is: have you found any other scenarios that would yield the same result (i.e. redirect the UE using the correct method making the authentication successful).
Answer:
Yes, These are two scenarios.
The first scenario is sending a malicious RCS message to victim(0 click).
UE sends request to XCAP server by the HTTP GET method.
Attacker can steal security infomation of victim.
We will send the poc to GSMA and request another CVD id soon.
The second scenario is RCS File upload resume.
UE send request to XCAP server by HTTP PUT method.
As we know, HTTP PUT method is more dangerous than GET method, So we submit it to GSMA as the first.
Do we understand it correctly: the XCAP server of the operator is available on the internet, so for your upstream (to reach the XCAP server) you don’t need to be on the mobile network and open e.g. a dedicated radio bearer?
Answer:
Yes, In china, Many service (5G RCS、MMS、VOLTE and so on) is both on the internet and mobile network.
We can access some servers of MNO from the internet.
UE has the UI for Supplementary service (calling forward, calling barring).
It is easy to setup test environment and reproduce the poc on the internet.
Compared to internet network, it is hard to set up MITM on a real mobile network.
But we still have success in first scenario(Q2) with femtocells on a real mobile network.
Moreover, It is illegal to setup pseudo base-station in china.
To summarize, we choose XCAP server and the internet network for POC.
In this paper, we introduce UMA+, an unauthorized multiangulation
attack that resolves such untouched yet critical
challenges of the prior attacks (§4). UMA+ shares general
key concepts of the unauthorized localization attack. UMA+
utilizes multiangulation as a localization method, which is
based on Angle of Arrival (AoA) measurement.
UMA+ tackles the challenges by taking advantage of the
following contributions:
(1) We present a bearer-knocking attack, which is to obtain
the victim’s temporary identifier regardless of the UE’s
status (§5). In this attack, we monitor the dedicated control
channel for the voice call and SMS signaling, instead of relying
on the silent calls and monitoring the paging channel.
(2) We propose a power-boosting attack, which enforces
UE to increase transmission power (§6). This attack mainly
exploits the transmit power control (TPC) command which
is delivered without any security protection. Therefore, with
the help of signal overshadowing attack [39], we inject the
manipulated TPC command into the victim UE. By doing
this, the attacker can detect the victim’s uplink signal, which
is undetectable without the power-boosting attack.
(3) Lastly, we analyze the impact of a cellular repeater to the
unauthorized localization attack (§7). Based on the analysis,
we establish a proper strategy for differentiating the signal
between the victim and the repeater. This strategy examines
the variations in signal strength of the UE and repeater after
the power-boosting attack to identify the UE’s signal.
Background: Transmit Power Control in LTE
In LTE radio network, eNB (base station) controls the uplink transmission power of UE (User Equipment) to handle network capacity and signal interference. To control uplink transmission power, eNB sends TPC (Transmit Power Control) command through DCI (Downlink Control Indicator) messages after random access procedure (i.e., PRACH). After receiving TPC command, UE adjusts its uplink transmission power with a closed-loop power control algorithm. With TPC command, eNB controls both control and data channels on the uplink (i.e., PUCCH and PUSCH).
Generally, the closed-loop power control algorithm adopts the accumulated power control that follows gradually changed as defined below table up to 23 dBm. The table shows uplink power control in PUSCH (i.e., ∆_𝑷𝑼𝑺𝑪𝑯 according to TPC command in DCI message).
TPC command in DCI msg.
0
1
2
3
Accumulated ∆_𝑷𝑼𝑺𝑪𝑯 (dB)
-1
0
+1
+3
Please refer to 3GPP TS 26.213.
Background: Uplink Scheduling in LTE
For radio communication in LTE, eNB allocates uplink resources for each UE through DCI messages. Over the downlink channel, eNB broadcasts DCI format 0 message that consists of the target RNTI, resource allocation for uplink data (i.e., PUSCH scheduling), and TPC command for PUSCH, etc. Each UE receives DCI 0 message corresponding to its RNTI and transmits its uplink data after 4 milliseconds over the allocated frequency area in the uplink channel. Uplink scheduling is required to guarantee radio channel quality and fair access to network resources.
Please refer to 3GPP TS 26.212.
Vulnerability
We found the vulnerability of transmission power control and uplink scheduling in the LTE radio network. DCI messages used for uplink transmission power control and scheduling are delivered to UE by eNB over the air. At this time, eNB transmits DCI messages without any security protection (i.e., encryption or integrity check). In other words, any authentication process is not performed to control UE’s transmission power and allocate radio resources. Therefore, anyone can eavesdrop and forge the transmission power control and uplink scheduling.
Implementation
We implemented an attack manipulating transmission power control and uplink scheduling. Since there is no security protection for transmission power control, we could compromise the radio control mechanism by exploiting the signal overshadowing attack*. The key idea is to inject manipulated subframes that contain DCI format 0 message to the target UE. In manipulated DCI 0 message, TPC is set to increase or decrease the target’s transmission power and uplink resource is arbitrarily allocated without eNB’s intention.
First, we identify the radio configuration of legitimate eNB to mimic its downlink subframe. The configuration includes target PCI (Physical Cell Identification), channel bandwidth, PHICH (Physical channel HybridARQ Indicator Channe) configuration, cyclic prefix and transmission mode of eNB. This configuration can be obtained by decoding MIB (Master Information Block), PSS (Primary Synchronization Signal), and SSS (Secondary Synchronization Signal) that are broadcasted by eNB.
Then, we generate a downlink subframe based on the radio configuration of eNB to manipulate the radio control mechanism. The downlink subframe includes a malicious DCI 0 message and it consists of the target RNTI, arbitrary scheduled uplink transmission information, and the TPC command having a value of 3 or 0 to increase/decrease the uplink transmission power.
Finally, the manipulated subframe is injected into the appropriate subframe number (i.e., signal overshadowing) on the downlink channel. In our work, we inject the manipulated subframe to subframe number 9 to minimize the impact on the target UE’s LTE service, but an attacker can exploit any subframe number to inject malicious DCI message. In addition, we repeatedly conduct signal overshadowing into every subframe number 9 to continuously allocate uplink resources and overcome the transmission power control from eNB.
Evaluation
We examined our attack in the industry-grade LTE network, AMARI Callbox Classic, and commercial LTE network to demonstrate the attack feasibility. As the target UE and signal generator (i.e., subframe injector), Samsung Galaxy S10 5G and USRP X310 are used, respectively.
First, we injected manipulated DCI 0 having a value of TPC command 3 and arbitrary resource allocation. In the result, we found that the transmission power of PUSCH increases up to 23dBm (i.e., maximum uplink transmission power) and UE continuously transmits the uplink signal over arbitrarily allocated resources. We figured out that BLER (Block Error Rate) of uplink decoding in eNB on AMARI Callbox Classic significantly increases to over 90% due to unexpected uplink transmission.
In addition, when we injected a value of TPC command 0, the uplink transmission power of UE continuously decreases. Then, UE is disconnected from the radio network and tries to reconnect to the radio network.
Location tracking
Many researchers have studied about location tracking attacks without any privileges in LTE networks*. In their works, an unprivileged attacker first identifies the target’s uplink signal and measures the ToA (Time of Arrival) or AoA (Angle of Arrival) of the uplink signal. Then, based on the measurement, the attacker estimates the location of the target (i.e., uplink signal source).
However, unfortunately, they overlooked the case that the uplink signal is undetectable (i.e., real-world challenges). When the attacker traces the location of UE in the real-world environment, the target’s uplink signal might be undetectable. For example, when UE is located close to eNB, UE transmits its uplink data with low signal power due to high channel quality with eNB**. If the target’s uplink signal is undetectable due to low transmission power, the attacker cannot estimate the target’s location.
To solve such problems during location tracking, the attacker should boost the uplink transmission power of the target UE. By exploiting this vulnerability, the attacker can boost UE’s transmission power without the target’s recognition and fully perform a stealthy location tracking attack.
Denial of Service (DoS)
By exploiting this vulnerability, an attacker can perform DoS attacks on LTE radio networks in two ways: 1) Network-bursting, and 2) Cancelling-out.
Network-bursting is an attack that compromises radio network capability by forcing all UEs connected to the same eNB to increase their uplink transmission power or transmit the uplink signal over unadmitted resources. If the attacker performs network-bursting on an eNB with many connected UEs, the hardware capability of the eNB, such as the antenna and signal processor, can be destroyed. In addition, when the eNB receives unexpected uplink data that a number of UEs transmit according to arbitrarily allocated resources by the attacker, the BLER is significantly increased. This scheduling corruption by multiple UEs might cause Distributed DoS and affect the network's capability. We confirmed that VoLTE service of two UEs connected to eNB on AMARI Callbox is terminated by force due to high BLER when we manipulate transmission power and resource allocation for both UEs.
Cancelling-out exploits this vulnerability to make the UE unable to communicate with the eNB. By repeatedly injecting manipulated DCI 0, including a value of TPC command 0, to the target UE, the attacker can cause radio communication failure for the target. Although the radio connection would be re-established and the target's RNTI would change after one attack, the attacker can trace the target’s RNTI based on previous identity tracking attacks* and retry the cancelling-out attack with the target’s RNTI value.
*S. Kumar et al. “LTE radio analytics mad easy and accessible”, ACM SIGCOMM 2014.
*M. Kotuliak et al. “LTRACK: Stealthy Tracking of Mobile Phones in LTE”, USENIX Security 2022.
**Y. Michalevsky et al. “PowerSpy: Location tracking using mobile device power analysis”, USENIX Security 2015.

## Slide 3: RCS MITM and File Transfer Vulnerabilities (1) CVD-2023-0075
MITM 1
1. RCS MITM Attack
Message impersonation, interception, modification
Exploits unprotected RCS traffic over cellular/Wi-Fi
Methods: Malicious VPN; ARP/DHCP/DNS spoofing
Outcome: GSMA/3GPP to mandate TLS/IPsec with proper certificate validation on RCS access interface (Gm, Mb)
RCS Messaging & File Transfer Architecture
MITM 2
Notes: In this paper, we introduce UMA+, an unauthorized multiangulation
attack that resolves such untouched yet critical
challenges of the prior attacks (§4). UMA+ shares general
key concepts of the unauthorized localization attack. UMA+
utilizes multiangulation as a localization method, which is
based on Angle of Arrival (AoA) measurement.
UMA+ tackles the challenges by taking advantage of the
following contributions:
(1) We present a bearer-knocking attack, which is to obtain
the victim’s temporary identifier regardless of the UE’s
status (§5). In this attack, we monitor the dedicated control
channel for the voice call and SMS signaling, instead of relying
on the silent calls and monitoring the paging channel.
(2) We propose a power-boosting attack, which enforces
UE to increase transmission power (§6). This attack mainly
exploits the transmit power control (TPC) command which
is delivered without any security protection. Therefore, with
the help of signal overshadowing attack [39], we inject the
manipulated TPC command into the victim UE. By doing
this, the attacker can detect the victim’s uplink signal, which
is undetectable without the power-boosting attack.
(3) Lastly, we analyze the impact of a cellular repeater to the
unauthorized localization attack (§7). Based on the analysis,
we establish a proper strategy for differentiating the signal
between the victim and the repeater. This strategy examines
the variations in signal strength of the UE and repeater after
the power-boosting attack to identify the UE’s signal.
Background: Transmit Power Control in LTE
In LTE radio network, eNB (base station) controls the uplink transmission power of UE (User Equipment) to handle network capacity and signal interference. To control uplink transmission power, eNB sends TPC (Transmit Power Control) command through DCI (Downlink Control Indicator) messages after random access procedure (i.e., PRACH). After receiving TPC command, UE adjusts its uplink transmission power with a closed-loop power control algorithm. With TPC command, eNB controls both control and data channels on the uplink (i.e., PUCCH and PUSCH).
Generally, the closed-loop power control algorithm adopts the accumulated power control that follows gradually changed as defined below table up to 23 dBm. The table shows uplink power control in PUSCH (i.e., ∆_𝑷𝑼𝑺𝑪𝑯 according to TPC command in DCI message).
TPC command in DCI msg.
0
1
2
3
Accumulated ∆_𝑷𝑼𝑺𝑪𝑯 (dB)
-1
0
+1
+3
Please refer to 3GPP TS 26.213.
Background: Uplink Scheduling in LTE
For radio communication in LTE, eNB allocates uplink resources for each UE through DCI messages. Over the downlink channel, eNB broadcasts DCI format 0 message that consists of the target RNTI, resource allocation for uplink data (i.e., PUSCH scheduling), and TPC command for PUSCH, etc. Each UE receives DCI 0 message corresponding to its RNTI and transmits its uplink data after 4 milliseconds over the allocated frequency area in the uplink channel. Uplink scheduling is required to guarantee radio channel quality and fair access to network resources.
Please refer to 3GPP TS 26.212.
Vulnerability
We found the vulnerability of transmission power control and uplink scheduling in the LTE radio network. DCI messages used for uplink transmission power control and scheduling are delivered to UE by eNB over the air. At this time, eNB transmits DCI messages without any security protection (i.e., encryption or integrity check). In other words, any authentication process is not performed to control UE’s transmission power and allocate radio resources. Therefore, anyone can eavesdrop and forge the transmission power control and uplink scheduling.
Implementation
We implemented an attack manipulating transmission power control and uplink scheduling. Since there is no security protection for transmission power control, we could compromise the radio control mechanism by exploiting the signal overshadowing attack*. The key idea is to inject manipulated subframes that contain DCI format 0 message to the target UE. In manipulated DCI 0 message, TPC is set to increase or decrease the target’s transmission power and uplink resource is arbitrarily allocated without eNB’s intention.
First, we identify the radio configuration of legitimate eNB to mimic its downlink subframe. The configuration includes target PCI (Physical Cell Identification), channel bandwidth, PHICH (Physical channel HybridARQ Indicator Channe) configuration, cyclic prefix and transmission mode of eNB. This configuration can be obtained by decoding MIB (Master Information Block), PSS (Primary Synchronization Signal), and SSS (Secondary Synchronization Signal) that are broadcasted by eNB.
Then, we generate a downlink subframe based on the radio configuration of eNB to manipulate the radio control mechanism. The downlink subframe includes a malicious DCI 0 message and it consists of the target RNTI, arbitrary scheduled uplink transmission information, and the TPC command having a value of 3 or 0 to increase/decrease the uplink transmission power.
Finally, the manipulated subframe is injected into the appropriate subframe number (i.e., signal overshadowing) on the downlink channel. In our work, we inject the manipulated subframe to subframe number 9 to minimize the impact on the target UE’s LTE service, but an attacker can exploit any subframe number to inject malicious DCI message. In addition, we repeatedly conduct signal overshadowing into every subframe number 9 to continuously allocate uplink resources and overcome the transmission power control from eNB.
Evaluation
We examined our attack in the industry-grade LTE network, AMARI Callbox Classic, and commercial LTE network to demonstrate the attack feasibility. As the target UE and signal generator (i.e., subframe injector), Samsung Galaxy S10 5G and USRP X310 are used, respectively.
First, we injected manipulated DCI 0 having a value of TPC command 3 and arbitrary resource allocation. In the result, we found that the transmission power of PUSCH increases up to 23dBm (i.e., maximum uplink transmission power) and UE continuously transmits the uplink signal over arbitrarily allocated resources. We figured out that BLER (Block Error Rate) of uplink decoding in eNB on AMARI Callbox Classic significantly increases to over 90% due to unexpected uplink transmission.
In addition, when we injected a value of TPC command 0, the uplink transmission power of UE continuously decreases. Then, UE is disconnected from the radio network and tries to reconnect to the radio network.
Location tracking
Many researchers have studied about location tracking attacks without any privileges in LTE networks*. In their works, an unprivileged attacker first identifies the target’s uplink signal and measures the ToA (Time of Arrival) or AoA (Angle of Arrival) of the uplink signal. Then, based on the measurement, the attacker estimates the location of the target (i.e., uplink signal source).
However, unfortunately, they overlooked the case that the uplink signal is undetectable (i.e., real-world challenges). When the attacker traces the location of UE in the real-world environment, the target’s uplink signal might be undetectable. For example, when UE is located close to eNB, UE transmits its uplink data with low signal power due to high channel quality with eNB**. If the target’s uplink signal is undetectable due to low transmission power, the attacker cannot estimate the target’s location.
To solve such problems during location tracking, the attacker should boost the uplink transmission power of the target UE. By exploiting this vulnerability, the attacker can boost UE’s transmission power without the target’s recognition and fully perform a stealthy location tracking attack.
Denial of Service (DoS)
By exploiting this vulnerability, an attacker can perform DoS attacks on LTE radio networks in two ways: 1) Network-bursting, and 2) Cancelling-out.
Network-bursting is an attack that compromises radio network capability by forcing all UEs connected to the same eNB to increase their uplink transmission power or transmit the uplink signal over unadmitted resources. If the attacker performs network-bursting on an eNB with many connected UEs, the hardware capability of the eNB, such as the antenna and signal processor, can be destroyed. In addition, when the eNB receives unexpected uplink data that a number of UEs transmit according to arbitrarily allocated resources by the attacker, the BLER is significantly increased. This scheduling corruption by multiple UEs might cause Distributed DoS and affect the network's capability. We confirmed that VoLTE service of two UEs connected to eNB on AMARI Callbox is terminated by force due to high BLER when we manipulate transmission power and resource allocation for both UEs.
Cancelling-out exploits this vulnerability to make the UE unable to communicate with the eNB. By repeatedly injecting manipulated DCI 0, including a value of TPC command 0, to the target UE, the attacker can cause radio communication failure for the target. Although the radio connection would be re-established and the target's RNTI would change after one attack, the attacker can trace the target’s RNTI based on previous identity tracking attacks* and retry the cancelling-out attack with the target’s RNTI value.
*S. Kumar et al. “LTE radio analytics mad easy and accessible”, ACM SIGCOMM 2014.
*M. Kotuliak et al. “LTRACK: Stealthy Tracking of Mobile Phones in LTE”, USENIX Security 2022.
**Y. Michalevsky et al. “PowerSpy: Location tracking using mobile device power analysis”, USENIX Security 2015.

## Slide 4: RCS MITM and File Transfer Vulnerabilities (2) CVD-2023-0075
2. RCS File Transfer URL Tampering Attack
UE information leakage; UE storage and data depletion; DDoS of victim Server
Exploits absence of thumbnail URL validation in SIP MESSAGE XML body
Attacker UE sends to victim XML body with manipulated thumbnail URL pointing to arbitrary Server instead of RCS Content Server
Victim UE automatically (no user action) accesses thumbnail URL, sending HTTP GET to arbitrary Server
Outcome: TBD
UE Storage & Data Depletion
DDoS of Victim Server
UE Information Leakage
Notes: In this paper, we introduce UMA+, an unauthorized multiangulation
attack that resolves such untouched yet critical
challenges of the prior attacks (§4). UMA+ shares general
key concepts of the unauthorized localization attack. UMA+
utilizes multiangulation as a localization method, which is
based on Angle of Arrival (AoA) measurement.
UMA+ tackles the challenges by taking advantage of the
following contributions:
(1) We present a bearer-knocking attack, which is to obtain
the victim’s temporary identifier regardless of the UE’s
status (§5). In this attack, we monitor the dedicated control
channel for the voice call and SMS signaling, instead of relying
on the silent calls and monitoring the paging channel.
(2) We propose a power-boosting attack, which enforces
UE to increase transmission power (§6). This attack mainly
exploits the transmit power control (TPC) command which
is delivered without any security protection. Therefore, with
the help of signal overshadowing attack [39], we inject the
manipulated TPC command into the victim UE. By doing
this, the attacker can detect the victim’s uplink signal, which
is undetectable without the power-boosting attack.
(3) Lastly, we analyze the impact of a cellular repeater to the
unauthorized localization attack (§7). Based on the analysis,
we establish a proper strategy for differentiating the signal
between the victim and the repeater. This strategy examines
the variations in signal strength of the UE and repeater after
the power-boosting attack to identify the UE’s signal.
Background: Transmit Power Control in LTE
In LTE radio network, eNB (base station) controls the uplink transmission power of UE (User Equipment) to handle network capacity and signal interference. To control uplink transmission power, eNB sends TPC (Transmit Power Control) command through DCI (Downlink Control Indicator) messages after random access procedure (i.e., PRACH). After receiving TPC command, UE adjusts its uplink transmission power with a closed-loop power control algorithm. With TPC command, eNB controls both control and data channels on the uplink (i.e., PUCCH and PUSCH).
Generally, the closed-loop power control algorithm adopts the accumulated power control that follows gradually changed as defined below table up to 23 dBm. The table shows uplink power control in PUSCH (i.e., ∆_𝑷𝑼𝑺𝑪𝑯 according to TPC command in DCI message).
TPC command in DCI msg.
0
1
2
3
Accumulated ∆_𝑷𝑼𝑺𝑪𝑯 (dB)
-1
0
+1
+3
Please refer to 3GPP TS 26.213.
Background: Uplink Scheduling in LTE
For radio communication in LTE, eNB allocates uplink resources for each UE through DCI messages. Over the downlink channel, eNB broadcasts DCI format 0 message that consists of the target RNTI, resource allocation for uplink data (i.e., PUSCH scheduling), and TPC command for PUSCH, etc. Each UE receives DCI 0 message corresponding to its RNTI and transmits its uplink data after 4 milliseconds over the allocated frequency area in the uplink channel. Uplink scheduling is required to guarantee radio channel quality and fair access to network resources.
Please refer to 3GPP TS 26.212.
Vulnerability
We found the vulnerability of transmission power control and uplink scheduling in the LTE radio network. DCI messages used for uplink transmission power control and scheduling are delivered to UE by eNB over the air. At this time, eNB transmits DCI messages without any security protection (i.e., encryption or integrity check). In other words, any authentication process is not performed to control UE’s transmission power and allocate radio resources. Therefore, anyone can eavesdrop and forge the transmission power control and uplink scheduling.
Implementation
We implemented an attack manipulating transmission power control and uplink scheduling. Since there is no security protection for transmission power control, we could compromise the radio control mechanism by exploiting the signal overshadowing attack*. The key idea is to inject manipulated subframes that contain DCI format 0 message to the target UE. In manipulated DCI 0 message, TPC is set to increase or decrease the target’s transmission power and uplink resource is arbitrarily allocated without eNB’s intention.
First, we identify the radio configuration of legitimate eNB to mimic its downlink subframe. The configuration includes target PCI (Physical Cell Identification), channel bandwidth, PHICH (Physical channel HybridARQ Indicator Channe) configuration, cyclic prefix and transmission mode of eNB. This configuration can be obtained by decoding MIB (Master Information Block), PSS (Primary Synchronization Signal), and SSS (Secondary Synchronization Signal) that are broadcasted by eNB.
Then, we generate a downlink subframe based on the radio configuration of eNB to manipulate the radio control mechanism. The downlink subframe includes a malicious DCI 0 message and it consists of the target RNTI, arbitrary scheduled uplink transmission information, and the TPC command having a value of 3 or 0 to increase/decrease the uplink transmission power.
Finally, the manipulated subframe is injected into the appropriate subframe number (i.e., signal overshadowing) on the downlink channel. In our work, we inject the manipulated subframe to subframe number 9 to minimize the impact on the target UE’s LTE service, but an attacker can exploit any subframe number to inject malicious DCI message. In addition, we repeatedly conduct signal overshadowing into every subframe number 9 to continuously allocate uplink resources and overcome the transmission power control from eNB.
Evaluation
We examined our attack in the industry-grade LTE network, AMARI Callbox Classic, and commercial LTE network to demonstrate the attack feasibility. As the target UE and signal generator (i.e., subframe injector), Samsung Galaxy S10 5G and USRP X310 are used, respectively.
First, we injected manipulated DCI 0 having a value of TPC command 3 and arbitrary resource allocation. In the result, we found that the transmission power of PUSCH increases up to 23dBm (i.e., maximum uplink transmission power) and UE continuously transmits the uplink signal over arbitrarily allocated resources. We figured out that BLER (Block Error Rate) of uplink decoding in eNB on AMARI Callbox Classic significantly increases to over 90% due to unexpected uplink transmission.
In addition, when we injected a value of TPC command 0, the uplink transmission power of UE continuously decreases. Then, UE is disconnected from the radio network and tries to reconnect to the radio network.
Location tracking
Many researchers have studied about location tracking attacks without any privileges in LTE networks*. In their works, an unprivileged attacker first identifies the target’s uplink signal and measures the ToA (Time of Arrival) or AoA (Angle of Arrival) of the uplink signal. Then, based on the measurement, the attacker estimates the location of the target (i.e., uplink signal source).
However, unfortunately, they overlooked the case that the uplink signal is undetectable (i.e., real-world challenges). When the attacker traces the location of UE in the real-world environment, the target’s uplink signal might be undetectable. For example, when UE is located close to eNB, UE transmits its uplink data with low signal power due to high channel quality with eNB**. If the target’s uplink signal is undetectable due to low transmission power, the attacker cannot estimate the target’s location.
To solve such problems during location tracking, the attacker should boost the uplink transmission power of the target UE. By exploiting this vulnerability, the attacker can boost UE’s transmission power without the target’s recognition and fully perform a stealthy location tracking attack.
Denial of Service (DoS)
By exploiting this vulnerability, an attacker can perform DoS attacks on LTE radio networks in two ways: 1) Network-bursting, and 2) Cancelling-out.
Network-bursting is an attack that compromises radio network capability by forcing all UEs connected to the same eNB to increase their uplink transmission power or transmit the uplink signal over unadmitted resources. If the attacker performs network-bursting on an eNB with many connected UEs, the hardware capability of the eNB, such as the antenna and signal processor, can be destroyed. In addition, when the eNB receives unexpected uplink data that a number of UEs transmit according to arbitrarily allocated resources by the attacker, the BLER is significantly increased. This scheduling corruption by multiple UEs might cause Distributed DoS and affect the network's capability. We confirmed that VoLTE service of two UEs connected to eNB on AMARI Callbox is terminated by force due to high BLER when we manipulate transmission power and resource allocation for both UEs.
Cancelling-out exploits this vulnerability to make the UE unable to communicate with the eNB. By repeatedly injecting manipulated DCI 0, including a value of TPC command 0, to the target UE, the attacker can cause radio communication failure for the target. Although the radio connection would be re-established and the target's RNTI would change after one attack, the attacker can trace the target’s RNTI based on previous identity tracking attacks* and retry the cancelling-out attack with the target’s RNTI value.
*S. Kumar et al. “LTE radio analytics mad easy and accessible”, ACM SIGCOMM 2014.
*M. Kotuliak et al. “LTRACK: Stealthy Tracking of Mobile Phones in LTE”, USENIX Security 2022.
**Y. Michalevsky et al. “PowerSpy: Location tracking using mobile device power analysis”, USENIX Security 2015.