## Slide 1: Reply LS Regarding AKA Protocols

## Slide 2: Overview
Review of LS from ITU-T Study Group 17 and previous reply LS
Discuss next step

## Slide 3: LS from ITU at SA3#113 (S3-234497)
LS on the proposal for a new work item: Guidelines for increasing security of the AKA protocols in IMT-2020 and beyond.
For information, discussion
This liaison statement requests 3GPP SA3 to provide comments about a new work item proposal on “Guidelines for increasing security of the AKA protocols in IMT-2020 and beyond” in ITU-T Study Group 17.
ITU-T Study Group 17 in Q2/17 which studies security threats and challenges introduced by the emerging network technologies received a new work item proposal on “Guidelines for increasing security of the AKA protocols in IMT-2020 and beyond”.
Since AKA-protocols were developed by 3GPP (ref.: 3GPP TS 33.501, 3GPP TR 33.846), SG17 kindly requests 3GPP SA3 to provide comments about this proposal which will be taken into account when considering the establishment of this new work item in SG17 at its next meeting.
Notes: SA3 received an LS at SA3#113 (Chicago) from ITU-T Study Group 17 on the proposal they received for a new work item: Guidelines for increasisn security of the AKA protocols in IMT-2020 and beyond.
This LS stated that it was for information, discussion but in the abstract, they specifically request that SA3 provide comments about this new work item proposal. Since AKA-protocols were developed by 3GPP.

## Slide 4: Summary of Proposal (from S3-234497)
Draft Recommendation ITU-T X.XXXX identifies threats in 5G-AKA (EAP-AKA’) protocols, which are used in International Mobile Telecommunications-2020 (IMT-2020) systems. This Draft Recommendation briefly reviews known attacks, potential threats and provides guidelines to mitigate threats in IMT-2020 and beyond.
Contents
Scope
References
Definitions
Abbreviations and Acronyms
Conventions
Overview
Authentication in 5G mobile networks
Linkability attacks
How to mitigate threats
Guidelines for increasing security of the AKA protocols in IMT-2020 and beyond
Notes: This discussion will only cover the overview, attacks, mitigations, and proposed guidelines.

## Slide 5: 6. Overview (from S3-234497)
6 Overview
The security of communication between telephony subscribers and their service providers requires mutual authentication and key agreement. In 5G systems, these requirements are fulfilled by either EAP-AKA’ or 5G-AKA, both Authentication and Key Agreement (AKA) protocols. EAP-AKA’ and 5G-AKA are quite similar with identical message flows but with minor differences in the way various keys get derived. Therefore, only 5G-AKA is considered in this paper.
6.1 5G-AKA protocol
See [b-3GPP TS 33.501], [b- Khan]
TBD

## Slide 6: 8. Linkability attacks (from S3-234497)
8.1 The LFM attack
In the Linkability of Failure Message attack (the LFM attack) (see [b-3GPP TR 33.846], [b‑Arapinis]), the attacker can detect the presence of a victim subscriber, in one of his monitored areas.
The active attacker needs to have previously intercepted one legitimate authentication request message containing the pair (RAND, AUTN) sent by the network to UE. The captured authentication request can be replayed by the adversary each time he wants to check the presence of UE in a particular area. In fact, thanks to the error messages, the adversary can distinguish any UE from the one the authentication request was originally sent to. On reception of the replayed authentication challenge and authentication vectors (RAND, AUTN), the victim UE successfully verifies the MAC and sends a synchronisation failure message. However, the MAC verification fails when executed by any other UE, and as a result a MAC failure message is sent. The implementation of few false base stations would then allow an attacker to trace the movements of a victim UE, resulting in a breach of the subscriber's untraceability.
Figure 2: LFM attack
Notes: There are 3 attacks described.
The first is the Linkability of Failure Message (LFM) attack. In this attack, an active attacker replays a previously intercepted authentication request message containing the pair (RAND, AUTN) sent by the network to the UE. The victim UE will respond by verifying the MAC and sending a synchronization failure message. All other UEs will respond with a MAC failure message, allowing the adversary to determine the presence of the target UE in the given area.
The adversary can replay the authentication request each time they want to check the presence of the target UE in a particular area.

## Slide 7: 8. Linkability attacks (from S3-234497)
8.2 The SUCI replay attack
In the SUCI replay attack (see [b-3GPP TR 33.846], [b-Fouque]) the attacker can detect the presence of a victim subscriber, in one of his monitored areas.
The attacker records a SUCI that is used over the radio interface by a UE. Next, the attacker sets up a base station in some location and actively changes the registration request of users registering to this base station. If some UE’ makes a registration request to this false base station operated as a relay by the same attacker, the attacker can modify registration request message of UE’ by exchanging the SUCI’ used in this request by the previously captured SUCI of UE. The modified request is forwarded to the network. The attacker observes whether a successful AKA run is performed, and the network accepts the registration request. If so, then UE’ needs to be the same as UE. The implementation of few false base stations would then allow an attacker to trace the movements of a victim UE, resulting in a breach of the subscriber's untraceability.
Figure 3: SUCI replay attack
Notes: The second attack is the SUCI replay attack.
The attacker records a target UE SUCI used over the radio interface. The active attacker then sets up a base station and uses it to actively change the registration requests of users that register to it. If the attacker changes the SUCI in the registration requests to the previously captured SUCI, they only need to observe whether the AKA run was successful or not to determine if that UE is the same as the victim UE. This allows the attacker to trace the movements of a victim UE.

## Slide 8: 8. Linkability attacks (from S3-234497)
8.3 The SUPI check attack
In the SUPI check attack (see [b-3GPP TR 33.846]), the attacker can determine whether a valid SUPI belongs to the victim subscriber or not.
At the beginning of the attack, the adversary has some value of SUPI’ that he wants to check and generates SUCI’ corresponding to it. Next, his actions are the same with SUCI replay attack. The attacker intercepts SUCI sent by the subscriber and changes it to SUCI’. Then he observes whether a successful AKA run is performed. If so, SUPI’ needs to be the same as SUPI of victim subscriber.
Figure 3: SUPI check attack
Notes: The 3rd attack is the SUPI check attack.
The attacker has a SUPI that they want to check and generates a corresponding SUCI. They then proceed as they did in the SUCI replay attack by changing the intercepted registration requests and observing whether the AKA run is successful.

## Slide 9: 9. How to mitigate threats (from S3-234497)
9 How to mitigate threats
TBD
Problem of mitigating these attacks can be solved by adding UE’s random value to the argument of the functions . As a random value, an ephemeral public key, which is x-coordinate of the elliptic curve point from ECIES scheme [b-3GPP TS 33.501], can be used. Both sides random values provide replay protection. The same method is used in SIGMA-like protocols [b-Krawczyk], for example TLS 1.3 [b‑IETF RFC 8446] and IKEv2 [b-IETF RFC 7296] protocols. The Figure 5 shows a possible modification of 5G-AKA protocol.
Notes: The proposal suggests mitigating these attacks by adding random values to both sides of the protocol to provide replay protection.

## Slide 10: 9. How to mitigate threats (from S3-234497)
Figure 1: 5G-AKA protocol
Figure 5: modified 5G-AKA protocol
Notes: The proposal includes a diagram showing the proposed changes to the 5G AKA protocol

## Slide 11: 10. Guidelines for increasing security of AKA protocols in IMT-2020 and beyond (from S3-234497)
10 Guidelines for increasing security of the AKA protocols in IMT-2020 and beyond
It is recommended to add random value on the UE side in 5G-AKA (EAP-AKA’) protocols to mitigate replay attacks, namely the LFM attack, the SUCI replay attack and the SUPI check attack. X-coordinate of the elliptic curve point from ECIES scheme can be used as a random value.
Notes: Text from guidelines: It is recommended to add random value on the UE side in 5G-AKA (EAP-AKA’) protocols to mitigate replay attacks, namely the LFM attack, the SUCI replay attack and the SUPI check attack. X-coordinate of the elliptic curve point from ECIES scheme can be used as a random value.

## Slide 12: Reply LS (S3-235006)
Reply LS on the proposal for a new work item: Guidelines for increasing security of the AKA protocols in IMT-2020 and beyond
Action: SA3 kindly asks ITU-T Study Group 17 to take this reply into account
  SA3 would like to thank ITU-T Study Group 17 for their LS on the proposal for increasing security of the AKA protocols in IMT-2020 and beyond. SA3 will carefully study the AKA security concerns and provide an update during the next meeting cycle (i.e., during SA3#115).
  SA3 believes that the specification of AKA and its update must be done by SA3 for consistency purposes. Therefore, SA3 kindly requests ITU-T Study Group 17 not to create new guideline/specification on AKA and allow 3GPP to resolve the concerns presented in this LS.
Notes: At SA3#113, we provided the following reply LS. In this liaison statement we state that we will study the security concerns and provide an update during the next meeting cycle (this meeting).
We also express our believe that the specification AKA and its update must be done by SA3. We request that ITU-T not create new guidelines for AKA protocols and instead allow 3GPP to resolve the concerns that are presented.

## Slide 13: Suggested Next Step
Suggested reply LS to ITU-T (S3-240377):
  Title: Reply LS- Update on SA3 initial review of AKA security concerns presented in the proposal for a new work item: Guidelines for increasing security of the AKA protocols in IMT-2020 and beyond
SA3 would again like to thank ITU-T Study Group 17 for their LS on the proposal for increasing security of the AKA protocols in IMT-2020 and beyond. SA3 has carefully studied the AKA security concerns. SA3 acknowledges ITU-T’s concerns with the AKA protocols and is making plans to address them in an upcoming release.
SA3 would like to thank ITU-T Study Group 17 for allowing 3GPP to resolve these concerns and maintain the consistency of the specifications of AKA and its update remaining in SA3.
Notes: Our suggested next step to send a reply LS to ITU-T SG 17 with one of the following wordings.
US NSA is not bringing this up to make any statement for or against the proposed solution. Our concern is that this work stays in the appropriate standards organization, which in this case, is 3GPP. For this reason we have not specified how SA3 will or should address the concerns or even which release it will be addressed in. However it is important that SA3 acknowledge and address the concerns that ITU-T has raised. The last slide of this presentation that we will not go over, has additional references to other studies identifying the same or similar vulnerabilities.
Any questions?
Maybe bring up the Tdoc of the LS

## Slide 14: References (from S3-234497)
[b-ITU-T X.1254] Recommendation ITU-T X.1254 (2012), Entity authentication assurance framework.
[b-ITU-T Y.2014] Recommendation ITU-T Y.2014 (2008), Network attachment control functions in next generation networks.
[b-3GPP TR 33.846] 3GPP TS 33.846, V 1.0.0 (2021), Study on authentication enhancements in the 5G System (5GS).
[b-3GPP TS 33.102] 3GPP TS 33.102, V 17.0.0 (2022), Security architecture.
[b-3GPP TS 33.501] 3GPP TS 33.501, V 17.6.0 (2022), Security architecture and procedures for 5G System.
[b-IETF RFC 7296] IETF RFC 7296 (2014), Internet Key Exchange Protocol Version 2 (IKEv2).
[b-IETF RFC 8446] IETF RFC 8446 (2018), The Transport Layer Security (TLS) Protocol Version 1.3.
[b-Arapinis] Arapinis, M., Mancini, L.I., Ritter, E., Ryan, M.D., Golde, N., Redon, K., Borgaonkar, R. (2012). New privacy issues in mobile telephony: fix and verification. Proceedings of the 2012 ACM conference on Computer and communications security.
[b-Fouque] Fouque, P., Onete, C., Richard, B. (2016). Achieving Better Privacy for the 3GPP AKA Protocol. Proceedings on Privacy Enhancing Technologies, 2016, 255 - 275.
[b-Khan] Khan, H., Martin, K.M. (2020). A Survey of Subscription Privacy on the 5G Radio Interface - The Past, Present and Future. J. Inf. Secur. Appl., 53, 102537.
[b-Krawczyk] Krawczyk, H. (2003). SIGMA: The 'SIGn-and-MAc' Approach to Authenticated Diffie-Hellman and Its Use in the IKE-Protocols. Annual International Cryptology Conference.

## Slide 15: Additional References
Other references highlight similar concerns with AKA protocols
“A Vulnerability in 5G Authentication Protocols and its Countermeasure”, IEICE TRANS. INF. & SYST., VOL.E103–D, NO.8 AUGUST 2020, Xinxin Hu, Caixia Liu, Shuxin Liu, Jinsong Li, Xiaotao Cheng
Proposes a fix leveraging the existing 5G PKI mechanism and encrypts “redesigned” error messages with the public key of the HN.
“New Privacy Threat on 3G, 4G and Upcoming AKA Protocol”, Proceedings on Privacy Enhancing Technologies, 2019, Ravishankar Borgaon, Lucca Hirschi, Shinjo Park and Altal Shaik
Discusses an SQN vulnerability based on performing an XOR with an “Anonymity key”. This is predictable and allows an adversary to calculate the SQN. This vulnerability reveals more than location of a UE; it allows an attacker to derive usage and activity patterns about the user.
The proposed fix is to use symmetric encryption to encrypt the SQN. They key is derived from the UE key and the random in the received authentication challenge. This also fixes the pre-auth error message linkability vulnerability.
“Novel 5G Authentication Protocol to Improve the Resistance Against Active Attacks and Malicious Serving Networks” IEEE Access, April 2019, An Braeken, Madhusakna Liyanage, Pardeep Kumar and John Murphy.
Proposes including random numbers in the initial authentication request of the SN and the corresponding response of the subscriber. A new random is generated at the HN and used for derivation of final authentication parameters. This eliminates different failure messages regarding SYN failure and reduces the number of required communications phases and protocol steps.
Note: Random can now be used because USIM can perform randomized asymmetric encryption which was not true with 3G and 4G. Removing the SQNs stops desynchronization attacks (affect availability) between user and HN by sending authentication requests to user or HN.
“5G IPAKA, An Improved Primary Authentication and Key Agreement Protocol for 5G Networks” March 2022, Yuelei Xiao, Yang Wu
Proposes the following: the pre-shared key between the user equipment (UE) and the home network (HN) is replaced with a key derived from that pre-shared key; add a challenge-–response mechanism for the serving network (SN); mutual authentication and key confirmation occurs between the UE and the SN; and the message authentication code (MAC) failure procedure is replaced with a timeout mechanism on the HN.
“Toward a Secure Access to 5G Networks”, 2018 17h IEEE International Conference on Trust, Security and Privacy in Computing and Communication, 12th IEEE International Conference on Big Data Scienc and Engineering, Fuwen Liu,
Proposes using a DH Key exchange with digital signature: DH public key of serving network (SN) is signed by long term private key of home network (HN); UE then verifies the SN DH digital signature by using the pre-configured long term public key of the home network (HN) to provide authenticity of the SN DH public key.
“The 5G-AKA Authentication Protocol Privacy” A. Koutsos. (2018).
Their thesis is that it’s not possible to achieve functionality, authentication and un-linkability at the same time when using a sequence number-based protocol with no random number generation capabilities in the UE side.
Proposes the UE encrypts both Sync and MAC error messages with the public key of the HN making them indistinguishable to the adversary.