## Slide 1: Discussion on ZTS Assumptions
Johns Hopkins University APL, MITRE Corporation, National Security Agency

## Slide 2: Outline
Control Plane to cross multiple trust domains
ZTA in 5GC SBA
Enabling Monitoring and Security Evaluation
Existing 5GC functions that support eZTS
Dynamic Policy Enforcement

## Slide 3: CP Crosses Multiple Trust Domains
For NPI-NPN, MNO can have 1 to N number of NPN service providers connecting to the control plane via the SBA.
In TR 33.757 KI #1 and #2 describe how an MNO can have a 1 to N H-UPF in PNI-NPN Operational domain opening the N4 interface to all those N second parties.
ZTS is meant to be effective against insider threats by assuming an insider threat is already present, making it an ideal security paradigm for use cases that invite an N number of second parties into the 5G control plane network.
SBA crosses multiple trust domains; exposure of SBI means trust may be out of MNO control

## Slide 4: ZTA in 5G SBA
Consider this article: Ericsson: Zero trust and 5G – Realizing zero trust in networks [1]:
  “This makes it possible to implement the zero trust model in the 5G Core, where an NF service consumer (subject) requests access to an NF service producer (resource) through the SCP (PEP), and the NRF (PDP) grants or denies access”
  “Policies are created to reflect an organization’s processes and acceptable level of risk as well as the sensitivity of the targeted asset. A policy specifies the required level of protection for an object, privileges of a subject and environmental conditions that can change the allowed behavior of the subject toward the object.”
With respect to the 5GC, policies are the allowed behavior between NF service producer and NF service consumer and the PDP (e.g., NRF) and PEP (e.g., SCP) help enforce the policy
[1] https://www.ericsson.com/en/reports-and-papers/ericsson-technology-review/articles/zero-trust-and-5g

## Slide 5: ZTA in 5G SBA
ZTA serves as a holistic active defense strategy for managing risk, and complementing established information security practices.
Transition to ZTA should be gradual and thus existing functionality should be reused when possible

## Slide 6: Enabling Monitoring and Security Evaluation
Network location alone does not imply trust. The 5GS should monitor, collect information about the current state of the network in order to measure, and gain insight into the current security posture.
To enable this, minimum requirements are as follows (but not limited to):
  Support data collection from NFs and AFs (and if available, network and system logs).
  Support data collection from OAM
  Support retrieval of information from data repositories
  Support subscription to events
  Support secure communications between an Operators Security Function (OSF) and the entity collecting the data
  Support exchange of information to an OSF to process available data, provide an evaluation, and if needed create policies or relay actions that need to be taken
  Support exchange of information from an OSF to consume decisions and take actions (i.e., policy enforcement)) according to the output of the the OSF

## Slide 7: Existing 5GC NFs that may support these Requirements (NRF / SCP)
The introduction of the service communication proxy (SCP) allows indirect communication between NFs.
NRF acts as an Authorization Server (AS) when providing NF consumers access to NF services (resource servers)
  NRF can take the role of the PDP and is a natural point for enforcing security policy (i.e., data collected and evaluated is used to inform NRF of the NF state)
  From the NF producer perspective, NRF is also a natural point for performing access token introspection (RFC 7662)
SCP is a natural gateway between two trust domains and can serve as an enforcement point.
  The SCP can take the role of the PEP and provide access control functionality by requesting authorization decisions from the NRF.
An NF service consumer requests access to an NF service producer through the SCP (PEP), and the NRF (PDP) grants or denies access - This makes it possible to implement the zero trust model in the 5GC
NRF and SCP are natural security policy enforcement points

## Slide 8: Existing 5GC NFs that may support these Requirements (DCCF)
In TR 23.700-91 clause 6.9, it was proposed to decompose the NWDAF so that there is a Data Management Framework for 5GC that is separated from Analytics functions.
The Data Management Framework for 5GC uses the Consumer/Producer model of the SBA to efficiently exchange data/information of different types. This includes:
  Data retrieved from various sources (e.g. OAM, and NFs such as AMF, SMF, PCF and AF), to be used as a basis for computing analytics
  Analytics output from an NWDAF Producer sent to an NWDAF Consumer (KI#2) to support a hierarchy of NWDAF instances or sent to multiple network functions.
Need to define what data is for collection, but there is a Data Management Framework already in place for the 5GC to enable data collection

## Slide 9: Existing 5GC NFs that may support these Requirements (DCCF)
The Framework consists of the following components:
  Data Collection Coordination Function (DCCF)
  with optional DCCF Adaptor (DA)
  Messaging Framework (for Data Forwarding and Replication),
  with optional Adaptors (3CA and 3PA) to isolate the Messaging Framework
  protocol from the Data Source and the Data Consumer.
Data management framework can function as a standalone system to perform data collection.

## Slide 10: Existing 5GC NFs that may support these Requirements (NWDAF)
The NWDAF monitors the behavior of all the NFs and ensures that the NFs behave as defined.
If the NFs behave erroneously, it should be possible to detect the anomaly so that appropriate steps can be taken (e.g. an OSF could apply policies to control the potentially damaging behavior).
  The undefined behavior of the NF may be caused by internal errors such as configuration mistakes or internal data corruption. This misbehavior may impact one or more UE services based on the type of NF.
  Thus, the correlation of which NF is handling which UE data is an important aspect, such that NWDAF is enabled to conclude from the reported UE-related data, which NF may have anomalous behavior.
While the NWDAF, may not be suitable for the security monitoring, the same interfaces that are already in place for the NWDAF should be used.
There is a need to enable NWDAF-type functions to receive or request reports by NFs which help detect anomalous NF behavior.

## Slide 11: Dynamic Security Policy Enforcement
Any determination that a NF is behaving abnormally should be responded to accordingly.
It is up to Operator to determine the appropriate action (enforcement) to mitigate or correct the NF behavior.
There should be a means for the 5GS to dynamically enforce security according to operator policy
  I.e., if MNO deems NF to be misbehaving and is a threat to the network, there should be a means for MNO to gracefully mitigate the threat faced via the 5GC at any phase of NF service

## Slide 12: Summary
SBA crosses multiple trust domains (e.g., N4 interface exposed to NPN); exposure of SBI means trust may be out of MNO control
DCCF is already enabled to collect data.
NWDAF is already enabled to collect and aggregate data
NRF and SCP are natural security policy enforcement points
To support 5GS security monitoring:
  Single data points collected may not be a direct indicator of compromise and should be analyzed with other data points prior to taking mitigating action
  Assumed that an analytics engine (e.g., XDR) is in use in the operator domain
There should be a means for MNO to gracefully mitigate the threat faced by a misbehaving or anomalous NF, via the 5GS, at any phase of NF communications

## Slide 13: Thank you