## Slide 1: Discussion on AIML Data Collection
SA3#118
vivo

## Slide 2
Background - 1
RAN2 has discussed the topic of UE side data collection for UE-side model training and agreed on a TP for TR 38.843 as shown below:
  1a. UE collects and directly transfers training data to the data collection entity outside the MNO (e.g. Over-The-Top (OTT) server) for UE-side model training. No 3GPP specification impact is expected.
  1b. UE collects training data and transfers it to the server for data collection for UE-side model training (inside the MNO) and then optionally from the server for data collection for UE-side model training to the OTT server (outside the MNO).
  2 .UE collects training data and transfers it to Core Network. Core Network transfers the training data to the server for data collection for UE-side model training/OTT server.
  3. UE collects training data and transfers it to OAM. OAM transfers the training data to the server for data collection for UE-side model training/OTT server.
  RAN#105 way forward and requirements
RAN has agreed to the following requirements for data collection for UE sided model training for standardized solution (if standardized) (i.e. Option 1b, 2, 3). Option 1a is not precluded. The data collected is secured and data integrity and confidentiality for that data is ensured. User data privacy, anonymity and user consent is respected. The MNO has full control of the standardized data collection transfer process and can manage data transfer to the server for UE-side data collection, without the need of SLA for this purpose. This includes initiating, terminating, and fully managing data transfer. MNO has full visibility for standardized data. The design is futureproof and extendable. FFS/study if and how to handle non-standardized data (i.e. partial visibility). FFS controllability on data collection Standardized Solutions should follow the principle of aiming to minimize air interface overhead and impact to NW operation

## Slide 3
Background - 2
RAN sends LS RP-242389 and asks TSG SA to initiate the work and request to provide inputs on solutions 1b, 2, and 3 by RAN#106. Following the way forward and requirements outlined in RAN#105, it is evident that requirements 1 Data integrity and confidentiality and 2 Privacy, anonymity and user consent are closely associated with the security aspect.
This paper is to
  Provide draft analysis for solution 1b, 2 and 3 in terms of MNO controllability, visibility and user data privacy & user consent

## Slide 4
Analysis for Option 1b
Option Aspect | Option 1b)
First termination entity | Server for data collection for UE-side model training
AI/ML-specific Data Transfer Path | UE ->Server for data collection for UE-side model training/OTT server(Note 4)
UP/CP tunnel | UP tunnel
Protocol layer for data transfer | Application layer
Controllability of MNO on data transfer (Note 1) | FFS: level of controllability (Note 5)
Solution for network controllability | Example: per PDU sessions
Possible Options for Visibility of data content in MNO and Data format (Note 2, Note 3) | FFS on level of visibility (Note 5)
Impacted WGs | SA2, SA3, RAN2, RAN3, CT1
Note 1: Full controllability: The MNO can manage data transfer to the server for UE-side data collection, without the need of SLA. This includes initiating, terminating, and fully managing data transfer. Note 2: Visibility of data content signifies that the MNO can, at least, be aware of, access, and comprehend the data without the need of SLA. Note 3: The following options are identified to realize the different levels of data content visibility to the MNO: Full visibility for standardized data content. Partial visibility for partially standardized data content (e.g. UE proprietary information can be included transparently together with the standardized data message). No standardized visibility (e.g. only UE proprietary information can be included transparently). Note 4: The potential involvement of NF or other higher layers entities/functionalities should be discussed in other WGs. Impact on the OTT server is not in the scope of RAN2 discussion. Note 5: RAN2 cannot reach consensus on the level of MNO controllability and visibility possible via solution 1b without input from SA groups. | 
RAN2 agreement for Option 1b
An example of call flow for Option 1b
Data integrity and confidentiality | Privacy, anonymity and user consent
Out of SA3 and rely on application layer security | Associated with MNO controllability and MNO visibility (whether MNO is data controller, and whether user consents reported data) The MNO will handle user consent, and requirements in Annex V of TS 33.501 is applied if DCAF(Data collection server) is within MNO domain. Out of SA3 if DCAF is within 3rd party domain.
Analysis for option 1b

## Slide 5
Option Aspect | Option 2)
First termination entity | Inside the CN
AI/ML-specific Data Transfer Path | UE-> CN -> Server for data collection for UE-side model training/OTT server (Note 4)
UP/CP tunnel | CP tunnel (provided that the data volume remains within the NAS signalling capacity) FFS: UP tunnel (Note 7)
Protocol layer for data transfer | NAS layer for CP tunnel FFS: the protocol layer for UP tunnel
Controllability of MNO on data transfer (Note 1) | Full controllability
Solution for network controllability | Via NAS procedure or FFS other procedures
Possible Options for Visibility of data content in MNO and Data format (Note 2, Note 3) | Opt A) Full visibility for standardized data contents. Opt B) Partial visibility for partially standardized data contents. (Note 6) Opt C) No standardized visibility. (Note 6)
Impacted WGs | SA2, SA3, RAN3, RAN2, CT1 and CT3
Note 1: Full controllability: The MNO can manage data transfer to the server for UE-side data collection, without the need of SLA. This includes initiating, terminating, and fully managing data transfer. Note 2: Visibility of data content signifies that the MNO can, at least, be aware of, access, and comprehend the data without the need of SLA. Note 3: The following options are identified to realize the different levels of data content visibility to the MNO: Full visibility for standardized data content. Partial visibility for partially standardized data content (e.g. UE proprietary information can be included transparently together with the standardized data message). No standardized visibility (e.g. only UE proprietary information can be included transparently). Note 4: The potential involvement of NF or other higher layers entities/functionalities should be discussed in other WGs. Impact on the OTT server is not in the scope of RAN2 discussion. Note 6: RAN2 has not concluded on the need for partial and no visibility options. Note 7: RAN2 could not reach consensus on the feasibility of UP solution in options 2 and 3. | 
RAN2 agreement for Option 2
An example of call flow for Option 2
Data integrity and confidentiality | Privacy, anonymity and user consent
CP tunnel: UE->AMF: reuse NAS security AMF->consumer: reuse SBA security UP tunnel: The same with 1b | As MNO has controllability and visibility (MNO is data controller and user consents reported data), the requirements in Annex V of TS 33.501 is applied. The CN NFs (e.g. AMF, DCNF) can be user consent enforcement point.
Analysis for option 2
Analysis for Option 2

## Slide 6
Option Aspect | Option 3)
First termination entity | Inside OAM domain
AI/ML-specific Data Transfer Path | UE-> gNB->OAM -> Server for data collection for UE-side model training/OTT server (Note 4)
UP/CP tunnel | CP tunnel (provided that the data volume remains within the RRC signalling capacity) FFS: UP tunnel (Note 7)
Protocol layer for data transfer | RRC layer for CP tunnel FFS: the protocol layer for UP tunnel
Controllability of MNO on data transfer (Note 1) | Full controllability
Solution for network controllability | Via RRC procedure
Possible Options for Visibility of data content in MNO and Data format (Note 2, Note 3) | Opt A) Full visibility for standardized data contents. Opt B) Partial visibility for partially standardized data contents. (Note 6) Opt C) No standardized visibility. (Note 6)
Impacted WGs | RAN2, RAN3, SA3, SA5, SA2
Note 1: Full controllability: The MNO can manage data transfer to the server for UE-side data collection, without the need of SLA. This includes initiating, terminating, and fully managing data transfer. Note 2: Visibility of data content signifies that the MNO can, at least, be aware of, access, and comprehend the data without the need of SLA. Note 3: The following options are identified to realize the different levels of data content visibility to the MNO: Full visibility for standardized data content. Partial visibility for partially standardized data content (e.g. UE proprietary information can be included transparently together with the standardized data message). No standardized visibility (e.g. only UE proprietary information can be included transparently). Note 4: The potential involvement of NF or other higher layers entities/functionalities should be discussed in other WGs. Impact on the OTT server is not in the scope of RAN2 discussion. Note 6: RAN2 has not concluded on the need for partial and no visibility options. Note 7: RAN2 could not reach consensus on the feasibility of UP solution in options 2 and 3. | 
RAN2 agreement for Option 3
An example of call flow for Option 3
Data integrity and confidentiality | Privacy, anonymity and user consent
CP tunnel: UE->gNB: reuse RRC security gNB->OAM->Server: out of SA3 UP tunnel: UE->gNB: reuse UP security gNB->OAM->Server: out of SA3 | As MNO has controllability and visibility (MNO is data controller and user consents reported data), the requirements in Annex V of TS 33.501 is applied. The gNB or OAM can be user consent enforcement point similar like SON/MDT procedure.
Analysis for option 3
Analysis for Option 3

## Slide 7: Summary
 | Option 1b | Option 2 | Option 3
Solution Feasibility | Y | Y (Technically Feasible) | Y (Technically Feasible)
Data integrity and confidentiality | Out of 3GPP and rely on application layer security | CP tunnel: UE->AMF: reuse NAS security AMF->consumer: reuse SBA security UP tunnel: The same with 1b | CP tunnel: UE->gNB: reuse RRC security gNB->OAM->Server: out of SA3 UP tunnel: UE->gNB: reuse UP security gNB->OAM->Server: out of SA3
privacy, anonymity and user consent | Associated with MNO controllability and MNO visibility (whether MNO is data controller, and whether user consents reported data) The MNO will handle user consent, and requirements in Annex V of TS 33.501 is applied if DCAF(Data collection server) is within MNO domain. Out of SA3 if DCAF is within 3rd party domain. | As MNO has controllability and visibility (MNO is data controller and user consents reported data), the requirements in Annex V of TS 33.501 is applied. The CN NFs (e.g. AMF, DCNF) can be user consent enforcement point. | As MNO has controllability and visibility (MNO is data controller and user consents reported data), the requirements in Annex V of TS 33.501 is applied. The gNB or OAM can be user consent enforcement point similar like SON/MDT procedure.
Proposal
Provide the above draft analysis as SA3 inputs on solutions 1b, 2, 3 to RAN working groups
Having MNO controllability and MNO visibility of UE data are essential for user consent as the data controller has responsibility to protect user privacy and user can only consent the data reporting if only the data content is fully visible to the user.