## Slide 1: Simplifying signalling and floor control in Rel-14
Peter Haigh
CESG (UK NCSC)

## Slide 2: Outline
Overview of Rel-13 signalling and floor control security
Discussion of Rel-14 requirements
Proposal for Rel-14.

## Slide 3: Rel-13 signalling and floor control protection keys
Uplink:
  CSK protects all data
Downlink:
  CSK protects all unicast signalling traffic
  MKFC protects all multicast signalling traffic, except:
  MSCCK protects all MBMS subchannel control messages

## Slide 4: Rel-13 Key distribution
CSK (unicast signalling):
  Generated by client
  Sent to server on initial connection
MKFC (multicast signalling):
  Generated by GMS
  Sent to clients and server on group setup.
MSCCK (MBMS-specific signalling):
  Generated by server
  Sent to client on bearer activation.

## Slide 5: Rel-13 Thoughts
More complex security than seems necessary (if multicast is supported.)
Multicast security is dependent on GMS support (which doesn’t seem necessary)
CSK rekeying is not clear/possible?
Can we have a simpler model?

## Slide 6: Rel-14 Requirement
A security relationship is required between the client and MCX Server.
Needs to secure:
  Uplink unicast transmissions
  Downlink unicast transmissions
  Downlink multicast transmissions (using an MCX-Server-defined set of users).

## Slide 7: Rel-14 Requirement
A security relationship is required between the client and MCX Server.
Needs to secure:
  Uplink unicast transmissions
  Downlink unicast transmissions
  Downlink multicast transmissions (using an MCX-Server-defined set of users).
This requires server->client key distribution
Protecting initial SIP REGISTER requires client->server key distribution

## Slide 8: Rel-14 Proposal
CSK uploaded in SIP REGISTER to MCX Server (same)
Distribute MSCCK from MCX Server (same)
Distribute MKFC from MCX Server (change!)
  No need to use GMS
Allow CSK, MKFC and MSCCK to be updated by MCX Server (change!)
Suggest that we use SIP NOTIFY for key distribution for multicast signalling keys (change from MSCCK).

## Slide 9: Rel-14 Proposal – another look
The MCX client can have a number of signalling keys
It uploads the initial CSK to the MCX Server as part of SIP REGISTER.
The MCX Server can send new signalling keys down to the client as required
  Update CSK
  Download new ‘Multicast Signalling Key’ (MSK)
A more flexible, simpler model?

## Slide 10: Questions/Thoughts?