## Slide 1: Manufacturers Usage Description- IETF RFC 8250
MUD: IETF Standard: RFC 8250
The goal of MUD is to provide a means for end devices to signal to the network what sort of access and network functionality they require to properly function. The initial focus is on access control. Later work can delve into other aspects.
https://tools.ietf.org/html/rfc8520

## Slide 2: Introducing Manufacturer Usage Descriptions (MUD)
https://manufacturer.example.com/mydevice.json
A URL:
A MUD File:
The MUD Manager:
The MUD File Server:

## Slide 3: MUD-enabled enterprise network
MUD
Manager
Devices
Router or Switch
Enterprise Network
MUD
File Server
Application Server
(2) MUD
URL
(5) Device traffic filters
(1) MUD URL in DHCP transaction
(6) IP
Address
MUD-file specified Intended Usages
(3) HTTPS get URL
(4) MUD file
Update Server
Network Services
(e.g., DNS)

## Slide 4: Communicating Manufacturer Usage Descriptions
Access
Switch
forwards
Device emits
a URI
https://example.com/mud/…
MUD File Server
Device
MUD Manager
Internet
Access Switch
MUD Manager
queries
manufacturer
DHCP,
LLDP,
or 802.1X
Radius
https
Enterprise Network
Notes: Uniform Resource Identifier

## Slide 5: Applying Manufacturer Usage Descriptions
https://example.com/mud/…
MUD File Server
Device
MUD Manager
Internet
Access Switch
Radius
https
Enterprise Network
Manufacturer
JSON file returned
Devices
Segmented
IT Admin Approval
Enterprise config created
Notes: Goals Automate learning what type of device each device on the network is
Learn from manufacturer what sort of access each device requires
  Limit device access to prevent attacks!
Provide administrator control with approval
Automate onboarding for the next device that is the same type

## Slide 6: MUD’s Potential Impact on Security
gateway
MUD-enabled IoT device
Potential victim
Known malicious actor
Previously unknown malicious actor
Intended services
Communication paths between IoT device and internal/external threats blocked
MUD File Server
Compromised
Mobile device