DTS/LI-102 232-7draft V0.1.0 (2007-10)

Technical Specification

Lawful Interception (LI);

Handover Interface and

Service-Specific Details (SSD) for IP delivery;

Part 7: Service-specific details for Mobile Services

Reference

DTS/LI 102 232-7

Keywords

IP, telephony, Lawful Interception, security

ETSI

650 Route des Lucioles

F-06921 Sophia Antipolis Cedex - FRANCE

Tel.: +33 4 92 94 42 00   Fax: +33 4 93 65 47 16

Siret N° 348 623 562 00017 - NAF 742 C

Association à but non lucratif enregistrée à la

Sous-Préfecture de Grasse (06) N° 7803/88

Important notice

Individual copies of the present document can be downloaded from:
http://www.etsi.org

The present document may be made available in more than one electronic version or in print. In any case of existing or perceived difference in contents between such versions, the reference version is the Portable Document Format (PDF). In case of dispute, the reference shall be the printing on ETSI printers of the PDF version kept on a specific network drive within ETSI Secretariat.

Users of the present document should be aware that the document may be subject to revision or change of status. Information on the current status of this and other ETSI documents is available at http://portal.etsi.org/tb/status/status.asp

If you find errors in the present document, please send your comment to one of the following services:
http://portal.etsi.org/chaircor/ETSI_support.asp

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© European Telecommunications Standards Institute 2007.

All rights reserved.

DECTTM, PLUGTESTSTM and UMTSTM are Trade Marks of ETSI registered for the benefit of its Members.
TIPHONTM and the TIPHON logo are Trade Marks currently being registered by ETSI for the benefit of its Members. 3GPPTM is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners.

Contents

Intellectual Property Rights	4

Foreword	4

Introduction	4

1	Scope	5

2	References	5

3	Definitions and abbreviations	5

3.1	Definitions	5

3.2	Abbreviations	6

4	General	6

4.1	Approach	6

4.2	Reference model	6

5	Headers, data exchange and networks	7

5.1	Approach	7

5.2	Structures	7

6	Intercept Related Information (IRI) and Content of Communication (CC)	7

6.1	Definition of IRI events and CC	7

6.2	IRI format	7

6.3	CC format	7

A.1	Note on integrating ASN.1 structures	8

A.1.1	Header field mappings	8

A.1.2	CIN allocation	9

A.2	Suggested changes to TS 102 232-1 [2] for circuit-switched IRI	9

History	11

# Intellectual Property Rights

IPRs essential or potentially essential to the present document may have been declared to ETSI. The information pertaining to these essential IPRs, if any, is publicly available for ETSI members and non-members, and can be found in ETSI SR 000 314: "Intellectual Property Rights (IPRs); Essential, or potentially Essential, IPRs notified to ETSI in respect of ETSI standards", which is available from the ETSI Secretariat. Latest updates are available on the ETSI Web server (http://webapp.etsi.org/IPR/home.asp).

Pursuant to the ETSI IPR Policy, no investigation, including IPR searches, has been carried out by ETSI. No guarantee can be given as to the existence of other IPRs not referenced in ETSI SR 000 314 (or the updates on the ETSI Web server) which are, or may be, or may become, essential to the present document.

# Foreword

This Technical Specification (TS) has been produced by ETSI Technical Committee Lawful Interception (LI).

The present document is part 6 of a multi-part deliverable. Full details of the entire series can be found in TS 102 232 part 1 [2].

# Introduction

The TS 102 232 series of standards aims to provide a common delivery interface for lawfully-intercepted material from a wide range of services. The aim of the present document is to increase the range of services to which the TS 102 232 interface applies, by including services from 3GPP TS 33.108 [3] within the TS 102 232 delivery framework.

# 1	Scope

The present document specifies an approach for the handover of the lawfully-intercepted information that is defined in 3GPPP TS 33.108 [3]. The present document uses the handover techniques defined in TS 102 232-1 [2]. In this way, the present document allows additional services to be delivered through a common interface.

Specifically, the scope of the present document includes the handover of lawfully-intercepted information from the following parts of 3GPP TS 33.108 [3]:

- IRI from the mobile circuit-switched domain (3GPP TS 33.108 [3] clause 5) . CC from the mobile circuit-switched domain is not covered by the present document.

- IRI and CC from the mobile packet-switched domain (3GPP TS 33.108 [3] clause 6).

- IRI and CC from the multi-media domain (3GPP TS 33.108 [3] clause 7)

The present document does not override or supersede any specifications or requirements in 3GPP TS 33.108 [3].

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

References are either specific (identified by date of publication and/or edition number or version number) or non-specific.

For a specific reference, subsequent revisions do not apply.

For a non-specific reference, the latest version applies.

Referenced documents which are not found to be publicly available in the expected location might be found at http://docbox.etsi.org/Reference.

NOTE:	While any hyperlinks included in this clause were valid at the time of publication ETSI cannot guarantee their long term validity.

[1]	ETSI TS 101 671: "Lawful Interception (LI); Handover interface for the lawful interception of telecommunications traffic".

NOTE:	Periodically TS 101 671 is published as ES 201 671. A reference to the latest version of the TS as above reflects the latest stable content from ETSI/TC LI.

[2]	ETSI TS 102 232-1: "Lawful Interception (LI); Handover Interface and Service-Specific Details (SSD) for IP delivery; Part 1: Handover specification for IP delivery ".

[3]	ETSI TS 133 108: Universal Mobile Telecommunications System (UMTS);3G security;Handover interface for Lawful Interception (LI) (3GPP TS 33.108)

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TS 102 232-1 [2] and TS 101 671 [1] apply.

## 3.2	Abbreviations

For the purposes of the present document, the following abbreviations apply:

ASN.1	Abstract Syntax Notation One

CC	Content of Communication

CIN	Communications Identity Number

CSP	Communications Service Provider

NOTE:	CSP covers all Access Providers, Network Operators and Service Providers.

HI1	Handover Interface 1 (for Administrative Information)

HI2	Handover Interface 2 (for Intercept Related Information)

HI3	Handover Interface 3 (for Content of Communication)

IP	Internet Protocol

IRI	Intercept Related Information

ISDN	Integrated Services Digital Network

LEA	Law Enforcement Agency

LEMF	Law Enforcement Monitoring Facility

LI	Lawful Interception

MF	Mediation Function (at CSP)

PDU	Protocol Data Unit

PSTN	Public Switched Telephone Network

RTP	Real-time Transport Protocol

SDP	Session Description Protocol

TISPAN	Telecommunications and Internet converged Services and Protocols for Advanced Networking

UDP	User Datagram Protocol

# 4	General

## 4.1	Approach

The present document forms part 7 of the TS 102 232 family of standards, in that it is a service-specific component of the TS 102 232-1 [2] framework.

3GPP TS 33.108 [3] defines the interception behaviour that leads to IRI events on the handover interface, for both the packet data domain and circuit switched domain.

## 4.2	Reference model

Figure 1: Reference model

# 5	Headers, data exchange and networks

## 5.1	Approach

TS 102 232-1 [2] describes a technique for data exchange, and specifies the headers that shall be associated with the results of interception. The present document follows TS 102 232-1 [2] regarding headers, data exchange and networks demonstrates how the header fields in TS 102 232-1 [2] can be populated in a direct and straightforward manner using the interception information available in 3GPP TS 33.108 [3].

## 5.2	Structures

IRI events from 3GPP TS 33.108 [3], for both circuit and packet switched servcies, are sent using the uMTSIRI element of IRIContents.

CC from packet switched services are sent using the uMTSCC element CCContents, which is an OCTET STRING.

# 6	Intercept Related Information (IRI) and Content of Communication (CC)

## 6.1	Definition of IRI events and CC

IRI events are defined as per 3GPP TS 33.108 [3].

## 6.2	IRI format

IRI events are defined as per 3GPP TS 33.108 [3] for both circuit and packet switched services. They are sent using the uMTSIRI element of IRIContents.

Fields which are duplicated in the 3GPP TS 33.108 [3] and TS 102 232-1 [2] structures should be populated consistently in both structures. Annex A.1 gives guidance on mapping between 3GPP TS 33.108 [3] elements and TS 102 232-1 [2] elements for IRI.

## 6.3	CC format

CC from packet switched services are sent using the uMTSCC element CCContents, which is an OCTET STRING. The OCTET STRING will be as defined in the payload element of the CC-PDU structure in 3GPP TS 33.108 [3] Annex B.4.

The information in the uLIC-header element of CC-PDU will be used to populate the header information in the LI-PS-PDU structure of TS 102 232-1 [2]. Clause A.1 gives guidance on the mapping between these elements.

Annex A (normative):
ASN.1 for IRI and CC

# A.1	Note on integrating ASN.1 structures

## A.1.1	Header field mappings

Table 1 shows how elements of the TS 102 232-1 [2] PSHeader structure should be populated from information in the 3GPP TS 33.108 [3] IRI-Parameters structure.

Table 1: 3GPP TS 33.108 [3] to TS 102 232-1 [2] PSHeader mapping

| TS 102 232-1 PSHeader element | Source from 3GPP TS 33.108 |
| --- | --- |
| lawfulInterceptionIdentifier | Copied directly from IRI-Parameters.lawfulInterceptionIdentifier |
| authorizationCountryCode | Supplied directly by the MF. |
| communicationIdentifier | See below for individual elements |
| networkIdentifier | See below for individual elements |
| operatorIdentifier | Copied directly from IRI-Parameters.networkIdentifier.operatorIdentifier |
| eTSI671NEID | Copied directly from IRI-Parameters.networkIdentifier.Network-Element-Identifier |
| communicationIdentityNumber | See clause A.1.2 |
| deliveryCountryCode | Supplied directly by the MF |
| sequenceNumber | Supplied directly by the MF |
| timeStamp | Copied from IRI-Parameters.timeStamp. This requires a conversion from HI2Operations.TimeStamp to GeneralizedTime. |

Table 2 shows how elements of the TS 102 232-1 [2] IRIPayload structure should be populated from information in the 3GPP TS 33.108 [3] structures

Table 2: 3GPP TS 33.108 [3] to TS 102 232-1 [2] IRIPayload mapping

| TS 102 232-1 IRIPayload element | Source from 3GPP TS 33.108 |
| --- | --- |
| iRIType | Inferred from UMTSIriContent |
| timeStamp | Copied from IRI-Parameters.timeStamp (assuming no aggregation of PDUs) This requires a conversion from HI2Operations.TimeStamp to GeneralizedTime. |
| iRIContents | See below for individual elements |
| uMTSIRI | See below for individual elements |
| iRI-Parameters | Copied directly from IRI-Parameters, if handing over packet domain IRI. |
| iRI-CS-Parameters | Copied directly from IRI-Paremeters, if handing over circuit switched IRI |

Table 3 shows how elements of the TS 102 232-1 [2] PSHeader structure should be populated from information in the 3GPP TS 33.108 [3] CC-PDU structure.

Table 3: 3GPP TS 33.108 [3] to TS 102 232-1 [2] mapping

| TS 102 232-1 PSHeader element | Source from 3GPP TS 33.108 |
| --- | --- |
| lawfulInterceptionIdentifier | Copied from CC-PDU.uLIC-header.lIID |
| authorizationCountryCode | Supplied directly by the MF. |
| communicationIdentifier | See below for individual elements |
| networkIdentifier | See below for individual elements |
| operatorIdentifier | Supplied directly by the MF (see 3GPP TS 33.108 [2] clause 5.2.4) |
| eTSI671NEID | Supplied directly by the MF (see 3GPP TS 33.108 [2] clause 5.2.4) |
| communicationIdentityNumber | See clause A.1.2 |
| deliveryCountryCode | Supplied directly by the MF |
| sequenceNumber | Supplied directly by the MF |
| timeStamp | Copied from CC-PDU.uLIC-header.timeStamp. This requires a conversion from HI2Operations.TimeStamp to GeneralizedTime. |

Table 4 shows how elements of the TS 102 232-1 [2] CCPayload structure should be populated from information in the 3GPP TS 33.108 [3] structures

Table 4: 3GPP TS 33.108 [3] to TS 102 232-1 [2] CCPayload mapping

| TS 102 232-1 CCPayload element | Source from 3GPP TS 33.108 |
| --- | --- |
| payloadDirection | Copied from CC-PDU.uLIC-header.t-PDU-direction. This requires a trivial translation between TPDU-direction and PayloadDirection enumerated types. |
| timeStamp | Copied from CC-PDU.uLIC-header.timeStamp. This requires a conversion from HI2Operations.TimeStamp to GeneralizedTime. |
| ccContents | See below for individual elements |
| uMTSCC | Bytes copied from CC-PDU.payload |

## A.1.2	CIN allocation

CIN allocation follows TS 102 232-1 [2] clause 5.2.4. The four charging-id bytes of the GPRS correlation number may be used as a CIN. Other CIN allocation schemes may be used subject to national agreement.

# A.2	Suggested changes to TS 102 232-1 [2] for circuit-switched IRI

EDITOR’S NOTE: In order to accommodate circuit-switched IRI traffic into the present document, the following changes are changes suggested to TS 102 232-1. Alternatively use 102 232 Part 6 (PSTN/ISDN services) and take IRIsContent from IRI-Parameters FROM HI2Operations FOR FURTHER STUDY..

IMPORTS

-- Any of the IMPORTs may be commented out if they are not used (see clause A.3)

-- from 3GPP TS 33.108 [3]

IRI-Parameters,

UmtsIRIsContent

FROM UmtsHI2Operations

{itu-t(0) identified-organization(4) etsi(0) securityDomain(2) lawfulIntercept(2) threeGPP(4) hi2(1)}

-- The relevant module (including the UMTS release and version number) needs

-- to be chosen when compiling the application.

IRI-Parameters,

UmtsCS-IRIsContent

FROM UmtsHI2CSOperations

{itu-t(0) identified-organization(4) etsi(0) securityDomain(2) lawfulIntercept(2) threeGPP(4) hi2CS(3)}

-- The relevant module (including the UMTS release and version number) needs

-- to be chosen when compiling the application.

UMTSIRI			::= CHOICE

-- This structure may be commented out if not used

{

iRI-Parameters	[0] UmtsHI2Operations.IRI-Parameters,

umtsIRIsContent	[1] UmtsIRIsContent,

...

iRI-CS-Parameters [2] UmtsHI2CSOperations.IRI-Parameters,

umtsCS-IRIsContent [3] UmtsCS-IRIsContent

}

Annex B (informative):
Bibliography

NOT REFERENCED IN SPEC ????

ETSI TR 102 503: "Lawful Interception (LI); ASN.1 Object Identifiers in Lawful Interception Specifications".

ETSI TR 102 053: "Telecommunications security; Lawful Interception (LI); Notes on ISDN lawful interception functionality".

# History

| Document history |
| --- |
| V0.0.1 | January 2007 | Proposed initial draft |
| V0.0.2 | April 2007 | Draft for Riga meeting |
| v0.0.3 | October 2007 | to TC I#16 Berlin |
| v0.1.0 | October 2007 | to SA3-LI in Seoul (clean version 0.0.3) |

# Text boxes

Source of mobile data (defined in TS 33.108 [3])

Handover interface

Law Enforcement Monitoring Facility (LEMF)

Mediation Function (MF)