## Slide 1: Solving Lawful Intercept for LIPA/SIPTO: Providing Automated Capability to Notify Law Enforcement of Small Cell Broadband Provider
Peter Musgrove
AT&T
3GPP SA3 LI, Dubrovnik, Croatia
Jan. 28, 2016

## Slide 2: LIPA and SIPTO solutions discussed to date
Place Intercept Access Point (IAP) in small cell itself
  SCF liaised this idea to multiple Standards Development Orgs (SDOs)
    No standardized solutions have yet been able to be created in 3GPP SA3 LI, ATIS WTSC LI, ETSI TC LI
  Many LI requirements difficult to meet (e.g., intercept traffic on backhaul detectable by user)
Dynamic Triggering of Interception in broadband provider by Cellular Service Provider (CSP)
  ETSI TC LI has defined generic dynamic triggering of interception capability (roughly 90% done, not yet published)
  This capability could be used to assist CSP with LI obligations when LIPA or SIPTO is used
  However, this new capability would require investment by broadband provider

## Slide 3: New Direction Needed
Recognize downsides experienced by law enforcement
  When user chooses to use Wi-fi when connected to a small cell, law enforcement may lose target communications if only the CSP has the LI obligation
Assist law enforcement with overcoming downsides
  What if CSP provided law enforcement with automated notification of the identity of the broadband provider for targets using small cells?
Could this result in a WIN-WIN for CSPs and Law Enforcement???

## Slide 4: Purpose of Notification
Allow law enforcement to quickly secure the appropriate legal obligation (court order/warrant) on the small cell broadband provider
Allow CSP to NOT have to support special procedures for LI for LIPA/SIPTO capabilities used for traffic offload from small cells

## Slide 5: Similarities with Existing Service System Report
Notification is similar to the existing service system reporting for changes in CSPs (except in this case, the new system is a broadband provider instead of another cellular provider)

## Slide 6: Providing IP address of Target Wi-fi User
Potentially provide IP address being used by target using Wi-fi to expedite ability of law enforcement to setup interception on broadband provider network
Issues to be worked include differentiating target from other users of the same broadband connection.

## Slide 7: Impacts on Stakeholder Parties
Law enforcement
  Receive traffic from target when LIPA/SIPTO used (via broadband provider) when target connected to small cell
  Receive traffic from target when target uses Wifi (via broadband provider) when target connected to small cell
Cellular Service Provider (CSP)
- Able to deploy LIPA/SIPTO capabilities to achieve traffic offload from mobile core network
- Must standardize/develop/deploy new automated small cell broadband provider
notification capability for law enforcement
Broadband Provider
- Do NOT have to develop/deploy anything new (use their existing LI capabilities)
Targets
  Get intercepted regardless of whether they use Wifi or Small Cells (whether or not their traffic is
  offloaded from the CSP using LIPA or SIPTO) when connected to a small cell.

## Slide 8: Next steps
Further brainstorming on what can/should be done in this area
Can such a WIN-WIN be justified to regulators/law enforcement and CSPs?
Can such an automated small cell broadband provider notification capability be standardized in short order?