## Slide 1: [FS_AMD] CDP Instantiation of CMMF
Source: Qualcomm Germany
Agenda Item: 2.6
Online, 24 October 2024
3GPP SA4 MBS SWG Post SA4#129-e
S4aI240196

## Slide 2: Background
ETSI TS 103 973 defines a Content Delivery based Instantation in Annex D (normative)
CMMF is considered as a Content Delivery Protocol (CDP) as defined in clause of 8 of [RFC5052].
Annex D provides a mapping of CMMF to the RFC 5052 principles and vice versa
This instantiation also permits to re-use existing FEC Code including Raptor (the 3GPP MBMS code) as defined in RFC 5053 and RaptorQ as defined in RFC 6330.
The protocol also makes use of 3GPP familiar concepts such as the File Delivery Table in FLUTE and used in MBMS and MBS

## Slide 3: CMMF Architecture
Simplified Architecture as developed by Qualcomm during CMMF specification development

## Slide 4: Defined Reference Points
CMMF-CI: This reference point provides Configuration Information describing the location and relationship of the source and coded/repair objects, may be provided to a CMMF receiver.
CMMF-S: This reference point provides the source transport objects. For CMMF, these objects are unmodified from original data. Parts of these objects may be used by Object Recovery to recover source objects.
CMMF-CR: This reference point provides the coded/repair transport objects. Details on the formats on this reference point are provided in clause.
Not explicitly mentioned in the diagram are the following reference points:
  The server-side configuration of the CMMF sender
  The client-side API to have an API between the CMMF receiver and the application
Note also that the application is completely independent of any manifest and so on

## Slide 5: Call flow for FLUTE-based CMMF CDP instantation (Figure D.1)

## Slide 6: CMMF Transport Objects and Transport Sessions
Information is provided to receiver through configuration information, describing
  Each logical flow that is operated
  Each object, metadata of the object and other information
  The type of the object as well encoding parameters
Source and Repair objects are assigned to TSI and TOI

## Slide 7: Configuration Parameters
The Configuration Information allows the CMMF client to map an application request to CMMF receiver operations.
Table D.1.5-1 provides examples of possible Configuration Information that can be used where source and coded/repair transport objects are described.
Some use cases may require additional information or only a subset of this information, and a simpler version of this parameter set may be used.
Updates of the CI information may happen
Parameter |  |  |  | Usage | Definition
Complete |  |  |  | OD | Indicates whether the Configuration Information is complete.
Location |  |  |  | O | Provides information where the Configuration Information can be accessed in carried externally.
Expires |  |  |  | M | Provides information when this Configuration Information is no longer valid and an update is needed, for example using a reload from Location.
Source Flow |  |  |  | 1 … S | Provides 1 … S source flows.
 | TSI |  |  | M | Identifier of the source flow.
 |  | Object |  | 1 … N | Provides 1 … N objects in the source flow.
 |  |  | TOI | M | Transport object identifier (TOI) value that represents the source object.
 |  |  | Size | M | Size of the transmission object in bytes.
 |  |  | Content-Type |  | Describes media type of file.
 |  |  | Encoding |  | Describes encoding of file .
 |  |  | Message Digest |  | Message digest of file.
 |  |  | Associated URI |  | Name, Identification, and Location of file (specified by the URI).
 |  |  | Access URL |  | The URL where the source object can be accessed. If the field is not present, then the source flow is not directly accessible.
 |  |  | availabilityStartTime |  | Provides a wall-clock time when the resource is accessible.
 |  |  | availabilityStartTime |  | Provides a wall-clock time when the resource ceases to be available.
 |  |  | <Additional metadata> |  | May include cache or E-Tag metadata.
 |  | Representation |  |  | Refers to a DASH Representation in an MPD or a Track in an HLS manifest.
Coded/Repair Flow |  |  |  | 1 … R | Provides 1 … R coded/repair flows.
 | TSI |  |  | M | Identifier of the coded/repair flow.
 |  | Object |  | 1 … N | Provides 1 … N objects in the coded/repair flow.
 |  |  | TOI | M | Transport object identifier (TOI) value that represents the coded/repair object.
 |  |  | FEC-OTI |  | If object is coded using a scheme based on [RFC5052], FEC Object transmission information including the FEC Encoding ID and, if relevant, the FEC Instance ID.
 |  |  | includedSourceTOI | M | List of (TSI, TOI pairs) of the included source transport objects forming super objects . Typically, only a single pair is provided.
 |  |  | Content-Type |  | Media Mime Type of the file.
 |  |  | completeObject | OD FALSE | Indicates whether the transport object includes sufficient information to recover all files included in this coded/repair object.
 |  |  | symbolArrangement |  | Provide this symbol arrangement in the object according to Table 78. If not present, the symbol Arrangement is unknown and only present in the bitstream.
 |  |  | sAParameters |  | may be present if the symbolArrangement is present. If present, it provides the parameters assigned to the symbol arrangement as defined in Table 36. For arrangement 2 and 3, this is a comma-separated list of: Index difference, Symbol group, Index in symbol group
 |  |  | Access URLs |  | The URLs where the coded/repair object can be accessed.
 |  |  | availabilityStartTime |  | Provides a wall-clock time, when the resource is accessible.
 |  |  | availabilityEndTime |  | Provides a wall-clock time, when the resource ceases to be available.
 |  |  | <Additional metadata > |  | 

## Slide 8: Encoding Options in Annex D
Repair Object 1
Repair Object 2
Repair Object 3
SBN=0 (30 source symbols)
Source Object with Kt=29
Encoding Symbols with ESI 30 to 119
Encoding Symbols
ESI 30 to 59
ESI 60 to 89
ESI 90 to 119
CMMF Receiver can recover source object from any 30 symbols (including byte ranges)

## Slide 9
block=0
block_num_symbols =10
block=1 block_num_symbols =10
block=2 block_num_symbols =9
Source Object with Kt=29 symbols
Encoded Symbols
mbpg_first_symbol_index=0
mbpg_difference=3
mbpg_first_symbol_index=1
mbpg_first_symbol_index=2
mbpg_symbol_group_subset_index =4
mbpg_num_symbols=25
mbpg_num_symbols=25
mbpg_num_symbols=25
0
0
0
1
1
1
2
2
2
24
27
27
25
28
28
26
29
29
3
3
3
4
4
4
5
5
5
24
25
26
24
25
26
Encoding Symbols with ESI 0 to 29
Encoding Symbols with ESI 0 to 29
Encoding Symbols with ESI 0 to 26

## Slide 10
0
3
6
9
1
4
7
2
5
8
0
1
2
3
4
7
5
8
6
9
0
3
6
1
4
7
2
5
8
block=0 (ESI 0-9)
block_num_symbols =10
block=1 (ESI 0-9) block_num_symbols =10
block=2 (ESI 0-8) block_num_symbols =9
Source Object with Kt=29 symbols
FEC with ESI 10 to 30
FEC with ESI 10 to 30
FEC with ESI 9 to 30
Source Symbols
9
10
10
10
11
11
11
12
12
Repair Symbols
24
25
25
25
26
26
26
27
27
mbpg_first_symbol_index=0
27
28
28
28
29
29
29
30
30
mbpg_difference=3
mbpg_first_symbol_index=1
mbpg_first_symbol_index=2
mbpg_symbol_group_subset_index=0
mbpg_num_symbols=30
mbpg_num_symbols=30
mbpg_num_symbols=29

## Slide 11: One Implementation of CI – Extended FDT
Aligned with File Delivery Table from FLUTE with extensions
<?xml version="1.0" encoding="UTF-8"?> <FDTInstance xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns="urn:ETSI:CMMF:2023:FDT" xsi:schemaLocation="urn:ETSI:CMMF:2023:FDT extendedFDT.xsd" Expires="2024-05-30T09:30:10Z" Complete="true" ContentType="video/mp4 codecs='avc1.42c01e,mp4a.40.29' profiles='iso8'" FEC-Encoding-ID="6" FEC-Encoding-Symbol-Length="64"> <File ContentLocation="https://example.com/efd1.mp4" TOI="0" Content-Length="64000"> <EncodedObjects type="source" independentObject="true">https://example.com/efd1.mp4</EncodedObjects> <EncodedObjects type="partial" interleavingType="sequential-sbn" includedSymbols="500,0,1001">https://example.com/part1.cmf</EncodedObjects> <EncodedObjects type="partial" interleavingType="sequential-sbn" includedSymbols="500,0,1501">https://example.com/part2.cmf</EncodedObjects> <EncodedObjects type="partial" interleavingType="sequential-sbn" includedSymbols="500,0,2001">https://example.com/part3.cmf</EncodedObjects> </File> </FDTInstance>
<FDTInstance xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns="urn:ETSI:CMMF:2023:FDT" xsi:schemaLocation="urn:ETSI:CMMF:2023:FDT extendedFDT.xsd" Expires="2024-05-30T09:30:10Z" Complete="true" FEC-OTI-FEC-Encoding-ID="6" FEC-OTI-Encoding-Symbol-Length="64"> <File ContentLocation="https://example.com/efd1-video.mp4" ContentType="video/mp4 codecs='avc1.42c01e' profiles='iso8'" TOI="0" Content-Length="64000"> <EncodedObjects type="self-contained" interleavingType="spread" independentObject="true" includedSymbols="1001,3,1,0,0,0">https://example.com/part1-video.cmf</EncodedObjects> <EncodedObjects type="self-contained" interleavingType="spread" independentObject="true" includedSymbols="1001,3,1,0,0,1">https://example.com/part2-video.cmf</EncodedObjects> <EncodedObjects type="self-contained" interleavingType="spread" independentObject="true" includedSymbols="1001,3,1,0,0,2">https://example.com/part3-video.cmf</EncodedObjects> </File> <File ContentLocation="https://example.com/efd1-audio.mp4" ContentType="audio/mp4 codecs='mp4a.40.29' profiles='iso8'" TOI="1" Content-Length="4800"> <EncodedObjects type="self-contained" interleavingType="spread" independentObject="true" includedSymbols="80,3,1,0,0,0">https://example.com/part1-audio.cmf</EncodedObjects> <EncodedObjects type="self-contained" interleavingType="spread" independentObject="true" includedSymbols="80,3,1,0,0,1">https://example.com/part2-audio.cmf</EncodedObjects> <EncodedObjects type="self-contained" interleavingType="spread" independentObject="true" includedSymbols="80,3,1,0,0,2">https://example.com/part3-audio.cmf</EncodedObjects> </File> </FDTInstance>
Single File – Source and Partial Encoding Object
Multiple Files – Self-contained objects including source symbols

## Slide 12: Proposal: It is proposed ...
To take into account this baseline call flow when defining Multi-CDN and CMMF in 5G Media Streaming
To progress the work to map multi-CDN, CMMF and the CDP instantation to the 5G Media Streaming architecture
To identify synergies with existing and deployed 3GPP specifications such as FLUTE, MBMS, TS 26.347 APIs etc