3GPP TSG-SA WG4 Meeting #122	S4-230186

# Athens, Greece, 20 – 24 February 2023

Source:	NTT

Title:	Version identification method of iRTCW signalling protocol

Agenda item:	10.5

Document for:	Discussion and Agreement

# 1. Overview

This contribution proposes the version identification method for WebRTC signalling protocol based on the agreed mechanism in S4-221560. This proposal assumes that WebSocket is adopted for the underlying transport protocol for WebRTC signalling protocol.

# 2. Proposed version identification method

Based on the agreement in S4-221560, the protocol version identification method is specified considering the following principle;

- the protocol version is determined per WebSocket connection for WebRTC signalling protocol,

- the protocol version is identified by the Request-URI of the HTTP upgrade request for establishing the WebSocket connection (for WebRTC signalling protocol messages),

- Secure WebSocket URI is adopted, and

- Backward compatibility is not required between different versions.

In addition, it is proposed that the use of HTTP Sec-WebSocket-Protocol header field is left for the version of the protocol, since the protocol name can be indicated in the WebSocket URI (i.e., The request is sent to the server which supports the protocol).

According to the above principles and consideration, the following descriptions (clause X and clause Y) are proposed for WebRTC signalling protocol version identification.

# X. Protocol Version Identification

The version of WebRTC signalling protocol shall be determined per WebSocket connection. The version of WebRTC signalling protocol shall be identified by the WebSocket URI for the HTTP upgrade request for WebSocket connection establishment (i.e., the Request-URI of the HTTP request). The WebSocket URI for the HTTP upgrade request shall be consistent with the WebSocket URI structure specified in clause Y.

The use of "Sec-WebSocket-Protocol" header field is dependent on the version of the WebRTC signalling protocol.

# Y. WebSocket URI structure

WebSocket URI of WebSocket connection for WebRTC signalling protocol message shall be:

{protocolRoot}/<protocolName>/<protocolVersion>

"protocolRoot" shall be a concatenation of the following parts:

-	scheme ("wss")

-	the fixed string "://"

-	authority (host and optional port) as defined in IETF RFC 3986. The host should be represented by the service provider (operator or OTT) specific FQDN (for FQDN examples see clause 28.3.2 in 3GPP TS 23.003).

-	an optional deployment-specific string (e.g., server prefix) that starts with a "/" character.

"protocolName" shall be "rtc".

"protocolVersion" shall indicate the version of the WebRTC signalling protocol. The protocol version shall be indicated as the concatenation of the letter "v" and the WebRTC signalling protocol version number. The other fields shall not be included in the URI.

For example, 'v1'.

NOTE 1:	The "protocolVersion" will only be increased if the new protocol version contains not backward compatible changes.

A URI should not contain a trailing slash, and if it contains one, then it should be ignored/removed.

# 3. Proposal

The proposed versioning method (i.e., clause X and clause Y) for WebRTC signalling protocol should be included into the TS.