## Slide 1
Huawei’s view on SA4 Rel-19 plan
S4-240138
3GPP SA4
Sophia-Antipolis, FR, 29th Jan – 2nd Feb 2024

## Slide 2
RTC (1/2)
FS_eiRTCW: R18 has defined the general architecture and signaling/media protocol of WebRTC real-time communication. However, the following issues are still not covered or fully discussed:
The scenarios for introducing such new architecture are not clear
The call flows are missing
The impact on current operator’s network, e.g. the relation with the IMS architecture (including interworking details)
The impact on the terminal side.
More groups (at least SA1/SA2 and GSMA) should get involved to make sure the potential impact of the new architecture is fully understood by all relevant stakeholders.
IBACS: Finish the call flow definition in R18. Start to define the details for split rendering operation in R19.
Protocol evolution (potential new SID)：
1) DC protocol stack evolution: SCTP has some problems like link setup delay (4RTT) and imperfect unreliable transmission mechanism (depending on the reliability of the FORWARD-TSN). This may not meet the future requirements for various XR/AI data transmission. Evolution to QUIC may be considered.
2) SDP negotiation mechanism simplification: Currently, the signaling and media processing of SIP-based SDP negotiation are severely coupled. All signaling-plane NEs are involved in the SDP negotiation process, and need to be aware of the negotiation status at all time. The re-negotiation process and the media connection delay is very long. A new simplified SDP negotiation mechanism should be considered.

## Slide 3
5G_RTP: Continuous work in R19
FEC usage and characteristics in real-time communications, including:
  Raptor/RaptorQ (RFC 6681)
  Reed-Solomon (RFC 6865)
  Flex FEC (RFC 8627)
  ULP FEC (RFC 5109)
  … …
Traffic multiplexing in real-time communications:
  RTP streams multiplexed in a single RTP session
  RTP/RTCP multiplexed on a single UDP port.
  … …
Potential improvements to RTP HE for PDU Set marking.
Other aspects:
Network assistance enhancements for media delivery.
  Latency, network congestion status, RT latency control, etc.
Requirements and traffic characteristics of multi-modal services.
RTC (2/2)

## Slide 4: Video (1/2)
FS_AI4Media: For R19, it’s suggested to divided the work into two parts：
  High priority (start the normative work in the near future):
  AI model distribution, metadata transmission protocol and data format definition
  Network-side AI inference architecture for both 5GMS and RTC (in collaboration with SA2)
  KPI definition
  Low priority (requires further research and test verification):
  Split AI inference (AI model split, model compression, and intermediate data compression): how to split AI models for the best effect, compatibility between different inference platforms after split, and problems caused by a large amount of intermediate data transmission.
  Distributed/Federated learning (lack of contribution).

## Slide 5: Video (2/2)
FS_AVATAR: Finish the R18 study, and start normative work in R19
  architecture definition and mapping to WebRTC/IMS (in collaboration with SA2)
  different types of animation technologies (voice, video, text, etc.) and models (2D/3D) considering resource consumption, efficiency and algorithm compatibility
MeCAR: Complete the R18 work item, and finish the leftover normative work in R19
FS_ARMQoE: complete FS_ ARMQoE at SA4#127, consider recommendations from the report

## Slide 6: MBS
SR_MSE: For R19 finish left overs from this release.
5GMS_Pro_Ph2: Finish the R18 work item, for R19:
  Consider developments from media streaming industry e.g. in potential new work item
  Consider improvements, maintenance feedback from other organizations
MBS:
  Support for in-session unicast repair for live and low-latency live services.
  MBMS functionalities not yet supported in MBS User Services.
  Enhancements on MBS User Service to align with other WGs if necessary.
Promise
  Continue left overs from R18.
  If no new work, consider maintenance and feedback.
  Take feedback from industry into account.
Other aspects:
  Network assistance enhancements for media delivery.
    Latency, network congestion status, RT latency control, etc.