## Slide 1: Authorisation of JavaScript access to DCMTSI client in terminal
Walter Zielinski, Huawei

## Slide 2: Problem Statement
  JavaScript needs to access DCMTSI client in terminal IMS Signaling Interface to send data media to its peer
  Access can be granted on the basis of trust with
    DCS and on the principle that some sort of controls takes place before the data channel applications are uploaded to DCS and before the code gets executed by UE
    the run-time and the fact that the run-time has the appropriate security controls implemented to allow DCMTSI usage
  By itself the JavaScript run time should provide the protection from malicious content through the existing mechanisms implemented by the OS and JavaScript engines, e.g. V8,SpiderMonkey, etc
  Signaling authorization would essentially protect from unauthorized usage of DCMTSI client in terminal and IMS exploits rather than from the general JavaScript security exploits, e.g. smart contracts for usage could be implemented
  Section 7 of TS.66 /CR1012 refers to this particular scenario as part of constructor

## Slide 3: Technical Explanation
DCS
APP(X)
UE A
Bootstrap
Case 1: Default access to DCMTSI client in terminal or implicit authorization through the run time (run-time authorized)
APP(X)
DCMTSI
Immediate
Access
Granted
By
Default
IMS Network
UNI
DCS
APP(X)
UE A
Bootstrap
APP(X)
DCMTSI
Authorize
Access
Before
Use
IMS Network
UNI
send()
send()
Case 2: Accessing DCMTSI client in terminal with authorization protocol per application (explicit application authorization)
auth(x)
Run-Time
auth

## Slide 4: Discussion Point
  Is authorization required or not?
  What should be the requirement reference source for this scenario?
  Mechanism
    Authorization process transparent to the programmer , e.g executed as part of object construction
    Should there be authorization of the run-time only or the authorization per application, or maybe both?
    What could be used for authorization e.g. certificate, token?
    Should DCS provide some token to use against DCMTSI and how to compute this token?
    Client side or server side authorization ?
    Should both ends implement the mechanism or it is possible for only one side applying the authorization
    Should a smart contract type mechanism be implemented on what the application is allowed with DCMTSI client in terminal, e.g. maximum number of IMS Signaling Interface invocations per session
    Does such mechanism makes external application , e.g. from 3rd parties sources, usage simpler
  LS to 3GPP or FASG consultation

## Slide 5
Thank you