## Slide 1: Telco PaaS framework in ETSI NFV VNF Generic OAM Functions and other PaaS Services
Kostas Katsalis (NTT DOCOMO) on behalf of ETSI NFV
NFV and 3GPP SA5 workshop
Wednesday June 5th, 2024
NFV(24)000134

## Slide 2: Disclaimer
The present slide-set presentation reuses material that ETSI NFV has presented at joint workshop/meeting events with other organizations or at public events or extracts from the specifications/reports delivered by ETSI NFV.
The slide templates, logos, etc. are reused as is from the sourced material with small modifications for the purpose of the present call, where necessary.

## Slide 3: Outline
PaaS Services framework in ETSI NFV
Interactions and interfaces specification
Relationship with 3GPP SA5 activities
Conclusion, next steps

## Slide 4: PaaS Services framework development in NFV
https://www.etsi.org/deliver/etsi_gr/NFV-IFA/001_099/029/03.03.01_60/gr_NFV-IFA029v030301p.pdf
https://www.etsi.org/deliver/etsi_gr/NFV-EVE/001_099/019/05.01.01_60/gr_NFV-EVE019v050101p.pdf
https://docbox.etsi.org/ISG/NFV/Open/Drafts/IFA049ed511/NFV-IFA049ed511v504.zip
Published
Published
Under publication

## Slide 5: PaaS Services framework development
https://www.etsi.org/deliver/etsi_gr/NFV-IFA/001_099/029/03.03.01_60/gr_NFV-IFA029v030301p.pdf
Platform as a Service (PaaS): capability provided to the consumer to deploy onto the cloud infrastructure consumer created or acquired applications.
PaaS service types:
VNF Common Service: modular service or a function with a lifecycle independent from its consumers and that is consumable by either one or multiple services.
VNF Dedicated Service: modular service or a function with a lifecycle dependent on its consumers and that can only be consumed by a specific set of applications or services.
Three main design options can be envisioned:
PaaS services are modelled as VNFs.
PaaS services are modelled as a new type of NFVI resources.
PaaS services are modelled as a new type of object specific to the PaaS layer.
Initial work on PaaS

## Slide 6
VNF Generic OAM functions
https://www.etsi.org/deliver/etsi_gr/NFV-EVE/001_099/019/05.01.01_60/gr_NFV-EVE019v050101p.pdf
Use cases related to LCM of VNF generic OAM functions
Use cases related to type of VNF generic OAM functions
Use cases: Management aspects related to VNF connectivity
Use cases: VNF generic OAM functions for autonomous management
Framework and potential solutions
Recommendations
VNF generic OAM functions (EVE019)
Release 5
NOTE: ETSI GR NFV-EVE 019 release 4 was used as a baseline for the previous Cloud-native OAM support study in 3GPP SA5.
Release 18: TR28.834 Study on management of cloud-native Virtualized Network Functions (VNF)

## Slide 7
VNF Generic OAM functions
https://www.etsi.org/deliver/etsi_gr/NFV-EVE/001_099/019/05.01.01_60/gr_NFV-EVE019v050101p.pdf
Traffic Enforcer
Network Configuration Manager
Upgrade VNF
Log Aggregator
Log Analyser
VNF Metrics Aggregator
VNF Metrics Analyser
VNF Configuration Manager
Time Function
Use cases related to type of VNF generic OAM functions
Use cases related to LCM of VNF generic OAM functions
Use cases: Management aspects related to VNF connectivity
Use cases: VNF generic OAM functions for autonomous management
Framework and potential solutions
Recommendations
VNF generic OAM functions (EVE019)
Policy Agent
VNF Testing Manager
NotificationManager
Release 5
Use cases related to LCM of VNF generic OAM functions
Instantiation/termination of VNFs using VNF generic OAM functions managed by NFV-MANO
Lifecycle management of VNF generic OAM function managed by NFV-MANO

## Slide 8: VNF generic OAM functions (EVE019)
Three solutions have been evaluated
Solution A: Introducing generic OAM as a new functional block.
Solution B: Extending existing functional blocks for Generic OAM functionality
Solution C: Generic OAM functions as VNFs
PaaS services as VNFs according to ETSI NFV GR IFA029
* NOTE: in the normative work, it is not regarded as a “functional block”, but rather as a “functional set”, that is composable as needed by applications, operator, etc. please refer to slide #29.
VNF Generic OAM functions
https://www.etsi.org/deliver/etsi_gr/NFV-EVE/001_099/019/05.01.01_60/gr_NFV-EVE019v050101p.pdf
Release 5
Endorsed
Endorsed

## Slide 9
FEAT24: VNF generic OAM functions and other PaaS Services framework development
  A VNF generic OAM function is a PaaS Service
In ETSI GS NFV-IFA 049 Release 5, the relationship between VNF generic OAM functions and PaaS Services is clarified:
Clause 4.2.1.2: “A VNF generic OAM function is a PaaS Service whose scope is to provide and handle generic OAM functionality for VNFs.”

## Slide 10: VNF generic OAM functions and other PaaS Services: Interfaces
Traffic Enforcer
Traffic management i/f
Network Configuration Manager
Network configuration management i/f
Upgrade VNF
VNF Upgrade management i/f
Log Aggregator
Log Exposure i/f
Log Analyser
Log Analysis Exposure i/f
VNF Metrics Aggregator
Metrics Exposure i/f
VNF Metrics Analyser
Metrics Analysis Exposure i/f
VNF Configuration Manager
VNF configuration management i/f
Time Function
Time management i/f
Policy Agent
Notification Manager
Configuration Server
CRUD policy operations
Notifications exposure
storing config. data
VNF generic OAM functions
Other PaaS Services
PaaS Services in NFV

## Slide 11
FEAT24: VNF generic OAM functions and other PaaS Services framework development
  A VNF generic OAM function is a PaaS Service
In ETSI GS NFV-IFA 049 Release 5, the relationship between VNF generic OAM functions and PaaS Services is clarified:
Clause 4.2.1.2: “A VNF generic OAM function is a PaaS Service whose scope is to provide and handle generic OAM functionality for VNFs.”

## Slide 12: Interactions and interfaces specification
Northbound-Management (NB-M): interface(s) exposed by the PaaS Service towards one or multiple corresponding management entity for the purpose of managing the PaaS Service.
Northbound-Function (NB-F): interface(s) exposed by the PaaS Service with specific functionality tailored to that PaaS Service.
Southbound-Function (SB-F): to perform the intended functionality, a PaaS Service can interact with different function producer entities (i.e. OSS, NFV-MANO, NFVI or other PaaS Services).
Southbound-VNF (SB-V): it comprises the interface(s) used to interact with the VNF instances that are being managed with the VNF generic OAM function.

## Slide 13: PaaS Services Management
PaaS Services have corresponding management functions for their lifecycle and repository aspects:
PSM: PaaS Services Manager
PSR : PaaS Services Repository
PSM and PSR when placed as NFV-MANO functions

## Slide 14: PaaS Services Management
PaaS Services have corresponding management functions for their lifecycle and repository aspects: PaaS Services Manager (PSM) and PaaS Services Repository (PSR).
Option 1: When a PaaS Service is deployed as a VNF, the PSM interacts with the VNFM to execute the corresponding lifecycle management of the VNF.
Option 2: When PaaS Services are deployed as one or multiple virtualised resources offered as new type of NFVI resource, the PSM interacts with the VIM.
Option 3: When PaaS Services are deployed as one or multiple managed object (e.g., Managed CIS Cluster Object (MCCO)), the PSM interacts with the CISM.
PM and PSR functional requirements are defined ETSI GS NFV-IFA 010 V5.0.1 (2023-11)

## Slide 15: Potential mapping with open-source solutions (example)
15
Log Analyzer
Log
Aggregator
Metrics
Aggregator
Metrics
analyzer
Notification Manager
VNF
Configuration
Manager
Network
Configuration
Manager
OSS/BSS
VNF
instance
VNFC
VNFC
CaaS
CIS
Upgrade
VNF
NFV-MANO
CISM
Time
Function
Traffic Enforcer
Elastalert
VNF generic OAM functions
CIS
・・・
NFVI
EM
VNFC
VIM
Common Service
DISCLAIMER
These are only potential options, that have neither been fully discussed in the ISG community, nor endorsed any specific one.
Purpose is to only visualize potential options that might also be relevant to the open-source community.

## Slide 16: FEAT24 VNF generic OAM functions and PaaS Services: Stage 3 work
DGS/NFV-SOL024 started based on NWI Proposal in NFV(24)000014r1
Work started on 2024-02-23
Scope description:
  The work item will develop a specification fulfilling the requirements specified in ETSI GS NFV-IFA 049. This work item will analyze existing solutions against ETSI GS NFV-IFA 049 requirements. Based on the analysis results, the WI will develop the protocol and data model for the NB-F interfaces of VNF generic OAM functions, prominently using the CRD schema format where feasible, and other formats for some VNF generic OAM functions if CRD is not feasible. The WI will specify requirements for the protocol(s) on the SB-V interfaces toward the VNF. The resulting deliverable will contain normative provisions.

## Slide 17: Stage 3 options - declarative API based on CRD (example)
Potential touchpoint of standardization with open-source development:
  Standardize CRD (define schema, one or maybe more).
  Open-source development of CR controller and other artifacts.
CR controller
apiVersion: apiextensions.k8s.io/v1
kind: CustomResourceDefinition
metadata:
name: myCustomResource.etsi.nfv
spec:
group: etsi.nfv
scope: Namespaced
names:
kind: MyCustomResource
versions:
- name: v1alpha1
schema:
openAPIV3Schema:
description: Schema for
MyCustomResource API
properties:
…
spec:
description: Desired state of
MyCustomResource.
properties:
…
type: object
CRD
Function consumer entity
Consumer
K8s
API
Server
CR controller
Create/update
CR object
Get status
CR object
apiVersion: etsi.nfv/v1alpha1
kind: MyCustomResource
metadata:
name: sample
spec:
…
CR
Open source project
Standard

## Slide 18: Telco PaaS and ETSI MANO
Telco PaaS in NFV: foundation
GS NFV-EVE019 (study phase)
GS NFV-IFA 049 (stages 1,2)
GS NFV-SOL024 (stage 3)
NFV-MANO evolution
What will the role of a Telco PaaS be in the revised NFV-MANO architecture?

## Slide 19: Relationship with 3GPP SA5 activities
Release 18: TR28.834 Study on management of cloud-native Virtualized Network Functions (VNF)
Release 19: TR28.869 Study on Cloud Aspects of Management and Orchestration
Open questions
How the Telco PaaS framework defined by ETSI NFV can interact with SBMA?
  Can VNF generic OAM functions can be considered MnFs/MnSs?
  If the Telco PaaS framework resides outside SBMA (like NFV-MANO), the MnS producers only interact with the VNF generic OAM functions through their exposed service interfaces?
What about LCM of the VNF generic OAM functions and other PaaS Services?
What is the relationship of the NFV Telco PaaS with open-source solutions considered by 3GPP?
How NFV Telco PaaS can be used to support interoperability and portability (TR28.869 WT-2, WT-2) ?

## Slide 20: Conclusion, next steps
ETSI NFV framework and its specifications have been enhanced to better support container-based/cloud-native VNF management and more cloud-native OAM.
Next steps in ETSI NFV (highlights):
  VNF generic OAM and other PaaS Services (part of FEAT21 and FEAT24 development)
    Completion of stage 2 work as part of Release 5 ed521.
      Improve/Simplify the descriptions for the relationship between VNF generic OAM functions and PaaS Services
    Continue work on stage 3 specification.
  NFV architecture evolution:
    Study being developed as part of DGR/NFV-IFA054 (to produce ETSI GR NFV-IFA 054).
    Evaluation of different concepts, approaches and solutions to make the NFV architecture simpler and more flexible, wherein Telco PaaS for cloud-native OAM and NF plays a key role.

## Slide 21: Thank you for your attention
Follow us on:

## Slide 22: Any questions?
Contact us:
katsalis@docomolab-euro.com

## Slide 23: Where to find further information
NFV Bits on YouTube: https://www.youtube.com/user/ETSIstandards
ETSI NFV drafts and Releases documentation: https://docbox.etsi.org/ISG/NFV/Open/
ETSI NFV published standards: https://www.etsi.org/committee/1427-nfv
ETSI NFV blog: https://www.etsi.org/newsroom/blogs/blog-nfv
ETSI NFV webpage: https://www.etsi.org/technologies/nfv