3GPP TR 32.842 V13.1.0 (2015-12)

Technical Report

3rd Generation Partnership Project;

Technical Specification Group Services and System Aspects;

Telecommunication management;

Study on network management of virtualized networks (Release 13)

The present document has been developed within the 3rd Generation Partnership Project (3GPP TM) and may be further elaborated for the purposes of 3GPP.
The present document has not been subject to any approval process by the 3GPP Organizational Partners and shall not be implemented.
This Report is provided for future development work within 3GPP only. The Organizational Partners accept no liability for any use of this Specification.
Specifications and Reports for implementation of the 3GPP TM system should be obtained via the 3GPP Organizational Partners' Publications Offices.

Keywords

virtualization,management,NFV

3GPP

Postal address

3GPP support office address

650 Route des Lucioles - Sophia Antipolis

Valbonne - FRANCE

Tel.: +33 4 92 94 42 00 Fax: +33 4 93 65 47 16

Internet

http://www.3gpp.org

Copyright Notification

No part may be reproduced except as authorized by written permission.
The copyright and the foregoing restriction extend to reproduction in all media.

© 2015, 3GPP Organizational Partners (ARIB, ATIS, CCSA, ETSI, TSDSI, TTA, TTC).

All rights reserved.

UMTS™ is a Trade Mark of ETSI registered for the benefit of its members

3GPP™ is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners
LTE™ is a Trade Mark of ETSI registered for the benefit of its Members and of the 3GPP Organizational Partners

GSM® and the GSM logo are registered and owned by the GSM Association

# Contents

Foreword	9

Introduction	9

1	Scope	10

2	References	10

3	Definitions and abbreviations	14

3.1	Definitions	14

3.2	Abbreviations	14

4	Concept and background	15

4.1 	Concept	15

4.2 	Background	15

5	Management use cases	16

5.1	Use cases for Fault management	16

5.1.1	Introduction	16

5.1.2	Failure management when VNF detects VNF failure	16

5.1.2.1	Introduction	16

5.1.2.2	Actor	16

5.1.2.3	Pre-condition	16

5.1.2.4	Description	16

5.1.2.5	Post-condition	17

5.1.3	Failure management when the alarm is generated by NFVI	17

5.1.3.1	Introduction	17

5.1.3.2	Actor	17

5.1.3.3	Pre-condition	17

5.1.3.4	Description	17

5.1.3.5	Post-condition	17

5.1.4	Failure management when the EM detects VNF failure	17

5.1.4.1	Introduction	17

5.1.4.2	Actor	18

5.1.4.3	Pre-condition	18

5.1.4.4	Description	18

5.1.4.5	Post-condition	18

5.1.5	Failure management when the alarm is generated by VNFC	18

5.1.5.1	Introduction	18

5.1.5.2	Actor	18

5.1.5.3	Pre-condition	18

5.1.5.4	Description	18

5.1.5.5	Post-condition	19

5.1.6	Notification of VNFCs impacted due to scheduled NFVI maintenance	19

5.1.6.1	Introduction	19

5.1.6.2	Actor	19

5.1.6.3	Pre-condition	19

5.1.6.4	Description	19

5.1.6.5	Post-condition	20

5.1.7	VM failure is detected by VNF application	20

5.1.7.1	Introduction	20

5.1.7.2	Actor	20

5.1.7.3	Pre-condition	20

5.1.7.4	Description	20

5.1.7.5	Post-condition	20

5.1.8	VNF snapshot capture	20

5.1.8.1	Introduction	20

5.1.8.2	Actor	21

5.1.8.3	Pre-condition	21

5.1.8.4	Description	21

5.1.8.5	Post-condition	21

5.2	Use cases for Configuration Management	21

5.2.1	VNF instantiation and configuration for mixed network	21

5.2.1.1	Introduction	21

5.2.1.2	Actor	22

5.2.1.3	Pre-condition	22

5.2.1.4	Description	22

5.2.1.5	Post-condition	22

5.2.2	NFV configuration management	22

5.2.2.1	Introduction	22

5.2.2.2	Actor	22

5.2.2.3	Pre-condition	23

5.2.2.4	Description	23

5.2.2.5	Post-condition	23

5.2.3	  VNF configuration management by EM in mixed network	23

5.2.3.1	Introduction	23

5.2.3.2	Configure the VNF application specific parameters after a VNF is instantiated	24

5.2.3.2.1	Introduction	24

5.2.3.2.2	Actor	24

5.2.3.2.3	Pre-condition	24

5.2.3.2.4	Description	24

5.2.3.2.5	Post-condition	24

5.2.3.3	Release logical resource dedicated to manage the terminated VNF	24

5.2.3.3.1	Introduction	24

5.2.3.3.2	Actor	24

5.2.3.3.3	Pre-condition	24

5.2.3.3.4	Description	24

5.2.3.3.5	Post-condition	25

5.2.3.4	Configure the VNF application specific parameters after a VNF is scaled, upgraded or updated	25

5.2.3.4.1	Introduction	25

5.2.3.4.2	Actor	25

5.2.3.4.3	Pre-condition	25

5.2.3.4.4	Description	25

5.2.3.4.5	Post-condition	25

5.2.4	Automatic re-connection of eNBs after lifecycle management of vMME	25

5.2.4.1	Introduction	25

5.2.4.2	Actor	26

5.2.4.3	Pre-condition	26

5.2.4.4	Description	26

5.2.4.5	Post-condition	26

5.3	Use cases for Performance Management	26

5.3.1	VNF Performance measurements reporting to EM	26

5.3.1.1	Introduction	26

5.3.1.2	Actor	26

5.3.1.3	Pre-condition	27

5.3.1.4	Description	27

5.3.1.5	Post-condition	27

5.3.2	Virtualized resource performance measurements	27

5.3.2.1       Introduction	27

5.3.2.2       Actors	27

5.3.2.3       Pre-condition	27

5.3.2.4       Description	27

5.3.2.4       Post-condition	27

5.4	Other Use cases involving Network Deployment	28

5.4.1	Information collection prior to capacity expansion	28

5.4.2.1	Introduction	28

5.4.2.2	Actor	28

5.4.2.3	Pre-condition	28

5.4.2.4	Description	28

5.4.2.5	Post-condition	28

5.5	Use cases for Core Network Lifecycle Management	28

5.5.1	Network Service Descriptor On-boarding	28

5.5.1.1	Introduction	28

5.5.1.2	Actor	28

5.5.1.3	Pre-condition	28

5.5.1.4	Description	29

5.5.1.5	Post-condition	29

5.5.2	Disable Network Service Descriptor	29

5.5.2.1	Introduction	29

5.5.2.2	Actor	29

5.5.2.3	Pre-condition	29

5.5.2.4	Description	29

5.5.2.5	Post-condition	29

5.5.3	Enable Network Service Descriptor	29

5.5.3.1	Introduction	29

5.5.3.2	Actor	29

5.5.3.3	Pre-condition	30

5.5.3.4	Description	30

5.5.3.5	Post-condition	30

5.5.4	Update Network Service Descriptor	30

5.5.4.1	Introduction	30

5.5.4.2	Actor	30

5.5.4.3	Pre-condition	30

5.5.4.4	Description	30

5.5.4.5	Post-condition	30

5.5.5	Query Network Service Descriptor	31

5.5.5.1	Introduction	31

5.5.5.2	Actor	31

5.5.5.3	Pre-condition	31

5.5.5.4	Description	31

5.5.5.5	Post-condition	31

5.5.6	Delete Network Service Descriptor	31

5.5.6.1	Introduction	31

5.5.6.2	Actor	31

5.5.6.3	Pre-condition	31

5.5.6.4	Description	32

5.5.6.5	Post-condition	32

5.5.7	VNF Package On-boarding	32

5.5.7.1	Introduction	32

5.5.7.2	Actor	32

5.5.7.3	Pre-condition	32

5.5.7.4	Description	32

5.5.7.5	Post-condition	32

5.5.8	Enabling VNF Package	32

5.5.8.1	Introduction	32

5.5.8.2	Actor	33

5.5.8.3	Pre-condition	33

5.5.8.4	Description	33

5.5.8.5	Post-condition	33

5.5.9	Disabling VNF Package	33

5.5.9.1	Introduction	33

5.5.9.2	Actor	33

5.5.9.3	Pre-conditions	33

5.5.9.4	Description	33

5.5.9.5	Post-condition	33

5.5.10	VNF Package Update	34

5.5.10.1	Introduction	34

5.5.10.2	Actor	34

5.5.10.3	Pre-condition	34

5.5.10.4	Description	34

5.5.10.5	Post-condition	34

5.5.11	Querying VNF Package	34

5.5.11.1	Introduction	34

5.5.11.2	Actor	34

5.5.11.3	Pre-condition	34

5.5.11.4	Description	35

5.5.11.5	Post-condition	35

5.5.12    Deleting VNF Package	35

5.5.12.1	   Introduction	35

5.5.12.2	   Actor	35

5.5.12.3    	   Pre-condition	35

5.5.12.4    	   Description	35

5.5.12.5    	   Post-condition	35

5.5.13	Instantiation of Core Network Service	35

5.5.13.1	Introduction	35

5.5.13.2	Actor	36

5.5.13.3	Pre-condition	36

5.5.13.4	Description	36

5.5.13.5	Post-condition	36

5.5.14	Network Service instance scaling	36

5.5.14.1	Introduction	36

5.5.14.2	Network Service instance scale out	36

5.5.14.2.1	Introduction	36

5.5.14.2.2	Actor	36

5.5.14.2.3	Pre-condition	36

5.5.14.2.4	Description	37

5.5.14.2.5	Post-condition	37

5.5.14.3	Network Service instance scale in	37

5.5.14.3.1	Introduction	37

5.5.14.3.2	Actor	37

5.5.14.3.3	Pre-condition	37

5.5.14.3.4	Description	37

5.5.14.3.5	Post-condition	37

5.5.15	Network Service instance update due to VNF instance modification	37

5.5.15.1 	Introduction	37

5.5.15.2	Actor	37

5.5.15.3	Pre-condition	38

5.5.15.4	Description	38

5.5.15.5	Post-condition	38

5.5.16	Termination of Core Network Service Instance	38

5.5.16.1	Introduction	38

5.5.16.2	Actor	38

5.5.16.3	Pre-condition	38

5.5.16.4	Description	38

5.5.16.5	Post-condition	39

5.5.17	VNF expansion	39

5.5.17.1	Introduction	39

5.5.17.2	Actor	39

5.5.17.3	Pre-condition	39

5.5.17.4	Description	39

5.5.17.5	Post-condition	39

5.5.18	VNF Contraction	40

5.5.18.1	Introduction	40

5.5.18.2	Actor	40

5.5.18.3	Pre-condition	40

5.5.18.4	Description	40

5.5.18.5	Post-condition	40

5.5.19	 Termination of Core VNF instance	40

5.5.19.1	Introduction	40

5.5.19.2	Actor	40

5.5.19.3	Pre-condition	41

5.5.19.4	Description	41

5.5.19.5	Post-condition	41

5.5.20	Notifications for VNF auto-scaling executed by VNFM	41

5.5.20.1	Introduction	41

5.5.20.2	Actor	41

5.5.20.3	Pre-condition	41

5.5.20.4	Description	41

5.5.20.5	Post-condition	42

6	Potential requirements	42

6.1	Introduction	42

6.2	Requirements for management of VNF only network	42

6.2.1 	General requirements	42

6.2.2 	CM requirements	43

6.2.3 	FM requirements	43

6.2.4 	PM requirements	43

6.2.5 	LCM requirements	43

6.3	Requirements for management of mixed network	45

6.3.1 	General requirements	45

6.3.2 	CM requirements	46

6.3.3 	FM requirements	46

6.3.4 	PM requirements	46

6.3.5 	LCM requirements	46

7	Potential solutions	46

7.1	Management architecture	46

7.1.1 	Overview	46

7.1.2 	Involvement of 3GPP SA5 for NFV Management and Orchestration interfaces	47

7.2	Management interfaces and models	50

7.2.1	Global view of data flows	50

7.2.1.1	FM & PM data flows	50

7.2.1.1.1	MANO GS defined FM & PM data flows	50

7.2.1.1.2	3GPP view of FM & PM data flows	52

7.2.1.2	CM notification data flows	53

7.3	Management procedures	53

7.3.1 	Introduction	53

7.3.2	LCM procedures	54

7.3.2.1 	Instantiation of VNF	54

7.3.2.2	VNF instance scaling procedures	57

7.3.2.2.1	VNF instance scaling procedures with resource allocation done by VNF Manager	57

7.3.2.2.1.1	VNF instance expansion procedure triggered by NM/EM	57

7.3.2.2.1.2	VNF instance contraction procedure triggered by NM/EM	59

7.3.2.3 	Termination of IMS/EPC VNF instance Procedure	60

7.3.2.4 	Instantiation of Network Service	62

7.3.2.5 	Termination of Network Service	63

7.3.3	FM procedure	64

7.3.3.1	FM procedure flow for correlation done in EM	64

7.3.3.1.1 	Introduction	64

7.3.3.1.2 	VR resource fault report procedure	64

7.3.3.1.3 	VNF application fault report procedure	64

7.3.3.1.4 	fault correlation done in EM procedure	65

7.3.3.2	FM procedure flow for correlation in VNFM	65

7.3.3.2.1 	Introduction	65

7.3.3.2.2 	VR fault report procedure	65

7.3.3.2.3 	VNF/VNFC fault report procedure	65

7.3.3.2.4 	Fault correlation in VNFM	66

7.3.3.3	FM procedure flow for notification of VNFCs impacted due to scheduled NFVI maintenance	66

7.3.3.4	FM procedure flows for healing through operation request to VNFM and auto-healing	67

7.3.3.4.1	Procedure flow for VNF healing through operation request to VNFM by EM	67

7.3.3.4.2	Procedure flow for VNF auto-healing by VNFM	68

7.3.3.5	VNF snapshot capture procedure	69

7.3.4 	CM procedures	70

7.3.4.1	Adding a MME VNF to the MME pool	70

7.3.4.2	Removing a MME VNF from the MME pool	71

7.3.4.3 	Information exchange following VNF lifecycle management	72

7.3.5 	PM procedures	73

7.3.5.1 VNF performance management	73

8	Conclusions and recommendations	73

8.1	General Conclusions	73

8.2	Conclusions on potential use cases	73

8.3	Conclusions on potential requirements	75

8.4	Conclusions on potential solutions	75

8.5	Recommendations	76

Annex A: Gap Analysis	77

A.1	Introduction	77

A.2	ETSI NFV terms relevant to the network management of 3GPP mobile networks and services	77

A.3	Summary of the gap with the existing 3GPP management functions	77

A.4	Summary of the gap with the ETSI specified MANO functions	78

A.4.1	Gaps related to PM data flows	78

A.4.1.1	Application level PM flow to be received by VNFM from VNF or EM	78

A.4.1.2	Application level PM flow to be received by OSS/BSS from NFVO	78

A.4.1.3	Virtualized resource level PM to be received by EM	78

A.4.2	Gaps related to FM data flows	78

A.4.2.1	Application level FM flow to be received by VNFM from VNF or EM	78

A.4.2.2	Application level FM flow to be received by OSS/BSS from NFVO	78

A.4.2.3	Virtualized resource level FM to be received by EM	78

A.4.3 	Gaps related to definition of NSD operations	78

A.4.3.1 	Network Service Descriptor Management interface	78

A.4.3.2 	Network Service Descriptor states	79

A.4.4	Use cases not supported by ETSI NFV GS MAN001 v1.1.1	79

A.4.4.1	Notification of VNFCs impacted due to scheduled NFVI maintenance	79

A.4.4.2	VNF snapshot capture	79

A.4.4.3	Notifications related to VNF auto-healing by VNFM	79

A.4.4.4	Notification related to VNF auto-scaling by VNFM	80

Annex B:  Ensemble	81

B.1 	Introduction	81

B.2 	Ensemble 1	81

B.3 	Ensemble 2	82

B.4 	Ensemble 3	83

Annex C: Change history	84

# Foreword

This Technical Report has been produced by the 3rd Generation Partnership Project (3GPP).

The contents of the present document are subject to continuing work within the TSG and may change following formal TSG approval. Should the TSG modify the contents of the present document, it will be re-released by the TSG with an identifying change of release date and an increase in version number as follows:

Version x.y.z

where:

x	the first digit:

1	presented to TSG for information;

2	presented to TSG for approval;

3	or greater indicates TSG approved document under change control.

y	the second digit is incremented for all changes of substance, i.e. technical enhancements, corrections, updates, etc.

z	the third digit is incremented when editorial only changes have been incorporated in the document.

# Introduction

Traditionally, telecommunication equipment is provided as physical equipment with software and hardware bound together. Virtualization technologies, in principle, can support network function software to be executed on COTS hardware. The benefits of using virtualization technologies in telecommunication network are:

-	Flexibility: Enabling services to be delivered via software on COTS hardware makes the deployment and redeployment of network functions more flexible and allows network functions to be scaled in and out dynamically.

-	Time-to-Market: Reducing the time for deployment of new services would improve the time-to-market, thus allowing operators to better support changing business requirements.

-	OPEX saving: The decoupling of hardware and software allows the reduction of space, power and cooling requirements and hardware diversity and makes the roll out, management and maintenance of network functions more efficient.

-	CAPEX saving: The decoupling of the network function software from purpose-built hardware allows the reuse of COTS hardware for new services and to eliminate wasteful over-provisioning.

Virtualized Networks, like non-virtualized networks, need also to be managed.

The present document investigates how virtualized networks can be managed. It investigates the relations of management architecture and management functions between virtualized network, non-virtualized networks and mixed networks. Whether the existing management architecture, management function and management models could be maximum reused and enhanced to satisfy the inclusion of the virtualized network management function are also studied.

# 1	Scope

The present document studies the network management of virtualized 3GPP specified core networks based on the architectural framework in ETSI GS NFV-MAN 001 [2]. It studies the network management of mobile networks that include virtualized core networks functions.

It also identifies the potential impacts on the existing 3GPP management architecture and to propose potential solutions for the network management of fully virtualized networks and mixed networks.

The objectives of this study are:

-	Study the use cases and concepts for the network management of virtualized networks, which are applicable to 3GPP, taking into account the relevant use cases from ETSI.

-	Analyse and classify the network management scenarios when all instances of 3GPP-defined network elements in a subsystem/domain are virtualized according to the architectural framework in ETSI GS NFV-MAN 001 [2] (i.e. in fully virtualized networks).

-	Identify the requirements for potential solutions for the network management of virtualized networks when all instances of 3GPP-defined network elements in a subsystem/domain are virtualized according to the architectural framework in ETSI GS NFV-MAN 001 [2] (i.e. in fully virtualized networks).

-	Analyse and classify the network management scenarios when some instances of 3GPP-defined network elements in a subsystem/domain are virtualized according to the architectural framework in ETSI GS NFV-MAN 001 [2] (i.e. in mixed networks).

-	Identify the requirements for potential solutions for the network management of virtualized networks when some instances of 3GPP-defined network elements in a subsystem/domain are virtualized according to the architectural framework in ETSI GS NFV-MAN 001 [2] (i.e. in mixed networks). Study whether or not a single management system for mixed networks is required.

-	Identify the potential impacts on the existing 3GPP Management reference model.

-	Analyse the existing 3GPP Management reference model, interfaces, protocols and procedures to determine what can be re-used, adapted or extended and whether new IRPs are needed for network management of virtualized networks.

-	Propose enhancements or extensions to the 3GPP Management reference model, if an impact is foreseen.

-	If needed, solution(s) for a single management system for mixed networks should be studied.

-	Provide recommendations for the standardization of the network management of fully virtualized networks and mixed networks, based on the result of the analysis and the potentially identified impacts, enhancements or extensions.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	ETSI GS NFV-MAN 001 (V1.1.1): "Network Function Virtualisation (NFV); Management and Orchestration".

[3]	3GPP TS 32.101: "Telecommunication management; Principles and high level requirements".

[4]	3GPP TS 32.600: "Telecommunication management; Configuration Management (CM); Concept and high-level requirements".

[5]	3GPP TS 28.708: "Telecommunication management; Evolved Packet Core (EPC); Network Resource Model (NRM); Integration Reference Point (IRP); Information Service (IS)".

[6]	Draft ETSI GS NFV-SWA 001 (V1.1.1): "Network Functions Virtualisation (NFV); Virtual Network Functions Architecture".

[7]	ETSI GS NFV 003 (V1.2.1): "Network Functions Virtualisation (NFV); Terminology for Main Concepts in NFV".

[8]	ETSI GS NFV-REL 001(V1.1.1): "Network Functions Virtualisation (NFV); Resiliency Requirements".

[9]	3GPP TS 36.413: "Technical Specification Group Radio Access Network; Evolved Universal Terrestrial Radio Access Network (E-UTRAN); S1 Application Protocol (S1AP)".

[10]	3GPP TS 32.102: "Digital cellular telecommunications system (Phase 2+); Universal Mobile Telecommunications System (UMTS); LTE; Telecommunication management; Architecture".

[11] 	ETSI GS NFV 001 (V1.1.1): "Network Functions Virtualisation (NFV); Use Cases".

[12]	ETSI GS NFV INF 001 (V1.1.1): "Network Function Virtualization (NFV); Infrastructure Overview".

[13]	3GPP TS 32.426: "Telecommunication management; Performance Management (PM); Performance measurements Evolved Packet Core (EPC) network".

[14]	3GPP TS 32.422: "Telecommunication management; Subscriber and equipment trace; Trace control and configuration management".

[15]	3GPP TS 32.410: "Telecommunication management; Key Performance Indicators (KPI) for UMTS and GSM".

[16]	3GPP TS 32.411: "Telecommunication management; Performance Management (PM) Integration Reference Point (IRP): Requirements".

[17]	3GPP TS 32.412: "Telecommunication management; Performance Management (PM) Integration Reference Point (IRP): Information Service (IS)".

[18]	3GPP TS 32.413: "Telecommunication management; Performance Management (PM) Integration Reference Point (IRP): Common Object Request Broker Architecture (CORBA) Solution Set (SS)".

[19]	3GPP TS 32.414: "Telecommunication management; Performance Management (PM) Integration Reference Point (IRP): Common Management Information Protocol (CMIP) Solution Set (SS)".

[20]	3GPP TS 32.415: "Telecommunication management; Performance Management (PM) Integration Reference Point (IRP); eXtensible Markup Language (XML) definitions".

[21]	3GPP TS 32.416: "Telecommunication management; Performance Management (PM) Integration Reference Point (IRP); Solution Set (SS) definitions".

[22]	3GPP TS 32.417: "Telecommunication management; Performance Management (PM) Integration Reference Point (IRP); SOAP Solution Set (SS)".

[23]	3GPP TS 32.406: "Telecommunication management; Performance Management (PM); Performance measurements; Core Network (CN) Packet Switched (PS) domain".

[24]	3GPP TS 32.407: "Telecommunication management; Performance Management (PM); Performance measurements; Core Network (CN) Circuit Switched (CS) domain; UMTS and combined UMTS/GSM".

[25]	3GPP TS 32.409: "Telecommunication management; Performance Management (PM); Performance measurements; IP Multimedia Subsystem (IMS)".

[26]	3GPP TS 32.611: "Telecommunication management; Configuration Management (CM); Bulk CM Integration Reference Point (IRP): Requirements".

[27]	3GPP TS 32.612: "Telecommunication management; Configuration Management (CM); Bulk CM Integration Reference Point (IRP): Information Service (IS)".

[28]	3GPP TS 32.613: "Telecommunication management; Configuration Management (CM); Bulk CM Integration Reference Point (IRP): Common Object Request Broker Architecture (CORBA) Solution Set (SS)".

[29]	3GPP TS 32.614: "Telecommunication management; Configuration Management (CM); Bulk CM Integration Reference Point (IRP): Common Management Information Protocol (CMIP) Solution Set (SS)".

[30]	3GPP TS 32.615: "Telecommunication management; Configuration Management (CM); Bulk CM Integration Reference Point (IRP): eXtensible Markup Language (XML) file format definition".

[31]	3GPP TS 32.616: "Telecommunication management; Configuration Management (CM); Bulk CM Integration Reference Point (IRP); Solution Set (SS) definitions".

[32]	3GPP TS 32.617: "Telecommunication management; Configuration Management (CM); Bulk CM Integration Reference Point (IRP): Bulk CM IRP SOAP Solution Set (SS)".

[33]	3GPP TS 32.621: "Telecommunication management; Configuration Management (CM); Generic network resources Integration Reference Point (IRP); Requirements".

[34]	3GPP TS 32.622: "Telecommunication management; Configuration Management (CM); Generic network resources Integration Reference Point (IRP); Network Resource Model (NRM)".

[35]	3GPP TS 32.623: "Telecommunication management; Configuration Management (CM); Generic network resources Integration Reference Point (IRP); Common Object Request Broker Architecture (CORBA) Solution Set (SS)".

[36]	3GPP TS 32.624: "Telecommunication management; Configuration Management (CM); Generic network resources: Integration Reference Point (IRP): Common Management Information Protocol (CMIP) Solution Set (SS)".

[37]	3GPP TS 32.625: "Telecommunication management; Configuration Management (CM); Generic network resources Integration Reference Point (IRP): Bulk CM eXtensible Markup Language (XML) file format definition".

[38]	3GPP TS 32.626: "Telecommunication management; Configuration Management (CM); Generic network resources Integration Reference Point (IRP); Solution Set (SS) definitions".

[39]	3GPP TS 32.631: "Telecommunication management; Configuration Management (CM); Core network resources Integration Reference Point (IRP); Requirements".

[40]	3GPP TS 32.632: "Telecommunication management; Configuration Management (CM); Core Network Resources Integration Reference Point (IRP); Network Resource Model (NRM)".

[41]	3GPP TS 32.633: "Telecommunication management; Configuration Management (CM); Core network resources Integration Reference Point (IRP); Common Object Request Broker Architecture (CORBA) Solution Set (SS)".

[42]	3GPP TS 32.634: "Telecommunication management; Configuration Management (CM); Core network resources Integration Reference Point (IRP): Common Management Information Protocol (CMIP) Solution Set (SS)".

[43]	3GPP TS 32.635: "Telecommunication management; Configuration Management (CM); Core network resources Integration Reference Point (IRP); Bulk CM eXtensible Markup Language (XML) file format definition".

[44]	3GPP TS 32.636: "Telecommunication management; Configuration Management (CM); Core network resources Integration Reference Point (IRP); Solution Set (SS) Definitions".

[45]	3GPP TS 32.661: "Telecommunication management; Configuration Management (CM); Kernel CM Requirements".

[46]	3GPP TS 32.662: "Telecommunication management; Configuration Management (CM); Kernel CM Information Service (IS)".

[47]	3GPP TS 32.663: "Telecommunication management; Configuration Management (CM); Kernel CM Integration Reference Point (IRP); Common Object Request Broker Architecture (CORBA) Solution Set (SS)".

[48]	3GPP TS 32.664: "Telecommunication management; Configuration Management (CM); Kernel CM Integration Reference Point (IRP); Common Management Information Protocol (CMIP) Solution Set (SS)".

[49]	3GPP TS 32.665: "Telecommunication management; Configuration Management (CM); Kernel CM Integration Reference Point (IRP); eXtensible Markup Language (XML) definitions".

[50]	3GPP TS 32.666: "Telecommunication management; Configuration Management (CM); Kernel CM Integration Reference Point (IRP); Solution Set (SS) definitions".

[51]	3GPP TS 32.667: "Telecommunication management; Configuration Management (CM); Kernel CM Integration Reference Point (IRP); SOAP Solution Set (SS)".

[52]	3GPP TS 32.671: "Telecommunication management; Configuration Management (CM); State Management Integration Reference Point (IRP); Requirements".

[53]	3GPP TS 32.672: "Telecommunication management; Configuration Management (CM); State Management Integration Reference Point (IRP); Information Service (IS)".

[54]	3GPP TS 32.673: "Telecommunication management; Configuration Management (CM); State Management Integration Reference Point (IRP); Common Object Request Broker Architecture (CORBA) Solution Set (SS)".

[55]	3GPP TS 32.674: "Telecommunication management; Configuration Management (CM); State Management Integration Reference Point (IRP): Common Management Information Protocol (CMIP) Solution Set (SS)".

[56]	3GPP TS 32.675: "Telecommunication management; Configuration Management (CM); State Management Integration Reference Point (IRP); Bulk CM eXtensible Markup Language (XML) file format definition".

[57]	3GPP TS 32.676: "Telecommunication management; Configuration Management (CM); State Management Integration Reference Point (IRP); Solution Set (SS) definitions".

[58]	3GPP TS 28.701: "Telecommunication management; Core Network (CN) Network Resource Model (NRM) Integration Reference Point (IRP); Requirements".

[59]	3GPP TS 28.702: "Telecommunication management; Core Network (CN) Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS)".

[60]	3GPP TS 28.703: "Telecommunication management; Core Network (CN) Network Resource Model (NRM) Integration Reference Point (IRP); Solution Set (SS) definitions".

[61]	3GPP TS 28.704: "Telecommunication management; IP Multimedia Subsystem (IMS) Network Resource Model (NRM) Integration Reference Point (IRP); Requirements".

[62]	3GPP TS 28.705: "Telecommunication management; IP Multimedia Subsystem (IMS) Network Resource Model (NRM) Integration Reference Point (IRP); Information Service (IS)".

[63]	3GPP TS 28.706: "Telecommunication management; IP Multimedia Subsystem (IMS) Network Resource Model (NRM) Integration Reference Point (IRP); Solution Set (SS) definitions".

[64]	3GPP TS 28.707: "Telecommunication management; Evolved Packet Core (EPC) Network Resource Model (NRM) Integration Reference Point (IRP); Requirements".

[65]	Void.

[66]	3GPP TS 28.709: "Telecommunication management; Evolved Packet Core (EPC) Network Resource Model (NRM) Integration Reference Point (IRP); Solution Set (SS) definitions".

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

VNF application specific parameters: The parameters, which are needed for realizing the network element function. These parameters are defined by 3GPP, such as network element name, network element address and so on.

VNF deployment specific parameters: The parameters, which are needed for instantiating/scaling/terminating a VNF. Generally, they are related to the deployment on virtualized infrastructure, such as VM parameters, connection point parameters and so on. These parameters are defined by ETSI NFV.

Network Functions Virtualization: see [7].

Network Functions Virtualization Orchestrator: see 5.4.1 of [2].

Network Service: see 6.2 of [2].

Virtualized Infrastructure Manager: see 5.4.3 of [2].

Virtualized Network Function Manager: see 5.4.2 of [2].

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in TR 21.905 [1] and the following apply. An abbreviation defined in the present document takes precedence over the definition of the same abbreviation, if any, in TR 21.905 [1].

CAPEX	CAPital EXpenditure

COTS	Commercial Off-The-Shelf

FFS	For Further Study

NFV	Network Functions Virtualization

NFVO	Network Functions Virtualization Orchestrator

NS	Network Service

OPEX	OPerating EXpense

OSS	Operations Support System

VIM	Virtualized Infrastructure Manager

VM	Virtual Machine

VNF	Virtualized Network Function

VNFM	Virtualized Network Function Manager

VR	Virtualized Resource

# 4	Concept and background

## 4.1 	Concept

Domain Manager (DM): provides element management functions and domain management functions for a sub-network which may include network elements with virtualized network functions or non-virtualized network functions or both. Inter-working domain managers provide multi-vendor and multi technology network management functions.

Element Manager (EM): provides a package of end-user functions for management of a set of closely related types of network elements which may include network elements with virtualized network functions or non-virtualized network functions or both. These functions can be divided into two main categories: Element Management Functions and Sub-Network Management Functions.

Network Element (NE): a discrete telecommunications entity (e.g. the RNC), which can be managed over a specific interface. The NE may contain virtualized or non-virtualized network function.

Network Manager (NM): provides a package of end-user functions with the responsibility for the management of a network which may include network elements with virtualized network functions or non-virtualized network functions or both, mainly as supported by the EM(s) but it may also involve direct access to the Network Elements. All communication with the network is based on open and well-standardized interfaces supporting management of multi-vendor and multi-technology Network Elements.

## 4.2 	Background

The 3GPP system may include a variety of different entities to deliver mobile services (see e.g. Figure 7.3.3.1 of [10]). It is expected that future implementation options for the entities of the 3GPP system include various technologies for virtualization.  Network and service providers make use of different information in several different ways which also may vary from network to network and from time to time. System architectures and technology choices, as well as the availability of off-the-shelf commercial systems and software components that fulfil the requirements established in the present document, may be critical to an operator's implementation of the specified management architecture. Large software systems, such as a network management system, are a capital investment that operators of mobile services cannot afford to replace every time its requirements change. Hence, entities of the 3GPP system that have been implemented with virtualization options should be managed in the same manner as entities implemented with non-virtualization options, to the extent possible.

The ETSI NFV ISG identified (see clause 4 of [11]) six business objectives for NFV:

-	Rapid service innovation through software-based deployment and operationalization of network functions and end-end services.

-	Improved operational efficiencies resulting from common automation and operating procedures.

-	Reduced power usage achieved by migrating workloads and powering down unused hardware.

-	Standardized and open interfaces between network functions and their management entities so that such decoupled network elements can be provided by different players.

-	Greater flexibility in assigning VNFs to hardware.

-	Improved capital efficiencies compared with dedicated hardware implementations.

The NFV business objectives for flexibility, operational efficiency and rapid service innovation requires a much more dynamic operating environment than traditional 3GPP operating environment.

In this dynamic operating environment the performance of the management interfaces is an important factor in delivering these business objectives. For example, the management interface performance in creation of new instances of 3GPP entities and their provisioning for operational readiness, are potentially significant factors in achieving the NFV business objectives.

The 3GPP defined VNFs still require some underlying hardware resources. The NFV business objective is that VNFs are procured independently from the hardware resources. This NFV business objective applies whether the entity has been partially virtualized (e.g. via SDN) or completely virtualized (see clause 6.4.2 of [12] for further discussion of partial vs complete virtualization). In many cases, the underlying hardware resources are expected to be administered independently from the virtualized entities required for the 3GPP system.  The ETSI NFV ISG has provided a number of use cases [11] illustrating multiple administrations with different types of service models. The default expectation is that the 3GPP defined VNFs would be one of potentially multiple tenants executing on an independently administered infrastructure.

# 5	Management use cases

## 5.1	Use cases for Fault management

### 5.1.1	Introduction

When a failure occurs in virtualized networks or mixed networks, several alarms associated with the failure might be generated and reported to one or more management functions (e.g. EM, VNFM or NFVO), which are defined in [2], to allow fault corrective action to be taken. This subclause includes use cases to show fault management flows including alarm reporting flows as follows:

1.	An alarm generated by NE (excluding NFVI)

2.	An alarm generated by NFVI

3.	An alarm generated by EM

4.	An alarm generated by VNFC

5.	TBD

### 5.1.2	Failure management when VNF detects VNF failure

#### 5.1.2.1	Introduction

This use case is to describe the management of VNF application layer failure detected by VNF.

#### 5.1.2.2	Actor

3GPP EM.

#### 5.1.2.3	Pre-condition

1.	EM is active.

2.	VNF has a fault.

#### 5.1.2.4	Description

1. 	VNF detects the fault and sends the alarms to EM.

2. 	EM may perform fault correlation. Based on the correlation analysis, the corrective action may trigger the execution of the VNF instance lifecycle management flows (e.g. VNF scaling) (Annex C in [2]). In case the corrective action needs to be performed by VNFM, EM sends a corrective action request toward VNFM.

3. The EM may further forward the alarms to NM.

4. 	NM may perform fault correlation anytime. Based on the fault correlation analysis, NM triggers a corrective action to repair the application layer failure. The corrective action may trigger the execution of the VNF instance lifecycle management flows (e.g. VNF scaling) or the Network Service instance lifecycle management flows. In case the corrective action needs to be performed by NFVO, NM sends a corrective action request toward NFVO.

5. 	Event representing VNF recovery is sent to NM because operator wants to know the change which is dynamically performed.

#### 5.1.2.5	Post-condition

The network operation works normally. The operator knows the recovery from the VNF failure.

### 5.1.3	Failure management when the alarm is generated by NFVI

#### 5.1.3.1	Introduction

This use case describes the failure management when the failure is generated by NFVI. The NFVI failure is processed by the VIM, and as a result the VIM exposes virtualized resource (VR) failure(s).

#### 5.1.3.2	Actor

ETSI MANO VNFM.

#### 5.1.3.3	Pre-condition

The VNF is active.

The VNF has detected an application failure and have reported it to EM.

The NFVI has detected a failure (e.g. compute, storage and networking related faults) and reported it to VIM.

#### 5.1.3.4	Description

1.	VIM sends VR failure reports to VNFM providing information about the possible cause of the failure (see step 1, in clause B.6 [1].

2.	VNFM identifies the VNF(s)/VNFC(s) affected by the VR failure. VNFM reports the failure to the EM(s) that manage the affected VNFs (see steps 2 to 3, in clause B.6 [1]).

3.	EM may correlate VNF’s VR failure reports from VNFM with VNF application failure reports from VNF. EM may request VNFM to initiate the healing process. EM may send the correlated or non-correlated failure reports to NM.

4.	NM may initiate healing process if needed.

#### 5.1.3.5	Post-condition

None.

### 5.1.4	Failure management when the EM detects VNF failure

#### 5.1.4.1	Introduction

This use case is to describe the management of VNF application layer failure detected by EM.

#### 5.1.4.2	Actor

3GPP NM and ETSI MANO NFVO.

#### 5.1.4.3	Pre-condition

1. 	EM is active.

2. 	The VNF has a fault.

#### 5.1.4.4	Description

1. 	EM detected the VNF fault.

2. 	Same steps as stated in 2 to 5 in clause 5.1.2.4.

#### 5.1.4.5	Post-condition

The network operation works normally. The operator knows the recovery from the VNF failure.

### 5.1.5	Failure management when the alarm is generated by VNFC

#### 5.1.5.1	Introduction

A VNF can be composed of a single or multiple VNF component(s) (VNFC). A VNFC is an internal component of a VNF providing a sub-set of that VNF's functionality defined by a VNF Provider, with the main characteristic that a single instance of this component maps one-to-one to a single virtualisation container [7]. A virtualisation container is a partition of a compute node that provides an isolated virtualized computation environment. An example of a virtualization container is a virtual machine (VM).

A single VNFC can fail due to diverse reasons. Possible failures can be related to virtualization aspects (e.g., configuration of VNF deployment specific parameters, interaction of a VNFC with another VNFC, etc.). Such failures can affect the overall VNF and need to be reported to trigger the automatic or on-demand healing of the VNF.

This use case exemplifies the failure management when the alarm is generated by the VNFC and the fault information is in the first instance sent to the VNFM (refer to clause 11.2 in [8] and step 4.2 in clause B.6 in [2] for examples). Refer to clause 5.1.4 in the present document for another option.

Note:	The fault information producer, i.e., VNF or EM, is to be determined. The following sub-clauses describe the use case where VNF provides such fault information.

#### 5.1.5.2	Actor

ETSI MANO VNFM.

#### 5.1.5.3	Pre-condition

The NFV management and orchestration (ETSI MANO) operation is active.

The 3GPP management operation is active.

The VNF is instantiated, configured (both deployment and application) and running.

The VNF may have detected an application failure and be already reported to EM.

#### 5.1.5.4	Description

The following steps are executed:

1.	The VNFC detects a failure, e.g., concerning its own virtualization context (e.g. configuration of VNF deployment specific parameters), the own VNF deployment (e.g. interaction of a VNFC with another VNFC).

2.	The VNF notifies the VNFM about the VNFC failure.

3.	The VNFM can correlate the VNFC failure with other virtualized resources failures received [2].

4.	In the case that the corrective action needs to be performed by the VNFM and the auto-healing is enabled, the VNFM can execute automatically the healing process notifying to the EM about the start and completion of the healing operation [2]. If the auto-healing is not enabled or the healing operation is not successful, the VNFM sends a notification of VNF failure to the EM.

5.	Same steps as stated in 2 to 5 in clause 5.1.2.4.

#### 5.1.5.5	Post-condition

If the VNF has self-healed, the network operation works normally, the operator knows the recovery from the VNF failure. If not, the operator knows about the VNF failure.

### 5.1.6	Notification of VNFCs impacted due to scheduled NFVI maintenance

#### 5.1.6.1	Introduction

The virtualization of the network function decouples the hardware from the software using virtualization technologies. Thus, the VNF makes use of virtualized resources.

The virtualized resources can be impacted, not only because of failures from the underlying hardware resources, but also because of possible scheduled maintenance of them. For instance, a scheduled update of the hypervisor software or the firmware of a physical machine (host) will likely impact the virtualized resources on top and consequently the execution of the VNF.

As a result, there is a need for notifying about VNF and any of its components, if they will be impacted due to maintenance of NFVI elements. Such notification is sent in advance to the actual maintenance. This is needed by the operator and management systems in order to act accordingly and minimize the impact and disruption of the VNF. This case is especially relevant when the network operator has different teams devoted to manage the 3GPP mobile network and the NFV infrastructure.

#### 5.1.6.2	Actor

ETSI MANO VNFM.

#### 5.1.6.3	Pre-condition

The NFV management and orchestration (ETSI MANO) operation is active.

The 3GPP management operation is active.

The VNF is running on top of NFVI.

#### 5.1.6.4	Description

The following steps are executed:

1.	ETSI MANO functional blocks process internally the notification of maintenance of an NFVI element (e.g. a physical machine), mapping such element to the virtualized resources (e.g. VM) that will be impacted due to such maintenance. In this process, the VNFM that manages the VNF whose virtualized resources are to be impacted is notified [2].

2.	The VNFM, if enabled and authorized, can try to mitigate the impact on the VNF. If the VNF will be impacted, the VNFM notifies the EM about the VNF and any of its components whose virtualized resources will be impacted due to maintenance of one or more than one NFVI element, identifying the cause (i.e. due to maintenance), the VNF and the components that are affected and the associated VIM.

3.	The EM can further forward such notification to the NM.

#### 5.1.6.5	Post-condition

The Operator and the 3GPP management system know about the maintenance status and further actions can be executed according to other management flows (e.g. change VNF configuration, migration of VNF components, request delaying the maintenance, etc.).

### 5.1.7	VM failure is detected by VNF application

#### 5.1.7.1	Introduction

This UC describes the expected VNF alarm reporting behaviour in case the VNF detects an alarm condition that is caused by the supporting VM (and not caused by its own VNF programming logic). Support of this UC does not imply a decision on the support of the following:

-	All VNFs should be capable of detecting VM failure;

-	All NFVIs should or should not report NFVI failure to VIM;

-	All VIMs should or should not detect NFVI failure.

This UC covers failure management cases which are detectable by VNF applications. The following failure case is out of scope of this UC:

- All VMs used by the VNF completely crash. It causes failure of all VNF functionalities.

#### 5.1.7.2	Actor

3GPP EM.

#### 5.1.7.3	Pre-condition

VNF is active.

#### 5.1.7.4	Description

1.	A VM service request failure occurs.

2.	VNF application determines that the VM service request failure is not caused by the VNF application programming logic:

a)	Sends the alarm indicating VM service request failure to EM; or

b)	If the VM service request failure causes a VNF application failure, sends an alarm indicating VNF application failure with probable cause indicating VM service request failure to EM.

3.	EM forwards alarm information to NM/OSS according to step 6.1 of clause B.6 of [2].

4.	EM can trigger a corrective action request towards VNFM according to step 6.2 of clause B.6 of [2].

#### 5.1.7.5	Post-condition

None.

### 5.1.8	VNF snapshot capture

#### 5.1.8.1	Introduction

By virtualizing a network function, capturing snapshots of the VNF and its components is possible. Together with other logging information, these snapshots can be used for multiple purposes, e.g. troubleshooting, rollback during erroneous VNF lifecycle management events or software upgrade, for fast VNF re-deployment, etc. A VNF snapshot can potentially contain one or several virtual machine snapshots, which in turn capture the state of the virtual machine configuration, the virtual disk and possibly memory dumps.

There is the possibility that capturing VNF and component snapshots can be executed automatically by the VNFM, or be triggered manually on-demand by the operator. In the manual case, the operator decides that a VNF or any of its components needs to be captured.

#### 5.1.8.2	Actor

3GPP EM and ETSI MANO VNFM.

#### 5.1.8.3	Pre-condition

The NFV management and orchestration (ETSI MANO) operation is active.

The 3GPP management operation is active.

#### 5.1.8.4	Description

Two initial triggers are possible:

a) 	In the manual case, three initial steps are processed:

1)	The operator initiates the snapshot capture of a VNF or any of its components by operating the 3GPP functional block.

2)	The EM requests to VNFM to execute the VNF lifecycle management operation of capturing snapshot of VNF or any of its components.

3)	The VNFM (ETSI MANO functional block) processes the request in the manual case.

b) 	In the automatic case, the following step is processed:

1)	The VNFM (ETSI MANO functional block) internally determines that capture of VNF or any of its components is necessary.

The following steps are executed both in the manual and automatic case:

1)	ETSI MANO functional blocks proceed with the capture of the VNF's virtual machine snapshots [2].

2)	The VNFM notifies to the EM with the information about the VIM and file paths to the snapshots.

3)	The EM can dump additional information (e.g. current configuration) and forwards to the NM such information together with the rest of information received from the VNFM.

#### 5.1.8.5	Post-condition

The operator has the information about where the snapshots and corresponding logs have been stored.

## 5.2	Use cases for Configuration Management

### 5.2.1	VNF instantiation and configuration for mixed network

#### 5.2.1.1	Introduction

This use case is intended to show how a VNF is instantiated in the mixed networks where PNF and VNF co-exist. That is a common scenario before NFV is fully deployed.

#### 5.2.1.2	Actor

3GPP EM (request originated by itself or by NM) and ETSI MANO NFVO (request originated by NM).

#### 5.2.1.3	Pre-condition

NM or EM detects that the PNF or VNF is overloaded and no VNF can be expanded to take over the load. In this case, NM or EM determines to initiate a new VNF instantiation.

#### 5.2.1.4	Description

1)	The request to instantiate a new VNF can come from NM (see step 1, in clause B.3.1.2 [2]), or EM (see step 1, in clause B.3.2.1 [2]).

2)	NFVO may call VNFM to instantiate the VNF and request VIM to allocate the resources required by the VNF instance (see steps 4 to 12 in clause B.3.1.2 [2]), if the request comes from NM. Otherwise, EM may call VNFM to instantiate the VNF and request VIM to allocate the resources required by the VNF instance (see steps 1 to 8 in B.3.2.1 [2]).

3)	After the successful resources allocation by VIM, VNFM configures the VNF with any VNF specific lifecycle parameters and notifies EM of the new VNF (see step 13, in clause B.3.1.2 [2]).

4)	EM then configures the VNF with application specific parameters (see step 14, in clause B.3.1.2 [2] and step 13, in clause B.3.2.2 [2]).

5)	NFVO acknowledges the completion of the VNF instantiation to NM after VNFM acknowledges the completion of the VNF instantiation (see steps 15 to 16, in clause B.3.1.2 [2]).

#### 5.2.1.5	Post-condition

A new VNF is instantiated to mitigate the overloaded PNF or VNF.

### 5.2.2	NFV configuration management

#### 5.2.2.1	Introduction

3GPP Configuration Management (CM) has the system modification functions and system monitoring functions (as described in [4]). It can support the operations of NE creation/deletion/conditioning and the other operations of information request/report or report control. NE can be configured into service or out of service and the NM can get the object creation/deletion and object attribute value change or state change notifications of NE.

NFV configuration management includes the configuration of VNF application specific parameters (3GPP mobile service related) and the configuration of VNF deployment specific parameters (non-3GPP mobile service related).

From 3GPP perspective, NE object and configuration parameters (e.g. identification, port, neighbour relation) are modelled as the Information Object Class attributes of CM. An example of IOC would be the MMEFunction defined in [5]. ETSI NFV MANO refers to IOC attributes as VNF application specific parameters.

The decoupling of software and hardware in NFV scenario gives rise to the need to model VNF deployment specific parameters  in a way that is applicable to all SDO's defined nodes. And VNF application specific parameters may need to be changed or enhanced by 3GPP.

Also, after the VNF deployment specific parameters or VNF application specific parameters are changed by VNFM or EM, EM should notify NM the necessary parameter change using CM capabilities (as described in [4]).

#### 5.2.2.2	Actor

3GPP EM, ETSI MANO NFVO (request originated by 3GPP NM).

#### 5.2.2.3	Pre-condition

Based on the operator's specified policy, the configuration management of VNF is triggered (e.g. scale out operation). EM or VNFM received the indication of VNF operation.

Before implementing the VNF operation, EM or VNFM may perform pre-operation activities (e.g. reconfiguring of nodes that are neighbour to the to-be-affected VNF).

#### 5.2.2.4	Description

1. EM sends the VNF lifecycle management request to VNFM (e.g. scale VNF, as described in [2], clause 7.2.4).

Or

1'. NM sends the configuration request to NFVO and NFVO interprets it into a specific VNF lifecycle management request and sends the request to VNFM.

Note 1: 	Some VNF lifecycle management operations (as described in [2], clause 7.2.4.2), which are Query VNF and Check VNF instantiation feasibility, may not be applicable in this use case.

2. VNFM receives this request then implements the corresponding operation to the VNF and completes configuration of VNF deployment specific parameters.

3. After the VNF deployment specific parameters are configured by VNFM, VNF is created, terminated or updated and the resource of the VNF is changed.

4. After the completion of the configuration, VNFM returns the success response to EM with necessary VNF change notification (as described in [2], clause 7.2.5).

5. EM performs post-operation activities (e.g. adjusting neighbour nodes of the affected VNF, configuring the VNF with application specific parameters).

6. EM notifies NM of all needed VNF resource changes through CM capabilities (as described in [4]).

Note 2: 	Whether the CM capabilities need to be enhanced is FFS. The hardware change information may not be needed and they may be replaced by Virtual Machine (VM) information.

Note 3: 	In order to manage the VNF network resource (as in NRM), the VNF application specific parameters, the VNF deployment specific parameters and the physical device parameters are specified or needed to be specified. 3GPP will study whether the VNF application specific parameters of the 3GPP-defined nodes should be changed or enhanced.

#### 5.2.2.5	Post-condition

The configured VNF can be managed by NM/EM and the all affected nodes are operational.

### 5.2.3	  VNF configuration management by EM in mixed network

#### 5.2.3.1	Introduction

The VNF application specific configuration management is needed during the lifecycle of VNF. In mixed network, the VNF application specific configuration management may be realized by EM and it may include:

1.	Configure the VNF application specific parameters after a VNF is instantiated;

2.	Release logical resource (e.g. managed objects, data structures) dedicated to manage the terminated VNF;

3.	Configure the VNF application specific parameters after a VNF is scaled, upgraded or updated.

Note:	Before VNF scale-in/scale-down/termination execution, there might be a need for NM/EM to adjust configuration parameters of nodes neighbour to the subject VNF.

The following use cases may be invoked by other use cases in present document when the VNF application specific parameters need to be configured, e.g. NFV configuration management use case in clause 5.2.2.

#### 5.2.3.2	Configure the VNF application specific parameters after a VNF is instantiated

##### 5.2.3.2.1	Introduction

After the VNF is instantiated, the VNF is in the Instantiated Not Configured state [6]. The VNF application specific parameters should be configured.

##### 5.2.3.2.2	Actor

ETSI MANO VNFM, 3GPP NM (request originated by NFVO or EM).

##### 5.2.3.2.3	Pre-condition

1. 	EM receives the VNF has been instantiated message from VNFM; or

2. 	NM receives the VNF has been instantiate message from NFVO; or

3. 	NM receives the VNF has been instantiated message from EM.

##### 5.2.3.2.4	Description

1. 	Under the pre-condition 2 or pre-condition 3, NM sends a configure VNF application parameters message to EM.

2. 	EM prepares the set of VNF application specific parameters for the newly instantiated VNF and creates the logical resource (e.g. managed objects, data structures) dedicated to manage the subject VNF.

3. 	EM performs pre-configuration activities e.g. reconfiguring of nodes that have relation with the subject VNF, if necessary.

4. 	EM configures the subject VNF with the prepared VNF application specific parameters (see step 12, in clause B.3.2.1 [2]).

##### 5.2.3.2.5	Post-condition

The VNF is operational.

#### 5.2.3.3	Release logical resource dedicated to manage the terminated VNF

##### 5.2.3.3.1	Introduction

After the VNF is terminated, EM may want to release its logical resource (e.g. managed objects, data structures) dedicated to manage the terminated VNF.

##### 5.2.3.3.2	Actor

ETSI MANO VNFM, 3GPP NM (request originated by NFVO).

##### 5.2.3.3.3	Pre-condition

1. 	EM receives the VNF has terminated message from VNFM; or

2. 	NM receives the VNF has terminated message from NFVO.

##### 5.2.3.3.4	Description

1. 	Under the pre-condition 2, NM forwards the VNF has terminate message to EM.

2. 	EM reconfigures nodes that have relation with the subject VNF, if necessary.

3. 	EM releases logical resource (e.g. managed objects, data structures) dedicated to manage the subject VNF.

##### 5.2.3.3.5	Post-condition

The logical resource (e.g. managed objects, data structures) dedicated to manage the subject VNF is released.

#### 5.2.3.4	Configure the VNF application specific parameters after a VNF is scaled, upgraded or updated

##### 5.2.3.4.1	Introduction

During the VNF lifecycle, VNF can be changed by some lifecycle operations, such as scale VNF, update VNF or upgrade VNF. After these lifecycle operations are executed, the VNF application specific parameters may also need to be configured.

##### 5.2.3.4.2	Actor

ETSI MANO VNFM, 3GPP NM (request originated by ETSI MANO NFVO or by 3GPP EM).

##### 5.2.3.4.3	Pre-condition

1. EM receives the VNF has been scaled message from VNFM; or

2. NM receives the VNF has been scaled or upgraded or updated message from NFVO; or

3. NM receives the VNF has been scaled message from EM.

##### 5.2.3.4.4	Description

1. 	Under the pre-condition 2 or pre-condition 3, NM decides whether the VNF application specific parameters need to be configured and if needed, NM sends a request to configure VNF application specific parameters to EM.

2. 	Under the pre-condition 1, EM decides whether the VNF application specific parameters need to be configured.

3. 	If needed, EM:

-	prepares the VNF application specific parameters to be configured in the subject VNF and update the logical resource (e.g. managed objects, data structures) dedicated to manage the subject VNF;

-	reconfigures nodes that have relation with the subject VNF, if necessary;

-	reconfigures the subject VNF with the prepared application specific parameters (see step 13, in clause B.4.4.1 and B.4.4.2 [2]).

##### 5.2.3.4.5	Post-condition

The VNF application specific parameters are updated.

### 5.2.4	Automatic re-connection of eNBs after lifecycle management of vMME

#### 5.2.4.1	Introduction

In the mixed network management, the scenario in which physical network elements are connected to virtualized network elements should be taken into consideration. Such scenario may occurr during a migration from the physical NE oriented network to virtualized NE oriented one. This clause considers the case in which non-virtualized eNBs are connected to vMMEs and includes one use case to show automatic re-connection of eNBs after lifecycle management of vMME.

This use case focuses on the recovery of connections between MMEs and eNBs so re-establishment of the connections between UEs and MMEs is out of scope of this use case.

#### 5.2.4.2	Actor

3GPP NM, 3GPP EM.

#### 5.2.4.3	Pre-condition

NFV management and orchestration operation is active. 3GPP management operation is active.

An MME pool consists of virtualized MMEs only and all vMMEs in the pool are active and controlled by single EM. These vMMEs do not have automatic recovery procedure using redundant back-up system.

The physical eNBs are connected to vMMEs.

#### 5.2.4.4	Description

1. 	All vMMEs of the MME pool have serious failure. The vMME failures result in complete shutdown of the vMMEs. Then the MME pool is completely shutting down based on the assumption described in the Pre-condition clause above.

2. 	The vMME failures are reported to the EM controlling the MMEs.  The EM determines the root cause and the corrective action which is described in the following steps.

Note: The failure detection and reporting procedure, root cause and impact analysis procedure and triggering procedure of the fault resolution action are FFS.

3. 	The EM controlling the MMEs issues sufficient number of Terminate VNF operations (7.2 of [2]) to terminate all vMMEs of the MME pool. For each successful response, the EM issues Instantiate VNF (7.2 of [2]) to instantiate a new VNF instance to replace the terminated vMME.

4. 	The EM controlling MME configures the newly instantiated VNFs for vMMEs.

5. 	The EM controlling MME notifies NM of vMME's re-instantiation.

Note: 	The following steps are needed in case an involvement of the EM controlling eNB is necessary for re-establishment of eNB-MME connection. In some cases (e.g. all the newly created vMMEs of the failed MME pool have identical GUMMEI to all those failure vMMEs, or only DNS involvement is needed for re-establishment), EM needs not reconfigure any eNBs.

6. 	NM notifies the EM controlling eNB of vMME's re-instantiation event.

7. 	The EM controlling eNB adjusts and reconfigures the affected eNBs, if required, e.g. so that the affected eNBs will connect to the newly instantiated and configured vMMEs.

8. 	The EM controlling eNB notifies NM of changes of eNBs' configuration.

#### 5.2.4.5	Post-condition

The eNBs have been successfully reconnected and are in operation.

## 5.3	Use cases for Performance Management

### 5.3.1	VNF Performance measurements reporting to EM

#### 5.3.1.1	Introduction

This use case consists of performance measurements related to VNF applications.

#### 5.3.1.2	Actor

3GPP NM, DM and EM.

#### 5.3.1.3	Pre-condition

NFV management and orchestration operation is active and 3GPP management operation is active.

A performance measurement has been generated in VNF.

#### 5.3.1.4	Description

1.	VNF sends VNF application-layer performance-related measurements (e.g. Mean and maximum numbers of dedicated EPS bearers in active mode (see TS 32.426 [13]) etc.) to EM.

2.	EM may forward the performance measurements to NM.

#### 5.3.1.5	Post-condition

Fault management function may be triggered by the performance measurement, if necessary.

### 5.3.2		Virtualized resource performance measurements

#### 5.3.2.1       Introduction

Virtualized resource performance measurements may be needed to provide additional information to indicate why VNF is not performing well.

This use case consists of performance measurements related to VR that are measured in NFVI.

#### 5.3.2.2       Actors

3GPP functional block (NM).

#### 5.3.2.3       Pre-condition

NFV management and orchestration operation is active, and 3GPP management operation is active.

A virtualized resources performance measurement has been generated in NFVI.

#### 5.3.2.4       Description

- VIM collects the performance data from NFVI. VIM reports the VR PM data to the correct VNFM managing the subject VNF/VNFC that consumes the VRs.

- VNFM identifies VNF/VNFC that consumes the VRs related to the received VR PM data, and forwards the received VR PM data to EM.

- EM maps the VNFC VR PMs to VNF level PMs and forwards the VNF PM data to NM.

Note: The requirement that NM needs VR PM data is TBD.

#### 5.3.2.4       Post-condition

VR PM data is successfully received.

## 5.4	Other Use cases involving Network Deployment

### 5.4.1	Information collection prior to capacity expansion

#### 5.4.2.1	Introduction

This use case is to show how the operator makes a decision to initiate the expansion of virtualized network functions or network services based on the available resources when doing the network planning of VNF/NS.

#### 5.4.2.2	Actor

3GPP NM.

#### 5.4.2.3	Pre-condition

Operator wants to do the large-scale capacity expansion.

#### 5.4.2.4	Description

1. 	NM queries NFVO the information about the currently available resources.

2. 	NFVO sends the information about the currently available resources to NM.

Note: 	If NFVO does not have the information about the currently available resources, it should request VIM to provide the information about the currently available resource.

3. 	Based on the statistic of the collected information about available resources, NM checks whether the currently available resources are sufficient for the expansion and if they are sufficient, NM can make a decision to initiate the expansion of virtualized network functions or network services (the expansion related use cases are described in clauses 5.2, 5.3 and 5.6).

#### 5.4.2.5	Post-condition

It is ready for the operator to do the large-scale capacity expansion.

## 5.5	Use cases for Core Network Lifecycle Management

### 5.5.1	Network Service Descriptor On-boarding

#### 5.5.1.1	Introduction

The use case assumes that the Network Service Descriptor (NSD) is supplied by the NM and on-boarding is triggered by the NM.

#### 5.5.1.2	Actor

3GPP NM.

#### 5.5.1.3	Pre-condition

1. 	NFVO is operational.

2. 	NM is operational.

3. 	NM possesses a valid NSD, with all needed mandatory elements, which is not on-boarded yet.

4. 	For VNFs that are part of the Network Service, there is on-boarded VNF Package and they possess all needed external interfaces.

#### 5.5.1.4	Description

1.	NM submits the NSD to the NFVO for on-boarding using the operation On-board Network Service Descriptor of the Network Service Descriptor interface as specified in [2] clause C.2.1.

2.	The NFVO processes the NSD as specified in [2] clause C.2.1 including validation of the NSD and checking presence of VNF Package for involved VNFs.

3.	The NFVO acknowledges the NSD on-boarding to the NM.

#### 5.5.1.5	Post-condition

The NSD is on-boarded.

### 5.5.2	Disable Network Service Descriptor

#### 5.5.2.1	Introduction

The use case assumes that the NSD is on-boarded and disablement of the NSD is triggered by the NM.

#### 5.5.2.2	Actor

3GPP NM.

#### 5.5.2.3	Pre-condition

1. 	NFVO is operational.

2. 	NM is operational.

3. 	NSD exists and is enabled

4. 	NM decided to disable on-boarded NSD.

#### 5.5.2.4	Description

1.	NM submits a request to disable a  NSD to the NFVO using the operation Disable Network Service Descriptor of the Network Service Descriptor interface according to [2] clause C.2.2.

2.	The NFVO processes the request according to [2] clause C.2.2.

3.	The NFVO acknowledges that the NSD has been disabled.

#### 5.5.2.5	Post-condition

The NSD is disabled.

### 5.5.3	Enable Network Service Descriptor

#### 5.5.3.1	Introduction

The use case assumes that the NSD is on-boarded and disabled; enablement of the NSD is triggered by the NM.

#### 5.5.3.2	Actor

3GPP NM.

#### 5.5.3.3	Pre-condition

1. NFVO is operational.

2. NM is operational.

3. NSD exists and is disabled.

4. NM decided to enable the NSD.

#### 5.5.3.4	Description

1.	NM submits a request to enable  the disabled  NSD to the NFVO, using the operation Enable Network Service Descriptor of the Network Service Descriptor interface according to [2] clause C.2.3.

2.	The NFVO processes and validates the request according to [2] clause C.2.3.

3.	The NFVO acknowledges that the NSD has been enabled to the NM.

#### 5.5.3.5	Post-condition

The NSD is enabled.

### 5.5.4	Update Network Service Descriptor

#### 5.5.4.1	Introduction

The use case assumes that the NSD is on-boarded; update of the NSD is triggered by the NM.

#### 5.5.4.2	Actor

3GPP NM.

#### 5.5.4.3	Pre-condition

1. 	NFVO is operational.

2. 	NM is operational.

3. 	NSD is on-boarded.

4. 	NM decided to update the NSD.

#### 5.5.4.4	Description

1.	NM submits modified NSD to the NFVO using the operation Update Network Service Descriptor of the Network Service Descriptor Management interface via the reference point Os-Ma-nfvo, according to the step 1 in [2], clause C.2.4.

Note:	This use case will be re-examined after ETSI provide a clear definition of NSD states (See clause A.4.3.1).

2.	The NFVO checks necessary conditions and performs all needed operations according to the steps 2 and 3 in [2], clause C.2.4

3.	The NFVO acknowledges the NSD update to the NM.

#### 5.5.4.5	Post-condition

The NSD is updated.

### 5.5.5	Query Network Service Descriptor

#### 5.5.5.1	Introduction

The use case assumes that the NSD is on-boarded.

#### 5.5.5.2	Actor

3GPP NM.

#### 5.5.5.3	Pre-condition

1. 	NFVO is operational.

2. 	NM is operational.

3. 	NSD is on-boarded.

4. 	NM decided to query the NSD.

#### 5.5.5.4	Description

1.	The NM sends a query request to the NFVO for the NSD using the operation Query Network Service Descriptor of the Network Service Descriptor Management interface via the reference point Os-Ma-nfvo, according to the step 1 in [2] clause C.2.5.

Note: 	This use case will be re-examined after ETSI provide a clear definition of NSD states (See clause  A.4.3.1).

2.	The NFVO performs needed operations, according to the step 2 in [2] clause C.2.5.

3.	The NFVO returns the NSD details to the NM.

#### 5.5.5.5	Post-condition

The NM possesses details of the NSD.

### 5.5.6	Delete Network Service Descriptor

#### 5.5.6.1	Introduction

The use case assumes that the NSD is on-boarded, disabled and not in use. There may be multiple versions of the NSD.

#### 5.5.6.2	Actor

3GPP NM.

#### 5.5.6.3	Pre-condition

1. 	NFVO is operational.

2. 	NM is operational.

3. 	NSD is on-boarded, disabled and not in use.

4. 	NM decided to delete the NSD.

#### 5.5.6.4	Description

1. NM submits the Request to delete the NSD to the NFVO, using the operation Delete Network Service Descriptor of the Network Service Descriptor Management interface via the reference point Os-Ma-nfvo, according to step 1 in [2] clause C.2.6.

Note:	This use case will be re-examined after ETSI provide a clear definition of NSD states (See clause A.4.3.1).

2.	The NFVO checks all needed conditions according to the step 2 in [2] clause C.2.6 and performs actions according to the step 3 in [2] clause C.2.6.

3.	The NFVO acknowledges to the NM execution of the NSD deletion.

#### 5.5.6.5	Post-condition

All versions of the NSD are removed.

### 5.5.7	VNF Package On-boarding

#### 5.5.7.1	Introduction

The use case assumes that the VNF Package is supplied by the NM and on-boarding is triggered by the NM and that the NFVO would perform the resource orchestration and the lifecycle management of network services and the 3GPP functional block NM would perform the network manager role for the virtualized network.

Note: 	No assumptions are made on mapping of OSS/BSS as described in [2] to 3GPP management reference model.

#### 5.5.7.2	Actor

3GPP NM.

#### 5.5.7.3	Pre-condition

1. 	NFV management and orchestration is operational.

2. 	Network management is operational.

3. 	NM possesses a VNF Package which is not on boarded yet.

#### 5.5.7.4	Description

1. 	The NM decides that VNF Package needs on-boarding and issues on-boarding request to the NFVO.

2. 	NFVO processes the VNF Package and on-boarding proceeds as specified in clause B.2.1 [2], steps 2 to 5.

3. 	NFVO acknowledges to the NM successful package on-boarding.

#### 5.5.7.5	Post-condition

The new VNF Package is on boarded.

### 5.5.8	Enabling VNF Package

#### 5.5.8.1	Introduction

The use case assumes that the VNF Package is on boarded and disabled; enablement is triggered by the NM and that the 3GPP functional block NM would perform the network manager role for the virtualized network and the ETSI MANO functional block NFVO would perform the resource orchestration and the lifecycle management of network services.

#### 5.5.8.2	Actor

3GPP NM.

#### 5.5.8.3	Pre-condition

1. 	NFV management and orchestration [2] is operational.

2. 	Network management is operational.

3. 	A VNF Package is on-boarded, disabled and is not marked as deletion pending.

#### 5.5.8.4	Description

1.	NM submits a request to the NFVO using the operation Enable VNF Package.

2.	The NFVO processes the request and enable the VNF Package.

3.	The NFVO acknowledges to the NM that the VNF Package is enabled.

#### 5.5.8.5	Post-condition

The new VNF Package is enabled.

### 5.5.9	Disabling VNF Package

#### 5.5.9.1	Introduction

The use case assumes that the VNF Package is on boarded and disablement is triggered by the NM and that the 3GPP functional block NM would perform the network manager role for the virtualized network and that the ETSI MANO functional block NFVO would perform the resource orchestration and the lifecycle management of network services.

#### 5.5.9.2	Actor

3GPP NM.

#### 5.5.9.3	Pre-conditions

1. 	NFV management and orchestration [2] is operational.

2. 	Network management is operational.

3. 	A VNF Package is on boarded

4. 	The VNF Package is enabled.

#### 5.5.9.4	Description

1.	NM submits a request to the NFVO using the operation Disable VNF Package.

2.	The NFVO processes the request and checks the VNF Package.

3. 	The NFVO disables the VNF Package.

4.	The NFVO acknowledges to the NM that the VNF Package has been disabled.

#### 5.5.9.5	Post-condition

The new VNF package is disabled.

### 5.5.10	VNF Package Update

#### 5.5.10.1	Introduction

The use case assumes that the VNF Package is on boarded and update is triggered by the NM and that the 3GPP functional block NM would perform the network manager role for the virtualized network and that the ETSI MANO functional block NFVO would perform the resource orchestration and the lifecycle management of network services. Note that "Update" means process by which a modified VNF Package is submitted to the NFVO to be included in the catalogue.

#### 5.5.10.2	Actor

3GPP NM.

#### 5.5.10.3	Pre-condition

1. 	NFV management and orchestration [2] is operational.

2. 	Network management is operational.

3. 	A VNF Package is on-boarded.

4. 	NM possesses a modified VNF Package which is not processed by NFVO.

#### 5.5.10.4	Description

1. 	The NM decides that VNF Package needs update; modified VNF Package is submitted to the NFVO using the operation Update VNF Package.

2. 	NFVO processes the modified VNF Package.

3. 	The NFVO acknowledges the VNF Package update.

#### 5.5.10.5	Post-condition

A modified VNF Package version is included in addition to the original one.

### 5.5.11	Querying VNF Package

#### 5.5.11.1	Introduction

Before running operations of VNF Package management, e.g. disable VNF Package, querying VNF Package is needed to retrieve the details of all VNF Package(s) or particular VNF Package(s) matching certain criteria(s), e.g. vendor(s). A VNF Package includes a VNFD and software image(s), according to clause 7.2.2.1[2]. The details of VNF Package(s), e.g. status and meta data of VNFD and image(s) (e.g. name, provider, version, size of the image(s)), could be available after the query. The use case assumes that the query is triggered by the NM.

#### 5.5.11.2	Actor

3GPP NM.

#### 5.5.11.3	Pre-condition

1. NFVO is operational.

2. NM is operational.

3. VNF Package(s) is on-boarded.

4. NM decided to query the VNF Package(s).

#### 5.5.11.4	Description

1.	The NM sends a query request to the NFVO for the VNF Package(s) using the operation Query VNF Package(s) of the VNF Package Management interface via the reference point Os-Ma-nfvo, according to the step 1 in [2] clause B.2.5.

2.	The NFVO performs needed operations, according to the step 2 in clause B.2.5 [2].

3.	The NFVO returns the details of VNF Package(s) to the NM.

#### 5.5.11.5	Post-condition

The NM possesses details of the VNF Package(s).

### 5.5.12    Deleting VNF Package

#### 5.5.12.1	   Introduction

For efficient management of VNF Packages there is a need to delete the packages that are not in use anymore.

The use case assumes that the VNF Packages are disabled and not in use. The use case describes deletion of VNF packages triggered by the NM.

#### 5.5.12.2	   Actor

3GPP NM.

#### 5.5.12.3    	   Pre-condition

1. NFV management and orchestration [2] is operational.

2. Network management is operational.

3. The VNF Package is onboarded, disabled and not in use.

#### 5.5.12.4    	   Description

- NM decides which VNF Package should be deleted.

- NM submits a request to the NFVO using the operation Delete VNF Package of the VNF Package management interface according to the step 1 in B2.6 [2].

- NFVO remove of the VNF Package from the catalogue.

- The NFVO processes the request as steps 4 to 5 in B.2.6 [2].

- NFVO acknowledges the VNF Package deletion request to the NM.

Note: From SA5’s perspective, deleting a particular VNF Package is a practical requirement.

#### 5.5.12.5    	   Post-condition

The VNF Package is deleted.

### 5.5.13	Instantiation of Core Network Service

#### 5.5.13.1	Introduction

This use case is to describe operator originated instantiation of core network service. To support the core network service, it may need the instantiation of multiple VNFs and setup the connections between the network elements.

#### 5.5.13.2	Actor

Operator.

#### 5.5.13.3	Pre-condition

Operator wants to deploy new network service.

#### 5.5.13.4	Description

1. 	Based on the network service requirements or the detection of constant traffic demand surging in a given area, operators plan and design the multi-vendor core network elements deployment which includes the related network elements information and the connection information between the network elements.

2. 	Operator performs VNF package on-boarding, if they are not on-boarded.

3. 	Operator performs network service descriptor on-boarding if they are not on-boarded.

4. 	Operator initiates the network service instantiation from the 3GPP functional block.

5. 	The instantiation of network service may include the instantiation of multiple related VNFs and the related connections.

6. 	For the instantiation of VNF, the virtual resources are allocated first by the ETSI MANO functional block.

7. 	After resources are allocated, the network element parameters and connections related configuration parameters are configured to VNF by the 3GPP functional block.

8. 	After all the network service related VNFs and the corresponding connections are configured, the virtualized network is ready to provide network service.

#### 5.5.13.5	Post-condition

The new network service is ready for operator to use.

### 5.5.14	Network Service instance scaling

#### 5.5.14.1	Introduction

Network Service scale out/in are important operations during the management of Network Services. They may be triggered at NM by operator manually or by some NM level functions (e.g. Load Balancing) automatically.

These UCs are to show the Network Service scale out/in operations once the needs are detected and the scaling actions are determined.

#### 5.5.14.2	Network Service instance scale out

##### 5.5.14.2.1	Introduction

None.

##### 5.5.14.2.2	Actor

3GPP NM.

##### 5.5.14.2.3	Pre-condition

NFV management and orchestration operation is active and 3GPP management operation is active.

NM detected the need to scale out and determined the scale out action.

##### 5.5.14.2.4	Description

1. 	NM requests NFVO to scale out a NS (Network Service) instance to a new deployment flavour.

2. 	NFVO initiates the corresponding NS instance scale out procedure. It is foreseen that NS can be scale-out either by expanding existing VNF instances or by instantiating new VNF instance(s).See clause C.4.1 in [2].

3. 	NM is informed by NFVO about the scaling out of NS.

4. 	NM configures the relevant scaled or instantiated VNFs via EM.

##### 5.5.14.2.5	Post-condition

NM configures the relevant scaled or instantiated VNFs via EM. The NS instance is scaled out to the new deployment flavour.

#### 5.5.14.3	Network Service instance scale in

##### 5.5.14.3.1	Introduction

None.

##### 5.5.14.3.2	Actor

3GPP NM.

##### 5.5.14.3.3	Pre-condition

NFV management and orchestration operation is active and 3GPP management operation is active.

NM detected the need to scale in and determined the scale in action.

##### 5.5.14.3.4	Description

1. 	NM requests NFVO to scale in a NS instance to a new deployment flavour.

2. 	NFVO initiates the corresponding NS instance scale in procedure. It is foreseen that NS can be scale-in either by contracting or terminating VNF instance(s). See clause C.4.2 in [2].

3. 	NM is informed by NFVO about completion of the scaling in of NS.

4. 	NM configures the relevant scaled VNFs via EM.

##### 5.5.14.3.5	Post-condition

NM configures the relevant scaled VNFs via EM. The NS instance is scaled in to the new deployment flavour.

### 5.5.15	Network Service instance update due to VNF instance modification

#### 5.5.15.1 	Introduction

Network Service update due to VNF instance modification is an important operation during the management of Network Services. It may be triggered at NM by operator manually or by some NM level functions (e.g. Self-healing) automatically.

This use case is to show the Network Service update due to VNF instance modification operation once the need is detected and the update action is determined.

#### 5.5.15.2	Actor

3GPP NM.

#### 5.5.15.3	Pre-condition

NFV management and orchestration operation is active and 3GPP management operation is active.

NM detected the need to update a NS instance and have determined the update action.

#### 5.5.15.4	Description

1. 	NM requests NFVO to update a NS instance.

2. 	NFVO initiates the corresponding NS instance update procedure. One or more new VNF(s) is/are instantiated and corresponding VNF(s) is/are terminated. See clause C.5 in [2].

3. 	NM is informed by NFVO about the update of NS.

4. 	NM configures the instantiated VNF(s) via EM.

#### 5.5.15.5	Post-condition

NM configures the instantiated VNF(s) via EM. The NS instance is updated due to the VNF instance modification.

### 5.5.16	Termination of Core Network Service Instance

#### 5.5.16.1	Introduction

The use case is intended to describe the termination of a core NS (instance). Multiple VNFs may need to be terminated in order to complete the core NS instance termination. The use case addresses the scenario whereby the termination of the core NS instance is initiated at NM, triggered by the operator. Note that the Use Case considers termination of core NS instances for both NS instances realized through a) mix network functions (i.e. virtualized network functions and physical network functions) and b) virtualized network functions only.

This use case addresses only the termination of an instance of a particular core NS previously instantiated using a relevant deployment template.

#### 5.5.16.2	Actor

3GPP NM.

#### 5.5.16.3	Pre-condition

The core NS exists and the 3GPP functional block is authorized to terminate the core NS instance.

The operator decides that a particular core NS instance is not required anymore and therefore the operator decides to terminate that particular core NS instance. For example the demand for a particular core NS instance has decreased to a point where its maintenance (continued offering) is no longer justifiable.

#### 5.5.16.4	Description

1. 	The operator triggers a particular core NS instance termination.

2. 	Based on the deployment template of the core NS instance targeted (requested by operator) for termination, NM may initiate termination of application level connections among VNFs/PNFs that are used by the targeted core NS instance. An example of application level connections that may be released during the termination of the core NS instance, could be the release of Data Radio Bearers as specified in [9] clause 8.2.3.2.1.

Note 1: 	NM should not terminate application level connections that are also used by other core NS instance(s) not targeted for termination.

3. 	NM initiates termination of the NS instance related to the targeted core NS instance toward NFVO, which may include termination of VLs [2] clause 6.4 and/or FGs [2] clause 6.5 set up by the ETSI MANO functional block in accordance to the procedure described in [2] clause C.6.. This step is not addressed further in this Use Case.

Note 2: 	NM should not initiate termination of the NS instance if the NS instance is also used by other core NS instances not targeted for termination.

4. 	Once the 3GPP functional block receives a positive response from the ETSI MANO functional block (i.e. acknowledgement that the NS instance termination is completed), the result of the NS instance termination is communicated by the 3GPP functional block to the operator.

#### 5.5.16.5	Post-condition

The Network Service Instance is terminated.

Some relevant connections (i.e. application level, VLs and FGs) among VNFs/PNFs used by the core NS instance targeted for termination and not used by other NS instances may have been terminated.

Some relevant VNFs used by the core NS instance targeted for termination and not used by other NS instances may have been terminated and their related resources may have been released.

The operator is notified with the result of the termination.

### 5.5.17	VNF expansion

#### 5.5.17.1	Introduction

VNF expansion refers to the addition of capacity that is deployed for a VNF and may result in a scale-out of a VNF by adding VNFCs to support more capacity or may result in a scale-up of virtualized resources in existing VNF/VNFCs (see clauses B.4.4.1 and B.4.4.2 in [2]).

This UC is to show the VNF expansion operations once the need is detected and the scaling action is determined.

#### 5.5.17.2	Actor

3GPP EM (request originated by self or by NM or by NFVO via NM).

#### 5.5.17.3	Pre-condition

NM or EM detected the need to scale and have determined the scaling action.

#### 5.5.17.4	Description

1.	EM, or NM (via EM or NFVO) requests capacity expansion to the VNFM (see step 2, in clause B.4.4.2 in [2]).

2.	VNFM notifies to the subscribed functional blocks (e.g., EM, NFVO) for lifecycle change notifications about initiating the scaling procedure.

Note: 	[2] does not contain information of such notification.

3.	VNFM expands the resources (see steps 8 to 10 in B.4.4.1 and B.4.4.2 in [2]).

4.	After successful resource expansion, VNFM sends EM the information that an existing VNF has additional capacity (see step 11 in clauses B.4.4.1 and B.4.4.2 in [2]).

5.	EM updates the VNF as a managed device (see step 12, in both clauses B.4.4.1 and B.4.4.2 in [2]).

6.	EM configures the VNF with application specific parameters (see step 13, in both clause B.4.4.1 and B.4.4.2 in [2]).

7.	EM sends information about the newly updated and configured additional capacity to the NM.

#### 5.5.17.5	Post-condition

VNF is in operational with expanded capacity.

### 5.5.18	VNF Contraction

#### 5.5.18.1	Introduction

VNF contraction refers to the removal of capacity from a deployed VNF and may result in scale-in of a VNF by removing VNFCs to free resources in the NFVI, or may result in scale-down of computing and memory resource from existing VNF/VNFCs (see clauses B.4.4.3, B.4.4.4 in [2]).

The goal is to show how VNF contraction operation can reduce capacity in NFVI, when NM or EM detects the capacity release opportunity.

#### 5.5.18.2	Actor

3GPP EM (request originated by self or by NM or by NFVO via NM).

#### 5.5.18.3	Pre-condition

NM or EM detects a capacity release opportunity and determines to trigger the VNF contraction.

#### 5.5.18.4	Description

1.	After NM, via EM, adjusts the configuration of the subject VNF and the nodes neighbour to the subject VNF if needed:

-	EM, or NM via EM requests capacity release for the VNF to the VNFM (see steps 2 to 5, in clause B.4.4.4 [2]) or

-	NM via NFVO requests VNFM to initiate VNF contraction.

2.	VNFM notifies to the subscribed functional blocks (e.g., EM, NFVO) for lifecycle change notifications about initiating the scaling procedure.

Note: 	[2] does not contain information of such notification.

3.	VNFM starts the process to terminate a VNF component (see step 6, in clauses B.4.4.3, B.4.4.4 [2]).

4.	Once the VNF component is gracefully terminated, the VNFM requests VIM directly to delete of the VM(s) (see step 7, in clauses B.4.4.3, B.4.4.4 [2]).

5.	After VIM acknowledging the successful resources release, VNFM notifies EM that an existing VNF has been updated with requested capacity reduction (see steps 8, 10 in clauses B.4.4.3, B.4.4.4 [2]).

6.	EM and VNFM update the VNF managed device (see step 12 in clauses B.4.4.3 [2], B.4.4.4 [2]).

7.	EM sends information about the VNF with reduced capacity to NM.

#### 5.5.18.5	Post-condition

VNF is in operational with reduced capacity.

### 5.5.19	 Termination of Core VNF instance

#### 5.5.19.1	Introduction

The use case is intended to show how VNF is terminated in the mixed networks where non-virtualized NE and VNF are co-existing. The use case addresses the scenario that the VNF termination is triggered at NM by the operator.

#### 5.5.19.2	Actor

This use case contains multiple sub use cases where each sub use case has its own actors that can be different than the actors of other sub use cases. The actors of sub use cases are not listed.

#### 5.5.19.3	Pre-condition

Operator decides a core VNF instance is not necessary any more. For example, operator may want to reduce the network capacity when the load of the network is continuously low and the network resources are not efficiently utilized.

#### 5.5.19.4	Description

1. 	Operator initiates the VNF instance termination operation from the 3GPP functional block.

2. 	The 3GPP functional block triggers application level termination. The influence of termination to the provided network service should be minimized.

3. 	After the application level termination is done, the selected core VNF instance related virtual resources are released by the ETSI MANO functional block.

4. 	The result of the VNF instance termination is reported to the operator.

#### 5.5.19.5	Post-condition

All VNF components of the selected VNF instance have been terminated, the related virtual resources (e.g. computing, storage, network and connectivity, etc.) have been released accordingly after the termination. Operator is notified with the result of the termination.

### 5.5.20	Notifications for VNF auto-scaling executed by VNFM

#### 5.5.20.1	Introduction

Auto-scaling refers to the automatic procedure controlled and executed by the VNFM to scale the capacity of a VNF (refer to clause B.4.1 in [2]). To execute such auto-scaling procedure, the VNFM does not need to request for an explicit granting of the operation to the EM, as long as it has been authorized to do so, e.g. through specific policies. However, it should be noted, that internally in ETSI NFV MANO, granting for resource provisioning or other procedures can still be performed, but these are outside of the scope of the current use case.

This use case illustrates the need for notifications to be sent by the VNFM to the EM with regards to auto-scaling procedure. Such notifications are useful for the EM, for instance, to assess any impact and needed reconfiguration of the managed VNF or other network functions.

Note: 	This use case will be re-examined after 3GPP SA5 has resolution of scaling request conflicts.

#### 5.5.20.2	Actor

3GPP EM.

#### 5.5.20.3	Pre-condition

The NFV management and orchestration (ETSI NFV MANO) operation is active.

The 3GPP management operation is active.

The VNFM has been granted to execute VNF auto-scaling.

There is no ongoing scaling procedure initiated by the EM and the EM does not perform any on-demand scaling request during the auto-scaling procedure.

#### 5.5.20.4	Description

The following steps are executed:

- The VNFM (ETSI MANO functional block) internally determines that auto-scaling of a VNF or any of VNF's components is necessary.

- The VNFM sends a notification to the EM about initiating the auto-scaling procedure.

Note 1: 	[2] does not contain information of such notification.

- ETSI MANO functional blocks proceed with the auto-scaling procedure. This can involve diverse interactions between ESTI MANO functional blocks to allocate/release virtualized resources or scaling existing virtualized resources (see clause 7.3.3.2 in [2]).

- In the case the auto-scaling finishes satisfactorily, the VNFM sends a notification to the EM about the successful execution of the VNF scaling (refer to clause 7.2.5 and clause B.4.4.1 in [2]). In the case that failures occur during the auto-scaling procedure, the VNFM sends notifications to the EM about the corresponding errors.

Note 2: 	[2] does not contain information of the auto-scaling error notifications.

#### 5.5.20.5	Post-condition

EM has the information about the initiation of VNF auto-scaling and whether the VNF auto-scaling execution including any of VNF's components is finished and if it was successful or faulty. With this information, the EM can perform VNF configuration or network adjustment, if required.

# 6	Potential requirements

## 6.1	Introduction

The following requirements are possible requirements to be used in a future normative work. The usage of "shall" or "should" should not be taken as mandatory in this study.

## 6.2	Requirements for management of VNF only network

### 6.2.1 	General requirements

REQ-NFVM_VN-GN-CON-1 Operator should be able to manage mobile networks that are composed of VNF instance(s) only.

Note: 	The following requirements defined in clause 6.1 also apply to management of mixed network.

REQ-NFVM_VN-GN-CON-2 The VNF corresponds to a 3GPP defined network element should be manageable by the same management interfaces as a non-virtualized 3GPP network element.

REQ-NFVM_VN-GN-CON-3 The performance of the management interface from the 3GPP Operations Support Systems in creation and provisioning of virtualized 3GPP entities should be adequate to achieve expected levels of mobile service performance.

REQ-NFVM_VN-GN-CON-4 For a VNF corresponding to an entity of a 3GPP system, the VNF’s underlying virtual resources, whose performance can affect or impact on the performance of the VNF, should be managed by ETSI-defined NFVO/VNFM/VIM in coordination with NM/EM managing the Managed Function corresponding to the subject VNF.

REQ-NFVM_VN- GN-CON-5 The following management functions should be supported:

-	The trace collection mechanism for virtualized nodes should follow the same trace collection for non-virtualized nodes as defined in TS 32.422 [14].

-	The performance management for virtualized nodes should follow the same performance management as defined in  TS 32.410 [15]/ TS 32.411 [16]/ TS 32.412 [17]/ TS 32.413 [18]/ TS 32.414 [19]/ TS 32.415 [20]/ TS 32.416 [21]/ TS 32.417 [22]/ TS 32.406 [23]/ TS 32.407 [24]/ TS 32.409 [25].

### 6.2.2 	CM requirements

REQ-NFVM_VN-CM-CON-1 EM should support the following CM functionalities through Itf-N:

-	The configuration management in term of IRPs should re-use as much as possible the configuration management capabilities defined in  TS 32.611 [26]/ TS 32.612 [27]/ TS 32.613 [28]/ TS 32.614 [29]/ TS 32.615 [30]/ TS 32.616 [31]/ TS 32.617 [32]/ TS 32.621 [33]/ TS 32.622 [34]/ TS 32.623 [35]/ TS 32.624 [36]/ TS 32.625 [37]/ TS 32.626 [38]/ TS 32.631 [39]/ TS 32.632 [40]/ TS 32.633 [41]/ TS 32.634 [42]/ TS 32.635 [43]/ TS 32.636 [44]/ TS 32.661 [45]/ TS 32.662 [46]/ TS 32.663 [47]/ TS 32.664 [48]/ TS 32.665 [49]/ TS 32.666 [50]/ TS 32.667 [51]/ TS 32.671 [52]/ TS 32.672 [53]/ TS 32.673 [54]/ TS 32.674 [55]/ TS 32.675 [56]/ TS 32.676 [57].

-	The configuration management for VNF application involving NRM should re-use as much as possible the configuration management capabilities defined in TS  TS 28.701 [58]/ TS 28.702 [59]/ TS 28.703 [60]/ TS 28.704 [61]/ TS 28.705 [62]/ TS 28.706 [63]/ TS 28.707 [64]/ TS 28.708 [5]/ TS 28.709 [66].

### 6.2.3 	FM requirements

REQ-NFVM_VN-FM-CON-1 EM should support the following FM capabilities:

-	Processing the alarms caused by virtualized resource faults affecting the VNF instance(s).

-	The correlation of alarms from VNF instance fault and relevant virtualized resource faults.

-	The reporting of VNF alarm with the virtualized resource fault information.

REQ-NFVM_VN-FM-CON-2 VNFM should support the following FM capabilities through Ve-Vnfm-em reference point:

-	The reporting of alarms caused by virtualized resource faults and virtual resource fault information with impacted VNF instance(s) identified to EM.

-	The reporting of alarms caused by failures concerning the VNF and the corresponding VNFC deployment on the virtualized infrastructure (e.g. configuration of the VNF, interactions of a VNFC with another VNFC).

REQ-NFVM_VN-FM-CON-3 VNFM should be provided with fault information that allows VNFM to perform virtualization-specific fault management regarding the fault-affected VNF in question. The producer, i.e., VNF or EM, of this information is to be determined.

### 6.2.4 	PM requirements

REQ-NFVM_VN-PM-CON-1 EM manages a number of VNFs. VNFM should be able to identify the VR performance measurements related to the managed VNFs, tag the VR performance measurements with the managed VNF identity and send the tagged VR performance measurements to the subject EM, via the Ve-Vnfm-em reference point.

REQ-NFVM_VN-PM-CON-2 EM should be able to emit notification indicating the PM measurement of a specific VNF instance or VNFC instance threshold crossing to NM. EM should emit notification indicating the PM measurement, of a specific VNF instance or VNFC instance threshold crossing to VNFM.

### 6.2.5 	LCM requirements

REQ-NFVM_VN-LCM-CON-1 EM should support the following lifecycle management functionalities:

-	Support the lifecycle management of VNF based on EM capabilities described in clauses 5.7.2, 7.2.4 and 7.2.5 [2] to allow NM acquire the information of lifecycle management through Itf-N, including:

-	Inform NM of the VNF lifecycle management events, such as the changes of VNF instance and virtualized resources of the VNF.

-	Inform NM of the VNF lifecycle operations' result.

REQ-NFVM_VN-LCM-CON-2 EM should be able to receive through Ve-Vnfm-em reference point a notification from VNFM about VNF and its components whose virtualized resources will be impacted due to scheduled maintenance of underlying infrastructure resources (e.g. scheduled update of the hypervisor software or the firmware of a physical machine (host)).

Note: 	[2] does not contain information about such notification and it is thus identified in the gap analysis (refer to A.4.4.1). This requirement will be re-examined after ETSI NFV provides a definition of the mentioned notifications from VNFM.

REQ-NFVM_VN-LCM-CON-3 EM should be able to request the snapshot capture of a VNF or any of its components through Ve-Vnfm-em reference point to VNFM

-	The result of the snapshot operation should provide to EM with enough information to locate and identify the snapshots.

Note 1: 	[2] does not contain information about VNF snapshot capture and it is thus identified in the gap analysis (refer to clause A.4.4.2). This requirement will be re-examined after ETSI NFV provides a definition of the mentioned snapshot capture functionality by VNFM.

REQ-NFVM_VN-LCM-CON-4 EM should be able to forward the snapshot information (e.g. file path and identifier of the snapshots) plus any additional information of the VNF (e.g. current configuration) to NM.

REQ-NFVM_VN-LCM-CON-5 EM should be able to receive the following healing (including healing through operation request to VNFM and auto-healing by VNFM) related notifications through Ve-Vnfm-em reference point from the VNFM, including:

-	A notification about the healing execution is to begin.

Note 2: 	[2] does not contain information of such notification and it is thus identified in the gap analysis (refer to clause A.4.4.3). This requirement will be re-examined after ETSI NFV provides a definition of the mentioned notification from VNFM.

-	A notification about the healing events related to the failures of VNF and its components.

-	A notification about the success or failure of the healing execution.

Note 3: 	In the context of this requirement, healing refers to corrective actions performed by the VNFM to recover the virtualization deployment of a faulty VNF and it concerns the actions for which the VNFM is responsible, i.e., instantiation of VNFC, configuration of VNF deployment specific parameters, etc.

REQ-NFVM_VN-LCM-CON-6 EM should be able to initiate VNF scaling request to VNFM through Ve-Vnfm-em reference point.

REQ-NFVM_VN-LCM-CON-7 NM should be able to initiate the VNF scaling request to NFVO through Os-Ma-nfvo reference point.

REQ-NFVM_VN-LCM-CON-8 NM should be able to initiate the NS scaling request to NFVO through Os-Ma-nfvo reference point.

REQ-NFVM_VN-LCM-CON-9 It should be possible for NM to obtain the information about currently available resources from NFVO.

REQ-NFVM_VN-LCM-CON-10 NM should be able to initiate the instantiation of VNF(s).

REQ-NFVM_VN-LCM-CON-11 NM should be able to initiate the termination of VNF instance(s).

REQ-NFVM_VN-LCM-CON-12 NM should be able to initiate the contraction of VNF instance(s).

REQ-NFVM_VN-LCM-CON-13 NM should be able to initiate the expansion of VNF instance(s).

REQ-NFVM_VN-LCM-CON-14 NM may consume the following interfaces related to Network Service lifecycle management, produced by NFVO through Os-Ma-nfvo reference point:

-	Network Service lifecycle management.

-	Network Service lifecycle change notification.

REQ-NFVM_VN-LCM-CON-15 NM should be able to consume the following operations with Network Service Descriptor (NSD), produced by the NFVO through Os-Ma-nfvo reference point:

-	On-board Network Service Descriptor

-	Disable Network Service Descriptor

-	Enable Network Service Descriptor

-	Update Network Service Descriptor

-	Query Network Service Descriptor

-	Delete Network Service Descriptor

REQ-NFVM_VN-LCM-CON-16 NM may support the following VNF lifecycle management capabilities through Os-Ma-nfvo reference point:

-	Support VNF lifecycle management.

-	Support VNF lifecycle change notification.

REQ-NFVM_VN-LCM-CON-17 NM should be able to consume the following operations related to VNF Package produced by NFVO through Os-Ma-nfvo reference point:

-	On-board VNF Package

-	Disable VNF Package

-	Enable VNF Package

-	Update VNF Package

-	Query VNF Packages

-	Delete VNF Package

REQ-NFVM_VN-LCM-CON-18 EM should be able to receive the following scaling (including on-demand scaling, scaling based on management request, and auto-scaling) related notifications through Ve-Vnfm-em reference point from the VNFM, including:

-	A notification that the scaling execution is about to begin.

Note 4:	 [2] does not contain information of such notification. Related requirement applying this notification for the auto-scaling methodology is identified in the gap analysis (refer to clause A.4.4.4). This requirement will be re-examined after ETSI NFV provides a definition of the mentioned notification from VNFM.

-	A notification about scaling events related to the virtualized resources of the VNF.

-	A notification about the success or failure of the scaling execution.

## 6.3	Requirements for management of mixed network

NOTE: 	The requirements defined in clause 6.2 also apply to management of mixed network.

### 6.3.1 	General requirements

REQ-NFVM_MN-GN-CON-1 EM(s) or EM(s)/NM(s) should have the capability allowing operator to manage the mobile network composed of VNF instance(s) and PNF(s).

REQ-NFVM_MN-GN-CON-2 EM should support the capability allowing the NM to manage VNFs and PNFs.

REQ-NFVM_MN-GN-CON-3 It should be possible to correlate application layer alarms of mixed network in a NM entity.

REQ-NFVM_MN-GN-CON-4 It should be possible to manage the application layer performance information of mixed network in a NM entity.

REQ-NFVM_MN-GN-CON-5 It should be possible to configure the application layer parameters of mixed network in a NM entity.

REQ-NFVM_MN-GN-CON-6 It should be possible to manage the trace functions and collect trace data of mixed network in a NM entity.

### 6.3.2 	CM requirements

TBD.

### 6.3.3 	FM requirements

TBD.

### 6.3.4 	PM requirements

REQ-NFVM_MN-PM-CON-1 VNFM should send performance measurements on virtualized resources to EM. The performance measurements on virtualized resources sent by VNFM is: a replication of performance measurements on virtualized resources received from VIM; or a correlated performance measurements on virtualized resources made by VNFM.

### 6.3.5 	LCM requirements

REQ-NFVM_MN-LCM-CON-1 NM informs relevant EM(s) about VNF lifecycle change.

REQ-NFVM_MN-LCM-CON-2 NM may consume the interfaces related to Network Service lifecycle management produced by NFVO through Os-Ma-nfvo reference point.

REQ-NFVM_MN-LCM-CON-3 EM should support the following functionalities when it is informed of VNF lifecycle change event:

-	Determine if adjustment of configuration parameters is required for its managed PNFs and VNFs, as a result of VNF lifecycle change event.

-	Perform the adjustment when the determination is positive.

# 7	Potential solutions

## 7.1	Management architecture

### 7.1.1 	Overview

Figure 7.1-1 illustrates the 3GPP management architecture which manages both virtualized and non-virtualized network functions and clarifies the relationship between 3GPP management framework and NFV-MANO framework. The NM and EM in figure 7.1-1 are both logical functions.

The following diagram does not imply extending the scope of 3GPP NFV study.

Figure 7.1-1: The mixed network management mapping relationship between 3GPP and NFV-MANO architectural framework

Note 1:	The network management role of OSS/BSS in ETSI NFV GSs is played by NM in 3GPP SA5.

Note 2: 	The relationship/impact of the interface between EM and VNFM with/on the 3GPP management reference model needs further discussion. Further specification and clarifications from ETSI NFV will be taken in consideration.

Note 3: 	The dash boxes of PNFs are optional for some specific virtualized network use cases.

Note 4: 	How to involve the MANO framework into the 3GPP management reference model is FFS.

### 7.1.2 	Involvement of 3GPP SA5 for NFV Management and Orchestration interfaces

Table 7.1.2-1 shows the possible functional areas which SA5 can contribute to the NFV management and orchestration standardization. However, it should be noticed that this list is not exclusive.

Table 7.1.2-1: Involvement of 3GPP SA5 for NFV Management and Orchestration Standardization

| Interfaces | Os-Ma-nfvo (OSS/BSS/NM - NFVO) | Ve-Vnfm-em (EM-VNFM) | Ve-Vnfm-vnf (VNF-VNFM) | Or-Vnfm (NFVO-VNFM) | Vi-Vnfm (VIM-VNFM) | Or-Vi (NFVO-VIM) | Itf-N (OSS/BSS/NM - EM) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Functions |  |  |  |  |  |  |  |
| Lifecycle management (LCM) | Network service(NS) (*1) | 3GPP SA5 (If NS is Infra NS, 3GPP plays no role. If NS is Mobile NS, 1. NM needs to trigger infra NS LCM when it is required for mobile NS. 2. NM needs to receive state/status information about the infra NS (supporting the mobile-NS)). |  |  |  |  |  | 3GPP SA5 (Define the operations and models for Mobile NS LCM) |
|  | VNF (*2) | 3GPP SA5 (If VNF is Generic VNF, 3GPP plays no role. If VNF is Mobile VNF, 1.NM needs to trigger Generic VNF LCM as part of the Mobile VNF LCM procedure. 2. NM needs to receive message about the outcome of Generic VNF LCM (supporting the mobile VNF.) | 3GPP SA5 (1. EM needs to trigger mobile VNF LCM. 2.EM needs to receive message about the outcome of VNF LCM ) | 3GPP SA5 (Ensure the initial configuration data for mobile network connectivity to be configured from VNFM to VNF) | 3GPP SA5 (Ensure the VNF LCM can satisfy the mobile VNF LCM needs) |  |  | 3GPP SA5 (Define the operations and models for Mobile VNF LCM) |
| FCAPS | Network services (*3) | 3GPP SA5 (NM needs to collect Infra NS FCAPS for correlation with the mobile network application layer NS FCAPS) |  |  |  |  |  | 3GPP SA5 (Define the operations and models for Mobile NS FCAPS) |
|  | VNF (*4) | 3GPP SA5 (NM needs to collect Generic VNF FCAPS for correlation with the mobile network application layer VNF FCAPS) | 3GPP SA5 (1.EM collects VNF related VR's FCAPS for correlation with mobile VNF FCAPS. 2. EM needs to trigger mobile VNF LCM) | 3GPP SA5 (Ensure the VNF whose VRs are impacted reports the VR data to VNFM) |  | 3GPP SA5 (Ensure the VR data can be correlated with Mobile VNF data) |  | 3GPP SA5 (Define the operations and models for Mobile VNF and mixed network FCAPS) |
| Virtualized Resource management (VRM) (*5) | 3GPP SA5 (NM may need to be able to trigger certain VRM) |  |  |  |  |  | 3GPP SA5 (make sure the VR data can be correlated with Mobile VNF data) |
| Policy administration (*6) | 3GPP SA5 (NM needs to be able to configure the VRM policy) |  |  | 3GPP SA5 (The forwarding of the VRM policy configuration) |  | 3GPP SA5 (Ensure the operator defined policy are forwarded) | 3GPP SA5 (Define Mobile VNF application level policy management) |
| Architecture (*7) | 3GPP SA5 (Define Mobile VNF and mixed network management architecture based on the ETSI NFV architecture) |
| E2E management procedures (mobile network) (*8) | 3GPP SA5 (Define Mobile VNF and mixed network E2E management for the mobile dedicated features with the reference of common procedures defined in ETSI NFV) |

Note1: "Life cycle management — Network Service": described in 7.1.1, 7.1.2, 7.1.3 [2].

NOTE 2: "Life cycle management — VNF": described in 7.2.1 to 7.2.5 [2].

NOTE 3: "FCAPS — Network Service": described in 7.1.4, 7.1.5, 7.5 [2].

NOTE 4: "FCAPS — VNF": described in 7.2.6 to 7.2.8 [2].

NOTE 5: "Virtualized Resource management": described in 7.3 [2].

NOTE 6: "Policy administration": described in 7.4 [2].

NOTE 7: "Architecture": described in 5 [2].

NOTE 8: "E2E management procedures (mobile network)" means the end-to-end procedures for NFV management (of mobile networks), including the interactions among all the relevant management entities (OSS/BSS/NM, EM, NFVO, VNFM, VIM) and VNF/PNF and if needed it will include the interactions between VNFs/PNFs too.

NOTE 9:"Infra NS": It's ETSI phase 1 defined NS. It involves the identifications of VNFs/PNFs and the properties of related virtual links and Forwarding Graphs."Mobile NS": It involves 3GPP defined nodes and the corresponding functions of 3GPP defined nodes. "Mobile VNF": It involves class attributes (extension of 3GPP non-virtualized XyzFunction like MmeFunction class)."Generic VNF": It's ETSI defined node. Generic VNF node is the node before applying domain specific parameters, it's not the 3GPP defined node.

## 7.2	Management interfaces and models

### 7.2.1	Global view of data flows

#### 7.2.1.1	FM & PM data flows

##### 7.2.1.1.1	MANO GS defined FM & PM data flows

The figure 7.2.1.1.1-1 below captures the FM data flows described in [2]. These flows are for a virtualized network. The flows are for virtualized resources, VNF and NS.

Figure 7.2.1.1.1-1: MANO GS defined data FM flows

Flow-1	VNF reports application level FM data to VNFM

Flow-2a	VNFM relays application level VNF FM data to NFVO

Flow-2b	VNFM relays resources FM data (mapped to VNF) to NFVO

Flow-3	VIM reports resources FM data to VNFM

Flow-4	VNFM relays resources FM data (mapped to VNF, correlated or not-correlated) to EM

Flow-5	VIM reports resources FM data to NFVO

Flow-6a	NFVO provides NS application level FM data to OSS/BSS (based on VNF FM received via flow 2a)

Flow-6b	NFVO provides resources FM data (based on VNF resources FM received via Flow-2b or Flow-5, mapped to VNF and NS, correlated or not-correlated) to OSS/BSS

Note 1:	According to ETSI, the necessity of Flow-1 is under discussion.

Note 2:	According to ETSI, the Flow-2b can carry correlated alarms regarding VNF FM data (received via Flow-1) and VR FM data (received via Flow-3). The use case for the Flow-2a is unclear (requires information from IFA WG).

The figure 7.2.1.1.1-2 below captures the PM data flows described in [2]. These flows are for a virtualized network. The flows are for virtualized resources, VNF and NS.

Figure 7.2.1.1.1-2: MANO GS defined PM data flows

Flow-1	VNF reports application level PM data to VNFM

Flow-2a	VNFM relays VNF application level PM data to NFVO

Flow-2b	VNFM relays resources PM data (mapped to VNF) to NFVO

Flow-3	VIM reports resources PM data to VNFM

Flow-4	VNFM relays resources PM data (mapped to VNF) to EM

Flow-5	VIM reports resources PM data to NFVO

Flow-6a	NFVO provides NS application level PM data to OSS/BSS (based on VNF application level PM data received via flow 2a)

Flow-6b	NFVO provides resources PM data (based on VNF resources FM received via Flow-2b or Flow-5, mapped to VNF and NS) to OSS/BSS

Note 1:	According to ETSI, the necessity of Flow-1 is under discussion. There is a dependency of Flow-2a and Flow-6a on the existence of Flow-1.

Note 2:	The term "application level PM data" used in this clause is equal to "application level PM measurements".

##### 7.2.1.1.2	3GPP view of FM & PM data flows

This clause covers both System Context A and B.

The figure 7.2.1.1.2-1 below captures the 3GPP view of FM data flows described in [2] plus the 3GPP defined FM data flows for non-virtualized NEs.

Figure 7.2.1.1.2-1: 3GPP view of FM data flows

Flow-X	Via 3GPP defined Reference Point VNF reports VNF FM data to EM

Flow-Y	Via 3GPP defined Reference Point EM reports/relays in correlated form to OSS/BSS the following: VNF FM data (received via Flow-X), resources FM data (received via Flow-4) and Non-virtualized NE FM data (received via Flow-Z)

Flow-Z	Via 3GPP defined Reference Point non-virtualized NEs report FM data to EM

Flow-1	EM relays VNF application level FM data to VNFM

Flow-2a	VNFM relays VNF application level FM data to NFVO

Flow-2b	VNFM relays resources FM data (mapped to VNF) to NFVO

Flow-3	VIM reports resources FM data to VNFM

Flow-4	VNFM relays resources FM data (mapped to VNF, correlated or not-correlated) to EM

Flow-5	VIM reports resources FM data to NFVO

Flow-6	NFVO provides NS FM data (based on resources FM data mapped to VNF and NS, correlated or not-correlated) to OSS/BSS

Note 1: According to ETSI, the necessity of Flow-1 is under discussion.

Note 2: According to ETSI, the Flow-2b can carry correlated alarms regarding VNF FM data (received via Flow-1) and VR FM (received via Flow-3). The use case for the Flow-2a is unclear (requires information from IFA WG).

The figure 7.2.1.1.2-1 below captures the 3GPP view of PM data flows described in [2] plus the 3GPP defined PM data flows for non-virtualized NEs.

Figure 7.2.1.1.2-2: 3GPP view of PM data flows

Flow-X	Via 3GPP defined Reference Point VNF reports VNF application level PM data to EM

Flow-Y	Via 3GPP defined Reference Point EM reports/relays in correlated form to OSS/BSS the following: VNF application level PM data (received via Flow-X), resources PM data (received via Flow-4) and Non-virtualized NE PM data (received via Flow-Z)

Flow-Z	Via 3GPP defined Reference Point non-virtualized NEs report PM data to EM

Flow-2b	VNFM relays resources PM data (mapped to VNF) to NFVO

Flow-3	VIM reports resources PM data to VNFM

Flow-4	VNFM relays resources PM data (mapped to VNF) to EM

Flow-5	VIM reports resources PM data to NFVO

Flow-6b	NFVO relays resources PM data (mapped to VNF and NS) to OSS/BSS

#### 7.2.1.2	CM notification data flows

TBD.

## 7.3	Management procedures

### 7.3.1 	Introduction

This clause describes the E2E management procedures regarding the management of mobile networks that include VNFs.

A dotted-line arrow in the procedures represents a request response or a notification. This dotted-line arrow is not a UML graphical notation.

### 7.3.2	LCM procedures

#### 7.3.2.1 	Instantiation of VNF

This procedure applies to the scenario that IP address is allocated by NM or EM/EM UI. The resources for VNF could be allocated by NFVO or VNFM.

NOTE: 	The IP address allocation needs FFS.

Scenario 1: VNFM allocates VNF resources

Main steps for this case are:

1.	VNFM receives VNF instantiation request, in which VNF IP address and the other relevant instantiate VNF operation input parameters (see clause 6.7 [2]) are included. There are three options for this step:

1)	Option 1: VNFM receives request from NFVO. NM initiates VNF instantiation and sends a request to NFVO, which forwards to VNFM. The IP address is allocated by NM. Refer to steps 1a.1-1a.2 in Figure 7.3.2.1-1.

2)	Option 2: VNFM receives request from EM/EM UI. NM initiates VNF instantiation and sends a request to EM, which forwards to VNFM. The IP address is allocated by NM. Refer to steps 1b.1-1b.2 in Figure 7.3.2.1-1.

3)	Option 3: VNFM receives request from EM/EM UI. EM/EM UI initiates VNF instantiation and sends a request to VNFM. The IP address is allocated by EM/EM UI. Refer to step 1c in Figure 7.3.2.1-1.

2.	VNFM sends Grant lifecycle operation to NFVO, which makes resource check and reservation, then optionally sends resource information to VNFM, which requests VIM to allocate resources (see steps 2 to 8, in clause B.3.2.1 [2]).

6.	VNFM configures VNF with deployment parameters, in which VNF IP address, or together with EM IP address is included and also VNFM allocated VNF ID.

7.	VNFM acknowledges successful VNF instantiation back to EM, here VNFM allocated VNF ID is included, if the VNF ID is unique within the management realm of VNFM, then VNMF should send VNF ID together with ID of itself.

8.	EM and VNFM both add VNF as managed object.

9.	EM, using the pre-allocated VNF IP address, sends application parameters to the VNF.

10.	 VNF Manager reports successful VNF instantiation to NFVO.

11. NFVO maps the VNF to the proper NFVI-PoP and Resource Pool.

Figure 7.3.2.1-1 VNF instantiation with resources allocated by VNFM

NOTE: 	Dotted rectangle area is indicated to be consistent with the agreement in ETSI NFV.

Scenario 2: NFVO allocates VNF resources

1.	NFV Orchestrator receives a request from NM to instantiate a new VNF, which includes VNF IP address, or EM IP address. The EM is the one that manages the VNF to be instantiated.

2.	NFV Orchestrator validates the request.

3.	Optionally, NFV Orchestrator runs a feasibility check of the VNF instantiation request to reserve resources before doing the actual instantiation.

4.	NFVO sends a VNF instantiation to NFVM, which includes VNF IP address or EM IP address.

5.	VNFM sends Allocate Resource request to NFVO, which together with VIM, makes resource allocation and sends response back to VNFM (see steps 5 to 12, in clause B.3.1.2 [2]).

6.	VNFM configures VNF with deployment parameters, which includes VNF IP, or EM IP, or VNFM allocated VNF ID.

7.	VNFM acknowledges successful VNF instantiation back to EM, here VNF ID and VNF IP are included, if the VNF ID is only unique within the management realm of VNFM, then VNMF should send VNF ID together with ID of itself.

8.	The EM configures the VNF with application specific parameters.

9.	VNF Manager acknowledges the completion of the VNF instantiation back to the NFV Orchestrator.

10.	 The NFV Orchestrator acknowledges the completion of the VNF instantiation.

Figure 7.3.2.1-2   VNF instantiation with resources allocated by NFVO

#### 7.3.2.2	VNF instance scaling procedures

##### 7.3.2.2.1	VNF instance scaling procedures with resource allocation done by VNF Manager

###### 7.3.2.2.1.1	VNF instance expansion procedure triggered by NM/EM

VNF expansion may be triggered by an automatic process or may be manually triggered by operator intervention.

VNF expansion may include the following actions:

-	configuration changes to the VM (scale up, e.g. add CPU or memory)

-	add a new VDU instance (scale out)

The main steps for the VNF instance expansion procedure triggered by command from NM/EM are:

1.	NM/EM/NM (via NFVO) requests capacity expansion to the VNF Manager using the operation Scale VNF of the VNF Lifecycle Management interface, see 1(a), 1(b) and 1(c).

2.	VNFM notifies to the subscribed functional blocks (i.e., EM and NFVO in this procedure as shown in diagram Figure 7.3.2.2-1 when they are subscribed to the notifications) for lifecycle change notifications about the start of the scaling operation using the VNF Lifecycle Change Notification interface.

Note: 	[2] does not contain information of such notification.

3. ~ 14. The VNF Manager requests a granting to the NFVO for the VNF expansion. VNF Manager reports successful VNF expansion to the NFVO (see step 13) and the EM (see step 11) using the VNF Lifecycle Change Notification interface. The NFVO is aware that the new VNF configuration is instantiated in the infrastructure. The NFVO maps the VNF to the proper VIM and resource pool. See clause B.4.4.2 [2].

Note: "new VNF configuration" needs further clarification (i.e. does it include VNF application configuration, or is it about only VNF deployment specific configuration)

15.	EM configures the VNF with application specific parameters.

Note: In [2], this step occurs before the notification of successful VNF expansion from the VNFM to the NFVO.

16.	EM sends information about the newly updated and configured additional capacity to NM.

Figure 7.3.2.2-1    VNF instance expansion procedure triggered by NM/EM

Note: For VNF expansion, the decision point and the trigger point is FFS.

###### 7.3.2.2.1.2	VNF instance contraction procedure triggered by NM/EM

VNF contraction may be triggered by an automatic process or may be manually triggered by operator intervention.

VNF contraction may include the following actions:

-	shut down and remove VMs (scale in)

-	release some virtualized resources from existing VMs (scale down)

The main steps for the VNF instance contraction procedure triggered by command from NM/EM are:

1.	NM/EM/NM (via NFVO) requests capacity contraction to the VNF Manager using the operation Scale VNF of the VNF Lifecycle Management interface, see 1(a), 1(b) and 1(c).

2.	VNFM notifies to the subscribed functional blocks (i.e., EM and NFVO in this procedure as shown in diagram Figure 7.3.2.2-2 when they are subscribed to the notifications) for lifecycle change notifications about the start of the scaling operation using the VNF Lifecycle Change Notification interface.

Note: 	[2] does not contain information of such notification.

3. ~ 11.	The VNF Manager requests validation to the NFVO for the VNF contraction. The NFVO grants the scale-in operation of the VNF to the VNF Manager. VNF gracefully terminates a VNF component. VNF Manager reports successful VNF contraction to the NFVO (see step 9) and EM (see step 10) using the VNF Lifecycle Change Notification interface. The NFVO updates the proper VIM and resource pool map. See clause B.4.4.4 [2].

12.	EM and VNF Manager update the VNF managed device.

13.	EM sends information about the newly updated capacity to NM.

Figure 7.3.2.2-2   VNF instance contraction procedure triggered by NM/EM

Note: For VNF contraction, the decision point and the trigger point is FFS.

#### 7.3.2.3 	Termination of IMS/EPC VNF instance Procedure

There are the following procedures for the termination of VNF instance when the resources are released by NFVO:

1. 	Termination request is sent from NM to EM.

2. 	Termination request is sent from NM to NFVO.

For Termination request is sent from NM to EM, there are following steps for VNF instance termination:

1.	NM finds it necessary to terminate a VNF instance and sends a request to EM.

2.	EM sends VNF instance termination request to VNFM.

3.	VNFM forwards the request to NFVO.

4.	NFVO validates the request and permits the termination of the VNF instance. VNFM releases VNF instance according to NFVO's request and VIM releases resources after receiving NFVO's request. (see steps 2 to 9, in clause B.5 [2])

5.	NFVO acknowledges the completion of the VNF instance termination back to VNFM.

6.	VNFM forwards the acknowledgement to EM.

7.	Upon receiving the request, EM deletes the corresponding Managed Object.

8.	EM sends acknowledgement to NM.

Figure 7.3.2.3-1 Termination request is sent from NM to EM

For Termination request is sent from NM directly to NFVO, there are following steps for VNF instance termination:

1.	NM finds it necessary to terminate a VNF instance and sends a request to NFVO.

2.	NFVO validates the request.

3.	NFVO calls VNFM to terminate of the VNF.

4.	VNFM sends terminate VNF request to EM.

5.	EM deletes the VNF from its managed device list.

6.	EM sends ACK back to VNFM.

7.	VNFM terminates the VNF and sends ACK to NFVO, which imitates resource release for the VNF in coordination with VIM. (see steps 4 to 9, in clause B.5 [2])

8.	NFVO acknowledges the completion of the VNF instance termination to NM.

NOTE: 	Step 7 could be parallel procedure with steps 4 to 6.

Figure 7.3.2.3-2 Termination request is sent from NM directly to NFVO

#### 7.3.2.4 	Instantiation of Network Service

The following steps are for NS instantiation procedure:

- NM sends a request to NFVO to instantiate a new Network Service.

- NFVO instantiates Network Service based on NSD. (see steps 2 to 12, in clause C.3 [2]).

Note1: Detailed content of NSD is to be defined in ETSI IFA.

- NFVO acknowledges completion of the Network Service instantiation to NM.

- NM instructs relevant EMs to activate/turn-on VNFs/PNFs virtual port and be ready to receive and transmit.

Note2: NM may request several EMs since the group of VNFs/PNFs can be managed by multiple EMs.

Figure 7.3.2.4   NS instantiation flow

#### 7.3.2.5 	Termination of Network Service

The following steps are for NS instance termination procedure:

- NM decides to terminate a NS, identifies all related VNFs, and instructs EM to terminate the VNF instance that serves the NS only.

- EM deletes management object for the VNF, and sends ACK to NM.

- NM instructs relevant EM(s) to deactivate/turn-off the VNFs/PNFs virtual port.

Note1: NM may request several EMs since the group of VNFs/PNFs can be managed by multiple EMs.

- NM sends NS termination request to NFVO.

- NFVO terminates VNFs according to requirement sent by NM. (see steps 2 to 8, in clause C.6 [2]).

- NFVO acknowledges NS termination to NM.

Figure 7.3.2.5    NS termination flow

### 7.3.3	FM procedures

#### 7.3.3.1	FM procedure flow for correlation done in EM

##### 7.3.3.1.1 	Introduction

There are two categories of fault reports related in the FM procedure:

-	VR fault report

-	VNF application fault report

##### 7.3.3.1.2 	VR resource fault report procedure

1.	The NFVI detects VR failure and reports to VIM.

2. 	When VIM receives the fault report, it will include the fault related VM information and creates a failure report and sends it to the corresponding VNFM.

3. 	VNFM identifies which VNFs are impacted based on VIM report.

4. 	VNFM creates VNF related virtual resource failure report and sends it to corresponding EM.

Note: 	Details of reporting process in dashed box are needed to be defined in ESTI NFV to support this function.

##### 7.3.3.1.3 	VNF application fault report procedure

5. 	VNF detects the VNF application failure (e.g. NFVI failure may lead to VNF application failure) and sends a failure report to EM.

##### 7.3.3.1.4 	fault correlation done in EM procedure

6. 	Based on VR fault report from VNFM and VNF application fault report from VNF, EM makes correlation and analysis of impact and if necessary, triggers corrective actions.

Figure 7.3.3.1-1   fault correlation done in EM

#### 7.3.3.2	FM procedure flow for correlation in VNFM

##### 7.3.3.2.1 	Introduction

In the present FM procedure flow, there are two categories of fault reports that can be correlated in VNFM:

-	VR fault report

-	VNF/VNFC fault report

The procedure shows correlation at another level other than correlation done in EM (see clause 7.3.3.1).

Note:	The producer of the VNF/VNFC fault report, i.e., VNF or EM, is to be determined. The following sub-clauses describe the procedure where VNF provides the VNF/VNFC fault report.

##### 7.3.3.2.2 	VR fault report procedure

1.	The NFVI detects VR failure(s) and reports it to the VIM.

2. 	When the VIM receives the failure report, it will supplement/amend the failure related VR information, create a VR fault report, and send it to the corresponding VNFM.

3. 	The VNFM identifies which VNFs are impacted based on the VR fault report.

##### 7.3.3.2.3 	VNF/VNFC fault report procedure

4.	The VNF detects failure(s) related to virtualization aspects (e.g., configuration of the VNF deployment specific parameters, interaction of a VNFC with another VNFC, etc) and reports the fault to the VNFM.

##### 7.3.3.2.4 	Fault correlation in VNFM

5. 	Based on the VR fault report from the VIM (see step 2 in clause 7.3.3.2.2) and the VNF/VNFC fault report (see step 4 in clause 7.3.3.2.3) from the VNF, the VNFM performs a correlation and analysis of the reported faults and their impact. If necessary, the VNFM triggers corrective actions.

6. 	The VNFM creates a VNF virtualization related fault report and sends it to corresponding EM.

Figure 7.3.3.2-1   FM procedure flow for correlation in VNFM

#### 7.3.3.3	FM procedure flow for notification of VNFCs impacted due to scheduled NFVI maintenance

The main steps for the FM procedure flow for notification of VNFCs impacted due to scheduled NFVI maintenance are:

1.	VIM marks the status of NFVI resources that will be affected by a maintenance procedure as maintenance.

2.	The VIM finds VRs that are affected by the maintenance status of the NFVI resources.

3.	The VIM notifies the VNFM, whose VNF(s) are consuming the virtualized resources, about the virtualized resources that will be affected by the maintenance of underlying NFVI resources.

Note 1: NFVI maintenance work may or may not maintain the serviceability of the VRs as expected. This UC is about the NFVI maintenance work that would not maintain the serviceability of the VR as expected.

Note 2: The notification due to maintenance is an example of type of notifications that VIM should issue when it determines the serviceability of the virtualized resources cannot be maintained as expected.

4.	The VNFM finds the VNF and corresponding VNFC(s) whose virtualized resources have been notified from step 3.

5.	The VNFM notifies the subscribed functional blocks (e.g., the EM and/or NFVO) about the VNF and any of its VNFCs whose virtualied resources will be impacted due to the maintenance of underlying NFVI resources. The VNFM provides information about the cause (e.g., due to maintenance), and identifies the VNF, its VNFCs, and the associated VIM.

-	The VNFM, if enabled and authorized, can try to mitigate the impact on the VNF (e.g. switch to a backup system, migrate the VNFs/VNFCs in question, etc.).

Figure 7.3.3.3-1   Notification of VNF and VNFCs impacted due to scheduled NFVI maintenance

#### 7.3.3.4	FM procedure flows for healing through operation request to VNFM and auto-healing

##### 7.3.3.4.1	Procedure flow for VNF healing through operation request to VNFM by EM

The main steps for the FM procedure flow for VNF healing through operation request to VNFM by EM are:

Note: 	In the context of this procedure, healing refers to corrective actions performed by the VNFM to recover the virtualization deployment of a faulty VNF and it concerns the actions for which the VNFM is responsible, i.e., instantiation of VNFC, configuration of VNF deployment specific parameters, etc.

1.	VNFM has received VR and VNF-related fault notifications. The VNFM identifies which VNFs are impacted based on such failure reports. No VNF auto-healing by VNFM is performed, e.g., because of unavailability of auto-healing scripts, or because the policy for auto-healing is not active or not applicable.

2.	VNFM creates a VNF-related virtualized resource fault report and sends it to the corresponding EM.

3.	VNF detects the VNF application failure (e.g., virtualized resource failures may lead to a VNF application failure) and sends a fault report to EM.

4.	Based on failure reports from steps 2 and 3, the EM makes correlation and analysis of impact. The EM determines the corrective action to be performed by healing the VNF.

5.	EM requests the VNFM to execute the VNF healing, passing enough information to determine the VNFC(s) that shall be recovered. The VNFM acknowledges the EM the request.

6.	Start notifications of the VNF lifecycle operation (i.e., healing in this procedure) are sent by the VNFM to subscribed functional blocks, including e.g., EM (refer to step 6a in Figure 7.3.3.4-1) and NFVO (refer to step 6b in Figure 7.3.3.4-1).

7.	VNFM executes the steps to terminate the impaired VNFCs, re-create the affected VNFCs, and configure the VNF/VNFCs based on the re-deployed VNFC instances. NFVO and VIM support this process with the necessary steps for lifecycle operation granting and virtualized resource management.

8.	End notifications of the VNF lifecycle operation  (i.e., healing in this procedure) are sent by the VNFM to subscribed functional blocks, including, e.g., EM (refer to step 8a in Figure 7.3.3.4-1), and NFVO (refer to step 8b in Figure 7.3.3.4-1).

Figure 7.3.3.4-1   VNF healing through operation request to VNFM by EM

##### 7.3.3.4.2	Procedure flow for VNF auto-healing by VNFM

The main steps for the FM procedure flow for VNF auto-healing by VNFM are:

Note: 	In the context of this procedure, healing refers to corrective actions performed by the VNFM to recover the virtualization deployment of a faulty VNF and it concerns the actions for which the VNFM is responsible, i.e., instantiation of VNFC, configuration of VNF deployment specific parameters, etc.

1.	VNFM has received VR and VNF-related fault notifications, and it identifies which VNFs are impacted based on such failure reports.

2.	VNFM determines auto-healing to be executed, e.g., because of availability of auto-healing scripts, and the auto-healing policy is active.

3.	Start notifications of the VNF lifecycle operation (i.e., healing in this procedure)  are sent by the VNFM to subscribed functional blocks, including, e.g., EM (refer to step 3a in Figure 7.3.3.4-2), and NFVO (refer to step 3b in Figure 7.3.3.4-2).

4.	VNFM executes the steps to terminate the impaired VNFCs and re-create the affected VNFCs and configure the VNF/VNFCs based on the new re-deployed VNFC instances. NFVO and VIM support this process with the necessary steps for lifecycle operation granting and virtualized resource management.

5.	End notifications of the VNF lifecycle operation (i.e., healing in this procedure) are sent by the VNFM to subscribed functional blocks, including, e.g., EM (refer to step 5a in Figure 7.3.3.4-2), and NFVO (refer to step 5b in Figure 7.3.3.4-2).

Figure 7.3.3.4-2   Auto-healing of VNF by VNFM

#### 7.3.3.5	VNF snapshot capture procedure

The main steps for the VNF snapshot capture procedure are:

1.	The EM requests to VNFM to execute the VNF lifecycle management operation of capturing snapshot of VNF or any of its components.

2.	The VNFM processes the request and identifies the VNF and VNFCs for which a snapshot is requested to be captured. The VNFM determines the order in which the individual VNFC snapshot captures need to be performed.

Note:	The steps of the procedure within the dotted line box in Figure 7.3.3.5-1 are expected to be detailed and specified by ETSI ISG NFV, and 3GPP SA5 will leverage the solution provided by ETSI ISG NFV. The steps shown in the present clause are described for completeness of the end-to-end procedure,

3.	For each VNFC to capture a snapshot, the VNFM sends a virtualized resource snapshot operation request to the VIM.

4.	The VIM and NFVI execute the virtualized resource snapshot, e.g., VM snapshots using the hypervisor support.

5.	The VIM acknowledges the result of the virtualized resource snapshot operation providing information about the filepath of the snapshot.

6.	The VNFM processes the results of the virtualized resource snapshot operation and prepares the VNF snapshot capture result report.

7.	The VNFM acknowledges the EM the result of the VNF snapshot capture providing information about the VIM and information to help locate the snapshots.

8.	The EM can dump additional information (e.g., current VNF configuration).

Figure 7.3.3.5-1    VNF snapshot capture procedure

### 7.3.4 	CM procedures

#### 7.3.4.1	Adding a MME VNF to the MME pool

This procedure shows how a MME VNF can be automatically instantiated, and added to the MME pool.

Note: The pre-condition is that the VNF package has been on-boarded.

1.  NM sends a request to NFVO to instantiate a new MME (VNF) (see step 1, in clause B.3.1.2 [2]).

2. NFVO requests the VNFM to instantiate the MME (VNF) instance. As part of the internal NFV-MANO procedure, VIM processes requests to create and start the VM(s) and relevant networking resources (see steps 2 to 12, in clause B.3.1.2, or steps 2 to 9 in Clause B.3.2.1 [2]).

3. VNFM sends a notification of successful MME VNF instantiation to EM (see step 13, in clause B.3.1.2 [2]).

4. EM works with NM to add the vMME to the MME pool by configuring the MME VNF with application specific parameters (see step 14, in clause B.3.1.2, or step 12 in clause B.3.2.1 [2])

5. VNFM sends an acknowledgement of successful MME VNF instantiation to NFVO (see step 15, in clause B.3.1.2 [2])

6. NFVO acknowledges the completion of the VNF instantiation to NM (see step 16 in clause B.3.1.2 [2]).

Figure7.3.4.1-1    Adding MME VNF to the MME pool procedure

#### 7.3.4.2	Removing a MME VNF from the MME pool

This procedure shows how a MME VNF instance can be terminated and removed from the MME pool.

Note: A MME VNF has been previously instantiated.

- NM requests EM to decommission MME services that are provided on the VNF to be terminated.

- EM gracefully decommissions MME VNF services, if MME VNF is providing services.

- EM works with NM to remove MME VNF from the MME pool.

- EM acknowledges the decommissioning of MME VNF services.

- NM sends a request to NFVO to terminate a MME VNF (see step 1 in B.5 [2]).

- NFVO validates the request, terminate MME VNF instance, and release the virtualized resources (see steps 2 to 9 in B.5 [2]).

- NFVO acknowledges the completion of the MME VNF termination to NM (see step 10 in B.5 [2]).

Figure7.3.4.2-1    Removing MME VNF from the MME pool procedure

#### 7.3.4.3 	Information exchange following VNF lifecycle management

This is the procedure when configuration change is needed as a result of VNF lifecycle management. This procedure is based on the premise that the decision of necessary lifecycle management procedure for causal failure has already been done.

In this procedure, there are two different EMs:

- EM-a: EM controlling the VNF in which the lifecycle management operation occurs.

- EM-b: EM controlling the VNF or the PNF (representing as a “NE” in the diagram) which may be affected by the VNF lifecycle management written above.

EM-a and EM-b do not have direct connection thus any information exchange should be supported via NM except for the case that the VNF and the NE are controlled by single EM.

The main steps for this procedure are:

- The lifecycle management operation for the VNF completed. This step includes a notification to the NM of the completion of lifecycle management of the VNF.

NOTE: This step corresponds to steps of VNF instantiation, update or termination notification/ack described in B.3, B.4 and B.5 of [2]. The EM-b does not engage in this step.

Following steps are executed based on the notification in step 1, if needed.

- NM identifies EM(s) which controls NE(s) affected by the VNF lifecycle management operation.

NOTE: In this procedure, EM-b is identified through this step.

- NM instructs EM-b to perform configuration changes invoked by the lifecycle management operation of the VNF controlled by EM-a.

- EM-b performs configuration change(s).

- EM-b may inform NM of the result of the adjustment if required.

Figure 7.3.4.3-1   Information exchange following VNF lifecycle management

### 7.3.5 	PM procedures

#### 7.3.5.1 VNF performance management

VNF performance management follows the same procedure of the non-virtualized network performance management.

# 8	Conclusions and recommendations

## 8.1	General Conclusions

In the study, the outcome of ETSI NFV ISG MANO has been taken into account.

The scope of the study is the management of mobile networks that include VNFs for core nodes but excludes VNFs for RAN nodes. The mobile network being studied can/may have all its core nodes virtualized.

Current SA5 network management standard focuses on the management of the node functions and have minimal or non-existent standard solution to manage the hardware supporting the node functions. The future SA5 management specifications for mobile networks that include VNFs would include (recommend) standard solutions to allowing the VNF's required hardware to be administrated independently.

The challenge, when introducing management solutions for mobile networks that include VNFs, is to:

a)	utilize the solutions specified by the ETSI NFV project as is, and

b)	reuse maximally the architecture/tools/management process that have been in deployment for the management of node functions.

## 8.2	Conclusions on potential use cases

The following management use cases for network management involving virtualized networks have been identified:

-	Use cases for Fault Management

1)	Failure management when VNF detects VNF failure

2)	Failure management when the alarm is generated by NFVI

3)	Failure management when the EM detects VNF failure

4)	Failure management when the alarm is generated by VNFC

5)	Notification of VNFCs impacted due to scheduled NFVI maintenance

6)	VM failure is detected by VNF application

7)	VNF snapshot capture

-	Use cases for Configuration Management

1)	VNF instantiation and configuration for mixed network

2)	NFV configuration management

3)	VNF configuration management by EM in mixed network

4)	Automatic re-connection of eNBs after lifecycle management of vMME

-	Use cases for Performance Management

1)	VNF Performance measurements reporting to EM

2)   Virtualized resource performance measurements

-	Other Use cases involving Network Deployment

1)	Information collection prior to capacity expansion

-	Use cases for Core Network Lifecycle Management

1)	Network Service Descriptor On-boarding

2)	Disable Network Service Descriptor

3)	Enable Network Service Descriptor

4) Update Network Service Descriptor

5) Query Network Service Descriptor

6)  Delete Network Service Descriptor

7)	VNF Package On-boarding

8)	Enabling VNF Package

9)	Disabling VNF Package

10)	VNF Package Update

11) Querying VNF Package

12) Deleting VNF Package

13)	Instantiation of Core Network Service

14	Network Service instance scaling

15)	Network Service instance update due to VNF instance modification

16)	Termination of Core Network Service Instance

17)	VNF expansion

18)	VNF Contraction

19)	Termination of Core VNF instance

20)	Notifications for VNF auto-scaling executed by VNFM

## 8.3	Conclusions on potential requirements

The following requirements for potential solutions for management of VNF only core network and the requirements for management of mixed core network are identified:

-	General requirements

-	CM requirements

-	FM requirements

-	PM requirements

-	LCM requirements

## 8.4	Conclusions on potential solutions

Based on the above use cases and requirements, the potential impacts on the existing 3GPP Management reference model are analysed and the enhancements to the 3GPP Management reference model are proposed with considering ETSI NFV ISG architectural framework.

Especially, the following gap analyses are identified to align the understanding between 3GPP SA5 and ETSI ISG NFV:

-	Summary of the gap between 3GPP SA5 and ETSI NFV terms.

-	Summary of the gap with the existing 3GPP management functions.

-	Summary of the gap with the ETSI specified MANO functions.

Also, a number of ensembles, which consider different deployment scenarios for different operators' requirements, are studied and captured in the annex B of the present document.

From end to end mobile network management point of view, the following management procedures have been identified:

-	LCM procedures:

- Instantiation of VNF

- VNF instance scaling procedures

- VNF instance scaling procedures with resource allocation done by VNF Manager

- Termination of IMS/EPC VNF instance Procedure

- Instantiation of Network Service

- Termination of Network Service

-	FM procedures:

- FM procedure flow for correlation done in EM

- FM procedure flow for correlation in VNFM

- FM procedure flow for notification of VNFCs impacted due to scheduled NFVI maintenance

- FM procedure flows for healing through operation request to VNFM and auto-healing

- VNF snapshot capture procedure

-	CM procedures:

- Adding a MME VNF to the MME pool

- Removing a MME VNF from the MME pool

- Information exchange following VNF lifecycle management

-	PM procedures:

- VNF performance management

Impacts on the management interfaces and models, especially FM, PM and CM notification data flows are analysed.

The areas which need involvement of 3GPP SA5 for NFV Management and Orchestration interfaces are identified and sent to ETSI NFV ISG by LS.

## 8.5	Recommendations

Based on the outcome of the study, normative work for the management of mobile networks that include VNFs which can be part of EPC or IMS is needed for next stage.

Potential areas for future normative work:

1)	Concept, reference model and requirements for the management of mobile networks that include VNFs

2)	LCM for mobile networks that include VNFs

3)	CM for mobile networks that include VNFs

4)	FM for mobile networks that include VNFs

5)	PM for mobile networks that include VNFs

6)	Policy management for mobile networks that include VNFs

7)	Network Resource Model, alarms types and performance measurements for the management of mobile networks that include VNFs

Item 1 will need to be addressed first as the other items have dependency on the progress of item 1.

SA5 work will be based on ETSI ISG NFV Group Specifications where applicable. SA5 will coordinate with ETSI ISG NFV as necessary.

If SA5 identifies issues in ETSI ISG NFV Group Specifications, SA5 should indicate that to ETSI ISG NFV.

Annex A:
Gap Analysis

# A.1	Introduction

This clause will capture the following information on management of networks that include VNFs:

-	Summary of the gap between 3GPP SA5 and ETSI NFV terms.

-	Summary of the gap with the existing 3GPP management functions.

-	Summary of the gap with the ETSI specified MANO functions.

# A.2	ETSI NFV terms relevant to the network management of 3GPP mobile networks and services

| ETSI NFV Term | Definition | 3GPP SA5 Definition |
| --- | --- | --- |
| OSS/BSS | From [2] clause 5.5.2. | The network management role of OSS/BSS in ETSI NFV GSs is played by NM in 3GPP SA5. |
| EM | From [2] clause 5.5.1. | It corresponds to DM/EM [3]. Note: 3GPP DM/EM can do the FCAPS management for both non-virtualized NE and VNF while ETSI EM only manages the VNF. |
| Virtualised Infrastructure Manager (VIM) | From [7] clause 3. | There is no corresponding term in 3GPP SA5. Note: The non-virtualized NE is managed by EM/DM, including inventory management. |
| VNF | From [7] clause 3. | It corresponds to NE Function defined in 3GPP SA5 [3]. |
| PNF | From [7] clause 3. | Non-virtualized NE in 3GPP SA5 is a typical example of PNF. |

# A.3	Summary of the gap with the existing 3GPP management functions

The following management functions are needed to be added or enhanced for management of mobile network that include VNFs:

-	The network resource model for virtualized related functions

-	LCM for VNF

-	FM for VNF

-	PM for VNF

-	CM for VNF

-	Policy management for VNF

# A.4	Summary of the gap with the ETSI specified MANO functions

## A.4.1	Gaps related to PM data flows

### A.4.1.1	Application level PM flow to be received by VNFM from VNF or EM

The potential purpose/motivation is unknown for VNF application level PM data to be received by the VNFM from VNF (over Ve-Vnfm-vnf RP or indirectly via Ve-Vnfm-ve RP, depicted as "Flow-1" on figure 7.2.1.1.1-2).

### A.4.1.2	Application level PM flow to be received by OSS/BSS from NFVO

The potential purpose/motivation is unknown for NS application level PM data to be received by the OSS/BSS from NFVO (over Os-Ma-Nfvo RP, depicted as "Flow-6" on figure 7.2.1.1.1-2).

### A.4.1.3	Virtualized resource level PM to be received by EM

VNFM should be able to identify the VR performance measurements related to the managed VNFs, tag the VR performance measurements with the managed VNF identity and send the tagged VR performance measurements to the subject EM, via the Ve-Vnfm-em reference point (see clause 6.2.4 PM requirements).

## A.4.2	Gaps related to FM data flows

### A.4.2.1	Application level FM flow to be received by VNFM from VNF or EM

The potential purpose/motivation is unknown for VNF FM data to be received by the VNFM from VNF (over Ve-Vnfm-vnf RP or indirectly via Ve-Vnfm-ve RP, depicted as "Flow-1" on figure 7.2.1.1.1-1).

### A.4.2.2	Application level FM flow to be received by OSS/BSS from NFVO

The potential purpose/motivation is unknown for NS FM data to be received by the OSS/BSS from NFVO (over Os-Ma-Nfvo RP, depicted as "Flow-6" on figure 7.2.1.1.1-1).

### A.4.2.3	Virtualized resource level FM to be received by EM

VNFM should be able to provide VNF related virtual resource fault report and to EM through Ve-Vnfm-em interface (see clause 7.3.3.1 FM procedure flow for correlation done in EM).

## A.4.3 	Gaps related to definition of NSD operations

This clause outlines gaps identified in [2], related to definition of NSD operations.

### A.4.3.1 	Network Service Descriptor Management interface

There are multiple references in [2], Annex C, to "Network Service Descriptor interface" with reference to operations Update Network Service Descriptor, Query Network Service Descriptor, Delete Network Service Descriptor. However such interface is not defined in [2]. On the other hand, there is Network Service Descriptor Management interface ([2], 7.1.1) which includes these three operations.

### A.4.3.2 	Network Service Descriptor states

The document [2] does not provide clear definition of NSD states. Such definition is needed to conclude which operations can be applied to the NSD at the given moment.

## A.4.4	Use cases not supported by ETSI NFV GS MAN001 v1.1.1

### A.4.4.1	Notification of VNFCs impacted due to scheduled NFVI maintenance

According to potential requirement identified in REQ-NFVM_VN-LCM-CON-2 and associated use case in clause 5.1.6 of the present document, the following requirement applicable to ETSI NFV and currently not supported in [2] is deemed necessary to be supported:

-	VNFM should provide the EM notification through Ve-Vnfm-em reference point about VNF and its components whose virtualized resources will be impacted due to scheduled maintenance of underlying infrastructure resources (e.g. scheduled update of the hypervisor software or the firmware of a physical machine (host)).

Such notification is sent by the VNFM to the EM in advance to the actual maintenance. This notification is necessary so that the operator and management systems can determine if anything can be done (e.g., reconfiguration of affected nodes that are neighbour to the subject VNF) to minimize the impact and disruption of the VNF. This case is also relevant when the network operator has different teams devoted to manage the 3GPP mobile network and the NFV infrastructure.

### A.4.4.2	VNF snapshot capture

According to potential requirement identified in REQ-NFVM_VN-LCM-CON-3 and associated use case in clause 5.1.8 of the present document, the following requirement applicable to ETSI NFV and currently not supported in [2] is deemed necessary to be supported:

-	VNFM should provide the capability to capture snapshot of a VNF or any of its components through Ve-Vnfm-em reference point to EM, providing as a result of the snapshot operation to EM with enough information to locate and identify the snapshots.

These snapshots can be used for multiple purposes, e.g. troubleshooting, rollback during erroneous VNF lifecycle management events or software upgrade, for fast VNF re-deployment, etc.

### A.4.4.3	Notifications related to VNF auto-healing by VNFM

According to potential requirement identified in REQ-NFVM_VN-LCM-CON-5 and associated use case in clause 5.1.5 of the present document, the following requirement applicable to ETSI NFV and currently not supported in [2] is deemed necessary to be supported:

-	VNFM should provide the following auto-healing notifications through Ve-Vnfm-em reference point to the EM:

-	A notification that the auto-healing execution is about to begin.

-	A notification(s) about auto-healing execution progress.

-	A notification about the success or failure of the healing execution.

The purpose of the notification of "the auto-healing execution is about to begin" is to make EM aware of the auto-healing being executed by VNFM. For instance, EM can delay or abandon actions that may impact the VNF which is going to be “auto-healed”. This is to avoid a conflict in case both EM and VNFM deal with a VNF failure independently. Such situation may happen, if the EM also detects some failure situation from VNF. EM can instruct the subject VNF neighbour nodes not to attempt connection with the subject node while it is in “auto-healing” execution.

### A.4.4.4	Notification related to VNF auto-scaling by VNFM

According to potential requirement identified in REQ-NFVM_VN-LCM-CON-18 and associated use case in clause 5.5.20 of the present document, the following requirement applicable to ETSI NFV and currently not supported in [2] is deemed necessary to be supported:

-	VNFM should provide the EM the following auto-scaling notifications through Ve-Vnfm-em reference point:

-	A notification that the auto-scaling execution is about to begin.

-	A notification(s) about auto-scaling execution progress..

-	A notification about the success or failure of the auto-scaling execution.

The purpose of the notification of "the auto-scaling execution is about to begin" is to make EM aware of the auto- scaling being executed by VNFM. For instance, EM can delay or abandon actions that may impact the VNF which is going to be “auto-scaled”. This would avoid scaling conflict in case the EM/NM decides to scale the subject VNF based on scaling on demand method or scaling by Management method..

EM can, if necessary, (re)configure the subject VNF neighbour nodes to account for the newly auto-scaled VNF configuration/capacity.

Annex B: 
Ensemble

# B.1 	Introduction

This annex introduces a number of ensembles. The benefits for identifying an ensemble are listed within each ensemble clause.

Note: 	The choice of zero, one or more ensembles (of same or different vendors) and zero, one or more functional blocks (of same or different vendors) for network deployment is made by the operator.

# B.2 	Ensemble 1

This Ensemble is an example that includes EM, VNFM, PNF and VNF as one package. The package of this Ensemble is provided by the same vendor as shown in Figure B.2-1.

From the Multi-vendor interoperability point of view:

a)	The interactions between members of the Ensemble are not visible to external (to Ensemble) entities and functional blocks and;

b)	The interactions between the Ensemble and external (to Ensemble) entities and functional blocks are visible.

Figure B.2-1   VNFM, EM, PNF and VNF as one Ensemble in mixed network

This Ensemble can be used in many deployment scenarios, one of which is illustrated as example below.

In this deployment scenario, the interfaces supporting multi-vendor interoperability from the perspective of the VNFM Ensemble are: Itf-N, Or-Vnfm, Vi-Vnfm.

Figure B.2-2   Multi-vendor Interoperability interfaces

The benefits for the use of Ensemble 1 are:

-	To provide fast time to market implementation and simplify interoperability provisioning and testing in multiple vendors environment.

-	To provide a migration path which minimizes the level of disruption of service when introducing virtualized entities (functional blocks) into operator's networks, whereby existing network management processes and tools can be reused.

-	Assembling EM with VNFM would allow the use of the same set of network management processes and tools to manage non-virtualized and virtualized network functions.

-	Assembling EM, VNFM, VNF and NE (PNF) would allow leveraging vendor's expertise on assembling existing EM and NE to coordinate with the new required VNF and VNFM functionality.

-	Support of this ensemble would focus towards interoperability of one vendor's VNFM with other vendors VIMs and NFVOs.

# B.3 	Ensemble 2

This Ensemble includes EM and VNF as one package. The package of this Ensemble is provided by the same vendor as shown in Figure B.3-1.

This Ensemble should be supplied as one package to provide for interoperability over the Type 1 interface as shown in Figure B.3-1. The EM and VNF typically are provided by the same vendor. They can be also provided by different vendors in case when the vendors employ private (not standardized in 3GPP) procedures to ensure interoperability between the EM and the VNF.

Figure B.3-1	 EM and VNF as one Ensemble

This Ensemble can be used in many deployment scenarios, one of which is illustrated as example below.

In this scenario, the interfaces supporting multi-vendor interoperability from the perspective of this ensemble are: Itf-N, OS-Ma-nfvo, Or-Vnfm, Vi-Vnfm, Ve-Vnfm-em, Ve-Vnfm-vnf, Or-Vi, Nf-Vi.

# B.4 	Ensemble 3

This Ensemble includes EM, DM and VNFM as one package, as shown in Figure B.4-1.

Figure B.4-1   VNFM, EM, and DM as one Ensemble in a mixed network

Annex C:
Change history

| Change history |
| --- |
| Date | TSG # | TSG Doc. | CR | Rev | Subject/Comment | Old | New |
| 2015-12 | SA-70 | SP-150692 | 002 | 1 | Correction of Requirement GN-CON-4 | 13.0.0 | 13.1.0 |
|  |  |  | 004 | - | Editorial cleanup on references |  |  |

# Text boxes

EM

NFVI

VNF

VNFM

2. VR fault report

VIM

1. NFVI failure report

6. VNF virtualization-related fault report

3. Identify related VNF

5. Fault correlation based on reports from 2 and 4

4. VNF/VNFC fault report

8.  EM processes the result

3. Virtualised resource snapshot request

6. VNFM processes virtualised resource snapshot capture result

2. VNFM identifies VNF and VNFCs to capture snapshot

5. Virtualised resource snapshot result response notification

7. VNF snapshot capture result response

4. Virtualised resource snapshot capture

VNF

1. VNF snapshot capture request

VIM

NFVO

VNFM

EM

NFVI

1. VNFM handles VR and VNF fault notifications

5b. VNF lifecycle change end notification

5a. VNF lifecycle change end notification

3b. VNF lifecycle change start notification

3a. VNF lifecycle change start notification

4. VNF healing procedure involving VNFC re-creation, activation and configuration of impaired VNFCs

2. VNFM determines auto-healing to be executed

VNF

VIM

NFVO

VNFM

EM

NFVI

1. VNFM handles VR and VNF fault notifications

8b. VNF lifecycle change end notification

8a. VNF lifecycle change end notification

6b. VNF lifecycle change start notification

6a. VNF lifecycle change start notification

5. VNF healing request

3. VNF fault report

7. VNF healing procedure involving VNFC re-creation, activation and configuration of impaired VNFCs

4. Fault correlation and determination of corrective action through healing

VNF

2. VNF related VR fault report (VNF specific)

VIM

NFVO

VNFM

EM

NFVI

NFVI

EM

VNFM

NFVO

VIM

1. Mark NFVI resources for maintenance

2. Find affected virtualised resources

3. Notify about virtualised resource state changes

4. Find affected VNF and VNFC(s)

5. Notify affected VNF and VNFC(s)

NM

EM-a

EM-b

NFVO

VNFM

VNF

1. Lifecycle management operation for the VNF completed

3. Informs the need of configuration changes

4. Perform configuration change(s)

5. Notify the result of the adjustment

2. Identify EM(s) controlling NE(s) affected by the VNF lifecycle management

NE