## Slide 1: Discussion paper for asynchronous solutions to support lifecycle management SA5#140e, 15 – 24 November 2021
Joey Chou, Intel

## Slide 2: Content
IOC is created prior to the completion of LCM
  LCM operation is initiated via an attribute in the IOC
  LCM operation is initiated if it is the NF IOC
IOC is created after the completion of LCM

## Slide 3: Way forward from TR 28.814 Study on enhancements of edge computing management
  Extensions in the provisioning MnS are needed to support the asynchronous mode of operations.
  The solutions to support asynchronous responses may include the following options with consideration of backward compatibility:
    The enhancements of existing operations and notifications.
    Define new operations to support asynchronous responses.

## Slide 4: Proposal 1: IOC is created prior to the completion of LCM LCM operation is initiated via an attribute in the IOC

## Slide 5: IOC attributes to support asynchronous operation (1)
Add asyncOperation and asyncOpStatus attributes in ManagedFunction IOC in TS 28.622
Attribute Name | S | isReadable | isWritable | isInvariant | isNotifyable
vnfParametersList | CM | T | T | F | T
peeParametersList | CM | T | T | F | T
priorityLabel | O | T | T | F | T
supportedPerfMetricGroups | O | T | F | F | T
asyncOperation | CM | T | T | F | T
asyncOpStatus | CM | T | F | F | T
asyncOperation and asyncOpStatus attributes Condition: asynchronous operation is supported

## Slide 6
asyncOperation and asyncOpStatus attributes definition
IOC attributes to support asynchronous operation (2)
Attribute Name | Documentation and Allowed Values | Properties
asyncOperation | This parameter defines if this is the asynchronous operation. allowedValues: TRUE, FALSE | type: Boolean multiplicity: 1 isOrdered: N/A isUnique: N/A defaultValue: None allowedValues: N/A isNullable: False
asyncOpStatus | This attribute specifies the status of asynchronous operation. allowedValues: in_progress success lcmFailure time_out Note: additional failure codes may be added. | type: ENUM multiplicity: 1 isOrdered: NA isUnique: NA defaultValue: None isNullable: False

## Slide 7: Example of LCM triggered by IOC attribute

## Slide 8: Questions associated LCM operation via IOC attribute
What happens if a consumer accidently invokes creatMOI without sending lcmOpStatus = TRUE to perform LCM?
MOI is created prior to the NF instantiation where the DN of the MOI has been given to the consumer
  What will happen when the instantiation failed?
    Option 1: The producer send a notifyAttributeValueChange with status = failure, then delete the MOI, and send a notifyMOIDelete to the consumer
    Option 2: Send a notifyAttributeValueChange with status = failure, It is up to the consumer to delete the MOI
    Option 3: Need to have process to clean if nobody delete the MOI
  What will happen if the consumer start to perform Modify or Delete operation on the MOI that has not been instantiated?

## Slide 9: Proposal 2: IOC is created prior to the completion of LCM LCM operation is initiated if it is the NF IOC

## Slide 10: IOC attribute to support asynchronous operation (1)
Add asyncOpStatus attributes in ManagedFunction in TS 28.622
Attribute Name | S | isReadable | isWritable | isInvariant | isNotifyable
vnfParametersList | CM | T | T | F | T
peeParametersList | CM | T | T | F | T
priorityLabel | O | T | T | F | T
supportedPerfMetricGroups | O | T | F | F | T
asyncOpStatus | CM | T | F | F | T

## Slide 11
asyncOpStatus attributes definition
IOC attribute to support asynchronous operation (2)
Attribute Name | Documentation and Allowed Values | Properties
asyncOpStatus | This attribute specifies the status of asynchronous operation. allowedValues: in_progress success failure time_out | type: ENUM multiplicity: 1 isOrdered: NA isUnique: NA defaultValue: None isNullable: False

## Slide 12
Example of LCM triggered by NF IOC

## Slide 13: Questions associated LCM operation via IOC attribute
MOI is created prior to the NF instantiation where the DN of the MOI has been given to the consumer
  What will happen when the instantiation failed?
    Option 1: The producer send a notifyAttributeValueChange with status = failure, then delete the MOI, and send a notifyMOIDelete to the consumer
    Option 2: Send a notifyAttributeValueChange with status = failure, It is up to the consumer to delete the MOI
    Option 3: Need to have process to clean if nobody delete the MOI
  What will happen if the consumer start to perform Modify or Delete operation on the MOI that has not been instantiated?

## Slide 14: Proposal 3: IOC is created after the completion of LCM

## Slide 15: IOC attribute to support asynchronous operation (1)
Add asyncOpStatus attributes in ManagedFunction in TS 28.622
Attribute Name | S | isReadable | isWritable | isInvariant | isNotifyable
vnfParametersList | CM | T | T | F | T
peeParametersList | CM | T | T | F | T
priorityLabel | O | T | T | F | T
supportedPerfMetricGroups | O | T | F | F | T
asyncOpStatus | CM | T | F | F | T

## Slide 16
asyncOpStatus attributes definition
IOC attribute to support asynchronous operation (2)
Attribute Name | Documentation and Allowed Values | Properties
asyncOpStatus | This attribute specifies the status of asynchronous operation. allowedValues: success failure time_out | type: ENUM multiplicity: 1 isOrdered: NA isUnique: NA defaultValue: None isNullable: False

## Slide 17: HTTP defined standard status codes
  https://restfulapi.net/http-status-codes/
Status Code | Description
200 OK | Indicates that the request has succeeded.
201 Created | Indicates that the request has succeeded and a new resource has been created as a result.
204 No Content | The server has fulfilled the request but does not need to return a response body. The server may return the updated meta information.
202 Accepted | Indicates that the request has been received but not completed yet. It is typically used in log running requests and batch processing.

## Slide 18: Add OperationPending to the status attribute
Parameter name | S | Matching Information / Legal Values | Comment
attributeListOut | M | LIST OF SEQUENCE< attribute name, attribute value> | This list of name/value pairs contains the attributes of the new managed object and the actual value assigned to each.
status | M | ENUM (OperationSucceeded, OperationFailed, OperationPending) | OperationPending is mapped to 202 accepted
Add OperationPending to the status attribute creatMOI output parameters in TS 28.532

## Slide 19
Example of asynchronous operation timeout

## Slide 20: The group is asked to endorse a proposal.

## Slide 21: Thank you!