## Slide 1: Discussion to Correct inconsistencies in Network Slicing S5-224292
Nokia, Nokia Shanghai Bell

## Slide 2
Rationale
  TS 28.530, TS 28.531, TS 28.541 explain concepts of network slicing along with the associated IOC definitions and object hierarchy. These should be consistent and complete across all specifications.
  Procedures for slice operations must consider various configurations as allowed by the above definitions and must be complete.
  Procedures for handling of shared network slice objects must be unambiguous

## Slide 3
Observations
Observation 1 (related to definitions and procedures)
TS 28.530
  This TS has definition of terms related to network slice, but does not clearly differentiate the terms used in SA2 and SA5. TR 28.811, clause 4.1 has specified the difference, but it is not introduced in normative specifications.
  Terms such as Top Network Slice Subnet or Root Network Slice Subnet are not sufficiently specified.
TS 28.531
  This TS refers to the terms defined in 28.530. But the updates done to differentiate SA2 and SA5 terms in TS28.530 are not reflected in this TS. For example, the NSI which is the identifier in the Core Network is still widely used in this TS.
  Use cases defined in this TS do not have corresponding procedures and attributes specified to implement the use case. For example, activation and de-activation use cases are specified in clause 5.1.7 and 5.1.8, but there are no attributes or procedures defined to perform this operation.
  Another example is, use case for Modification of network slice related requirements is defined in clause 5.1.25, but corresponding procedures are not defined. For example, when the Network Slice MnS Producer terminates an NSI and allocates a new NSI, how such information is communicated to the network slice consumer is not specified.
  Clause 5.1.9 and 5.1.25 both are for modification of network slice, with ServiceProfile as input and hence seem to be redundant.
(contd.)

## Slide 4
Observations
Observation 1 (related to definitions and procedures)
TS 28.541
  NetworkSlice and NetworkSliceSubnet have attributes operationalState, administrativeState – but the corresponding 5G Network NRMs, the NR and Core NRM, where the S-NSSAIs are configured do not have these states.
  ServiceProfile has redundant definitions for SST, as attributes sST and pLMNInfoList.sNSSAI.sST. The need or the difference between the two, and the relation between the two are not specified.
  Clause 6.3.6.1. mentions top network slice subnet, but the description of a top network slice subnet is not specified anywhere.

## Slide 5
Observations
Observation 2 (related to object hierarchy)
TS 28.530
  Top Network Slice Subnet or Root Network Slice Subnet relationship to the NetworkSlice are not sufficiently specified.
  Clause 4.1.3 provides an illustration of relationship between communication service, network slice, network slice subnet, network slice subnet CN, network slice subnet AN and network slice subnet TN, but such relationship is not specified.
TS 28.531
  Procedures do not clearly specify the hierarchy for creation. For example, clause 5.1.1 specifies that NetworkSlice instance allocation does not specify the root/top NetworkSliceSubnet creation and association. This clause also describes the interaction with TN Manager which is not specified in the procedures related to this use case.
TS 28.541
  The relation between NetworkSlice, NetworkSliceSubnet related to Top NetworkSliceSubnet, CN NetworkSliceSubnet and RAN NetworkSliceSubnet and the allowed cardinality for the NetworkSlice and different types of NetworkSliceSubnet are not specified. For example, Clause 6.3.25.1 specifies that top network slice subnet is a network slice subnet directly associated with the network slice, but it is not specified if RAN network slice subnet and Core network slice subnet are allowed to be directly associated with the network slice or not.
  Clause Annex B specifies the state handling for NetworkSlice instance and NetworkSliceSubnet instance, but does not specify the effect of change of state of one MOI over the other. For example, if the NetworkSlice administrativeState is configured to locked by the operator, then the effect of the same over all the constituent NetworkSliceSubnet MOIs and their constituent NetworkSliceSubnet MOIs is not specified. Also, the effect of configuring NetworkSlice administrativeState to locked on the 5G network itself is not specified.

## Slide 6
Observations
Observation 3 (related to shared slices)
TS 28.531
  Defines usecases and procedures for allocation where network slices and network slice subnets are shared. But the effect of state management attributes administrativeState and operationalState in such scenarios are not specified. For example, the effect on slices of NetworkSlice (which supports multiple slices), when operationalState for one of the constituent NetworkSliceSubnet is changed to disabled.
  The NetworkSlice MOI can support slices from multiple PLMNs, and hence multiple operators, hence the effect of state management attributes from slices of one operator might impact the slices of another operator.
  Effect of state management attributes administrativeState and operationalState on the managed resources, managed entities, and managed function when the network slices are shared is not specified.
TS 28.541
  NetworkSlice has an attribute serviceProfileList and ServiceProfile has an attribute list pLMNInfoList. Similarly, NetworkSliceSubnet has a list sliceProfileList and SliceProfile has a list pLMNInfoList. This allows the NetworkSlice and NetworkSliceSubnet MOI to be shared across operators (PLMNs).
  Relation between attributes SliceProfile.plmnInfoList, and coverageAreaTAList are not specified.

## Slide 7
Proposal
Proposal 1 (related to definitions and procedures)
TS 28.530, TS 28.531 and TS 541 need to be enhanced to clearly define the terms, definitions and procedures for management of network slices.
Terms used in all the SA5 specifications must be consistent, and without clash with terms used in SA2.
All specified use case should have procedures and involved IOCs and attributes clearly documented.
Proposal 2 (related to object hierarchy)
The allowed hierarchy between network slice and the different variants of network slice subnets needs to be specified.
The allowed hierarchy between the different variants of network slice subnets needs to be specified.
The relation between the states of network slice, the network slice subnets and the managed elements needs to be specified.
Proposal 3 (related to shared slices)
The relation between attributes needs to be specified when NetworkSlice and NetworkSlice subnet MOIs are shared across multiple slices.
The effect of state management attributes needs to be specified when the NetworkSlice and NetworkSlice subnet MOIs are shared across multiple slices.

## Slide 8: Thank you!