## Slide 1: Discussion on common issue on AI/ML solution
Huawei, Hisilicon
Yajie

## Slide 2
The AI/ML enabler server invoke other SEAL service as proxy
There are two ways for VAL server to invoke multiple SEAL service, take following cases as example
  Case#1: the AI/ML enabler server work as proxy to transparent transfer the data transmission requirement to SEALDD, and VAL server invoke both AI/ML function and SEALDD function but using single AI/ML API
  Case#2: the VAL server directly interact with both AI/ML enabler server and SEALDD for AI/ML model training and data transmission respectively
Issues on case#1
  the AI/ML enabler server cannot provide any additional benefit but introduce unnecessary forwarding, increase the complexity of the AI/ML enabler server and increase the latency
Benefit on case#2
  the AI/ML enabler server and SEALDD server can provide independent microservices without parsing unnecessary information, which reduce the complexity of the AI/ML enabler server and reduce the latency
VAL
server
AI/ML E server
SEALDD
server
Invoke AI/ML operation
AI/ML model training
AI/ML data/task transmission (providing data transmission policy)
Invoke SEALDD operation
AI/ML data/task transmission (providing data transmission policy)
Case#1 - not optimal
AI/ML model training
data transmission
VAL
server
AI/ML E server
SEALDD
server
Case#2 - optimal
AI/ML model training
data transmission
①
②
①
②
Invoke AI/ML operation
AI/ML model training
Invoke SEALDD operation
AI/ML data/task transmission (providing data transmission policy)

## Slide 3
Way Forward
Propose to clarify the benefit of using AI/ML enabler layer to invoke other SEAL service, then further evaluate the rationality of the solution.
Notes: https://aws.amazon.com/ec2/autoscaling/faqs/?nc1=h_ls

## Slide 4: The end