## Slide 1: Discussion about SEAL service usage and related architecture selection
Jian Zhang
Huawei, Hisilicon

## Slide 2: Overall perspective of service exposure
Exposed services towards APP
CAPIF Core
3GPP SA6
3GPP SA3/SA6
3GPP North bound APIs [APP use case]
Operate APIs
CAPIF-AEF
API-invoking control
3GPP API invoker system
3GPP network capability layer
3GPP service exposed layer
Exposed services towards APP
Network functions & capabilities
Network function API
Network functions & capabilities
Network function API
Exposed services layer
Network centric
Network functions & capabilities
Network function API
3GPP North bound APIs
3GPP SA2,SA3,SA4,SA5,SA6
Network-APP transition services
APP use case Centric
SAx
SAy
SAz
CAPIF provides the general API exposure framework, which can support the application developer (acting as API invoker) to discover and invoke the required north bound API(s) provided by network-centric layer (e.g. NEF in SA2) or app-centric layer (e.g. SEAL service in SA6)

## Slide 3: CAPIF implementation in different software development phases

## Slide 4: API gateway and SA6 enabler in service exposure
API routing: API gateway acts as an single entry endpoint to route requests to multiple services or multiple service instances
API transformation and aggregation in API gateway: API gateway adapts backend microservices (mainly including aggregation and format adaptation) and exposes friendly and unified API to Frontend application
Security authentication, load balancing, etc
APP
API gateway
Microservice#1
(e.g. product)
Microservice#2
(e.g. ordering)
…
Microservice#x
(e.g. payment))
API#y
API#1
API#2
API#x
API gateway in IT
CAPIF-AEF (Border AEF)
APP
API#y
SEAL service
EDGEAPP
…
5GC
API#1
API#2
API#x
CAPIF-AEF/border AEF mapping into API gateway
SA6 enabler(border AEF) has consistent principles with API gateway in IT, can as a capability exposure bridge between third party application and carrier network

## Slide 5: Internal invocation in SEAL domain
SEAL domain
Third party consumer
SEALDD
NRM
LMS
NSCE
…
APP#1
APP#2
…
APP#x
SEAL service exposed API(s)
ADAES
…
SDd
SLm
SAdae
SNsce
SNrm
In SEAL domain, SEAL server can invoke each other internally as shown in the service-based representation
Different SEAL servers can expose the dedicated/different APIs for application consumer. After invoking the services of other server internally, the SEAL server should provide the new SEAL service without overlapping
If there are overlapping between SEAL services provided by different SEAL servers, will cause the conflict during API routing phase