## Slide 1: Discussion on the use of Group ID in Location Requests
Mythri Hunukumbure, Sivasubramaniam Ramanan
UK Home Office

## Slide 2: Content
Example use case
New proposal (changes from CR S6-240396)
Justification
Annex – on obtaining affiliation data

## Slide 3: Example use case
A major incident will require multiple groups from many agencies (who would have own MC service servers) to attend, and work under the command of one supervisor.
  The supervisor will be from primary MC agency, assume already in command of group 1.
  Group 2 from partner MC agency also serves the incident and we need to create a temporary group (through temporary group formation of section 10.2.4.2 of TS 23.280).
  The supervisor will now need to get location updates from affiliated members of this temporary group 3.
The incident can be in a remote area which can introduce several communication challenges to the supervisor on ground on connecting back to the servers.
  The supervisor will require location updates to be set-up quickly, with fewer messages as possible.
  Also, there is a need to limit the length of uplink transmit messages (from the supervisor device to the LMS/service servers) so battery life of this device can be extended.

## Slide 4: New Proposal
The main objection for this CR in the last meeting was that it combines group operations with LMS, which is intentionally kept apart in TS 23.280.
  We have further studied group affiliation and recognize that affiliation need not be requested in Location, as the supervisor can subscribe to dynamic data as in 10.1.5.6.1.1 (in Annex).
Our new proposal is just to include group ID in location requests and subscriptions by the LMC (supervisor) and the LMS to resolve this ID at the MC service server.
Information element | Status | Description
MC service ID | M | Identity of the requesting MC service user
MC service ID list/ MC Group ID/ MC Group ID list | M | List of MC service users whose location information is requested
Time between consecutive reports | M (see NOTE) | Indicates the interval time between consecutive reports. The provided time is to be used for all MC service IDs provided in the MC service ID list.
NOTE: If the interval time has a value of zero then the location management server will send the Location information notification immediately the location information report is received from the MC service user in the MC service ID list. |  | 
Table 10.9.2.5-2: Location information subscription request (LMC – LMS)

## Slide 5: New Proposal II
The suggested changes to TS 23.280, section 10.9.2 Information Elements:
  Inclusion of group ID/ group ID list (as in previous slide) for section 10.9.2.3 – Location information request, section 10.9.2.4 – Location reporting trigger, section 10.9.2.5 - Location information subscription request, section 10.9.2.8 - Location information cancel subscription request.
Changes to TS 23.280, section 10.9.3 Procedures:
  A procedure similar to section 10.9.3.8 (diagram )
  Just as the LMS has subscribed to receive Functional Alias updates from MC service server for this procedure, a similar subscription for LMS to receive Group ID updates from the MC service server. The event supervisor has issued the request to LMS to activate location related procedures for this Group ID.

## Slide 6: Justification
The emergency services have strict policies that define certain procedures when attending emergencies. The requests made to groups and handling group dynamics is one of key areas they want to preserve when moving from TETRA to LTE.
The ID list for some groups can contain hundreds of entries. If these group entries were to expand to ID lists at the supervisor for location requests, they will generate very long messages (many IP packets). This can take longer and also impact power consumption for supervisor device – critical for events in remote locations.
The main concern about last CR (S6-240396) as not to have group ID in location requests was to avoid the interactions the LMS need to have with other servers. However, when the Functional Alias (FA, with group binding) is used in certain information flows (eg: Table 10.9.2.3-3), there is interaction between the LMS and other service server(s).

## Slide 7: Annex - Affiliation in ‘dynamic information’
The full set of dynamic data associated with a group is held at the primary MC service server. This data includes ‘Affiliation status’, as in section 10.1.5.5.1.
The GMS of the primary MC (GMC 1) can also request to receive some of this affiliation data from the MC service server, as mentioned in section 10.1.5.5.2.
Dynamic data also includes regroup status, which implies this data is available for temporary groups.
So, the authorized client can subscribe to receive notifications of this dynamic data of this combined group from the MC service server.
  Procedures shown in the next slide.
Parameter description
Status i.e. indication of potential emergency or in-peril status of the group, together with the identification of the user who has performed the last modification of this status.
Affiliation status of each MC service ID of the group corresponding to the MC service and the Contact URI(s) from which the user affiliated.
Contact URIs used for designation of the group e.g. aliases of group broadcast, group regroup group URIs.
Media description for group media, including transport and multiplexing information.
Group call ongoing.
Regroup status of group where regrouping using a preconfigured group is used, e.g. whether group is regrouped, MC service group identity of regroup group.
Functional alias binding information for each user within the group.
Table 10.1.5.5.1-1: Dynamic data associated with a group

## Slide 8: Annex - Subscribe to Affiliation information
10.1.5.6.1.1 Subscribe group dynamic data request
Table 10.1.5.6.1.1-1 describes the information flow subscribe group dynamic data request from the MC service client to the MC service server and from the group management server to the MC service server.
Table 10.1.5.6.1-1: Subscribe group dynamic data request
The MC service client (supervisor) can subscribe to receive the dynamic data from the MC service server.
  The data type can be specified to contain only affiliation status, if needed.
This requires only a few IP packets to be transmitted from the supervisor device.
  For larger groups, the affiliated list can span many IP packets, but these packets are now received by the supervisor device.
The procedure for this subscription is shown opposite.
Information element | Status | Description
MC service group ID | M | The MC service group ID for which dynamic data is requested.
List of group dynamic data type (see NOTE) | O | The type of group dynamic data requested, e.g., affiliated status, regroup status, emergency status
NOTE: If the Group dynamic data type IE is not present, all types of group dynamic data is requested. This IE shall be present from when the request is sent from the group management server. |  | 
Figure 10.1.5.6.2-1: Subscription for group dynamic data