## Slide 1: MCGWUE feature
Tim Woodward
Harish Negalaguli
Motorola Solutions
March 2024

## Slide 3: Solved/Closed Issues
Authentication/authorization of MCGWUE with 3GPP network
  Determined to be in accordance with existing 3GPP network mechanisms.
  Update to 23.280 needed to state it is addressed in 33.180.
Authentication/authorization of N3GPP device with 3GPP network
  Determined to be outside the scope of 3GPP.
  Update to 23.280 needed to state it is addressed in 33.180.
Connection between MCGWUE and N3GPP device
  Determined to be outside the scope of 3GPP.
  Update to 23.280 needed to state it is addressed in 33.180.
MC Client authentication
  Determined to be in accordance with existing MC mechanisms.
  Update to 23.280 needed to state it is addressed in 33.180.
MC Services between MC Client and MC System
  Determined to be in accordance with existing SA6 specifications (i.e. no changes needed).
  Update in 23.280 needed to state it is addressed in existing documentation (i.e. 23.379, etc).
SIP & HTTP path management when MC Client(s) for a single MC user are hosted either on N3GPP device or MCGWUE.
  Determined to be in accordance with existing SA6 specifications (i.e. no changes needed).

## Slide 4: Unsolved/Open Issues
MCGWUE authorization with MC System
  Current proposal in 23.280 does not provide trusted authorization.
  Because all MC Clients are authenticated and authorized, MSI feels that additional and specialized authorization of the MCGWUE is unnecessary and doesn’t provide any benefit.
SIP & HTTP path management (MC Client to MC System) when MCGWUE supports multiple MC users.
  All MC Clients are hosted on N3GPP devices.
  All MC Clients are all hosted on MCGWUE.
  Mix of MC Clients hosted on N3GPP devices and MCGWUE.

## Slide 5: What can we achieve in R-18?
If it’s not too late to clean up 23.280, then SA6 should add or clarify:
Authentication/authorization of MCGWUE with 3GPP network is per SA3.
MC Client authentication/authorization with MC System is per 33.180.
Restrict the use of a MCGWUE to a single MC user.
  This means one N3GPP device with the MC client(s) hosted on either the N3GPP device or on the MCGWUE, but not mixed).
  NOTE: This does not impact the number of services (MCPTT, MCData, MCVideo) supported for a single MC user. This would be no different than we do today with a regular MC device.
Remove problematic MCGWUE authorization with MC System procedure.
Stage 3 is currently out of sync with SA6. An LS needs to be sent to CT1 explaining this fact. CT1 should synchronize their R-18 stage 3 implementation with the R-18 SA6 architecture for this feature.

## Slide 6: What gets pushed into R-19?
Support for multiple N3GPP devices on a single MCGWUE.
Support for multiple MC users on a single MCGWUE.
  SIP & HTTP path management between MC Client(s) and MC System.
  MC Clients may be hosted on multiple N3GPP devices.
  MC Clients may be hosted on single MCGWUE.
  Mix of MC Clients may be hosted on N3GPP devices and the MCGWUE.
Support for single MC user on multiple MCGWUEs.
  SIP & HTTP path management between MC Client(s) and MC System.
  MC Client(s) hosted on N3GPP device are routed through multiple MCGWUEs.
  MC Client(s) hosted on multiple MCGWUEs.
  Mix of MC Clients hosted on N3GPP devices and MCGWUE.
Further discussions on the need for MCGWUE authorization with the MC System.
NOTE: The requirements we’ve been discussing and interpreting in recent face-to-face meetings are the scope and limitations for the above.

## Slide 7: Comments or Questions?