## Slide 1: FS_Metaverse_App Discussion
Sapan Shah
Samsung

## Slide 2: Contents
Avatar Management or Asset Management?
Architecture Options

## Slide 3: Avatar Management or Asset Management
Current Status
  Key issue #3: Digital avatars support
    Open issues:
      What SA6-defined information is required to expose the SA2-defined, SA4-defined and SA3-defined avatar information to support allowed application configuration, location-based avatar contextual information?
      Whether and how application enablement layer manages and exposes information about digital avatars to the consumers (i.e. application clients and servers) or across verticals?
  Solution #5 Support for digital avatars
  Solution #6 Avatar support using Metaverse Digital Representation Block (MDRB)
    Solution covers asset management aspect too.
  Solution #7: Digital avatar support by A-DACM
    Although DAC is for Digital Asset Container – all procedures are for Avatar management

## Slide 4: Avatar Management or Asset Management
Discussion
  Is SA6 fine to study Asset management? (If yes, interested companies need to update the KI description)
  How asset will be represented?
    For Avatar we know that SA4 has defined base avatar and then it has associated/related information (as specified in different SA1 use cases)
  How asset profile/related information block will look like?
  LS from SA3
Need to be clear on the scope of the study
  Our open issue is to combine information from all groups – but are other groups (like SA2) will provide base avatar information or base asset information.

## Slide 5: Architecture Options
Solution analysis:
Solution # | Title | Mapping KI # | Architecture Option
1 | Spatial anchor discovery | 1 | Application enablement architecture
2 | Support for spatial anchor management | 1 | Enhancement to SEAL LM
3 | Spatial anchor subscription | 1 | Application enablement architecture
4 | Support for spatial anchor analytics information | 1, 8 | Application enablement architecture
5 | Support for digital avatars | 3 | Enhancement to SEAL CM
6 | Avatar support using Metaverse Digital Representation Block (MDRB) | 3 | Application enablement architecture
7 | Digital avatar support by A-DACM | 3 | A-DACM (A separate server)
8 | Support for spatial map management | 4 | Enhancement to SEAL LM
There are 3 options discussed till now
  To define new application enablement architecture
  To enhance existing enabler server (like SEAL LM, SEAL CM)
  To define new server for the specific management

## Slide 6: Architecture Options - Comparison
Criteria | Meaning | New Application Enabler Architecture | Enhancing existing enabler server | New Server/Function
modularity | architecutre can be divided into separate individual modules per feature | Less | Moderate to High | High
scalability | How easy to add or remove resources from the system | High | High | High
reliability | To recover from failure | ? | ? | ?
security | To authenticate and authorize the access | Can be done by 3GPP SA3 | Already in-place | Can be done by 3GPP SA3
usability | User interactions | Easy | Easy | Easy
Cost effective | Cost of development and deployment | High | Low | High
Pros | General | - All metaverse application enablement features can be made available at one server. - Follows client-server architecture model. | - Easy to deploy by adding new feature - Location can be available by the same server - Does not crete a new layer - Follows client-server architecture model | - Does not create new layer - May follow client-server model
Cons | General | - Create a new layer - May need to rely on other servers for more information (like location information from SEAL LM server) | - Metaverse features are on different servers (*) | - Metaverse features are on different servers (*) - May need to rely on other servers for more information (like location information from SEAL LM server)

## Slide 7: Architecture Options
Other points
  For KI#6 and #7 – existing enabler architecture will be enhanced (either procedure enhancement or architecture enhancement or both)
Summary
  All architecture options are feasible and deployable
  Only differences are related to associated cost and architecture layer
  Considering the comparison and direction towards other KIs, it is suggested to enhance existing SEAL services.