## Slide 1: FS_eEDGEAPP: Discussion on CAS initiated ACR for Architecture Option#5
Yonatan Shiferaw, KPN N.V.

## Slide 2: Background
Key issue #11: ACR between EAS ad Cloud Application Server has the following open issue
  Whether and what are the impacts of CAS initiated ACR
Solution #25 Updates procedures for the scenarios in TS 23.558 for ACR between EAS and CAS
  For an ACR from EAS to CAS, DNS based solution can be used to discover CAS.
  But for an ACR from CAS to EAS, the rich SA6 way of discovering EAS should be used rather than DNS.
EES is essential for utilizing SA6 specified rich way of Rel-17 T-EAS Discovery (TS 23.55)
  EES plays a key role in the discovery procedures as discovery requests are sent to an EES whether the request originates from EEC, S-EAS or S-EES (when the T-EES is different).
  Therefore, for CAS to use the Rel-17 SA6 specified EAS discovery methods and utilize EDGE-14, it needs to know the EES before the discovery.
  This is captured also in TR 23.700-98 Clause 7.25.2.2.5: “Editor's Note: How CAS knows the EES is FFS. ”

## Slide 3: Options for CAS to know the EES
Option 1: Configuring the CAS with EES endpoint information (like in TS 23.558 clause 8.4.3.2.2) : This option will not work because there is no fixed EES for CAS and the EES changes with the mobility of the UE.
Option 2: Discover the EES via the ECS with EDGE-15 : this will require the ECS to maintain the EES in use, so that it can help in discovering the EES that is serving the desired EEC.
Option 3: Discover the EES vis the UE by triggering service provisioning in the EEC and receiving the EES endpoint via the AC.
Option 4: Have a global EES provided by the ECSP which does not have service area restriction, which can be configured in the CAS (like TS 23.558 clause 8.4.3.2.2)

## Slide 4: Proposal and Question
Option 3 or/and Option 4 are feasible directions.
Option 3 reuses existing procedures from Rel-17 but requires the EES endpoint information (e.g. URI) to be shared from the EEC to the CAS via the AC.
Option 4 is similar with Solution#24 CES based solution with an exception that it is used only for an ACR from CAS to EAS.
What are the dispositions of companies for the options?