## Slide 1: Discussion on AHGC end2end encryption
Samsung

## Slide 2: Outline
Background
End-to-end encryption
Preconfigured group
Discussion points

## Slide 3: Background
Draft TR 23.700-76 captured the following solutions for the AHGC
  AHGC where the participants list is provided by the initiator of the communication
  AHGC where the participants list determined by the MC system based on the criteria provided by the initiator of the communication
  AHGC involving users from multiple MC system
  Modifying the participants list of on-going ad hoc group communication
  Configuration parameters required for the AHGC
Note : Procedures for AHGC shall need to support end-to-end encryption

## Slide 4: End-to-End encryption
Following methods are proposed in AHGC study to achieve end-to-end encryption:
  Originator of the AHGC generates the AHGC Key and shares with the participants of the AHGC – This is proposed for the case where participants list is provided by the initiator of AHGC
  Pre-configured group is used for achieving end-to-end encryption for both the cases [Initiator providing the participants list and MC system determining the participants list]

## Slide 5: End-to-End encryption [Initiator generating the AHGC key]
  Initiator of the ad hoc group call generates the AHGC key on the similar lines of PCK and PCK ID
  Security key generated for AHGC shared to the target participants individually encrypted using the target participant’s user ID (similar to the private call)
  Please note that the same security material is shared by the initiator to all the participants for the ad hoc group call
  Required precondition for this mechanism to work :
  Initiating MC service user shall have the MC Service ID and the KMS URI of the users being invited for the call

## Slide 6: End-to-End encryption [Using Pre-Configured Group]
AHGC request carries the pre-configured group ID which serves as the source of security related information
The MC service group identity and group configuration for the preconfigured MC service group have to be preconfigured in MC service clients participating in AHGC

## Slide 7: Pre-configured Group [Excerpts]
Excerpts from 23.280
  Definition : An MC service group used only for regrouping that has been configured in advance of a group or user regrouping operation to serve as the source of regroup group configuration.
  A group regroup may be achieved by regrouping MC service groups into a new MC service regroup group which uses the configuration of a separate preconfigured MC service group.
  A preconfigured group which is intended only to provide configuration for the preconfigured regroup process is identified by a parameter in group configuration described in this specification.
  The preconfigured MC service group that provides the configuration is not used as the MC service regroup group itself, it only provides configuration for one or more MC service regroup groups
Excerpts from 33.180
  All users invited to join a secure group regroup with preconfigured group call shall be members of the indicated preconfigured group and shall have obtained the preconfigured group configuration and GMK.

## Slide 8: Discussion Points
For user regroup and group regroup to work, it is said that pre-configured group shall be available in advance before regroup operation is triggered. i.e., the dispatcher/authorized user can create pre-configured group and then does the regroup operation. But AHGC call can be initiated by normal user also and in this case how can user make sure that pre-configured group is available at all the participants ?
Pre-configured group is like any other group but its just labelled as pre-configured group and it cannot be user for communication and also it cannot participate in regroup operation. Pre-configured group has group members or not? As per 33.180 it is clear that it has members.
When the participants list is determined by the MC system, it can choose the appropriate pre-configuration and if nothing available pre-configuration can be created by the system before AHGC request is sent. Is it possible for the end-user (normal user) to do this ?
Usage of Preconfigured group for the AHGC where the participant list is provided by the initiator would be a limitation since user cannot assess whether the Preconfigured group is available at all the participants.
In case where the participants list is determined by the MC system, availability of preconfigured group at all the participants client can be assessed by the system before placing AHGC request

## Slide 9
Thank You !!!