## Slide 1: Discussion about DAA
Niranth (Huawei)

## Slide 2: KI on DAA
4.4 Key issue #4: Support of detect and avoid services and applications
  Development of the Support of Detect and Avoid Mechanism in 3GPP system is being studied in 3GPP TR 23.700-58 [6]. The 5GC enhancement work for DAA includes services for network assisted DAA and direct DAA via PC5.
  Considering the stage 1 requirements and also 5GC enhancements for DAA, it is required to study the aspects that UAE layer and SEAL can be supported for DAA.
  Further study is also required for UAE layer to support DAA scenarios where UAVs belong to multiple PLMNs.
  It is required to study the following:
  a) Whether and how the UAE layer and/or SEAL services can be enhanced to support DAA services and applications for collision avoidance considering the Stage 1 requirements.
  b) How the UAE layer can support DAA scenarios where UAVs belong to multiple PLMNs.
  NOTE: Solutions for DAA will be coordinated with the conclusions of the work outlined by 3GPP TR 23.700-58 [6] and based on requirements for DAA specified in 3GPP TS 22.125 [2].

## Slide 3: Understanding DAA
It is well understood based on several industry references that DAA is an application specific layer mechanism which deals with:
  A host UAV detecting other UAVs or objects with whom collision is possible.
  An USS detecting other UAVs or objects with whom a host UAV may collide.
  The action of a host UAV (either self initiated or as commanded by USS) to position the host UAV to avoid collisions.
  Interactions between host UAV and other UAVs or host UAV and USS for DAA related signaling.

## Slide 4: Possible UAE layer support for DAA
In TS 23.255, clause 7.5 provides a capability to report real-time UAV location update to UASS (USS).
  This capability further utilizes SEAL capabilities.
  The USS collects all the UAVs real-time information to manage DAA scenarios.
Provide real-time location based UAVs report to host UAV or USS by using existing SEAL capabilities.
  Provides information of UAVs to support the application logic of DAA.
  Potential solution contribution to SA6#52.

## Slide 5: Summary
Focus on capabilities at UAE layer to SUPPORT the mechanisms of DAA.
Whether 3GPP can specify DAA mechanisms at UAE layer requires more clarifications from SA1 or suitable UAS fora.