## Slide 1
Source:
Airbus, Airwave, CESG, French MoI, Harris, Motorola Solutions, Qualcomm, Selex, Sepura, Thales
Functional Architecture
for MCPTT
3GPP TSG SA6 Meeting #1 S6-150013
Sorrento, IT; 26th – 30th January 2015

## Slide 2: Introduction
This presentation is a multi-company input contribution to 3GPP SA6
A joint workshop was held between members of OMA PCPS and ETSI TCCE WG4 on 2-4 December 2014 in Cambridge, UK.
The workshop produced a high level functional architecture, and mapped this to existing OMA PCPS and TCCE stage 2 architectures which include PTT functionality
This presentation summarises the architecture produced, and its comparison to PCPS and TCCE work
The contributing companies recommend that the architecture is considered for the SA6 MCPTT TR
The strong alignment with OMA PCPS and TCCA CCA allows reuse of concepts from existing work from OMA and ETSI

## Slide 3
SIP
registrar
Authent-ication
SIP routing
User Identity
function
Media control
Media distribut-ion
PTT services
Group manage-ment
Resource Manage-ment
SecurityManage-ment
Bearer network
PCRF
BMSC
Administration database
PGW
PGW
AS6
AS7
AS8
AP1
AP2
AP3
AP4
AP5
AP6
AP7
AP8
AP9
High Level Functional Architecture from Workshop
Client
AS3-1
AS5
AS4-1
AS4-2
AS3-2
AS1
AS2
AS9

## Slide 4: Functional Entity Description - 1
User Identity: Function enabling the authentication of the user identity. Sits above SIP registrar contains details of user independent of services and devices; includes security parameters related to the user (but not to groups; control vs media TBC).
SIP registrar: maps user’s address of record (SIP URI) to contact IP addresses
SIP routing: Enables routing of SIP messages to appropriate destinations to allow services between clients & servers
  May also have function for connection maintenance (firewall, NAT etc)
PTT Services: Master logic responsible for call control and management; destination for SIP routing related to PTT calls; timer management, configuration and settings management; + resource control (priority, queueing, pre-emption management…), mobility tracking (cell/MBSFN awareness) etc
  Currently includes both home and local functions; may be divided later
  Big bucket of functions, may be further divided later

## Slide 5: Functional Entity Description - 2
Media control: floor control and possible other functions
Media distribution: distribution of media for both unicast and multicast bearer, including replication of media content where needed
Resource management: controls bearers under direction from PTT services’ resource control function (controls via RX, MB2-c etc)
Group management: contains provisioning information related to groups and mapping of users to groups; responsible for distribution of group information to clients, and group-membership information to PTT services
Security management: policy & key management for media, related to groups and individual media.
NOTE: IP route setup and maintenance is out of scope for current discussion

## Slide 6: Interface descriptions 1
Interface types
  AS: Application Service interface, likely to be standardised
  AP: Application Provisional interface, may be standardised
AS1:
  Supports user identity function
    Used for log-on purposes
  Flows through SGi and Uu
  Non SIP based
AS2:
  Supports client SIP interactions with the application function
  Flows through SGi and Uu
    May utilise Gm* if IMS is in use
AS3-1:
  Media control unicast interface
  Non SIP; carried on UDP; format is based on (S)RTCP
  Flows through SGi and Uu
NOTE: APx interfaces may be split or extended depending on decomposition of PTT services entity

## Slide 7: Interface descriptions 2
AS3-2
  Media control multicast interface
  Non SIP; format similar (or identical) to AS3-1
  Flows through MB2-u and Uu
AS4-1
  Unicast media distribution interface
  Non SIP; (S)RTP based
  Flows through SGi and Uu
AS4-2
  Multicast media distribution interface
  Non SIP; (S)RTP based
  Flows through MB2-u and Uu
AS5
  Group management to/from client
  Based on XCAP; possibility of OMA XDM
  Flows through SGi and Uu
AS6
  MB2-c
NOTE: APx interfaces may be split or extended depending on decomposition of PTT services entity

## Slide 8: Interface descriptions 3
AS7
  Rx
AS8
  Support for administrative and call control functions for PTT services
  SIP based
AS9
  Supports key distribution function to client for end to end media encryption
  AS9 interface may not be required if transport can be SIP based (interface to SIP routing and AS2) or if it can reuse another transport interface
  Security associations shall be able to be independent of other interfaces (AS2, AS3-1, AS3-2 etc)
AP1
  Supports user identity function for PTT services
    E.g. OAuth, SAML
NOTE: APx interfaces may be split or extended depending on decomposition of PTT services entity

## Slide 9: Interface descriptions 4
AP2
  Supports SIP registrar functions for PTT services
  AP2 interface may not be required if all functions can be SIP based, and so flow over AS8
  Protocol TBD
AP3
  Supports floor control and other media management for PTT services
  Non SIP based
  Protocol TBD
AP4
  Supports control of media distribution function
  Non SIP based
  Protocol TBD
AP5
  Supports control of resource management function for PTT services
  Non SIP based
  Protocol TBD
NOTE: APx interfaces may be split or extended depending on decomposition of PTT services entity

## Slide 10: Interface descriptions 5
AP6
  Supports group management for PTT services
  Based on XCAP; possibility of OMA XDM
AP7
  Supports user identity function for SIP Registrar
    E.g. OAuth, SAML
  May be unnecessary: alternative flows could be AP1-AP2 or AP1-AS8-AP8
AP8
  Interface for SIP Registration function
AP9
  Supports information transfer concerning users and groups from PTT services to Security Management (to enable end to end media encryption associations etc)
  Protocol TBD
NOTE: APx interfaces may be split or extended depending on decomposition of PTT services entity

## Slide 11: Identities
Visible in bearer network
IMEI – 3GPP equipment identifier
USIM
  UICC application
  IMSI – 3GPP subscription identifier, necessary for access to 3GPP network (contained on USIM)
    Root of security
ISIM – IMS subscription identity module
  UICC application
  IMPI – Private identity to route to registrar
  IMPU – Public identity known to others
  Can reuse IMSI security, or can be separate
******************************************************************
Visible to application domain only
User + device instance specific identifier
  SIP device specific routable contact address (URI) for the user following ‘logon process’
  Multiple devices, multiple URIs per user supported
  Application level security
User Identity
  Use for logon + security credential
  Device independent
  Identity useable across multiple services
  Temporary identity for emergency situation

## Slide 12: Security considerations
Architectural model has to fit different ownership and trust relationships:
  System can be divided between users, application, registration, routing and bearer networks
  Separate organizations may own one or more of each of these with limited trust between them

## Slide 13: Architecture mapping

## Slide 14: Mapping of Workshop Architecture Interfaces to PCPS and TCCE Architecture Interfaces
Workshop Architecture Interface | PCPS Architecture Interface | TCCE Architecture Interface
AS2 | POC1 | A1
AS8 | POC2 | No mapping
AS3-1, AS4-1 | POC3 | A2
AS3-2, AS4-2 | POC16, POC17 | A3
AS5 | XDM3 | No mapping
AP6 | XDM14 | No mapping
AS1, AS9 | No mapping | No mapping
AP1, AP2, AP3, AP4, AP5, AP7, AP8, AP9 | No mapping | No mapping
AS6 | No mapping | A5
AS7 | No mapping | A4

## Slide 15: Mapping of Workshop Architecture Functions to PCPS Architecture Functional Entities
* Colour coding on subsequent architecture diagrams shows mapping to equivalent functional entities.
Workshop Architecture Functions* | PCPS Architectural Diagram Functions | TCCE CCA Stage 2 Architectural functions
SIP Registrar, SIP Routing, SIP Authentication | SIP / IP Core | SIP Application Server + optional SIP Proxy
Bearer Network | Access Network | Broadband IP access network
Client on the UE | PoC Client, XDMC | Critical Communications Architecture – mobile part
PTT Services, Media Control, | PoC Server | Application Server Resource Management (controlling part) Mobility Management
Media Distribution |  | Media Distribution
Group Management | XDMS | Group Management
Resource Management | No mapping | Resource Management (interface part)
Security Management |  | Security Management - part
User Identity Function, |  | No Mapping

## Slide 16: Mapping of Workshop Architecture Interfaces to PCPS Architecture Interfaces
Client
SIP
registrar
Authent-ication
SIP routing
User Identity
function
Media control
Media distribut-ion
PTT services
Group manage-ment
Resource Manage-ment
SecurityManage-ment
Bearer network
PCRF
BMSC
Administration database
PGW
PGW
AS1
AS2
AS3-1
AS3-2
AS4-1
AS4-2
AS5
AS6
AS7
AS8
AP1
AP2
AP3
AP4
AP5
AP6
AP7
AP8
AS9
AP9

## Slide 17: Mapping of Workshop Architecture Interfaces to TCCE Architecture Interfaces
SIP
registrar
Authent-ication
SIP routing
User Identity
function
Media control
Media distribut-ion
PTT services
Group manage-ment
Resource Manage-ment
SecurityManage-ment
Bearer network
PCRF
BMSC
Administration database
PGW
PGW
AS1
AS2
AS3-1
AS3-2
AS4-1
AS4-2
AS5
AS9
Client
AP3
AP4
AP5
AP6
AP9
AS8
AP1
AP2
AP7
AP8
AS6
AS7

## Slide 18: Summary
Workshop developed a high level functional architecture which maps to existing PCPS and Stage 2 TCCE architectures
Commonality with both PCPS and TCCE has been mapped and shows reuse of both architectures may be possible
The architecture is provided to SA6 for consideration for inclusion in a Technical Report