## Slide 1: Registration, calling and roaming topics For discussion Agenda item 8.1
Dave Chater-Lea
(david.chater-lea@motorolasolutions.com)
Motorola solutions UK Ltd

## Slide 2
The purpose of this presentation is to step through the processes of registration, call set up and roaming for discussion, to attempt to achieve a common view before proposed architectures are discussed and evaluated.
Its basis is the simplified functional architecture presented in the conference call on 12 February 2015
  Three ‘internal’ interfaces to the application space have also been labelled B1, B2, B3
Presentation contents

## Slide 3
High Level Functional Architecture simplified
SIP core
MCPTT core
User Services Core
PCRF
BMSC
Client
PGW
Rx
MB2-c
MB2-u
SGi
HSS
SGW
MME
EPC
RAN
User Based Services
MCPTT application
A1a
A1b
A2
A3
A1a
A1b
A2
A3
A4
A5
Interfaces: A1: application control
A1a: Mgmt, identity,
security
A1b: SIP
A2: Media unicast
A3: Media multicast
A4: Rx
A5: MB2-c
B1: MCPTT to USC;
application
B2: MCPTT to SIP
core, SIP
B3: USC to SIP core,
control
A1a=AS1, 5, 9
A1b=AS2
A2=AS3-1, AS4-1
A3=AS3-2, AS4-2
A4=AS7 = Rx
A5=AS6 = MB2-c
B1
B2
B3

## Slide 4
Relevant requirements from 22.179:
  [R-5.13-002] The MCPTT Service shall support MCPTT User with globally unique identities, independent of the mobile subscriber identity (IMSI) assigned by a 3GPP network operator to UEs.
  [R-5.13-003] The MCPTT identities shall be part of the MCPTT application service domain.
  [R-5.13-004] The MCPTT identities shall form the basis of the MCPTT application layer security for the MCPTT Service.
We assume (at least) three application identities relevant to a user in a session:
  Primary private identity, with which user logs on, associated with some credential (password, biometric, token etc)
  Primary and generic permanent public identity
    SIP URI e.g. Officer_321_Smith@Thames_Valley.Police.UK
    This is the identity stored in other users’ phone books to allow this officer to be called
    This can also be used in off-network mode as calling (/talking party?) address
  Device and instance specific identity sent to the SIP Core by the MCPTT Client during registration
    Device specific SIP URI dynamically provided by MCPTT Client based on IP address of device on current Network
    E.g. PTT-Client321-Dev1@PTTClient321Dev1.networkA.UK (handheld)
    or PTT-Client321-Dev2@PTTClient321Dev2.networkA.UK (tablet)
    This identity is used by the MCPTT system to register and route to this user
Identities

## Slide 5
Registration process
SIP core
MCPTT core
User Services Core
PC
RF
BMSC
PGW
Rx
MB 2-c
MB 2-u
SGi
HSS
SGW
MME
EPC
RAN
User Based Services
MCPTT
application
A1a
A1b
A2
A3
A1a
A1b
A2
A3
B1
B2
B3
Client
User activates client application
Secure session (HTTPS/TLS) set up over A1a to USC. Logon identity and credentials (password, biometric etc) supplied by the user to authenticate user of this device
Client is provided authentication/security token by Identity Management within USC to be included during SIP registration
Client performs SIP registration with SIP core (interface A1b); Client supplies Generic SIP URI (public identity), Device specific SIP URI, and authentication/security token
  SIP core could validate authentication/security token with USC if necessary, using interface B3
SIP Core forwards client registration to MCPTT Core (or other service as needed); MCPTT Core subscribes to registration state information for this client; notification of registration events are passed to MCPTT server over the B2 interface
  MCPTT server uses Generic Identity, authentication/security token, and MCPTT portion of USC database to either accept or reject the this client’s registration
Result: Client is registered with SIP core with Generic URI and associated Device specific dynamic identity; PTT Client is registered with MCPTT service

## Slide 6: Group configuration & affiliation process
Groups are configured by the USC; services (MCPTT, video etc) that are allowed to use a group are also stored within the USC
Group affiliation can be performed without starting a communication session by using SIP SUBSCRIBE, or together with session start using a SIP INVITE
Affiliations using SUBSCRIBE are routed to USC over B3
Session setup using SIP INVITE (using A1b) are routed to the Service being requested (i.e. MCPTT) over B2
  The USC could be optionally informed by the MCPTT core using interface B1
200 OK response to INVITE carries address/port number of media function
Group call session setup can be linked to affiliation (‘open session’) or deferred (‘discrete calls’)
SIP core
MCPTT core
User Services Core
PC
RF
BMSC
PGW
Rx
MB 2-c
MB 2-u
SGi
HSS
SGW
MME
EPC
RAN
User Based Services
MCPTT
application
A1a
A1b
A2
A3
A1a
A1b
A2
A3
B1
B2
B3
Client

## Slide 7: Individual (Private) call
Calling user sends SIP INVITE (specifying a speech call) towards SIP core and is addressed to a user’s generic URI (interface A1b)
SIP core routes INVITE to MCPTT server over B2
  For another service in the future, the SIP core would route to a different application
Address/port for media signalling is carried in 200 OK response to INVITEs
Floor control in call is exchanged directly between MCPTT core and client using A2
SIP core
MCPTT core
User Services Core
PC
RF
BMSC
PGW
Rx
MB 2-c
MB 2-u
SGi
HSS
SGW
MME
EPC
RAN
User Based Services
MCPTT
application
A1a
A1b
A2
A3
A1a
A1b
A2
A3
B1
B2
B3
Client

## Slide 8: Group call
After group affiliation has been achieved, floor control uplink signaling is carried out directly using unicast media interface A2
Group downlink signalling may be sent over multicast interface A3 or unicast interface A2
If session has not been setup at group affiliation time, an INVITE needs to be sent at call setup, and the response will contain the details of the media interface
SIP core
MCPTT core
User Services Core
PC
RF
BMSC
PGW
Rx
MB 2-c
MB 2-u
SGi
HSS
SGW
MME
EPC
RAN
User Based Services
MCPTT
application
A1a
A1b
A2
A3
A1a
A1b
A2
A3
B1
B2
B3
Client

## Slide 9: Roaming
There are two cases of roaming:
  Home routing using the standard S8 interface between EPSs to provide IP connection back to the home MCPTT application
  Application roaming/Migration/Mutual aid case, where the client registers as a ‘guest’ on the visited server and is controlled by that visited server
Inter-MCPTT system calls could be considered to be a third case, where calls are placed between users who are at home at their different MCPTT servers
Both Mutual aid and inter-MCPTT system calls could allow group members to share the same MCPTT group
  It is FFS whether clients registered in a different server join the same group, or whether their local server hosts its own instance of that group, and the groups are linked

## Slide 10
Roaming with Home Routing
PCRF
BMSC
HSS
SGW
MME
PCRF
BMSC
PGW
HSS
Rx
MB2-c
MB2-u
SGi
S8
A1a
A1b
A2
SIP core
MCPTT core
User Services Core
User Based Services
MCPTT application
A1a
A1b
A2
A3
A4
A5
Client
RAN
NOTE: FFS whether multicast is possible in roamed environment
The UE roams at the 3GPP level, using inter-operator interfaces (and agreements)
All application functionality is carried out by the home server
QoS is controlled by the home network, subject to policy
S6a

## Slide 11
Application level migration (mutual aid etc)
Client
PCRF
BMSC
PGW
Rx
MB2-c
MB2-u
SGi
SGW
MME
EPC
RAN
A1a
A1b
A2
A3
SIP core
MCPTT core
User Services Core
User Based Services
MCPTT application
A1a
A1b
A2
A3
A4
A5
SIP core
MCPTT core
User Services Core
User Based Services
MCPTT application
M1
M2
Migration/roaming interfaces
M1: Identity, security, registration
M2: Inter-system call services
NOTE: SIP is not used inter-system for migrated client registration
HSS
S6a

## Slide 12: Application level migration
In this case, a client migrates to provide mutual aid
In this situation, he is directly controlled by the visited MCPTT server after registration – and is operationally controlled by dispatchers connected to the visited MCPTT server
The credentials are provided by the home USC; but client performs a SIP registration to the visited SIP core, and uses a URI addressed at that network
Call routing is performed by the visited application server
In a fallback case, where the inter-system application level links are not available, provided there is some default credential stored in the client and visited USC for the visiting user, all call services to and from that user are available, as the home system does not play a part in call routing