## Slide 1: Application Level Migration and PLMN Roaming: Scenarios for drafting Output from drafting call 29 April 2015
David Chater-Lea
Motorola Solutions UK Ltd

## Slide 2: Purpose
These slides have evolved over two drafting group sessions in SA6 #3, and the drafting call 29 April 2015

## Slide 3: Summary
Three scenarios were selected to be the basis of definition of interfaces
  Scenario 1: UE in visited PLMN using Primary MCPTT Service
  Scenario 2: UE in visited PLMN using Partner MCPTT Service with connection to Primary MCPTT server
  Scenario 3: Communicating between UEs in different home PLMNs using different Primary MCPTT Services (Interconnect)
Remaining scenarios considered to be subset of the above, or to have no MCPTT functionality
  See slide 16 for list

## Slide 4: Definition of MCPTT service Migration
Obtaining an MCPTT service from a partner MCPTT service provider

## Slide 5: Scenario 1: UE4 in visited PLMN using Primary MCPTT Service
UE1
MCPTT
Service A
UE2
UE3
UE4
Primary A
PLMN Home
PLMN Visited
Communications boundary for scenario (UE4 perception)
PLMN roaming only
No MCPTT service migration
Interconnection
MCPTT call related communication

## Slide 6: Scenario 1 variations
1.1 – all SIP entities in MCPTT service provider domain
1.2 – Registrar in MCPTT service provider domain, remaining SIP functionality in home PLMN
1.3 – All SIP entities in home PLMN
1.4 – Registrar in MCPTT service provider domain, outbound SIP proxy in visited PLMN, remaining SIP functionality in home PLMN
1.5 – Outbound SIP proxy in visited PLMN and remaining SIP functions in home PLMN

## Slide 7: Scenario 1 assumptions
Similar scenarios for HTTP may need to be evaluated (if not done in this exercise)
No assumptions made about database locations – each will be where needed
Resource management and bearer control is for further study

## Slide 8: Scenario 1.1 – all SIP entities in MCPTT service provider domain
EPS
SIP core
Application Services Layer Home
EPS
UE4
Home MCPTT service provider domain
SIP signalling
Non SIP signalling
Media inc floor control
Composite (all of above)
S8?
SIP/Gm*
Home PLMN domain
Visited PLMN domain

## Slide 9: Scenario 1.2 – Registrar in MCPTT service provider domain, remaining SIP functionality in home PLMN
EPS
SIP registrar
Application Services Layer Home
EPS
UE4
Home MCPTT service provider domain
SIP signalling
Non SIP signalling
Media inc floor control
Composite (all of above)
S8?
SIP/Gm*
SIP core*
SIP/Mw*
Home PLMN domain
Visited PLMN domain

## Slide 10: Scenario 1.3 – All SIP entities in home PLMN
EPS
SIP core
Application Services Layer Home
EPS
UE4
Home MCPTT service provider domain
SIP signalling
Non SIP signalling
Media inc floor control
Composite (all of above)
S8?
SIP/Gm*
SIP/ISC*
Home PLMN domain
Visited PLMN domain

## Slide 11: 1.4 – Registrar in MCPTT service provider domain, outbound SIP proxy in visited PLMN, remaining SIP functionality in home PLMN
EPS
SIP registrar
Application Services Layer Home
EPS
UE4
Home MCPTT service provider domain
SIP signalling
Non SIP signalling
Media inc floor control
Composite (media and non-SIP)
S8?
SIP/Gm*
SIP core*
SIP/Mw*
SIP proxy
SIP/Mw*/ICI*
Home PLMN domain
Visited PLMN domain

## Slide 12: 1.5 – Outbound SIP proxy in visited PLMN and remaining SIP functions in home PLMN
EPS
Application Services Layer Home
EPS
UE4
Home MCPTT service provider domain
SIP signalling
Non SIP signalling
Media inc floor control
Composite (media and non-SIP)
S8?
SIP/Gm*
SIP core
SIP/ISC*
SIP proxy
SIP/Mw*/ICI*
Home PLMN domain
Visited PLMN domain

## Slide 13: Scenario 2 : UE4 in visited PLMN using Partner MCPTT Service with connection to Primary MCPTT server
MCPTT
Service A
UE4
Primary A
PLMN Home
UEw
MCPTT
Service B
UEx
UEy
UEz
Partner A
PLMN Visited
Primary B
Interconnection
Communications boundary for scenario (UE4 perception)
MCPTT call related communication
Note: MCPTT service A may be involved in communication e.g. for logging purposes

## Slide 14: Scenario 2 possibilities
2.1 SIP entities in partner MCPTT service provider domain only
2.2 SIP entities in both MCPTT service provider domains (needs more breakdown?)
2.3 Registrar in visited MCPTT service provider domain, SIP core also in visited MCPTT service provider domain
2.4 Registrar in visited MCPTT service provider domain, SIP core within visited PLMN
2.5 Registrar and remaining SIP core functions in visited PLMN
NOTE: to consider further scenarios where the Registrar is located in the home PLMN or MCPTT server

## Slide 15: Scenario 2.1 – all SIP entities in partner MCPTT service provider domains
EPS
Application Services Layer Primary
EPS
UE4
Home MCPTT service provider domain
SIP signalling
Non SIP signalling
Media inc floor control
Composite (all of above)
Home PLMN domain
Visited PLMN domain
SIP core
Application Services Layer Partner
SIP/Gm*
Visited MCPTT service provider domain
PLMN level roaming signalling
Non SIP signalling (relation to red TBA)
IP network
Domain separation indicates some form of wide area IP networking

## Slide 16: Scenario 2.1 – all SIP entities in partner MCPTT service provider domains - steps
UE roams and authenticates at EPS level to home HSS
APN mapped to PGW in visited PLMN
  Requires subscription to permit this
MCPTT UE is provided with local breakout and uses IP connection to primary MCPTT service to authenticate, and receive a credential allowing access to partner MCPTT service
MCPTT UE uses credential to authenticate to partner MCPTT service
  Higher level authority may be used in validation process of credential, e.g. by signing the credential
MCPTT UE completes SIP registration with partner MCPTT service SIP core
Sequence ordering is not defined, at least with respect to SIP registration and user authentication

## Slide 17: Scenario 2.2 – all SIP entities in primary and partner MCPTT service provider domains
EPS
SIP core
Application Services Layer Primary
EPS
UE4
Home MCPTT service provider domain
SIP signalling
Non SIP signalling
Media inc floor control
Composite (all of above)
S8?
SIP/Gm*
Home PLMN domain
Visited PLMN domain
SIP core
Application Services Layer Partner
SIP/Gm*
Visited MCPTT service provider domain
SLIDE NOT YET WORKED ON: FOR FUTURE DRAFTING

## Slide 18: Scenario 3: Communicating between UEs in different home PLMNs using different Primary MCPTT Services (Interconnect, not a roaming/MCPTT service migration scenario)
UE1
MCPTT
Service A
UE2
UE3
UE4
Primary A
PLMN Home
UEw
MCPTT
Service B
UEx
UEy
UEz
Primary B
PLMN Home
Communications boundary for scenario (UE4 perception)
Interconnection
MCPTT call related communication
Example: group communications between MCPTT authorities in two different countries
MCPTT service A and MCPTT service B have a business relationship
May become the basis in the future for interworking with other (non-3GPP) technologies
Path that may or may not be necessary to support the service interconnection

## Slide 19: Remaining scenarios
The following scenarios were not analysed, as they were covered by previous scenarios, or combinations of those scenarios, or outside the scope of SA6 MCPTT work
Scenario 4: UEs in home PLMNs using Primary MCPTT Services
  No roaming, no migration, therefore no roaming interfaces involved
Scenario 5: UE in visited PLMN using Partner MCPTT Service without making use of real time connection to Primary MCPTT server
  Migration but without real time interfaces
  Waiting for response from SA1 whether this case is required
Scenario 6: UE in visited PLMN not using any MCPTT Service
  Normal PLMN services only, no MCPTT functionality: out of SA6 scope
Scenario 7: UE in visited PLMN using Partner MCPTT Service, communicating with both members of home and Partner MCPTT Service
  A combination of scenarios 1 ,2 and 3: will not add further interface requirements
Scenario 8: UE in same home PLMN using Partner MCPTT Service with connection to Primary MCPTT server
  A subset of scenario 2, where no further interfaces will be observed
Scenario 9: Communicating between UEs on the same home PLMN using different Primary MCPTT Services
  A subset of scenario 3, where no further interfaces will be observed
Scenario 10: UE in home PLMN using a Primary MCPTT Service not in UE4’s Home PLMN
  A subset of scenario 3 (interworking) where no further interfaces will be observed
Scenario 11: UE in home PLMN using a Partner MCPTT Service not in UE4’s Home PLMN
  A subset of scenario 3 (interworking) where no further interfaces will be observed

## Slide 20: Scenario 4 : UEs in home PLMNs using Primary MCPTT Services
UE1
MCPTT
service
UE2
UE3
UE4
Primary
PLMN Home
Communications boundary for scenario (UE4 perception)
Home case, no PLMN roaming, no MCPTT service migration, no further discussion
Note: case could include MCPTT service and PLMN provider being the same or different
Interconnection
MCPTT call related communication

## Slide 21: Scenario 5 : UE4 in visited PLMN using Partner MCPTT Service without making use of real time connection to Primary MCPTT server
MCPTT
Service A
UE4
Primary A
PLMN Home
UEw
MCPTT
Service B
UEx
UEy
UEz
Partner A
PLMN Visited
Primary B
Interconnection
Communications boundary for scenario (UE4 perception)
MCPTT call related communication
R6.18.2 – 005
MCPTT services A and B have a relationship
Online connection is not present or not used in this scenario
e.g. emergency communication, loss of MCPTT service A
Scenario subject to confirmation by SA1

## Slide 22: Scenario 6 : UE4 in visited PLMN not using any MCPTT Service
UE4
PLMN Home
UEw
UEx
UEy
UEz
PLMN Visited
Communications boundary for scenario (UE4 perception)
Note: has no impact on MCPTT service
Scenario is noted, for no further work
Out of scope of SA6 work
Interconnection
MCPTT call related communication

## Slide 23: Scenario 7: UE4 in visited PLMN using Partner MCPTT Service, communicating with both members of home and Partner MCPTT Service
UE1
MCPTT
Service A
UE2
UE3
UE4
Primary A
PLMN Home
UEw
MCPTT
Service B
UEx
UEy
UEz
Primary B
PLMN visited
Partner A
Communications boundary for scenario (UE4 perception)
Interconnection
MCPTT call related communication
Scenario 7 represents the combination of scenarios 1 and 2, using the interconnection of scenario 3
No new connections (Note: was 2 and 4 using 6)

## Slide 24: Scenario 8: UE4 in same home PLMN using Partner MCPTT Service with connection to Primary MCPTT server
MCPTT
service
UE4
Primary
PLMN Home
(all UEs)
UEw
MCPTT
service
UEx
UEy
UEz
Partner
Primary
Communications boundary for scenario (UE4 perception)
Note: this is a simplified case of scenario 2 (was 4) (two PLMNs)
No further work foreseen
Interconnection
MCPTT call related communication

## Slide 25: Scenario 9: Communicating between UEs on the same home PLMN using different Primary MCPTT Services
UE1
MCPTT
service
UE2
UE3
UE4
Primary
UEw
MCPTT
service
UEx
UEy
UEz
Primary
Communications boundary for scenario (UE4 perception)
PLMN Home
(all UEs)
Simplified case of scenario 3 (was 6) (two PLMNs)
No further work foreseen
Interconnection
MCPTT call related communication

## Slide 26: Scenario 10: UE4 in home PLMN using a Primary MCPTT Service not in UE4’s Home PLMN
MCPTT
Service A
UE4
Primary A
PLMN Home
UEw
MCPTT
Service B
UEx
UEy
UEz
Primary B
PLMN Visited
Communications boundary for scenario (UE4 perception)
MCPTT services A and B have a relationship
e.g. patch in member of a different network
Scenario better achieved by scenario 6: no further work on this case
Also similarities with scenario 3
NB: this could still be a backup case
Use case covered by scenario 3 (was 6) – this case rejected
Interconnection
MCPTT call related communication

## Slide 27: Scenario 11: UE4 in home PLMN using a Partner MCPTT Service not in UE4’s Home PLMN
MCPTT
Service A
UE4
Primary A
PLMN Home
UEw
MCPTT
Service B
UEx
UEy
UEz
Primary B
PLMN Visited
Communications boundary for scenario (UE4 perception)
Partner A
Use case covered by scenario 3 (was 6) – this case rejected
Interconnection
MCPTT call related communication